## Slide 1: Radiation Protection in Dental Radiology
General Principles of Radiation Protection
L01
Training material developed by the International Atomic Energy Agency
in collaboration with: World Health Organization, FDI World Dental Federation, International Association of Dento-Maxillofacial Radiology, International Organization for Medical Physics, and Image Gently Alliance

## Slide 2: Educational Objectives
Understand the importance of adhering to the principles of radiation protection in dentistry
Understand the properties of ionizing radiation (esp. x-rays), and their effects on living tissue
Distinguish between stochastic effects and tissue reactions
Distinguish between absorbed dose, equivalent dose and effective dose
Understand the linear-non-threshold model and its implication for radiation protection
Understand the dose-risk relation of stochastic effects, and the effect of age and gender
Understand the principles of justification, optimization of protection, and application of dose limits
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 3: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 4: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 5: Why radiation protection in dentistry?
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Modern dental office:
  Variety of radiographic equipment
    Intra-oral, panoramic, cephalometric, cone-beam CT, ….
  Several people prone to radiation exposure
    Patient being imaged, other patients, dentist, other dental workers, …

## Slide 6: Why radiation protection in dentistry?
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
High frequency of dental radiographs performed worldwide: conservative estimate >1.5 billion / year (EC 2014, Farris & Spelic 2015)
Source: UNSCEAR, 2008

## Slide 7: Why radiation protection in dentistry?
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Use of cone-beam CT in dental practice
  Higher patient radiation dose than 2D radiography and panoramic radiography (see L09)
  Increased availability & frequency of use

## Slide 8: Why radiation protection in dentistry?
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Relatively high % of pediatric radiographs in dentistry, e.g. for:
  Caries assessment
  Orthodontic planning
  Developmental disorders (e.g. cleft palate)
See L02 for general radiation protection considerations for children

## Slide 9: Why radiation protection in dentistry?
Self-referral issue in dentistry (Farman 2009)
  May increase the frequency of imaging examinations compared with referral to a radiologist
  Issue is compounded due to the introduction of CBCT in dentistry
    Economical considerations
    Legal considerations (“protective imaging” is not in line with the justification principle and should be avoided)
    Training and expertise to interpret CBCT images
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 10: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 11: What is radiation?
Radiation refers to the transmission of energy (as waves or particles) in a medium
  Electromagnetic radiation (e.g. visible light, X rays)
  Particle radiation (e.g. α, β, neutron)
  Acoustic radiation (e.g. sound, ultrasound)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Smoke detector
(contains α-emitter)
Ultrasound image
The sun
(EM radiation)

## Slide 12: The electromagnetic spectrum
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
    Minimal energy for ionization:13.6 eV or 2.18*10-18 J
    (binding energy of hydrogen electron)
Energy
(eV or J)
NON-IONIZING
IONIZING

## Slide 13: Biological effects of ionizing radiation
At a sub-cellular level, ionizations due to radiation can lead to direct and indirect effects on the DNA
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
DNA
Direct effect
(radiation interacts with DNA molecule)
H2O
Indirect effect
(radiation interacts with water and generates reactive free radicals, which then interact with DNA)

## Slide 14: Biological effects of ionizing radiation
At a cellular/tissue level, effects are categorized as stochastic or deterministic (tissue reactions)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
LOW DOSES
HIGH DOSES
STOCHASTIC EFFECTS (PROBABILISTIC)
Cell death
DETERMINISTIC EFFECTS (TISSUE REACTIONS)
Cell mutations
Loss of function (organ/ system/ organism)
Cancer, leukaemia
Hereditary effects
Germ cell
Somatic cell

## Slide 15: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 16: Radiation dose
Different quantities are used to express radiation ‘dose’
Absorbed dose: mean energy E imparted by ionizing radiation to matter of mass m
  D = (unit: 1 gray (Gy) = 1 J/kg)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
X ray tube
Image receptor
An X ray beam contains a certain amount of energy
Part of this energy is absorbed by the patient

## Slide 17: Absorbed dose
In humans, absorbed dose is considered per organ or tissue
  e.g. absorbed dose to brain = (total) energy absorbed by brain divided by (total) mass of brain
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 18: Absorbed dose
For non-whole-body exposures (i.e. most medical exposures), the absorbed dose to an organ or tissue highly depends on its exposed fraction
    For dental radiographic examinations, the highest absorbed doses for whole organs/tissue are typically at the thyroid gland, salivary glands, oral mucosa and extrathoracic airways
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
    Another 0.3% of the skin receives scattered and non-attenuated primary exposure (see further), with a local absorbed dose of ~0.5 mGy*
    The other 99.6% of the skin receives ~0 mGy*
    → Absorbed dose to (total) skin: 3.5 µGy (0.0035 mGy)
Typical X ray beam size for intra-oral radiograph
    ~0.1% of the skin receives a direct X ray exposure, with a local absorbed dose of ~2 mGy*

## Slide 19: Equivalent dose
Equivalent dose: absorbed dose multiplied by radiation weighting factor wR
  H = wR.D (unit: sievert [Sv])
  Used for tissues/organs; wR is related to biological effectiveness (see figure and slide notes)
  Higher value of wR indicates more damaging radiation
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
X ray / gamma ray (wR=1)
e-
β radiation (wR=1)
Neutron radiation
(wR between ~2 ~20)
n
Proton radiation (wR=2)
p
α radiation
Fission fragments
Heavy ions
(wR=20)
Notes: Current radiation weighting factors, determined by the ICRP in their Publication 103 (2007), are:
Photons: 1
Electrons and muons: 1
Protons and charged pions: 2
Alpha particles, fission fragments, heavy ions: 20
Neutrons: a continuous function of neutron energy (between ~2 and ~20)

## Slide 20: Equivalent dose
  For an absorbed dose of 1 mGy of:
    X rays, the equivalent dose is 1 mSv
    i.e. numerical value of absorbed dose and equivalent dose is the same for X rays, and they are often used interchangeably; only the unit is different
  Alpha particles, the equivalent dose is 20 mSv
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Notes: Current radiation weighting factors, determined by the ICRP in their Publication 103 (2007), are:
Photons: 1
Electrons and muons: 1
Protons and charged pions: 2
Alpha particles, fission fragments, heavy ions: 20
Neutrons A continuous function of neutron energy (between ~2 and ~20)

## Slide 21: Effective dose
Effective dose: tissue-weighted sum of equivalent doses to all tissues/organs in the body at risk for stochastic effects
  e.g. red bone marrow, thyroid gland, salivary glands, skin, brain
  Not the eye lens (radiation-induced cataract is not a stochastic effect)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 22: Effective dose
Tissue weighting factors wT
  Determined by ICRP, periodically revised
  (last version: ICRP Publication 103, 2007)
  Based on epidemiological & experimental data (e.g. atomic bomb survivors)
  A higher wT implies increased sensitivity to radiation (higher probability of stochastic effects for that organ/tissue at a given equivalent dose)
  The sum of all wT is 1
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 23: Effective dose
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
*Adrenals, Extrathoracic region, Gall bladder, Heart, Kidneys, Lymphatic nodes, Muscle, Oral mucosa, Pancreas, Prostate, Small intestine, Spleen, Thymus, Uterus/cervix
Organs of interest for dental exams are highlighted

## Slide 24: Effective dose
Calculation of effective dose:
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Equivalent dose to brain tissue * 0.01
+
Equivalent dose to thyroid * 0.04 +
Equivalent dose to bone marrow * 0.12
+
Equivalent dose to salivary glands * 0.01
+
Etc. (for all exposed organs/tissues)
Sum of these = Effective dose (Sv)

## Slide 25: Effective dose
Note: tissue weighting factors (wT) are updated by the ICRP when new evidence is available regarding dose vs. risk
Older (pre-2007) literature uses wT from ICRP Publication 60 to calculate effective dose
More recent literature uses wT from ICRP Publication 103
Notable changes for dental exposures: wT for salivary glands introduced (i.e. 0.01), thyroid wT lowered from 0.05 to 0.04
On average, doses for dental exposures estimated using ICRP 103 factors have been estimated to be 32-422% higher than those using ICRP 60 factors (Ludlow et al. 2008)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 26: Estimation of patient dose (1)
Anthropomorphic phantoms
  Represent ‘standard’ patient (adult, pediatric, female, …)
  Point measurements inside phantom allow for estimation of absorbed organ dose & effective dose
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 27: Estimation of patient dose (2)
Simulation (e.g. Monte Carlo)
  Dose calculated based on computer simulation of X ray source and X ray photon interactions
  Simulated object can be real patient (e.g. radiation therapy planning) or phantom
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Zhang et al. 2013
Courtesy of G. Zhang

## Slide 28: Estimation of patient dose (3)
Dose index & conversion factors
  Dose measurement in standardized set-up
  e.g. dose-area product
  Conversion factors (e.g. to effective dose) determined through physical measurements and/or simulation
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 29: Radiation dose
Effective doses from dental examinations
(For more details: see L09 & L11)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Adapted from: FGDP (UK), Selection Criteria For Dental Radiography

## Slide 30: Radiation dose
Effective doses from dental radiographic examinations are relatively low
  Many tissues/organs with high wT receive no or negligible radiation
  e.g. colon-lung-stomach-breast → combined contribution of 48% to effective dose, but receive no dose for a typical dental examination
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 31: Radiation dose
Stochastic risks from dental radiographs are limited to a few tissues
  Mostly salivary glands, thyroid gland, red bone marrow, oral mucosa, extrathoracic airways
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Based on data from Pauwels et al. 2014
Relative contribution of organs/tissues to effective dose from dental CBCT examinations
(RBM: red bone marrow)

## Slide 32: Radiation dose
Frequencies from dental radiographic examinations are relatively high
  UNSCEAR (2008): 17% of all medical examinations in regions with health care level I
  EC (2014): 32% of all plain radiography in Europe
In 2007, it was estimated that dental examinations account for less than 1% of the ‘collective dose’ from medical exposures
  Situation has likely changed due to wide spread of CBCT
  Pivotal to keep radiation doses from dental examinations low, to avoid considerable effect on population dose
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 33: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 34: Radiation dose vs. risk
How is ‘dose’ related to ‘effect’?
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
J. Scott Campbell &
Tim Townsend, Marvel Comics
Steve Ditko,
Marvel Comics
?

## Slide 35: Dose-effect relationship
For stochastic effects: linear-non-threshold model
Supported by epidemiological data for doses > 100 mSv e.g. life span study on atomic bomb survivors
Extrapolated for lower doses
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 36: Dose-effect relationship
The cancer risk from radiation depends on additional factors:
  Age (risk generally decreases with age; somewhat tissue-specific)
  Gender (overall cancer risk higher for females; highly tissue-specific)
  Individual sensitivity, presence of other risk factors such as obesity, smoking which increase the susceptibility to radiation-induced cancer
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 37: Dose-effect relationship
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Based on data from BEIR VII (2006)
Overall higher risk for females
Relative difference in risk between males and females is highest for children and decreases with age

## Slide 38: Dose-effect relationship
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Based on data from BEIR VII (2006)
Thyroid:
Much higher risk for females
Strong age-dependence
(negligible risk > 50 y.o.)

## Slide 39: Dose-effect relationship
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Based on data from BEIR VII (2006)
Leukemia:
Slightly higher risk for males
Age-dependence similar to overall risk, but remains relatively high at old age

## Slide 40: Dose-effect relationship
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Threshold dose
(no risk below this dose)
For tissue reactions (i.e. deterministic effects):

## Slide 41: Dose-effect relationship
For tissue reactions (i.e. deterministic effects):
  Threshold value is tissue-dependent
    Dose at which effects are seen for 1% of population
    e.g. eye lens: 0.5 Gy for a single exposure
    At doses well below the threshold, tissue reactions are absent
    At doses above the threshold, the severity of the effect increases
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 42: Dose-effect relationship
In dental radiology: deterministic effects extremely unlikely (even for repeated and/or over-exposures)
  e.g. high-dose CBCT scan: ~0.01 Gy locally at skin level
    intra-oral radiograph: typically 0.002-0.003 Gy at skin
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
 | Stochastic effects | Tissue reactions
Low dose (e.g. medical exposure) | Low probability | Will not occur
High dose (e.g. radiation therapy, accidents) | High probability | Will occur (if dose above threshold)

## Slide 43: Dose-effect relationship
What if I had many repeated (low-dose) exposures over my lifetime: will I experience tissue reactions?
  Apart from the dose, the dose rate also determines the risk for radiation-induced effects
  A lower dose rate allows cells/tissues to repair/heal between exposures
    A single exposure of 1 Gy is worse than 1000 exposures of 1 mGy over a prolonged period
  For tissue reactions in particular, thresholds are highly dependent on dose rate
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 44: Dose-effect relationship
Effects of radiation on the foetus
  Both stochastic effects (cancer, leukemia) and tissue reactions (early death, congenital malformations, mental retardation)
  Effects depend on absorbed dose and stage of pregnancy
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 45: Dose-effect relationship
Radiation risk highest during organogenesis and in the early foetal period (1st trimester), somewhat less in the 2nd trimester, and least in the 3rd trimester (ICRP 2000)
Effects on central nervous system (>100 mGy) particularly during week 8-15
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Less risk
Least risk
Most risk
“All or nothing” no malformations
1 – 2 weeks

## Slide 46: Overview
Why radiation protection in dentistry?
Ionizing radiation & its biological effects
Radiation dose
Dose vs. risk
General principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 47: Radiation protection: history
At discovery of X rays (1895): effects unknown
Soon after application of X rays: early and late deterministic/stochastic effects became obvious
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 48: Radiation protection: history
Early development of radiation protection was slow, with a few pioneers
  William Rollins (dentist): leaded tube housing, collimation
Recommendations by British Roentgen Society (1915) and American Roentgen Ray Society (1922)
1925: first tolerance doses reported
1928: Roentgen unit for measuring radiation
1928: International Commission on Radiological Protection (ICRP ) established (ICRU: 1925)
1957: International Atomic Energy Agency (IAEA) established
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 49: International standards
UNSCEAR
Effects of radiation
ICRP
Recommendations for protection
IAEA
Essential requirements
(legal obligation)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Notes: The jointly sponsored edition of the Safety Requirements “Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards” was published as General Safety Requirements Part 3 in July 2014. This edition supersedes the Interim Edition that was published in 2011, which itself superseded the International Basic Safety Standards that were issued as IAEA Safety Series No. 115 in February 1996. The joint sponsors are EC, FAO, IAEA, ILO, OECD/NEA, PAHO, UNEP, and WHO. The BSS will be published in all the official languages of the IAEA in due course.

## Slide 50: International Basic Safety Standards
Published by the IAEA in 2014
Jointly sponsored by eight international organizations
Essential requirements that must be met to ensure safety of radiation sources and protection of people
Based on the ICRP principles of radiation protection
Used as template for national regulations
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 51: Radiation protection: principles
ICRP defined three fundamental principles of radiation protection
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Justification of Practices
Optimization
of Protection
Application of
Dose Limits

## Slide 52: Radiation protection: principles
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
ICRP defined three categories of exposure:
  Medical exposure: exposure of patients for the purpose of medical or dental diagnosis or treatment; carers and comforters; volunteers in a programme of biomedical research involving their exposure
  Occupational exposure: exposure of workers incurred in the course of their work
  Public exposure: exposure of members of the public, excluding any occupational exposure or medical exposure

## Slide 53: Radiation protection: principles
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
 | Occupational exposure | Public exposure | Medical exposure
Justification of practices | Apply | Apply | Apply
Optimisation of protection | Apply | Apply | Apply
Dose limits | Apply | Apply | Do not apply

## Slide 54: Radiation protection: justification
The principle of justification: Any decision that alters the radiation exposure situation should do more good than harm (see L09)
  3 levels of justification of medical exposure:
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 55: Radiation protection: justification
What needs to be considered?
  Appropriateness of the request
  Urgency of the procedure
  Characteristics of the exposure
  Characteristics of the individual patient
    Special considerations for children, pregnant & breastfeeding patients
  Relevant information from previous radiological procedures
Relevant national or international referral guidelines to be taken into account
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 56: Radiation protection: optimization
The principle of optimization of protection: the likelihood of incurring exposures, the number of people exposed, and the magnitude of their individual doses should all be kept as low as reasonably achievable, taking into account economic and societal factors (see L11)
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Underexposure
(high noise)
Optimized exposure
(adequate image quality)
Overexposure
(high image quality, but high dose)

## Slide 57: Radiation protection: optimization
Factors to consider in optimization
  Design considerations for equipment
  Operational considerations
  Calibration
  Dosimetry of patients
  Diagnostic Reference Levels (DRLs)
  Quality assurance
  Dose constraints
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 58: Radiation protection: dose limits
The principle of application of dose limits: the total dose to any individual from regulated sources in planned exposure situations other than medical exposure of patients should not exceed the appropriate limits recommended by the ICRP (see L12).
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Type of limit | Occupational | Public
Annual effective dose | 20 mSv (100 mSv in 5 years) | 1 mSv
Annual equivalent dose to: |  | 
Eye lens | 20 mSv (100 mSv in 5 years) | 15 mSv
Skin | 500 mSv | 50 mSv
Hands and feet | 500 mSv | -
Dose limits for occupational and public exposure, according to the current ICRP recommendations and International Basic Safety Standards (2014)

## Slide 59: International Basic Safety Standards
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection
Crucial roles in radiation protection for medical exposures:
  Radiological medical practitioner (incl. dentistry)
  Medical physicist
  Medical radiation technologist
  Radiopharmacist (nuclear medicine)
John Wong,
John Hopkins Medicine
US Marine Corps
GE Healthcare

## Slide 60: International Basic Safety Standards
  Radiological medical practitioner:
  “A health professional with specialist education and training in the medical uses of radiation, who is competent to perform independently or to oversee radiological procedures in a given specialty (e.g. radiology, radiation therapy, nuclear medicine, dentistry, cardiology).”
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 61: International Basic Safety Standards
  “Competence of persons is normally assessed by the State by having a formal mechanism for registration, accreditation or certification of radiological medical practitioners in the given specialty. States that have yet to develop such a mechanism need to assess the education, training and competence of any individual and to decide whether such an individual could undertake the functions of a radiological medical practitioner, within the required specialty.”
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 62: References
EC, European Commission (2014) Medical Radiation Exposure of the European Population
Farman AG. (2009) Self-referral: an ethical concern with respect to multidimensional imaging in dentistry? J Appl Oral Sci. 17(5).
Farris K & Spelic D (2015) Nationwide Evaluation of X‐Ray Trends: Highlights of the 2014‐15 NEXT Dental Survey. Proceedings of the 47th National Conference on Radiation Control. CRCPD Publication: E-15-4, August 2015.
IAEA, International Atomic Energy Agency (2014). Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards. General Safety Requirements Part 3.
ICRP, International Commission on Radiological Protection (2000) Pregnancy and Medical Radiation. ICRP Publication 84, Ann ICRP 30,
ICRP, International Commission on Radiological Protection (2007) The 2007 Recommendations of the International Commission on Radiological Protection. ICRP Publication 103. Oxford: Pergamon.
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection

## Slide 63: References
ICRP, International Commission on Radiological Protection (2012) ICRP statement on tissue reactions and early and late effects of radiation in normal tissues and organs - threshold doses for tissue reactions in a radiation protection context. ICRP publication 118. Ann ICRP 2012;41:1-322.
National Research Council of the National Academies (2006) Health Risks from Exposure to Low Levels of Ionizing Radiation: BEIR VII. Washington, DC: The National Academies Press.
Pantos et al (2011) Adult patient radiation doses from non-cardiac CT examinations: a review of published results. Br J Radiol. 84:293-303.
Pauwels et al (2014) Effective radiation dose and eye lens dose in dental cone beam CT: effect of field of view and angle of rotation. Br J Radiol 87:20130654.
UNSCEAR, United Nations Scientific Committee on the Effects of Atomic Radiation (2008) Sources and Effects of Ionizing Radiation: Report to the General Assembly.
Zhang et al (2013) Monte Carlo modeling for dose assessment in cone beam CT for oral and maxillofacial applications. Med Phys. 40:072103.
Radiation Protection in Dental Radiology L01 General Principles of Radiation Protection