## Slide 1: Radiation Protection in Dental Radiology
Fundamentals of Extraoral Projectional Radiography
L07
Training material developed by the International Atomic Energy Agency
in collaboration with: World Health Organization, FDI World Dental Federation, International Association of Dento-Maxillofacial Radiology, International Organization for Medical Physics, and Image Gently Alliance

## Slide 2: Educational Objectives
Differentiate between lateral cephalometric, posteroanterior cephalometric, submentovertex, occipito-mental and occipito-frontal projections, in terms of positioning of patient & image receptor and respective clinical applications
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 3: Overview of most common techniques
Radiographs courtesy of P. Pittayapat, Chulalongkorn Univ.
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
LATERAL CEPH | SUBMENTO-VERTEX | OCCIPITO-MENTAL | PA CEPH | OCCIPITO-FRONTAL

## Slide 4: Planes used for patient positioning
Frankfurt Horizontal Plane
  Superior border of external auditory meatus
  Infra-orbital rim
Canthomeatal line
  Center of external auditory canal
  Outer canthus of eye
Alar-Tragus line
  Alar of nose
  Center of tragus
B
A
C
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 5: Image receptors in EOR
Film & different types of digital receptors
Film: in combination with intensifying screens (as in panoramic, but not intra-oral) (see L04)
Digital receptors (L04):
  Photostimulable phosphor (PSP)
  CCD, CMOS
  TFT
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 6: Skull radiography units
Cephalometric radiography units
  Focus-receptor distance 150-200 cm
  Typically combined with panoramic units (or with CBCT and pano, i.e. 3-in-1)
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 7: Skull radiography units
Other skull units
  Isocentric: most widely available; receptor and beam always perpendicular
  Lysholm: not widely used nowadays
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
R. Schulze

## Slide 8: Anti-scatter grids in EOR
Grid aligned with primary X ray beam: primary X rays pass through holes, majority of scatter will be absorbed
Higher (~2x) patient dose needed: only use when high contrast is required (e.g. normally not needed for lateral ceph)
Scatter grid for a parallel-beam geometry. A grid of lead strips ( ) is placed in front of the image receptor. Scattered radiation ( ) which is not parallel to the primary X rays ( ) will be absorbed by the grid. Only a small fraction of scattered radiation will pass through the grid ( )
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 9: Cephalometric radiography
Used to evaluate the relationship between anatomical points at the teeth, jaws and skull bones
  Orthodontics, maxillofacial surgery
  Covers more than maxillofacial area: should always be evaluated for any head & neck pathology (see step-wise evaluation White & Pharoah (2014))
Lateral and postero-anterior (PA) radiograph
Acquired at a relatively long source-to-patient distance
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 10: Lateral cephalometric radiograph
Most common extraoral projectional radiograph used in dentistry
Covers most of the head
Head in ‘natural position’ (vertical marker added as reference), Frankfort plane horizontal
Image receptor parallel to sagittal plane
Mouth closed, centric occlusion (i.e. biting back teeth together), lips relaxed
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
P. Pittayapat, Chulalongkorn Univ.

## Slide 11: Lateral cephalometric radiograph
Wedge filter used in anterior part of beam: reduces exposure to anterior soft tissue, enabling it to be visualized
Slight difference in magnification between anatomical structures on tube & detector side
  Difference in magnification increases with distance to midsagittal plane
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
Larger
magnification
Smaller
magnification

## Slide 12: P-A cephalometric radiograph
Second most common
  Facial asymmetries
  Orthognatic surgery
X ray tube behind the patient’s head, image receptor in coronal plane
Patient orientation: natural head position, Frankfort plane perpendicular to image receptor
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
P. Pittayapat, Chulalongkorn Univ.

## Slide 13: Cephalometric tracing & landmarks
Radiograph can be traced (digitally or on paper) for cephalometric analysis and to evaluate changes during treatment through superimposition
Landmarks: specific anatomical points
Can be used to evaluate angles and planes
Different types of analysis used
  e.g. Steiner, Ricketts, McNamara
Similar to lateral ceph: entire image should be evaluated
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography

## Slide 14: Cephalometric tracing & landmarks
Lateral ceph
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
Tracing (Ricketts)
Courtesy of K. de Faria Vasconcelos

## Slide 15: Occipito-mental projection
A.k.a. Waters’ projection
Beam angled (37-45°) to orbito-meatal line
Visualizes: Maxillary sinuses (primarily), orbits, frontal/ethmoidal sinus, zygomaticofrontal suture, nasal cavity, sphenoidal sinus (if mouth open)
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
D.M. Brasil

## Slide 16: Occipito-mental projection
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
D.M. Brasil
P. Pittayapat
Examples with closed mouth

## Slide 17: Submentovertex projection
Acquired with neck in maximal extension, with image receptor on top of the head (parallel to orbito-meatal plane)
X-ray beam: perpendicular to cantho-meatal line
Visualizes:
  Base of the skull (e.g. foramina)
  Sphenoid sinuses
  Mandibular condyles
  Zygomatic arch
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
P. Pittayapat, Chulalongkorn Univ.

## Slide 18: Occipito-frontal with cranial angulation
A.k.a. Reverse Towne’s projection
Fracture of condylar neck, medially displaced condyle, posterolateral wall of maxillary antrum
Patient position: canthomeatal line at 15-30° to image receptor, mouth open as wide as possible
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
P. Pittayapat, Chulalongkorn Univ.

## Slide 19: Other projections
PA skull (similar to PA ceph)
PA jaws
Oblique PA
Lateral oblique
Mandibular body
Mandibular ramus
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
R. Schulze
Lateral oblique radiograph

## Slide 20: Note: positioning
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography
For certain radiographic projections, slightly different positioning criteria may exist than those selected for this training material
  e.g. PA cephalometric radiograph: Frankfort plane perpendicular to image receptor vs. orbitomeatal line perpendicular to image receptor
  e.g. occipito-frontal projection: mouth open vs. mouth closed

## Slide 21: References
Erkan M et al. (2012) Reliability of four different computerized cephalometric analysis programs. Eur J Orthod.;34:318-21.
Jung PK et al. (2015) Comparison of cone-beam computed tomography cephalometric measurements using a midsagittal projection and conventional two-dimensional cephalometric measurements. Korean J Orthod.;45:282-8.
White SC & Pharaoh MJ. (2014) Oral Radiology: Principles and Interpretation. 7thed. St. Louis: CV Mosby Company.
For more projections and detailed positioning and evaluation guidelines:
Stewart Whitley A, Jefferson G, Holmes K, Sloane C, Anderson C, Hoadley G. (2015) Clark’s Positioning in Radiography. 13th ed. CRC Press: Taylor&Francis Group.
Radiation Protection in Dental Radiology L07 Fundamentals of Extraoral Projectional Radiography