## Slide 1: Radiation Protection in Dental Radiology
Fundamentals of CT and CBCT
L08
Training material developed by the International Atomic Energy Agency
in collaboration with: World Health Organization, FDI World Dental Federation, International Association of Dento-Maxillofacial Radiology, International Organization for Medical Physics, and Image Gently Alliance

## Slide 2: Educational Objectives
Understand the general principle of image acquisition and reconstruction in CT and CBCT
Understand fundamental similarities and differences between MDCT and CBCT, and how this affects their respective clinical application
Be familiar with CT image manipulation and visualization methods
Understand the cause and effect of various types of CT artefacts
Understand the issues related to density estimations in CBCT

## Slide 3: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 4: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 5: Introduction
CT and CBCT are two similar (but different) forms of 3D imaging
Dentists may opt for 3D imaging if 2D imaging is insufficient for diagnostics and/or treatment planning
(see also L09)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
D. Schulze
?
?
!
Intra-oral
Panoramic
CBCT

## Slide 6: Introduction
CBCT and CT are not equivalent options! If both are available, one should use each modality for their appropriate applications
The main focus of this dental training material is on CBCT. More on CT can be found in the “Diagnostic and Interventional Radiology” training material
(https://rpop.iaea.org/RPOP/RPoP/Content/AdditionalResources/Training/1_TrainingMaterial/Radiology.htm)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 7: History of CT & CBCT
Computed tomography (CT): originated in the 1970s
  Theoretical principles as old as 1915 (Radon transform)
Cone-beam CT (CBCT): first (non-dental) applications in the 1980s
  CBCT reconstruction technique: 1984 (Feldkamp-Davis-Kress, FDK) (Feldkamp et al. 1984)
  Second half of 1990s: first dental CBCTs introduced to market
  Currently (2017): >50 dental CBCT models
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 8: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 9: Imaging chain in CBCT
R. Pauwels
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 10: Imaging chain in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Image acquisition
    Rotation of x-ray tube and detector around patient
    Acquisition of projections (raw data) from various angles
R. Pauwels

## Slide 11: Imaging chain in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Image reconstruction
  3D image consisting of voxels; grey values according to attenuation (cfr. 2D radiography)
R. Pauwels

## Slide 12: Imaging chain in CBCT
R. Pauwels
The 3D image which is reconstructed is referred to as the field of view (FOV)
In CBCT, FOVs are cylindrical in shape; the FOV size can thus be described by its diameter and height (e.g. 10x5 cm)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 13: Imaging chain in CBCT
R. Pauwels
A CBCT FOV consists of millions of cubical voxels
The voxel size (in mm or µm) is expressed as the length of the side of the voxels
Voxel size (e.g. 0.2 mm)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 14: CBCT models
R. Pauwels
Patient can be seated, standing or (rarely) supine
Acquisition principle remains the same
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 15: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 16: ‘Cone-beam’ vs. ‘fan-beam’
Scarfe et al. 2006
CT (fan-beam)
CBCT (cone-beam)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 17: ‘Cone-beam’ vs. ‘fan-beam’
‘Cone-beam’ CT
  Nowadays, a pyramidal shape is used almost exclusively i.e. rectangular projections rather than circular
  Flat (2D) detector array
  ‘Volumetric’ acquisition
    Entire scanned volume acquired in 1 rotation (or less)
  Different alternative names
    Most common: digital volume tomography (DVT)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Scarfe et al. 2006

## Slide 18: ‘Cone-beam’ vs. ‘fan-beam’
‘Fan-beam’ CT
  Arched detector array
  ‘Slice-by-slice’ acquisition
    Ca. 1 image slice acquired per rotation
    Patient is moved through gantry during rotation (hence: ‘spiral’ or ‘helical’ CT)
    Nowadays: multiple detector rows (4, 16, …, 320) used simultaneously: ‘multi-slice’ CT (MSCT) or ‘multi-detector’ CT (MDCT)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Scarfe et al. 2006

## Slide 19: CBCT vs. MDCT
 | Similarities | Differences
X-ray beam shape | Pyramid-shaped beam | Full coverage in MDCT in terms of beam diameter; diameter of beam is collimated to as small as 4cm in CBCT Beam divergence in CBCT at upper and lower border of the FOV is typically larger than that of MDCT, even when many detector rows are used Beam in MDCT can be narrow if few detector rows are used
Detector | Typically indirect x-ray detection | Different scintillator material used Flat detector used in CBCT; detector arc used in MDCT Higher proportion of detected x-ray scatter in CBCT
Technique factors | kVp, mA, field of view settings determine image quality and patient radiation dose | Automatic exposure control is ubiquitous in MDCT but virtually non-existent in CBCT CBCT typically operates at a low mAs (although low-dose MDCT protocols can reach similar mAs levels) Dual energy imaging possible in MDCT
Exposure |  | Scan time typically 15-20 s in CBCT modern MDCT scanners allow for sub-second scans
Image viewing | Image processing possible e.g. contrast, brightness, zoom, filtering | Isotropic voxels in CBCT. In MDCT, coronal and sagittal slices can have poorer resolution than axial images. Advanced reconstruction techniques common in MDCT but not yet in CBCT.
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 20: Image quality: CBCT vs. MDCT
CBCT (generally) has:
  Better spatial resolution
  Higher noise
  Lower contrast
  Worse motion artefacts
  Similar metal artefacts (highly dependent on scanner model)
  than MDCT
Radiation dose CBCT vs. MDCT: see L09 & L11
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 21: Image quality: CBCT vs. MDCT
Loubele et al. (2007)
CBCT
MDCT
Lamina dura
PD ligament
Trabecular bone
Maxillary sinus
Cortical bone
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 22: Image quality: CBCT vs. MDCT
Liang et al. (2010)
(MDCT images are shown in red boxes, all other images are CBCT)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 23: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 24: Detectors used in CBCT
Flat panel detector (FPD)
  Indirect FPD: scintillator converts X rays to light, photodiode converts light to charge
  Direct FPD: direct conversion from X rays to charge (not commonly used in clinical models yet)
  Photon counting / energy-resolving detectors could be expected in the near future
  Read-out using TFT or CMOS
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 25: Detectors used in CBCT: FPD
(Ubiquitous in clinical CBCT)
(Not yet common in clinical CBCT)
R. Pauwels, loosely based on Seibert (2006) (Creative Commons Attribution Noncommercial License)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 26: Detectors used in CBCT
Image intensifier
  Conversion of X ray to visible light (input phosphor) → conversion to e- (photocathode) → acceleration in electric field → re-conversion (output phosphor)
  Read-out using charge-coupled device (CCD)
  No longer used in current-generation CBCT models
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 27: FOV categories used in dental CBCT
Maximum FOV size ~ detector size
R. Pauwels
R. Pralier
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 28: Stitching of multiple scans in CBCT
For full jaw / maxillofacial scan using small detector
  Overlap between scans to allow automated merging (‘stitching’) of the scans into 1 image: patient dose ↑
R. Pauwels
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 29: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 30: Image reconstruction: pre-processing
W. Scarfe
R. Pauwels
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Before reconstruction, several corrections are made to the projection data, based on calibration data specific to each detector pixel

## Slide 31: Image reconstruction: FBP technique
Filtered backprojection (FBP): Most common technique in CBCT
  Feldkamp-Davis-Kress (FDK) algorithm
  Iterative reconstruction (see further) sparsely used due to computational power required
Inverse of detector signal (i.e. forward projection or ray sum) is assigned to every voxel along the X ray path
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 32: Image reconstruction: FBP technique
The result of image reconstruction is that, for each voxel in the FOV, the grey value is ‘guessed’ based on the projection data. The guessed value can differ from the true value due to several factors (noise, artefacts)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 33: Image reconstruction: FBP technique
R. Pauwels
Step 1: forward projections (i.e. detector signal) are collected from different angles (covering at least 180°)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Projections of a circular object from 3 different angles (for a parallel-beam geometry)

## Slide 34: Image reconstruction: FBP technique
R. Pauwels
Step 2: the inverse of the detector signal at each detector pixel is given to every voxel along the line connecting the X ray source and detector
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Actual object
Back-projection

## Slide 35: Image reconstruction: FBP technique
R. Pauwels
Step 3: all backprojections are averaged
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Backprojections
Avg. of 4 backprojections

## Slide 36: Image reconstruction: FBP technique
R. Pauwels
Animation showing 180 backprojections (at intervals of 1°) being averaged, for the circular object shown in the previous slides
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 37
36 (back)projections
Image reconstruction: FBP technique
R. Pauwels
180 (back)projections
Artefacts (albeit outside the FOV)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 38
The result of image reconstruction using backprojection will be blurry; a filter is therefore applied
The choice of the filter can affect sharpness & noise of the reconstructed image
Unfiltered BP
Image reconstruction: FBP technique
R. Pauwels
Filtered BP
Original image
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 39: Image reconstruction: iterative technique
Iterative reconstruction: Group name of different types of reconstruction techniques including a repetitive step
  Result is a “best fit” solution
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
R. Pauwels

## Slide 40: Image reconstruction: iterative technique
Common in current-day MDCT (Beister et al. 2012)
  Implemented by all manufacturers
Still hardly used in clinical CBCT
  Computationally expensive (reconstruction time ~ number of iterations)
  Expected to become more common in the near future
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 41: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 42: Image display: MPR
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Axial
Coronal
Sagittal
Brain Tumour Analysis Project, Univ. of Alberta
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Multi-planar reformatting: three interconnected windows with 2D orthogonal slices

## Slide 43: Image display: MPR
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Which is the left/right side of the patient???
  Convention: Left side of patient = right side of screen, but images can be flipped
When interpreting CBCT images, one should always be aware of what is the left and right side
  Should be clearly indicated in viewer (“L/R”, diagram showing head/FOV orientation, …)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 44: Image display: oblique slicing
Through manipulation of the slicing angle, the entire mandibular canal can be displayed in a single slice (middle) → oblique slicing
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 45: Image display: standard
Curved reformatting: manual or (semi-) automatic curve drawn along dental arch, shown as a 2D slice
  Similar to panoramic radiograph (but no anatomical overlap & no magnification/distortion)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 46: Image display: curved reformatting
If the slice thickness is thin, separate curves need to be drawn for the upper and lower jaw
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 47: Image display: curved reformatting
Increased thickness of the reformatted slice results in greater coverage of the jaw but increased anatomical overlap
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
0.16 mm
14.9 mm

## Slide 48: Image display: curved reformatting
Cross-sectional slices (perpendicular to the curve) allow the user to easily browse along the dental arch
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 49: Image display: slice thickness
Example: slice thickness = 2 times the voxel size → every 2 consecutive slices are averaged
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Consecutive slices can be averaged by increasing the slice thickness (reduces noise, but reduces sharpness as well)

## Slide 50: Image display: slice interval
Example: slice interval = 2 times the voxel size: one slice is retained for every 2 consecutive slices
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Slices can be skipped by increasing the slice interval (retains sharpness & noise in a given slice)
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish

## Slide 51: Image display: slice interval
Increasing the slice interval reduces the amount of imaging data
Slice interval ↑
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 52: Image display: slice thickness/interval
Increasing thickness/interval not advised when small pathology is suspected (e.g. root fracture)
  Slice thickness too large: pathology may be obscured by averaging several slices
  Slice interval too large: pathology may be hidden between slices
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 53: Image display: advanced
3D rendering
  Surface or volume rendering
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 54: Image display: advanced
Threshold needed to separate bone from soft tissue
  Amount of visible bone can be affected by threshold
Can be used as an aid, but diagnosis and treatment planning best done using 2D slices
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 55: Image display: advanced
Maximum intensity projections (MIP)
  Projection of the 3D volume, showing only the voxel with the highest density (i.e. grey value) along each projection line
  Alternative: minimum intensity projection
  Can be rotated and cropped
  (cfr. 3D rendering)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Pauwels et al. (2015), under the British Institute of Radiology's License to Publish

## Slide 56: Image quality in CT
Normal image
Poor spatial resolution (i.e. unsharp / blurry)
Poor contrast
High noise
R. Pauwels
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 57: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 58: Artefacts in CT & CBCT
Image artefacts
  Aberrations in the image; parts of the image not corresponding to physical reality
  Noise: strictly speaking also an artefact, but normally considered separately
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 59: Artefacts in CT & CBCT
Different types/causes of image artefacts in CT & CBCT
  Metal artefacts (frequent for dental imaging)
  Beam hardening, exponential edge gradient effect
  Motion artefacts (scan time in CBCT: 5-40 s)
  X ray scatter (if non-homogeneous)
  Aliasing (undersampling; i.e. too few projections)
  Ring artefacts (due to detector defects / improper calibration)
  …
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 60: Image quality in CT: metal artefacts
Pauwels et al. (2013)
Different causes (photon extinction, beam hardening, scatter, EEGE)
Severity depends on size and density of metal + relative location of metal objects
Combination of dark and bright areas/streaks
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 61: Image quality in CT: metal artefacts
Pauwels et al. (2013)
Can interfere with image interpretation
Typical example: dark regions between implants, masking the bone
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 62: Image quality in CT: motion artefacts
“Geometric” artefacts: reconstruction algorithm assumes a perfectly stationary object
R. Pauwels
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
No motion
Moderate motion
Severe motion

## Slide 63: Image quality in CT: aliasing artefacts
a
b
c
d
Simulated data; R. Pauwels
18 projections
36 projections
60 projections
180 projections
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 64: Overview
Introduction, history
The imaging chain
‘Cone-beam’ vs. ‘fan-beam’ (CBCT vs. CT)
Detectors in CBCT
Image reconstruction
Image display
Image artefacts in CBCT & CT
Hounsfield Units in CBCT
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 65: Density estimation using CBCT
In MDCT: grey value calibrated as Hounsfield units (HU), according to their X ray attenuation (µ)
HU are also referred to as CT numbers
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 66: Density estimation using CBCT
The HU scale is defined by air (-1000 HU) and water (0 HU)
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
…
Air
Water
Lung
Fat
Soft tissue
Bone
Air | -1000 HU
Lung | -600 to -400 HU
Fat | -100 to -60 HU
Water | 0 HU
Soft tissue | +40 to +80 HU
Bone | +400 to +1000 HU

## Slide 67: Density estimation using CBCT
In CBCT:
  Depending on manufacturer, grey values may or may not be calibrated according to a (pseudo-) HU scale
  Even when calibrated, several issues related to grey value stability are inherent to the CBCT technique
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 68: Density estimation using CBCT: issues
Uniformity issues due to beam hardening (and improper correction thereof) + asymmetrical FOV position (with mass irregularly distributed outside the FOV) can lead to A-P, L-R or central-peripheral ‘shading’
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Perfect
uniformity
A-P shading
Central
shading
Peripheral
shading

## Slide 69: Density estimation using CBCT: issues
For certain manufacturers, grey values are assigned based on the density distribution in the FOV
  High-density material in FOV can leads to grey value shift towards lower values
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT
Periphery = same material (PMMA)! Grey value shift when a high-density material (here: aluminium) is in the FOV
Pauwels
et al. (2013)
Notes: Figure reproduced under the British Institute of Radiology's License to Publish

## Slide 70: Density estimation using CBCT: issues
Quantitative use of grey values in CBCT should be done with great care and with proper knowledge of the grey value stability of the CBCT model being used
CBCT users should rely on visual interpretation of bone quality rather than density measurements
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 71: References
Ambrose J. (1973) Computerized transverse axial scanning (tomography): Part 2. Clinical application. Br J Radiol. 46:1023-47.
Arai Y et al. (1999) Development of a compact computed tomographic apparatus for dental use. Dentomaxillofac Radiol. 28:245-8.
Beister et al. Iterative reconstruction methods in X-ray CT (2012). Phys Med. 28:94-108.
Feldkamp LA et al. (1984) Practical cone-beam algorithm. J Opt Soc Amer. A, 1:612-9
Hounsfield GN (1973) Computerized transverse axial scanning (tomography): Part I. Description of system. Br J Radiol. 46:1016-22.
Kalender WA. (2006) X-ray computed tomography. Phys Med Biol. 51:R29-43.
Liang et al. (2010) A comparative evaluation of Cone Beam Computed Tomography (CBCT) and Multi-Slice CT (MSCT) Part I. On subjective image quality. Eur J Radiol. 75:265-9.
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT

## Slide 72: References
Loubele et al. (2007) A comparison of jaw dimensional and quality assessments of bone characteristics with cone-beam CT, spiral tomography, and multi-slice spiral CT. Int J Oral Maxillofac Implants. 22:446-54.
Pauwels R et al. (2013) Quantification of metal artifacts on cone beam computed tomography images. Clin Oral Implants Res. A100:94-9.
Pauwels R et al. (2013) Variability of dental cone beam CT grey values for density estimations. Br J Radiol. 86:20120135.
Pauwels R et al. (2015) Technical aspects of dental CBCT: state of the art. Dentomaxillofac Radiol. 44:20140224
Scarfe WC et al. (2006) Clinical applications of cone-beam computed tomography in dental practice. J Can Dent Assoc. 72:75-80.
Seibert JA. (2006) Flat-panel detectors: how much better are they? Pediatr Radiol 36:173-81.
Radiation Protection in Dental Radiology L08 Fundamentals of CT and CBCT