## Slide 1: Radiation Protection in Dental Radiology
Special Considerations for Radiation Protection in Children
L02
Training material developed by the International Atomic Energy Agency
in collaboration with: World Health Organization, FDI World Dental Federation, International Association of Dento-Maxillofacial Radiology, International Organization for Medical Physics, and Image Gently Alliance

## Slide 2: Educational Objectives
To understand the need for special considerations for radiation protection in children
To understand why radiation doses for children are higher than for adults (unless exposure parameters are adapted appropriately)
To understand why radiation risks for children are higher
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 3: Overview
Why special considerations for children?
How to protect children?
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 4: Overview
Why special considerations for children?
How to protect children?
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 5: Why special considerations for children?
Extra care is needed when exposing children to radiation because:
  Children receive a higher radiation dose than adults if exposure settings are not adapted
  Children are more sensitive to radiation-induced stochastic effects than adults (i.e. more likely to develop cancer at a given radiation dose)
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 6: Why special considerations for children?
When adults and children are exposed using the same FOV, the dose for children will be higher!
  e.g. a FOV which covers upper & lower jaw for a large adult (left) would cover the entire maxillofacial region for a small child (right)
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 7: Why special considerations for children?
Furthermore, the absorbed dose (for a given combination of exposure settings e.g. kV, mAs) increases with a decreasing patient size
AAPM Report 204: Size-Specific Dose Estimates (SSDE) in Pediatric and Adult CT Examinations;
Reproduced with permission
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 8: Why special considerations for children?
Higher sensitivity for children
  Radiation-induced cancer risk highly dependent on age at exposure (see L01):
  Ionizations of molecules in a living cell can lead to DNA mutations and other types of damage
  Mutations are more likely to be transferred to next-generation cells (and eventually manifest as cancer) in cells which are actively dividing
  As children are growing, they have a higher proportion of dividing cells than adults
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 9: Why special considerations for children?
In addition, children have a longer life span (higher probability that cancer, which typically occurs several years after exposure, will manifest)
Illustrative graph showing the probability that a cancer, which takes 10 years to express, will manifest before a subject dies from other causes
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 10: Why special considerations for children?
High frequency of dental radiographic examinations in children
  Orthodontic treatment, trauma, cleft palate, developmental disorders, tumors, …
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children
K. Horner, University of Manchester

## Slide 11: Overview
Why special considerations for children?
How to protect children?
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 12: How to protect children?
Justification of medical exposures is more stringent in children than adults (depends on risk-benefit relation)
“The justification of medical exposure for an individual patient shall be carried out […] with account taken, in particular for patients who are pregnant or breast-feeding or are paediatric”
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 13: How to protect children?
Exposures to children can be optimized through adjustment of exposure parameters and the use of shielding
  See L11 for general considerations regarding optimization
Children can be exposed at a lower tube output (e.g. mAs) in order to reach the same image quality level as adults
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children

## Slide 14: How to protect children?
Patients with a smaller head circumference require a lower relative mAs to reach the same image quality level
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children
Pauwels et al. (2017), with permission from Springer
Head circumference vs. mAs for dental CBCT

## Slide 15: How to protect children?
The mAs should therefore be adapted to patient age (taking individual variability in head size into account)
Age vs. mAs in CBCT
(Percentiles refer to growth reference charts for head circumference)
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children
Pauwels et al. (2017), with permission from Springer

## Slide 16: References
Image Gently (www.imagegently.org)
Pauwels et al. (2017) Determination of size-specific exposure settings in dental cone-beam CT. Eur Radiol. 2017;27:279-285.
UNSCEAR (2013) United Nations Scientific Committee on the Effects of Atomic Radiation, 2013 Report to the General Assembly, Volume II: Scientific Annex B: Effects of radiation exposure of children (http://www.unscear.org/unscear/en/publications/2013_2.html)
WHO (2016), Communicating radiation risks in paediatric imaging (http://www.who.int/ionizing_radiation/pub_meet/radiation-risks-paediatric-imaging/en/
Radiation Protection in Dental Radiology L02 Special Considerations for Radiation Protection in Children