## Slide 1: Radiation Protection in Dental Radiology
Justification and appropriate use of dental radiology
L09
Training material developed by the International Atomic Energy Agency
in collaboration with: World Health Organization, FDI World Dental Federation, International Association of Dento-Maxillofacial Radiology, International Organization for Medical Physics, and Image Gently Alliance

## Slide 2: Educational Objectives
Understand the general principles regarding the use of radiation in medicine
Judge the appropriateness of using 2D and 3D imaging techniques for a given patient
Can judge the current referral criteria for CBCT for various clinical applications
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 3: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 4: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 5: The justification principle
One of three fundamental principles of radiation protection (see L01)
Is related to the appropriate selection of an imaging technique in a given situation
“Any decision that alters the radiation exposure situation should do more good than harm.” (ICRP 103, 2007)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 6: The justification principle
The “good”
  Improved diagnosis of pathology
  Improved treatment planning / outcome
The “harm” (if using ionizing radiation)
  Increased risk of cancer & hereditary effects (i.e. stochastic effects)
  Tissue reactions (a.k.a deterministic effects)
    Will not occur during normal operation, but are possible in case of (severe) accidents
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 7: The justification principle
Difficult to balance both sides!
  Actual benefit for individual patient often unknown before imaging
  Large uncertainty & individual variability regarding stochastic effects
  Only general recommendations can be made, eventual selection of imaging technique always case-by-case
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 8: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 9: Radiation dose in dental radiography
There is no such thing as ‘the dose’ of a dental imaging modality
Depending on the modality, a moderate or broad dose ‘range’ can be seen
For more information on patient dose (incl. dose ranges for each dental imaging modality): see L01
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 10: Dose of dental X ray exposures
Radiation dose varies greatly for different imaging techniques, and for a given technique depending on the technology used (see L01)
  Dose of CT / CBCT higher than that of 2D radiograph
  Intraoral radiography: exposure time of D-speed film 4x higher than that of CCD (Anissi et al. 2014)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 11: Dose of dental X ray exposures
The process of justification of a high-dose exposure requires more scrutiny to ensure that the benefits outweigh the risks than for low-dose one, but an expected benefit should always be there
  No ‘routine’ practice e.g. no standard panoramic or full-mouth series for a new patient
  History, clinical examination and individual prescription needed
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 12: Dose of dental X ray exposures
The process of justification is more scrutinized for children:
  Higher dose for a given exposure (see L02)
  Higher cancer risk for a given dose (see L02)
  Different types of pediatric patients in dentistry, with different imaging needs
    e.g. caries assessment, orthodontic treatment planning, cleft palate treatment
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 13: Dose of dental X ray exposures
Effective doses from dental examinations
Radiographic technique | Effective dose (µSv)
Intraoral radiograph | 0.3-21.6
Panoramic radiograph | 2.7-38
Lateral cephalometric radiograph | 2.2-14
CBCT | 11-1025 (generally <300)
CT (mandible) | 250-1410
CT (mandible & maxilla) | 430-860
Adapted from: FGDP (UK), Selection Criteria For Dental Radiography
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 14: Dose of dental X ray exposures
CBCT
  Wide dose range reported
    Within studies: 16- to 23-fold difference between highest and lowest effective dose (Ludlow et al. 2008b, Pauwels et al. 2012, Rottke et al. 2013a)
    Between studies: 100-fold range in effective dose
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 15: Dose of dental X ray exposures
CBCT
  Wide dose range reported
    Absorbed dose ranges:
      Thyroid gland 0.03-10.0 mGy
      Brain 0.02-9.3 mGy
      Eye lens (i.e. cfr. skin) 0.03-16.7 mGy
    More information on CBCT dose: see reviews by Al-Okshi et al. (2015), Bornstein et al. (2015) & Ludlow et al. (2015)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 16: Dose of dental X ray exposures
CBCT
  Justification process should take dose into account
  e.g. a maxillofacial scan requires a higher benefit than a single tooth scan
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 17: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 18: Referral criteria
European guidelines on radiation protection in dental radiology (EC RP 136, 2004) (note: outdated regarding the use of CBCT e.g. for implant planning)
Cone beam CT for dental and maxillofacial radiology (Evidence-based guidelines) (EC RP 172, 2012)
UK: Selection Criteria for Dental Radiography (Faculty of General Dental Practice)
Other national guidelines
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 19: Referral criteria
International BSS, Requirement 36: “Registrants and licensees shall ensure that no person incurs a medical exposure unless there has been an appropriate referral…”
Justification takes into account:
(a) The appropriateness of the request;
(b) The urgency of the radiological procedure;
(c) The characteristics of the medical exposure;
(d) The characteristics of the individual patient;
(e) Relevant information from the patient’s previous radiological procedures.
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 20: Referral criteria
Self-referral issue in dentistry (Farman 2009)
  May increase the frequency of imaging examinations compared with referral to a radiologist
  Issue is compounded due to the introduction of CBCT in dentistry
    Economical considerations
    Legal considerations (“protective imaging” is not in line with the justification principle and should be avoided)
    Training and expertise to interpret CBCT images
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 21: Referral criteria
International BSS: “Relevant national or international referral guidelines shall be taken into account for the justification of the medical exposure of an individual patient in a radiological procedure.”
  Evidence-based
    Lack of (conclusive) evidence is a common issue
    Different guidelines may disagree in their interpretation of the available evidence
    Periodic revision is needed, as new evidence becomes available
  Referral criteria should not be applied blindly, but considered on a case-by-case basis
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 22: Referral criteria
Guidelines and referral criteria are not rules!
  Never follow blindly, but apply the concepts of good practice according to individual patient needs
  "Guidelines are defined as systematically developed statements designed to assist the clinician and patient in making decisions about appropriate healthcare for certain specific circumstances" (Field & Lohr, 1992)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 23: Referral criteria
EC RP 136 (2004) proposes:
  “All X ray examinations must be justified on an individual patient basis by demonstrating that the benefits to the patient outweigh the potential detriment. The anticipated benefits are that the X ray examination would add new information to aid the patient’s management.”
  “No radiographs should be selected unless a history and clinical examination have been performed. ‘Routine’ radiography is unacceptable practice.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 24: Referral criteria
  EC RP 136 (2004) proposes:
    “When referring a patient for a radiographic examination, the dentist should supply sufficient clinical information (based upon a history and clinical examination) to allow the practitioner taking clinical responsibility for the X ray exposure to perform the justification process.”
  “Access to previous radiographs will avoid unnecessary exposures and aid patient management.”
    Made easier owing to the increased digitalization of radiography
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 25: Note: CBCT or MDCT?
CBCT advised when:
  High sharpness is needed when compared with MDCT (e.g. small anatomy/pathology)
  Only a localized region needs to be scanned (e.g. single tooth region); large amount of dose can be saved through horizontal collimation
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 26: Note: CBCT or MDCT?
MDCT advised when:
  Soft tissue discrimination is needed
  Neurological symptoms
  Contrast agent needed
  MRI not available
Not univocally clear for certain applications whether CBCT or MDCT provides better diagnostic image quality at the same dose
  CBCT: wide image quality range in function of technology, exposure factors, reconstruction factors, …
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 27: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 28: Specific clinical applications
Caries diagnosis
Orthodontics
Periodontics
Endodontics
Implant planning
Tooth extraction
Other surgery
Temporomandibular joint
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 29: Specific clinical applications: caries
Prior risk evaluation required as a key aspect of the justification process:
  Clinical evidence of previous disease, dietary habits, social history, use of fluoride, plaque control, saliva, medical history
Radiographic examination is then considered on an individual basis
  No routine adherence to intervals proposed in guidelines
  Certainly no screening!
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 30: Specific clinical applications: caries
EC RP 136 (2004) proposes:
  General:
    “Prescription of bitewing radiographs for caries diagnosis should be based upon caries risk assessment. Intervals between subsequent bitewing radiographic examinations must be reassessed for each new period, as individuals can move in and out of caries risk categories with time.”
  Children:
    “It is recommended that when children are designated as high caries risk they should have six-monthly posterior bitewing radiographs taken. This should continue until no new or active lesions are apparent and the individual has entered a lower risk category.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 31: Specific clinical applications: caries
EC RP 136 (2004) proposes:
  Children (cont):
    “It is recommended that when children are designated as moderate caries risk they should have annual posterior bitewing radiographs. This should continue until no new or active lesions are apparent and the individual has entered a lower risk category.”
    “Radiography for caries diagnosis in low caries risk children should take into account population prevalence of caries. Intervals of 12-18 months (deciduous dentition) or 24 months (permanent dentition) may be used, although longer intervals may be appropriate where there is continuing low caries risk.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 32: Specific clinical applications: caries
European Academy of Paediatric Dentistry (EAPD) guidelines proposes different intervals for caries assessment in children:
Espelid et al. (2003)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 33: Specific clinical applications: caries
EC RP 136 (2004) proposes:
  Adults:
    “It is recommended that adults designated as high caries risk have six-monthly posterior bitewing radiographs taken until no new or active lesions are apparent and the individual has entered another risk category.”
    “It is recommended that adults designated as moderate caries risk have annual posterior bitewing radiographs taken until no new or active lesions are apparent and the individual has entered another risk category.”
    “It is recommended that adults designated as low caries risk have posterior bitewing radiographs taken at approximately 24-month intervals. More extended intervals may be used where there is continuing low caries risk.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 34: Specific clinical applications: caries
EC RP 136 (2004) proposes:
  “Alternative methods to using ionising radiation in caries diagnosis should be considered once their diagnostic validity has been clearly established.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 35: Specific clinical applications: caries
CBCT should not be used for caries assessment
  Similar diagnostic efficacy between intra-oral, panoramic, and CBCT (Gaalaas et al. 2016)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 36: Summary: caries
Disclaimer
The summary presented on the following slides provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 37: Summary: caries
Terminology
  Low usefulness: may be indicated for specific cases only
  Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
  High usefulness: generally accepted as the modality of choice for (nearly) all cases
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 38: Summary: caries
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Children – low caries risk |  |  |  |  |  |  | 
Children – moderate caries risk |  |  |  |  |  |  | 
Children – high caries risk |  |  |  |  |  |  | 
Adults – low caries risk |  |  |  |  |  |  | 
Adults – moderate caries risk |  |  |  |  |  |  | 
Adults – high caries risk |  |  |  |  |  |  | 
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
(Disclaimer: see slide #36 and slide notes)
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 39: Specific clinical applications: orthodontics
Involves children (typically starting at 12-13 y)
  Increased radiation risk vs. adults (see L02)
Clinical examination required to determine the required type(s) of radiographs for treatment planning & monitoring
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 40: Specific clinical applications: orthodontics
EC RP 13 (2004) proposes:
  “Specialist guidelines on orthodontic radiography should be consulted as an aid to justification in the management of the developing dentition in children.”
    e.g. British Orthodontic Society guidelines
    AAOMR (2013) & EC RP 172 (2012): regarding use of CBCT in orthodontics
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 41: Specific clinical applications: orthodontics
Projection | Function
Panoramic radiograph or lateral oblique views | Identification of the developing dentition. Confirmation of the presence/absence of teeth.
Lateral cephalometric view | To assess skeletal pattern and labial segment angulation. Assessment of unerupted teeth.
Posteroanterior view | Occasionally needed in patients with facial asymmetry and certain jaw anomalies.
Occlusal views generally Anterior oblique occlusal of maxilla (standard occlusal) and mandibular anterior oblique occlusal | Identification of abnormality/ potential pathology and to localise unerupted teeth. To obtain views of incisor region when lateral oblique films have been taken.
Various radiographic views and their function in orthodontic practice
EC RP 136 (2004), modified from Isaacson & Thom (2001)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 42: Specific clinical applications: orthodontics
Projection | Function
Occlusal views specifically: Anterior oblique occlusal of maxilla (standard occlusal) True occlusal of the mandible | Localization of tooth/teeth by vertical parallax involving: anterior oblique occlusal in combination with panoramic film or anterior oblique occlusal in combination with a periapical film. Localization of unerupted teeth.
Periapicals | To assess root morphology and angulation. To assess root resorption. To assess apical pathology. In combination with an oblique occlusal or second periapical, to localise unerupted teeth by parallax.
Bitewings | To assess teeth of doubtful prognosis. Caries identification and assessment of periodontal bone levels.
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
EC RP 136 (2004), modified from Isaacson & Thom (2001)

## Slide 43: Specific clinical applications: orthodontics
CBCT?
  Often large FOV required for orthodontic applications (excl. impacted canines): radiation dose ↑↑ vs. 2D radiography (see L08)
  Should not be used solely to generate a simulated 2D cephalometric radiograph
  Little evidence for benefit of CBCT except for orthodontic applications requiring surgical intervention & impacted canines
    If no effect on treatment outcome is expected, CBCT should not be used
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 44: Specific clinical applications: orthodontics
CBCT?
  Should be considered on a case-by-case basis, usually as an alternative for MDCT if no soft tissue discrimination is needed
  Usually not post-treatment
  Use low-dose protocols (see L11)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 45: Specific clinical applications: orthodontics
CBCT for specific ortho-related applications:
  Orthodontic planning
    Treatment planning may not be affected by the use of CBCT, but confidence and intra/inter-observer agreement may be increased (Al-Qerban et al. 2014; Pittayapat et al. 2014)
    No evidence for effect on patient outcome
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 46: Specific clinical applications: orthodontics
CBCT for specific ortho-related applications:
  Airway evaluation (e.g. sleep apnea)
    Allows for volumetric assessment of airway, rather than estimations of area/volume from 2D radiographs: effect on treatment (outcome)?
    Effect of patient position (supine vs. upright) should be taken into account
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 47: Specific clinical applications: orthodontics
CBCT for specific ortho-related applications:
  Tooth impaction
    Could lead to improved canine localization and detection of root resorption, and may thus affect the (confidence in the) treatment plan (Alqerban et al. 2015)
  Temporary anchorage (mini-implants)
    CBCT not normally indicated (EC RP 172, 2012)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 48: Specific clinical applications: orthodontics
More clinical research needed to assess the diagnostic validity of CBCT for orthodontic applications
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 49: Summary: orthodontics
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Regular orthodontic treatment planning |  |  |  |  |  |  | 
Facial asymmetry, jaw anomaly |  |  |  |  |  |  | 
Airway evaluation |  |  |  |  |  |  | 
Maxillary canine impaction |  |  |  |  |  |  | 
Temporary anchorage |  |  |  |  |  |  | 
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
(Disclaimer: see slide #36 and slide notes)
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 50: Specific clinical applications: periodontics
Note: implant planning not included in this section (see further)
EC RP 136 (2004) proposes:
  “Radiographs should be used in the management of periodontal disease if they are likely to provide additional information that could potentially change patient management and prognosis.”
  “There is insufficient evidence to propose robust guidelines on choice of radiography for periodontal diagnosis and treatment, but existing radiographs e.g. bitewing radiographs taken for caries diagnosis should be used in the first instance.”
CBCT: could be considered for extensive or complicated periodontal bone loss
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 51: Specific clinical applications: periodontics
Systematic review on the use of CBCT for periodontal diagnosis and treatment planning (Walter et al. 2016):
  “[…] high accuracy of CBCT in detecting intrabony defect morphology when compared to periapical radiographs.”
  “CBCT has demonstrated advantages, when more invasive treatment approaches were considered in terms of decision making and cost benefit. […] CBCT may improve diagnostic accuracy and optimize treatment planning in periodontal defects, particularly in maxillary molars with furcation involvement.”
  Higher radiation dose remains a factor (esp. if large FOV coverage is needed): further study needed to truly evaluate cost-benefit
No evidence regarding the value of CBCT in general periodontal treatment
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 52: Summary: periodontics
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Periodontal disease: General Advanced treatment considered |  |  |  |  |  |  | 
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
(Disclaimer: see slide #36 and slide notes)
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 53: Specific clinical applications: endodontics
Different stages of endodontic treatment may require radiographic examination:
  Pre-operative: evaluation of pulp and root canal anatomy + periradicular anatomy
  Working length estimation (but: can be done using apex locator)
  Intra-operative, pre-condensation: to check integrity of the apical constriction before obturation
  Post-operative (immediate): to verify quality of root canal filling + as baseline for follow-up
  Review: after one year (peak incidence of healing and chronic apical periodontitis) + possible additional radiographs if further treatment is advised
Two periapical radiographs with different horizontal beam angulation (parallax) can be useful, mainly for multi-rooted teeth, at any stage during endodontic treatment
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 54: Specific clinical applications: endodontics
Relatively high degree of consensus regarding the applicability of CBCT for endodontic applications
  Position statement ESE (Patel et al. 2014)
  Position statement AAE-AAOMR (American Association of Endodontists and American Academy of Oral and Maxillofacial Radiology 2011)
  EC RP 172 (2012)
CBCT advised for complex endodontic cases (periapical pathology if 2D radiography is insufficient, horizontal root fracture, complex canal systems), but not during/after treatment (if no complication)
CBCT for endodontic purposes should be acquired using a small FOV (~ 4-6 cm in any dimension) to save radiation dose (see L11), but it should be ensured that image quality is high enough to visualize small details (e.g. high-resolution scanning protocol)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 55: Summary: endodontics
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Regular endodontic treatment: Treatment planning During treatment Follow-up |  |  |  |  |  |  | 
Complex cases: Treatment planning During treatment Follow-up |  |  |  |  |  |  | 
(Disclaimer: see slide #36 and slide notes)
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 56: Specific clinical applications: implants
Assessment of quality and quantity of bone + the presence of pathology at the proposed implant site
The paradigm of radiographic dental implant planning has changed dramatically after the introduction of CBCT
No consensus regarding the absolute need for CBCT (Tyndall et al. 2012, Harris et al. 2012, EC RP 172 2012)
  Strong evidence regarding the benefit of CBCT for implant planning, but may not affect treatment outcome for all types of patients
Note: bone classification schemes based on Hounsfield units should not be used in CBCT due to issues regarding grey value stability (see L08)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 57: Summary: implants
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Regular cases |  |  |  |  |  |  | 
Complicated cases (e.g. suspected pathology, limited bone quantity, potential bone augmentation) |  |  |  |  |  |  | 
(Disclaimer: see slide #36 and slide notes)
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 58: Specific clinical applications: surgery
EC RP 136 2004 proposes: “Pre-extraction radiography may be indicated in the following situations:
  A history of previous difficult extractions
  A clinical suspicion of unusual anatomy
  A medical history placing the patient at special risk if complications were encountered
  Prior to orthodontic extractions
  Extraction of teeth or roots that are impacted, buried or likely to have a close relationship to anatomical structures (i.e. mental/inferior dental nerve, the maxillary antrum and/or tuberosity and the lower border of the mandible).”
CBCT: can provide additional, 3D information (e.g. impacted third molars vs. mandibular canal), but true added value in terms of improved patient outcome still to be demonstrated
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 59: Specific clinical applications: surgery
CBCT for specific surgery applications:
  Removal of impacted (lower) third molars
    A relatively ‘simple’ type of surgery; main pre-operative decision is to extract as a whole, or a coronectomy (or other sectioning) of the tooth
    CBCT can improve localisation of teeth (e.g. exact trajectory of roots for mandibular third molars in close contact with mandibular canal)
    But: CBCT only advised when it is expected to alter (or significantly increase confidence in) the treatment plan
    Decision of removal could be affected by increased visualization of pathology on CBCT (Matzen et al. 2017)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 60: Specific clinical applications: surgery
No evidence for benefit of CBCT in terms of prevention of nerve injury for lower third molar removal:
Guerrero et al. (2012): “CBCT was not superior to [panoramic radiography] in predicting postoperative sensory disturbances but was superior in predicting [inferior alveolar nerve] exposure during third molar removal in cases judged as having "moderate" risk.”
Petersen et al. (2016): “The use of CBCT before removal of the mandibular third molar does not seem to reduce the number of neurosensoric disturbances [compared with the use of panoramic radiography].”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 61: Specific clinical applications: surgery
(cont.) No evidence for benefit of CBCT in terms of treatment outcome for lower third molar removal:
Korkmaz et al. (2017): “Additional CBCT imaging was not superior to PAN in reducing IAN injury after third molar surgery during long-term follow-up. Nonetheless, CBCT may decrease the prevalence of temporary IAN injury and improve the surgical outcomes in high-risk patients.”
Ghaeminia et al. (2015): “[…] the use of CBCT does not translate into a reduction of IAN injury and other postoperative complications, after removal of the complete mandibular third molar”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 62: Specific clinical applications: surgery
CBCT for specific surgery applications:
  Cleft palate treatment
    Different treatment steps e.g. surgical repair of cleft, bone grafting, orthodontic treatment and monitoring/correction of jaw growth
    MDCT used frequently (despite radiation dose & young age of patients)
    CBCT can be used as an alternative if it can operate at a lower dose than an (optimized) MDCT scan, using the smallest possible FOV which fits the region of interest
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 63: Specific clinical applications: surgery
CBCT for specific surgery applications:
  Orthognathic surgery
    For extensive facial deformity, surgical planning using 3D imaging can be advised
    CBCT can be used as a substitute of MDCT, if it can be assured that the CBCT examination results in a lower patient dose
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 64: Summary: surgery
Clinical indication | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT / CT
 | Periapical | Bitewing | Occlusal |  |  |  | 
Lower third molar removal: Low-risk Clinically judged complex high-risk situations |  |  |  |  |  |  | 
Cleft palate treatment |  |  |  |  |  |  | 
Orthognathic surgery: - Regular - Advanced deformity |  |  |  |  |  |  | 
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
(Disclaimer: see slide #36 and slide notes)
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 65: Specific clinical applications: TMJ
Majority of temporomandibular disorder patients: myofascial cause or TMJ disc issue
  MRI as method of choice (but may not affect treatment plan)
Osteoarthritis or rheumatoid arthritis: radiography can show bony changes
  But: the (degree of) information regarding these changes may not have any effect on patient management
  Potential effect on treatment should be considered before radiographic examination (esp. for CBCT; to be used for cases for which MDCT would otherwise be required)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 66: Summary: TMJ
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Clinical indication | MRI | Intra-oral radiograph |  |  | Panoramic radiograph | Lateral ceph. | P-A ceph. | CBCT
 |  | Periapical | Bitewing | Occlusal |  |  |  | 
Regular TMD (myofascial / disc pathology) |  |  |  |  |  |  |  | 
Osteoarthritis / rheumatoid arthritis |  |  |  |  |  |  |  | 
(Disclaimer: see slide #36 and slide notes)
Low usefulness
Medium usefulness
High usefulness
No symbol: not recommended
Notes: Disclaimer: this summary provides a schematic overview of the relative usefulness of different imaging modalities for a particular clinical indication. It has been determined by an IAEA expert panel, based on available literature and guidelines. For certain clinical applications, large discrepancies between different guidelines may exist due to a lack of conclusive evidence. Please refer to the information in these slides as well as any relevant guidelines before making an informed decision regarding the selection of an imaging modality.
Low usefulness: may be indicated for specific cases only
Medium usefulness: may be indicated for a certain proportion of cases, but not as a routine tool
High usefulness: generally accepted as the modality of choice for (nearly) all cases

## Slide 67: Pregnant patients?
Dose to the foetus is extremely low: no contraindication for dental radiographs of pregnant women (but: usually no harm to postpone exposure)
Dose inside FOV of CBCT scan (%)
Dose outside FOV of CBCT scan (A-P or L-R of FOV)
Dose outside FOV of CBCT scan (above/below FOV)
Scattered radiation decreases sharply with increasing distance to FOV border
No measurable scatter ~10 cm or more from upper/lower border of FOV
Pauwels et al. (2012), under the British Institute of Radiology's License to Publish
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Z

## Slide 68: Pregnant patients?
Lead apron:
  CBCT: no protective effect for organs receiving high dose (e.g. thyroid), but can reduce the (already low) dose to breasts and gonads (Schulze et al. 2017)
  Can be recommended for downward exposures e.g. maxillary occlusal radiograph
  Can used at the very least as an assurance to the patient
(see also L11 & L12)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 69: Overview
The justification principle
Radiation dose in dental radiology
Referral criteria
Specific clinical applications
Informing the patient
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 70: Informing the patient
International BSS:
  “The patient or the patient’s legal authorized representative has been informed as appropriate of the expected diagnostic or therapeutic benefits of the radiological procedure as well as the radiation risks.”
EC RP 136 (2004) proposes:
  “Informed consent should be obtained from patients prior to radiography in accordance with national requirements.”
  “Information given to patients prior to dental radiography should stress the very low risk set against the potential benefits for their treatment.”
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 71: Informing the patient
Prior to any radiographic exposure, patient consent is needed
  Not implied consent (i.e. absence of refusal)!
The patient should be informed regarding the benefit and risk of a potential exposure
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 72: Informing the patient
How to ‘translate’ dose & risk to a patient?
  Compare dose for the upcoming exposure with other sources of radiation
    Natural background radiation (world-wide: 2.4 mSv/year [~6.5 µSv/day], but varies greatly between geographical regions)
    Other medical exposures (see further)
    Long-distance flights (~5 µSv/h), high-altitude skiing trips (~2x dose at sea level) → increased exposure to cosmic radiation
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 73: Informing the patient
European Radiological Data Exchange Platform
https://remap.jrc.ec.europa.eu
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 74: Informing the patient
Calculated using the European Program Package for the Calculation of Aviation Route Doses (EPCARD)
http://www.helmholtz-muenchen.de/en/epcard-portal/epcard-home/index.html
Radiation dose received during airplane travel |  | 
From | To | Effective dose (µSv)
Paris | Tokyo | 35
London | New York | 40
Los Angeles | New York | 35
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 75: Informing the patient
Diagnostic procedure | Equivalent number of chest X-rays | Equivalent period of exposure to natural radiation | Typical effective dose
Chest X-ray (single PA film) Adult 5-year-old | 1 1 | 3 d 3 d | 0.02 mSv 0.02 mSv
CT head Adult 5-year-old 10-year-old Paediatric head CT angiography | 100 100 110 250 | 10 m 10 m 11 m 2 y | 2 mSv 2 mSv 2.2 mSv 5 mSv
CT chest Adult 5-year-old 10-year-old | 350 150 175 | 3 y 1.2 y 1.4 y | 7 mSv 3 mSv 3.5 mSv
CT abdomen Adult 5-year-old 10-year-old | 350 185 185 | 3 y 1.5 y 1.5 y | 7 mSv 3.7 mSv 3.7 mSv
Dental examinations Intraoral radiograph Panoramic radiograph Lateral cephalometric radiograph CBCT CT (mandible) CT (mandible & maxilla) | 0.015-1 0.1-2 0.1-0.7 0.5-50 (generally <15) 12.5-70 20-40 | 1 h – 3 d 10 h – 6 d 8 h – 2 d 1.5 d – 5 m (generally <1.5 m) 1 – 7 m 2 – >4 m | 0.3-21.6 µSv 2.7-38 µSv 2.2-14 µSv 11-1025 µSv (generally <300 µSv) 250-1410 µSv 430-860 µSv
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Sources: see slide notes
Notes: Dental data from FGDP (UK), Selection Criteria For Dental Radiography
Other data from “WHO: Communicating radiation risk in paediatric imaging” which makes use of the following sources:
“Summary of patient dose data for paediatric CT examinations” (UNSCEAR, 2010)
Mettler FA Jr, Huda W, Yoshizumi TT, Mahesh M (2008). Effective doses in radiology and diagnostic nuclear medicine: a catalogue. Radiology. 248(1):254-263.
http://www.imagegently.org
Johnson JN et al. (2014). Cumulative radiation exposure and cancer risk estimation in children with heart disease. Circulation. 130(2):161-167
Bacher K et al. (2005). Patient-specific dose and radiation risk estimation in pediatric cardiac catheterization. Circulation. 111:83-89.
Brody AS, Frush DP, Huda W, Brent RL (2007). Radiation risk to children from computed tomography. Pediatrics. 120(3):677-682.
Comparison with natural radiation is based on a worldwide average of 2.4 mSv/year

## Slide 76: Informing the patient
What if the patient wants to know the actual cancer risk from a certain exposure?
  Several considerations should be mentioned:
    Very large uncertainty regarding cancer risk at low doses (see L01)
    Very high individual variability in cancer expression and risk
    Impossible to prove (at this moment) if any future cancer of the patient may be radiation-induced (DNA damage similar to that of other agents)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 77: Informing the patient
What if the patient wants to know the actual cancer risk?
  Risk at a population level can be roughly estimated
    Cancer incidence: ~10% per Sv
    Cancer mortality: ~5% per Sv
    Linear relation between dose and risk assumed (see L01: LNT hypothesis)
    Patient’s age / gender could be accounted for to provide a more accurate risk estimation (see further)
      But risk is always population-based
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 78: Informing the patient
Data from BEIR VII
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 79: Informing the patient
World Health Organization (2016)
Communicating radiation risks in paediatric imaging: information to support healthcare discussions about benefit and risk
http://www.who.int/ionizing_radiation/pub_meet/radiation-risks-paediatric-imaging/en/

## Slide 80: References
Alqerban A et al. (2014) Orthodontic treatment planning for impacted maxillary canines using conventional records versus 3D CBCT. Eur J Orthod. 36:698-707.
Alqerban et al. (2015) Radiographic predictors for maxillary canine impaction. Am J Orthod Dentofacial Orthop. 147:345-54.
American Academy of Oral and Maxillofacial Radiology (2013) Clinical recommendations regarding use of cone beam computed tomography in orthodontics [corrected]. Position statement by the American Academy of Oral and Maxillofacial Radiology. Oral Surg. Oral Med. Oral Pathol. Oral Radiol. 116:238–57.
American Association of Endodontists and American Academy of Oral and Maxillofacial Radiology (2011) Use of cone-beam computed tomography in endodontics. Joint Position Statement of the American Association of Endodontists and the American Academy of Oral and Maxillofacial Radiology. Oral Surg. Oral Med. Oral Pathol. Oral Radiol. Endod. 111:234-7.
Anissi HD et al. (2014) Intraoral radiology in general dental practices - a comparison of digital and film-based X-ray systems with regard to radiation protection and dose reduction. Rofo. 186:762-7.
EC, European Commission (2008) Referral Guidelines For Imaging, radiation protection publication 118, update 2008. European Commission, Luxembourg.
EC, European Commission (2004). European guidelines on radiation protection in dental radiology - The safe use of radiographs in dental practice, radiation protection publication 136, European Commission, Luxembourg. [https://ec.europa.eu/energy/sites/ener/files/documents/136.pdf]
EC, European Commission (2012) Cone beam CT for dental and maxillofacial radiology: evidence based guidelines, radiation protection publication 172. 2012, European Commission, Luxembourg. [https://ec.europa.eu/energy/sites/ener/files/documents/172.pdf]
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology

## Slide 81: References (cont.)
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology
Espelid et al. (2003) EAPD guidelines for use of radiographs in children.
Farman AG. (2009) Self-referral: an ethical concern with respect to multidimensional imaging in dentistry? J Appl Oral Sci. 17(5).
Field MJ & Lohr KN. (1992) Guidelines for Clinical Practice: From Development to Use.
Gaalaas L et al. (2016) Ex vivo evaluation of new 2D and 3D dental radiographic technology for detecting caries. Dentomaxillofac Radiol. 45:20150281.
Ghaeminia H et al. (2015) Clinical relevance of cone beam computed tomography in mandibular third molar removal: A multicentre, randomised, controlled trial. J Craniomaxillofac Surg. 43:2158-67.
Guerrero ME et al. (2012) Inferior alveolar nerve sensory disturbance after impacted mandibular third molar evaluation using cone beam computed tomography and panoramic radiography: a pilot study. J Oral Maxillofac Surg. 70:2264-70.
Harris D et al. (2012) E. A. O. Guidelines for the use of diagnostic imaging in implant dentistry 2011. a consensus workshop organized by the European Association for Osseointegration at the Medical University of Warsaw. Clin. Oral Implants Res. 23:1243-53.
International Commission on Radiological Protection (2007) The 2007 Recommendations of the International Commission on Radiological Protection. ICRP Publication 103. Oxford: Pergamon.
Isaacson KG & Thom AR (ed.) (2001) Guidelines for the use of radiographs in clinical Orthodontics, 2nd ed. British Orthodontic Society, London.
Jung PK et al. (2015) Comparison of cone-beam computed tomography cephalometric measurements using a midsagittal projection and conventional two-dimensional cephalometric measurements. Korean J Orthod. 45:282-8.

## Slide 82: References (cont.)
Korkmaz YT et al. (2017) Does additional cone beam computed tomography decrease the risk of inferior alveolar nerve injury in high-risk cases undergoing third molar surgery? Int J Oral Maxillofac Surg.; 46:628-635.
Matzen LH et al. (2017) Radiographic signs of pathology determining removal of an impacted mandibular third molar assessed in a panoramic image or CBCT. Dentomaxillofac Radiol.;46:20160330.
NCRP (2009) Ionizing Radiation Exposure of the Population of the United States. NCRP Report No. 160, NCRP Publications, Bethesda, MD.
Patel S et al. (2014) European society of endodontology position statement: the use of CBCT in endodontics. Int. Endod. J; 47:502-4.
Pauwels R et al. (2012) Dose distribution for dental cone beam CT and its implication for defining a dose index. Dentomaxillofac Radiol. 41:583-93.
Petersen LB et al. (2016) Neurosensoric disturbances after surgical removal of the mandibular third molar based on either panoramic imaging or cone beam CT scanning: A randomized controlled trial (RCT) Dentomaxillofac Radiol 45:20150224.
Pittayapat P et al. (2014) Agreement between cone beam computed tomography images and panoramic radiographs for initial orthodontic evaluation. Oral Surg Oral Med Oral Pathol Oral Radiol;117:111-9.
Schulze R et al. (2017) Influence of a commercial lead apron on patient skin dose delivered during oral and maxillofacial examinations under Cone Beam Computed Tomography (CBCT). Health Phys J. 113:129-34.
Tyndall DA et al. (2012) Position statement of the American Academy of Oral and Maxillofacial Radiology on selection criteria for the use of radiology in dental implantology with emphasis on cone beam computed tomography. Oral Surg. Oral Med. Oral Pathol. Oral Radiol.113:817-26.
Walter C et al. (2016) Cone beam computed tomography (CBCT) for diagnosis and treatment planning in periodontology: A systematic review. Quintessence Int. 47:25-37.
Radiation Protection in Dental Radiology L09 Justification and appropriate use of dental radiology