## Slide 1: International Atomic Energy Agency Learning programme: Radon gas
Module 2:
Requirements in the International Basic Safety Standards (General Safety Requirements Part 3)

## Slide 2: Content
Basis of the General Safety Requirements (GSR) Part 3
General Requirements
Exposure Situations
Requirement 47: Identify and Evaluate
Requirement 48: Justify and Optimise
Requirement 50: Protection of the Public
Requirement 51: Exposure due to Commodities
Requirement 52: Exposures in Workplaces
Summary of Learning Points

## Slide 3: Basis of the General Safety Requirements (GSR) Part 3
Effects of radiation
Recommendations
for protection
Fundamental safety objectives and principles
Requirements for protection of people and environment
Specific safety guidance
Notes: The protection of people, society and the environment from the harmful effects of ionizing radiation is at the heart of the work of the IAEA Department for Nuclear Safety and Security. The IAEA Safety Standards, provide the fundamental principles, requirements and recommendations to ensure nuclear safety. They serve as a global reference for protecting people and the environment and contribute to a harmonized high level of safety worldwide. The internationally agreed IAEA safety standards provide a basis for States to demonstrate their performance in fulfilling their obligations. They are a cornerstone of the Global Nuclear Safety and Security Regime, which supports the implementation of binding international instruments and national safety infrastructure.
The Safety Standards consists of three sets of publications: the Safety Fundamentals, the Safety Requirements and the Safety Guides. The Safety Fundamentals establish the fundamental safety objective and principles of protection and safety. The Safety Requirements set out the requirements that must be met to ensure the protection of people and the environment, both now and in the future. The Requirements are governed by the objective and principles of the safety fundamentals. The format and style of the requirements facilitate their use for the establishment, in a harmonized manner, of a national regulatory framework. Requirements, including numbered ‘overarching’ requirements, are expressed as ‘shall’ statements. Many requirements are not addressed to a specific party, the implication being that the appropriate parties are responsible for fulfilling them.
The Safety Guides provide recommendations and guidance on how to comply with the requirements, indicating an international consensus that it is necessary to take the measures recommended (or equivalent alternative measures). The Safety Guides present international good practices, and increasingly they reflect best practices, to help users striving to achieve high levels of safety. The recommendations provided in Safety Guides are expressed as ‘should’ statements.
The new International Basic Safety Standards (BSS) (2015) represents an update on the previous version published in 1996. Its development followed an open process of consultation with its eight co-sponsoring bodies and with member states through the four IAEA Safety Standards Committees.
The findings of the United Nations Scientific Committee on the Effects of Atomic Radiation (UNSCEAR) and the recommendations of international expert bodies, notably the International Commission on Radiological Protection (ICRP), are taken into account in developing the IAEA safety standards. UNSCEAR (which is part of the United Nations Environment Program) assesses and reports levels and effects of exposure to ionizing radiation. Governments and organizations throughout the world rely on the Committee's estimates as the scientific basis for evaluating radiation risk and for establishing protective measures.
ICRP is an independent, international organisation with more than two hundred volunteer members from approximately thirty countries across six continents. These members represent the leading scientists and policy makers in the field of radiological protection. ICRP has developed recommendations for radiological protection based on (i) the current understanding of the science of radiation exposures and effects and (ii) value judgements. These value judgements take into account societal expectations, ethics, and experience gained in application of the system.

## Slide 4
“…. There is mounting direct evidence to confirm a small but detectable risk of lung cancer from living with radon in the home, says the United Nations Scientific Committee on the Effects of Atomic Radiation.” (UNSCEAR)
UNSCEAR 2006 Report. Effects of Ionizing Radiation, Volume II Annex E. Sources-to-Effects Assessment for Radon in Homes and Workplaces.
Publications regarding radon

## Slide 5
International Commission on Radiological Protection (ICRP): Publications on Radon
Publication 137: Occupational Intakes of Radionuclides: Part 3 (2018)
Publication 126: Radiological Protection against Radon Exposure (2014)
Publication 115: Lung Cancer Risk from Radon and Progeny and Statement on Radon (2010)
Publication 103: The 2007 Recommendations of the International Commission on Radiological Protection (2007)
Publication 65: Protection Against Radon-222 at Home and at Work (1993)
World Health Organization (WHO)
WHO handbook on indoor radon - a public health perspective (2009)
Publications regarding radon (continued)

## Slide 6: IAEA Safety Standards relating to radon
Safety Fundamentals (SF-1): Fundamental Safety Principles (2006)
General Safety Requirements (GSR Part 3): Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards (2014)
Specific Safety Guide (SSG-32): Protection of the Public against Exposure Indoors due to Radon and Other Natural Sources of Radiation (2015)
Notes: The IAEA safety standards are applicable, as relevant, throughout the entire lifetime of all facilities and activities — existing and new — utilized for peaceful purposes and to protective actions to reduce existing radiation risks. They can be used by States as a reference for their national regulations in respect of facilities and activities.
Protection of the public, as specified in GSR Part 3, has always been part of the radiation protection requirements. However, there has been relatively little guidance provided specifically on the protection of the public against exposure due to natural sources of radiation.
The Specific Safety Guide SSG-32 Protection of the Public against Exposure Indoors due to Radon and Other Natural Sources of Radiation provides recommendations and guidance on meeting the requirements of GSR Part 3 for protection of the public against exposure indoors due to natural sources of ionizing radiation.
This Safety Guide is intended to fill that gap by focusing on the identification and implementation of appropriate measures for protection of members of the public against exposure indoors due to natural sources of radiation. Exposure indoors is usually higher than exposure outdoors, but is more readily controllable.
In the next slides we will elaborate on the elements of the IAEA standards that apply to radon in particular

## Slide 7
SF-1: Fundamental Safety Principles (2006)
Establishes the safety objective and safety principles for the protection of people and the environment
  Principle 10: “Protective actions to reduce existing or unregulated radiation risks must be justified and optimized.”
  This includes exposure to natural sources of radiation such as due to radon1 in dwellings and workplaces
1the term ‘radon’ is used to mean any
combination of the two main isotopes of the
element radon (222Rn and 220Rn).
Notes: The IAEA Safety Fundamentals publication “Fundamental Safety Principles” establishes the safety objective and safety principles for the
protection of people and the environment from harmful effects of ionizing radiation.
Principle 10 states that: “Protective actions to reduce existing
or unregulated radiation risks must be justified and optimized.” One type of situation covered by this principle is exposure due to natural sources of radiation, including exposure due to radon in dwellings and workplaces.
Protection of the public, as specified in GSR Part 3, has always been part of the radiation protection requirements. However, there has been relatively little guidance provided specifically on the protection of the public against exposure due to natural sources of radiation.
This Safety Guide is intended to fill that gap by focusing on the identification and implementation of appropriate measures for protection of members of the public against exposure indoors due to natural sources of radiation. Exposure indoors is usually higher than exposure outdoors, but is more readily controllable.

## Slide 8
IAEA Basic Safety Standards GSR Part 3
Requirement 1: Application of the principles of radiation protection.
Parties with responsibilities for protection and safety shall ensure that the principles of radiation protection are applied for all exposure situations.
Requirement 2: Establishment of a legal and regulatory framework
The government shall establish and maintain a legal and regulatory framework for protection and safety and shall establish an effectively independent regulatory body with specified responsibilities and functions.
Notes: This slide and the next ones set out the text of the 5 general requirements of the BSS that apply to radon whether directly or indirectly. The general requirements apply to exposure to radon in that the BSS regards radon exposure no differently to other exposure situations, but interpretation of the requirements reflects the unique aspects of control radon exposure.

## Slide 9
Basic Safety Standards GSR Part 3
General Requirements (cont’d)
Requirement 3: Responsibilities of the regulatory body
The regulatory body shall establish or adopt regulations and guides for protection and safety and shall establish a system to ensure their implementation.
Requirement 4: Responsibilities for protection and safety
The person or organization responsible for facilities and activities that give rise to radiation risks shall have the prime responsibility for protection and safety. Other parties shall have specified responsibilities for protection and safety.

## Slide 10
Basic Safety Standards GSR Part 3
General Requirements (cont’d)
Requirement 5: Management for protection and safety
The principal parties shall ensure that protection and safety are effectively integrated into the overall management system of the organizations for which they are responsible.

## Slide 11
Basic Safety Standards GSR Part 3:
Types of Exposure Situations
General Safety Requirements (GSR) Part 3 distinguishes between 3 types of exposure situations:
Planned Exposure Situations
Emergency Exposure Situations
Existing Exposure Situations
Indoor radon exposure in homes and workplaces is regarded as an Existing Exposure Situation.
Radon exposure over 1000 Bq/m3 in workplaces as well as in uranium mining and producing operations is regarded as Planned Exposure Situation.
Notes: For the purpose of establishing practical requirements for protection and safety, the IAEA Standards distinguish between three different types of exposure situation: planned exposure situations, emergency exposure situations and existing exposure situations. Together these three situations cover all exposure scenarios that can arise.
A planned exposure situation is a situation of exposure that arises from the planned operation of a source or from a planned activity that results in an exposure due to a source. Since provision for protection and safety can be made before embarking on the activity concerned, the associated exposures and their likelihood of occurrence can be restricted from the outset.
An emergency exposure situation is a situation of exposure that arises as a result of an accident, a malicious act or any other unexpected event, and requires prompt action in order to avoid or to reduce adverse consequences.
An existing exposure situation is a situation of exposure that already exists when a decision on the need for control needs to be taken. Existing exposure situations include situations of exposure to natural background radiation. Radon exposure in homes and workplaces are considered existing exposure situations in that the radiation exposure already exists and the situation must be managed. The management required will vary from scenario to scenario.

## Slide 12
Existing Exposure Situations
Requirement 47 in GSR Part 3
Requirement 47: Responsibilities of the government specific to existing exposure situations
The government shall ensure that existing exposure situations that have been identified are evaluated to determine which occupational exposures and public exposures are of concern from the point of view of radiation protection.
5.2. …responsibilities for protection and safety are assigned and appropriate reference levels are established.
5.3. …include in the legal and regulatory framework for protection and safety…provision for the management of existing exposure situations.
Notes: In the generic safety requirements for Existing Exposure Situations the BSS sets out the obligations of government for:
The identification and assessment of radiation exposure due to radon,
The assignment of responsibility for action on radon and for setting reference levels,
The establishment a regulatory infrastructure and plans for the management of radon exposure.
These requirements are presented as “shall” statements - in other words they are mandatory requirements.

## Slide 13
Requirement 47 (cont’d): Responsibilities of the government specific to existing exposure situations
…provision for the management of existing exposure situations.
In the case of exposure due to radon, this will include exposure in workplaces for which the exposure due to radon is not required by or directly related to the work and for which annual average activity concentrations of radon might be expected not to exceed an established reference level.
Notes: The government, in the legal and regulatory framework, as appropriate:
“Shall specify the exposure situations that are included in the scope of existing exposure situations;
In the case of exposure due to radon, this will include exposure in workplaces for which the exposure due to radon is not required by or directly related to the work and for which annual average activity concentrations of radon might not be expected to exceed an established reference level.”

## Slide 14
Requirement 47 (cont’d): Responsibilities of the government specific to existing exposure situations
…provision for the management of existing exposure situations.
The Government shall:
Assign responsibility for the establishment and implementation of protection strategies
Involve interested parties in their development and implementation
Arrange for evaluation of remedial and protective actions
Ensure health and protection information is available to expose persons
Notes: The government
Shall specify the general principles underlying the protection strategies developed to reduce exposure when remedial actions and protective actions have been determined to be justified;
Shall assign responsibilities for the establishment and implementation of protection strategies to the regulatory body and to other relevant authorities and, as appropriate, to registrants, licensees and other parties involved in the implementation of remedial actions and protective actions;
Shall provide for the involvement of interested parties in decisions regarding the development and implementation of protection strategies, as appropriate.
The regulatory body or other relevant authority shall implement the protection strategy, including:
Arranging for evaluation of the available remedial actions and protective actions for achieving the objectives, and for evaluation of the efficiency of the actions planned and implemented;
Ensuring that information is available to individuals subject to exposure on potential health risks and on the means available for reducing their exposures and the associated risks.

## Slide 15
Requirement 48 in GSR Part 3: Justification for protective actions and optimization of protection and safety
The relevant authority shall ensure that remedial actions and protective actions are justified and that protection and safety is optimized.
The government shall ensure that:
the protection strategy for the management of radon exposure, is commensurate with the associated radiation risks
remedial or protective actions yield sufficient benefits to outweigh the detriments.
The implementation of remedial actions does not imply the elimination of all radioactivity or all traces of radioactive substances.
Notes: The government and the regulatory body or other relevant authority shall ensure that the protection strategy for the management of existing exposure situations, is commensurate with the radiation risks associated with the existing exposure situation; and that remedial actions or protective actions are expected to yield sufficient benefits to outweigh the detriments associated with taking them, including detriments in the form of radiation risks.
The regulatory body or other relevant authority and other parties responsible for remedial actions or protective actions shall ensure that the form, scale and duration of such actions are optimized.
The implementation of remedial actions (remediation) does not imply the elimination of all radioactivity or all traces of radioactive substances. The optimization process may lead to extensive remediation but not necessarily to the restoration of previous conditions.

## Slide 16
Requirement 48 (cont’d): Justification for protective actions and optimization of protection and safety
The Government shall ensure that the form, scale and duration of such actions are optimized.
Priority shall be given to those groups for whom the dose exceeds the reference level.
All reasonable steps shall be taken to prevent doses from remaining above the reference levels.
Reference levels shall typically be expressed as an annual effective dose to the representative person in the range of 1–20 millisievert(s) (mSv)
The Reference levels will be periodically reviewed to ensure that they remain appropriate
The optimization process may lead to extensive remediation but not necessarily to the restoration of previous conditions.
The relevant authority shall ensure that remedial actions and protective actions are justified and that protection and safety is optimized.
Notes: The regulatory body or other relevant authority and other parties responsible for remedial actions or protective actions shall ensure that the form, scale and duration of remedial or protective actions are optimized.
While this optimization process is intended to provide optimized protection for all individuals subject to exposure, priority shall be given to those groups for whom the dose exceeds the reference level. All reasonable steps shall be taken to prevent doses from remaining above the reference levels.
Reference levels shall typically be expressed as an annual effective dose to the representative person in the range of 1–20 mSv or other corresponding quantity, the actual value depending on the feasibility of controlling the situation and on experience in managing similar situations in the past.
The regulatory body or other relevant authority shall periodically review the reference levels to ensure that they remain appropriate in the light of the prevailing circumstances.
The implementation of remedial actions (remediation) does not imply the elimination of all radioactivity or all traces of radioactive substances. The optimization process may lead to extensive remediation but not necessarily to the restoration of previous conditions.

## Slide 17
Requirement 50 in GSR Part 3: Public Exposure due to Radon Indoors
“Where activity concentrations of radon that are of concern for public health are identified…, the government shall ensure that an action plan is established comprising coordinated actions to reduce activity concentrations of radon in existing buildings and in future buildings”.
The government shall assign responsibility for establishing and implementing an action plan and for determining the circumstances under which actions are to be mandatory, or voluntary, taking account of legal, social and economic circumstances.
Notes: The Generic Safety Requirement 50 calls for a specific action on radon, i.e. the establishment of an action plan to address identified health risks due to radon.
This is a key requirement in the BSS regarding radon.
Requirement 50 specifically states that the action plan should be co-ordinated and focus on existing and future buildings.
Bearing in mind that radon is a natural occurrence and is highly variable around the world, the BSS requirement 50 allows for flexibility in the approach taken in each member state, provided that the general principles and generic requirements are applied.

## Slide 18
Action Plan for Radon in dwellings and high occupancy buildings
An Action Plan shall comprise co-ordinated actions to reduce activity concentration of radon in existing and future buildings including:
Establishing a reference level for Radon, that in general will not exceed an annual average activity concentration of 300 Bq/m3*;
(b) Reducing activity concentrations of Radon and consequent exposures to levels at which protection is optimized;
(c) Prioritising actions to reduce radon activity concentrations in those situations for which such action is likely to be most effective;
(d) Including in building codes or standards preventive measures and corrective actions to prevent the ingress of Radon and to facilitate further actions wherever necessary.
* Corresponds to annual effective dose of the order 10 mSv.
RADON ACTION PLAN
Notes: An action plan informed by gathered radon data will consist of actions aimed at reducing exposure in existing and future buildings. As the actions may involve contributions from different agencies and over extended time scales it is important that these actions are co-ordinated and integrated.
Government shall assign responsibility for:
(a) establishing and implementing an action plan for controlling public exposure due to radon indoors; and
(b) determining the circumstances under which actions are to be mandatory or are to be voluntary, with account taken of legal requirements and of the prevailing social and economic circumstances.
The action plan will include:
(a) Establishing an appropriate reference level for radon for dwellings and other buildings with high occupancy factors for members of the public, with account taken of the prevailing social and economic circumstances, that in general will not exceed an annual average activity concentration due to radon of 300 Bq/m3; the value of 300Bq/m3 is recommended as an upper limit for a reference level on the assumption of an equilibrium factor for 222Rn of 0.4 and an annual occupancy of 7000 hours. With these assumptions, 300 Bq/m3 corresponds to an annual effective dose of the order of 10 mSv;
In Publication 65 the ICRP presents its recommendations for action levels in existing dwellings, new dwellings and aboveground and underground workplaces, as well as its recommendations for identifying radon prone areas, and for applying preventive measures and corrective actions. In its ‘Statement on Radon’, (ICRP, Publication 115, (2010) the ICRP suggests an annual effective dose of around 10 mSv from 222Rn as a level at which action would almost certainly be warranted to reduce exposure. The ICRP, taking account of new findings, revised the upper value for the reference level for radon gas in dwellings from 600 Bq/m3 — the value suggested in its 2007 Recommendations — to 300 Bq/m3.
The World Health Organization (WHO) addressed public health aspects of exposure indoors due to radon by reflecting the epidemiological evidence that public exposure indoors due to radon is responsible for a substantial number of lung cancers in the general population. The WHO Handbook on Indoor Radon provides detailed recommendations on reducing health risks due to radon as well as policy options for preventing and reducing radon exposures. The WHO proposes a reference level of 100 Bq/m3 to minimize health hazards of exposure indoors due to radon, adding that “if this level cannot be reached under the prevailing country specific conditions, the chosen reference level should not exceed 300 Bq/m3”;
(b) Reducing activity concentrations of radon and consequent exposures to levels at which protection is optimized;
(c) Giving priority to actions to reduce activity concentrations of radon in those situations for which such action is likely to be most effective (Examples of this include: (i) specifying the levels of activity concentrations of radon in dwellings and other buildings with high occupancy factors at which protection can be considered optimized; (ii) identifying radon prone areas; (iii) identifying characteristics of buildings that are likely to give rise to elevated activity concentrations of radon; and (iv) identifying and requiring preventive measures for radon in future buildings that can be introduced at relatively low cost.);
(d) Including in building codes or standards the appropriate preventive measures and corrective actions to prevent the ingress of radon and to facilitate further actions wherever necessary.

## Slide 19
Requirement 51 in GSR Part 3: Exposure due to radionuclides in commodities
The responsible authority shall establish reference levels for exposure due to radionuclides in commodities.
The responsible authority shall
establish specific reference levels for exposure due to radionuclides in commodities such as construction materials, food and feed, and in drinking water,
the annual annual effective dose to the representative person generally does not exceed a value of about 1 mSv.
In establishing reference levels the authority shall
consider the guideline levels for radionuclides in food traded internationally that could contain radioactive substances as a result of a nuclear or radiological emergency, which have been published by the Joint Food and Agriculture Organization of the United Nations/World Health Organization Codex Alimentarius Commission
consider the guideline levels for radionuclides contained in drinking water that have been published by the World Health Organization.
Notes: Requirement 51 requires the establishment of reference levels for exposure due to radionuclides in commodities. This pertains to radon in situations where commodities such as building materials contain naturally occurring radon. Where these materials are used in construction they can contribute to indoor radon exposure. The contribution from building materials to indoor radon concentrations tends to be less significant that that from the soil, but there are exceptional circumstances where this is not the case.
Similarly, radon dissolved in drinking water and transferred to foods and feeds must be taken into account in radon exposure management, but subject to regional exceptions, the contribution from these sources tends to be minor.
The regulatory body or other relevant authority shall establish specific reference levels for exposure due to radionuclides in commodities such as construction materials, food and feed, and in drinking water, each of which shall typically be expressed as, or be based on, an annual effective dose to the representative person that generally does not exceed a value of about 1 mSv.
The regulatory body or other relevant authority shall consider the guideline levels for radionuclides in food traded internationally that could contain radioactive substances as a result of a nuclear or radiological emergency, which have been published by the Joint Food and Agriculture Organization of the United Nations/World Health Organization Codex Alimentarius Commission [23]. The regulatory body or other relevant authority shall consider the guideline levels for radionuclides contained in drinking water that have been published by the World Health Organization.

## Slide 20
Requirement 52 in GSR Part 3: Exposure due to radon in workplaces
The regulatory body shall establish and enforce requirements for the protection of workers in existing exposure situations.
Government shall assign responsibility for the establishment of a strategy for protection against exposure due to Radon in workplaces.
The responsible authority shall
Establish a strategy for protection against radon exposure in workplaces
Establishment of a reference level not more than 1 000 Becquerels per meter cubed (Bq/m3)
Ensure that protection is optimised
If reasonable efforts fail, shall manage as a planned exposure situation
Notes: While the BSS Requirement 50 relates primarily to the protection of the public, the Requirement 52 establishes specific requirements for the protection of workers exposed to radon in the workplace. The requirement places responsibilities on employers. This can present some difficulties in regard to radon control where the workplace is an rented property; in this case the government must decide where responsibility lies to mitigate radon ingress – with the employer or the landlord.
Exposure due to radon in workplaces
The regulatory body or other relevant authority shall establish a strategy for protection against exposure due to 222Rn in workplaces, including the establishment of an appropriate reference level for 222Rn. The reference level for 222Rn shall be set at a value that does not exceed an annual average activity concentration of 222Rn of 1000 Bq/m3, with account taken of the prevailing social and economic circumstances.
On the assumption of an equilibrium factor for 222Rn of 0.4 and an annual occupancy of 2000 h, the value of activity concentration due to 222Rn of 1000 Bq/m3 corresponds to an annual effective dose of the order of 10 mSv.
Employers shall ensure that activity concentrations of 222Rn in workplaces are as low as reasonably achievable below the established reference level, and shall ensure that protection is optimized.
If, despite all reasonable efforts by the employer to reduce activity concentrations of radon, the activity concentration of 222Rn in workplaces remains above the reference level, the relevant requirements for occupational exposure in planned exposure situations as outlined in Section 3 of the International BSS shall apply.

## Slide 21
Specific Safety Guide (SSG-32): Protection of the Public against Exposure Indoors due to Radon and Other Natural Sources of Radiation
Scope - Public exposure due to natural sources of radiation
Specifically covering:
Radon in dwellings and other buildings with high occupancy factors for the public.
Public exposure due to 220Rn in dwellings.
Public exposure to external gamma radiation from radionuclides of natural origin in the soil and in building materials.
Not including: Public exposure due to radon in workplaces with low occupancy factors for members of the public, such as offices and factories.
Notes: Protection of the public, as specified in GSR Part 3, has always been part of the radiation protection requirements. However, there has been relatively little guidance provided specifically on the protection of the public against exposure due to natural sources of radiation.
This Safety Guide focuses on the identification and implementation of appropriate measures for protection of members of the public against exposure indoors due to natural sources of radiation. Exposure indoors is usually higher than exposure outdoors, but is more readily controllable.
The scope of this Safety Guide covers exposure of the public indoors due to natural sources of radiation. It provides recommendations and guidance to be followed by the regulatory body and all other authorities and organizations with responsibilities in relation to exposure to radiation from natural sources.
It discusses public exposure due to radon in dwellings and other buildings with high occupancy factors for the public. This includes buildings such as kindergartens, schools and hospitals. High total occupancy by individuals (Ref. [1], para. 3.23) as well as high occupancy factors need to be considered. The exposure pathways considered are: ingress of radon from the soil; radon released from building materials used in the construction of the dwelling; and radon entering the dwelling via the water supply.
Public exposure due to 220Rn in dwellings. The exposure pathways considered are: 220Rn released from soil, and 220Rn released from building materials used in the construction of the dwelling. Radon-220 entering the dwelling via the water supply is seldom a source of significant radiation exposure.
Public exposure to external gamma radiation from radionuclides of natural origin in the soil and in building materials. ‘Building materials’ are construction materials that are used for the construction of buildings such as dwellings, and offices, industrial premises and other workplaces.
Not included: Public exposure due to radon in workplaces with low occupancy factors for members of the public, such as offices and factories. Visitors to caves in which guides provide tours for the general public are likely to be exposed to radon for a short period only and this will usually not necessitate control.

## Slide 22: Summary Learning Points
The General Safety Requirements (Part 3) on radon are an internationally agreed set of standards that represent the latest opinion of experts from member states and international scientific organisations
In these standards the term radon is taken to mean any combination of the two isotopes of the element radon (222Rn and 220Rn)
Radon exposure is addressed in the standard as an Existing Exposure Situation
Requirement 47 sets out the responsibilities of government for radon – evaluating and assessing the extent of the radon exposure
Requirement 50 sets out the requirement for government to establish and implement an action plan for controlling public exposure due to radon indoors
The action plan applies to dwellings and high occupancy buildings.
High occupancy is regarded as 7 000 hours per annum
Detailed information on establishing an action plan will be addressed in the next module (3).

## Slide 23: Further Reading
International Atomic Energy Agency (2014). Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards. General Safety Requirements Part 3.
International Atomic Energy Agency (2015). Protection of the Public against Exposure Indoors due to Radon and Other Natural Sources of Radiation. Specific Safety Guide. IAEA Safety Standards Series No. SSG-32.
World Health Organization (2009). Handbook on Indoor Radon: A Public Health Perspective, Geneva.
International Commission on Radiological Protection (IRCP) (2010). Lung Cancer Risk from Radon and Progeny and Statement on Radon, Publication 115, Elsevier, Oxford.

## Slide 24: July 2018