## Slide 1: Transport of NORM

## Slide 2
Content
IAEA Transport Regulations
Applicability of the Transport Regulations to NORM
Low specific activity (LSA) material
Surface contaminated objects (SCO)
Marking and labelling
Documentation
Summary

## Slide 3
IAEA Transport Regulations
The IAEA Regulations for the Safe Transport of Radioactive Material (also known as the ‘Transport Regulations’) are IAEA “requirements”.
The transport requirements for all types of radioactive materials are set down in SSR-6 (Rev. 1), 2018.
This means that they should be complied with.
NORM falls within the definition of radioactive material, however, not all NORM is subject to the requirements of the Transport Regulations
The scope of application of the Transport Regulations to NORM depends on:
  Activity concentrations
  Whether or not the radionuclide content is incidental to the use of the material

## Slide 4
Purpose of the Transport Regulations
Protect people, property and the environment during transport of radioactive materials by;
  Containment of radioactivity
  Control of external radiation levels
Designed to cover all radioactive materials

## Slide 5
Application of the Regulations
Depending upon the materials, there are different levels of application of the regulations with different requirements.
The levels depend upon the material and are;
  Regulations do not apply
  Exempt
  Excepted
  Full application of regulations
NORM can fall into any level (depending upon radionuclides and concentrations)

## Slide 6
Application of the Regulations
The regulations do not apply to;
  Natural materials and ores containing naturally occurring radionuclides, in secular equilibrium, which may have been processed, provided the activity concentration does not exceed 10 times the values in Table 2 of the Regulations. (clause 107(f))
  This equates to material that contains less than 10Bq/g of Unat and 10Bq/g of Thnat
Therefore exemption may apply to ores or processed materials

## Slide 7
Exemption of the Regulations
NORM that has been processed for purposes of extraction of its radionuclides, or is intended to be processed for use of these radionuclides:
  The Transport Regulations apply if both the following criteria are exceeded:
    The activity concentration for exempt material in transport
    The activity limit for an exempt consignment
NORM in its natural state, or which has been processed for purposes other than for extraction of its radionuclides, and which is not intended to be processed for use of these radionuclides:
  The Transport Regulations apply if both the following criteria are exceeded:
    10 times the activity concentration for exempt material in transport
    The activity limit for an exempt consignment

## Slide 8
Exemption of the Regulations
Examples of activity concentrations for exempt material in transport:
  UNAT, ThNAT: 1 Bq/g
  234U (lung class M): 100 Bq/g
  234Th: 1000 Bq
  All other U, Th series : 1 or 10 Bq/g
  40K : 100 Bq/g
Examples of activity limit for an exempt consignments:
  UNAT, ThNAT : 1000 Bq
  Individual U, Th series: 10 000 or 100 000 Bq
  40K: 1 000 000 Bq

## Slide 9
NORM Considerations
For U, Th series radionuclides, the values for activity concentration and total activity automatically take into account the presence of certain specified decay products in equilibrium
  For Unat and Thnat, all decay products are included
  This is why the exemption levels are at the low end of the range
For most NORM, the activity concentration rather than the total activity is likely to be the deciding factor
  The amounts of material involved are such that the limits on total activity will usually be exceeded

## Slide 10
NORM Considerations
When radionuclides are out of equilibrium, there is a formula
The concentration of each radionuclide is divided by its respective exemption level and the fractions are added together, as follows:
or
where
  x(i) = activity concentration of radionuclide i
  X(i) = activity concentration for exempt material for radionuclide I
(Note that there are two formulae because of clause 107(f))

## Slide 11
Low specific activity (LSA) material
LSA material — radioactive material which by its nature has a limited specific activity, or radioactive material for which limits of estimated average specific activity apply
External shielding materials surrounding the LSA material are not considered in determining the estimated average activity concentration
NORM that is subject to the Transport Regulations could be classified as LSA-I, LSA-II or LSA-III, depending on the activity concentration and other characteristics
The LSA classification determines the specific requirements for transport, such as packaging and labelling
LSA-I material may be transported unpackaged subject to certain conditions

## Slide 12
Low specific activity (LSA) material
NORM LSA material may also be transported in industrial packages such as drums, bags and ISO containers

## Slide 13
Surface contaminated objects (SCO)
SCO — a solid object which is not itself radioactive but which has radioactive material distributed on its surfaces
A surface contaminated object that is subject to the Transport Regulations could be classified as SCO-I or SCO-II, depending on the surface activity concentration, the radionuclides involved and whether the contamination is fixed or non-fixed
SCO-I objects may be transported unpackaged under certain conditions

## Slide 14
Surface contaminated objects (SCO)
Contamination is defined as the presence of a radioactive substance on a surface in amounts exceeding the following:
  Beta, gamma, low toxicity alpha emitters: 0.4 Bq/cm2
  All other alpha emitters: 0.04 Bq/cm2
Low toxicity alpha emitters include:
  Unat, Udep, Thnat, 235U or 238U, 232Th, 228Th and 230Th when contained in ores or physical and chemical concentrates
  Alpha emitters with a half-life of less than 10 days
Only objects whose surfaces are ‘contaminated’ according to this definition are subject to the Transport Regulations

## Slide 15
Packaging
Must be suitable to contain the radioactive material and prevent the spread of radioactivity during any incident which might occur during the transportation
Type of package depends on;
  Activity of material
  Radionuclides present
  Form of material (liquid, gas, solid)
Radioactive material must be packed and stowed so that contents are retained under ‘routine conditions of transport’
Does not need to be a rigid box
  Eg pallet of drillcore trays, securely wrapped with plastic

## Slide 16
Excepted Packages
Doserate on surface less than 5 µSv/h (clause 516)
Quantity of Unat is unlimited (clause 408)
UN Number 2910
Transport documents describe package as:
  Radioactive Material – Excepted Package limited Quantity of Material
  Name and address of consignor and consignee
No labels on outside of package expect for UN number
Dangerous good certificate completed

## Slide 17
Marking and Labelling
UN number
Labelling
  2 per package
Placards
  4 per container
Transport Index
  Related to the radiation level 1 m from the package exterior
Hazard labels
  Includes secondary hazards

## Slide 18
Marking and Labelling
Examples of UN numbers relevant to NORM:
  2910 Radioactive Material, Excepted Package — Limited quantity of material
  2912 Radioactive Material, Low specific Activity (LSA-I)
  3321 Radioactive Material, Low specific Activity (LSA-II)
  3322 Radioactive Material, Low specific Activity (LSA-III)
  2913 Radioactive Material, Surface Contaminated Objects (SCO-I or SCO-II)

## Slide 19
Category I-White
Dose rate at surface < 5 μSv/h
Dose rate at 1m < 0. 5 μSv/h
Describe contents and estimate total activity, for NORM, use LSA
If the surface dose rate is higher than figures above, it can be repacked

## Slide 20
Category II-Yellow
Used when dose rate at 1 m is > 0.5 mSv/h
Describe contents and estimate total activity
Need to add “Transport Index”

## Slide 21
Transport Index
Maximum dose rate at one metre from the package in mSv/h, multiplied by 100

## Slide 22
Labelling Requirements
White Label I
  Dose rate on surface must not exceed 5µSv/h
Yellow Label II
  Dose rate on surface must not exceed 500µSv/h
  Transport Index must not exceed 1
Yellow Label III
  Dose rate on surface must not exceed 2000µSv/h
  Transport index must not exceed 10

## Slide 23
Placard
Placards go on the vehicle
  Same style as dangerous goods placards
2 sides and rear of a vehicle
4 sides of a container

## Slide 24
Documentation
Dangerous goods declaration
Consignor’s note
  Information on the consignor and consignee
  Description of the radioactive material
  Any additional safety information
  Emergency instructions, telephone numbers, etc.

## Slide 25
Declaration Form Information
Proper shipping name
  Radioactive Material Low Specific Activity (LSA-1)
Radioactive material
  Uranium ore
  UN number 2912
Activity, Hazard Category, Transport Index
  As for label
Package Classification
  IP-1

## Slide 26
Responsibilities
There are three ‘players’
  The consignor (the person sending the package)
    Responsible for packaging, labelling and providing accurate documentation
  The carrier
    Responsible for carriage. Proper stowage, interim storage, undelivered packages, radiation protection, training of drivers and storekeepers etc
  The driver
    Safety and security of load, emergency procedures

## Slide 27
Key Messages
IAEA Transport Regulations are mandatory
Regulations can appear to be detailed and complex
Need to have good understanding of material being transported
NORM is at low end of requirements