## Slide 1: Radiation Protection Programme (RPP)

## Slide 2
Content
Radiation protection perspectives
Radiation protection programme – main elements
Control of exposure
Qualified experts
Local operating instructions
Classification of areas
Monitoring for operational control
Monitoring for assessment of dose
Education and training
Workers’ health surveillance
Key messages

## Slide 3
Radiation Protection Programme (RPP)
Purpose to demonstrate management responsibility for protection, safety and optimization using management structures, policies, procedures and organizational arrangements
Employer to establish and manage RPP in close co-operation with company’s Health & Safety team
Roles and responsibilities to be documented

## Slide 4
Radiation Protection Perspectives
Radiation protection is only one element in ensuring the overall health and safety of workers, the public, and protection of the environment
The radiation protection programme (RPP) should be established in close cooperation with those responsible for other areas of protection and safety such as: Industrial hygiene, Industrial safety, Fire safety, Environmental protection etc.
RPP should consider all radiation sources including natural radioactive sources.
Notes: Artificial sources include; industrial radiography and radioactive sources which are generally much greater than hazards due to NORM.

## Slide 5
RPP – main components
The RPP for a NORM industrial facility shall contain the following components:
  Management system
  Assignment of responsibilities
  Controlled and supervised areas
  Local rules and supervision
  Monitoring, recording and reporting
  Education and training
  Health surveillance

## Slide 6
RPP – main components
The content of the RPP should be commensurate with the nature and extent of the risks:
  Many NORM operations involve only low risks
  There is no real prospect of a radiological emergency
  It is essential to consider the effectiveness of other forms of regulation in minimizing radiological risks:
    OHS regulation
    Environmental protection regulation

## Slide 7
The hierarchy of control measures
Engineered controls and design features
Administrative controls (systems of work)
Personal Protective Equipment (PPE)
Use these first
Containment, ventilation, design for ease of decontamination (and shielding)
Where use of engineered controls is not sufficient alone to restrict exposures, consider admin controls
Use when engineered controls and admin controls are not sufficient to provide adequate protection

## Slide 8
Control of exposure - Gamma
Time, distance and shielding
Control measures are usually only required for high activity NORM:
  Facility design with respect to bulk material
    Distance (dedicated storage areas)
    Shielding (walls, stockpiles of low activity material)
  Rules and working procedures
    Exposure times
  Warning signs, physical barriers
  Training and awareness

## Slide 9
Control of exposure - Dust
Complete containment of material in NORM industrial facilities is often impractical, especially where large quantities involved
Spills and spread of materials to other areas are often of no radiological significance unless activity concentrations are high
Workplace ventilation (dust may already be controlled by OHS regulation for non-radiological reasons)

## Slide 10
Control of exposure - Radon
Ventilation
  In underground mines especially, this can be crucial
Occupancy time
  Where there are practical limitations on the provision of adequate ventilation
Workplaces involving minerals with a high 232Th content, e.g. monazite, attention may have to be given also to the control of thoron (220Rn)

## Slide 11
Personal Protective Equipment (PPE)
Selection of PPE depends on the hazards involved in the work
Employer should specify appropriate protective clothing in accordance with risk of internal and external exposure
PPE should provide adequate protection and be comfortable and convenient to use
For example:
  overalls or protective coats
  head coverings
  safety eyewear
  gloves
  impermeable footwear
  respiratory protection
Individuals should be trained and wear PPE provided

## Slide 12
Qualified experts
Depending on the nature of the operation and the risks involved, the following expert services may be needed in a NORM facility:
  Radiation protection and dosimetry
    Radiation protection officer (RPO)
  Ventilation engineer:
    e.g. in underground mines and other facilities with high potential for dust and/or radon
  Occupational medicine (for health surveillance)
  Industrial hygiene and safety
  Environmental practitioner
Notes: In facilities where the services of a ventilation officer are necessary, the ventilation officer should:
  Advise management on all matters relating to ventilation and air purification systems

## Slide 13
Qualified Experts and Radiation Protection Officer
Radiation Protection Officer (RPO) to be appointed to oversee compliance with regulatory requirements
QE and RPO to be provided with adequate equipment, resources and staff
Employer to consult QE as appropriate on all aspects of the RPP
QE to report to employer representative with overall responsibility for safety
Notes: Refer to para 3.65 and 3.66 of GSG 7

## Slide 14
Local Rules and Procedures
Management required to establish Local Rules, to ensure protection and safety of workers
Local Rules to be made known to workers and be prominently displayed or otherwise made available
Local Rules to be adequately supervised and all workers to be given adequate training to enable them to comply with Local Rules and procedures

## Slide 15
Local Rules and Procedures
Local rules and procedures must be developed and tailored to the type of NORM facility involved
For example, in underground mines and other workplaces where exposure to airborne dust and/or radon is of significant concern, special reference may need to be made to:
  Monitoring of dust and/or radon
  The maintenance of adequate quality/quantity of ventilation air
  The control of ventilation
  The provision of alternative means of ventilation if the normal ventilation system fails

## Slide 16
Classification of areas
Area classification should be considered when there is occupational exposure to radiation
Prior radiological evaluation to identify areas in need of classification
Two types of areas to be clearly defined in the RPP;
  Controlled Areas
  Supervised Areas

## Slide 17
Controlled areas
To be designated when specific measures for protection and safety are required for:
  Controlling exposures or preventing the spread of contamination
  Preventing or limiting the likelihood and magnitude of exposures in anticipated operational occurrences and accident conditions

## Slide 18
Requirements for Controlled Areas -1
Delineated by physical or other suitable means
Radiation warning symbol and access instructions to be displayed at access points
Access restriction by physical or administrative means as appropriate
Information, instruction and training for persons working in area

## Slide 19
Requirements for Controlled Areas -2
Measures for protection and safety within area to be established, e.g.
  Physical measures to control the spread of contamination
  Local rules and procedures
Personal Protective Equipment, changing facilities and monitoring equipment to be provided at entrance to area (where appropriate)
Monitoring equipment, washing facilities and storage for contaminated PPE to be provided at exit from area (where appropriate)

## Slide 20
Supervised areas
To be designated when it is necessary for exposure conditions to be kept under review (when not already designated as a controlled area)
Areas where prior radiological evaluation predicts effective dose greater than 1 mSv per year should be designated as supervised areas
Delineation and signs may be appropriate but not always (eg. if accessible to the public)

## Slide 21
Classification of areas
The classification of areas and means of access control may require special consideration in some types of NORM facility.
It may be appropriate in some underground mines with high exposure potential (e.g. radon) to designate the entire underground area as a controlled area, rather than trying to distinguish between controlled and supervised areas
Physical barriers or existing access controls provide a means for classification of areas.
  e.g. physical barriers, locks and interlocks
Notes: In mines, the most practical means of access control may be in the form of cards, tags and supervision

## Slide 22
Overview of Monitoring
Measurement of radiological parameters in an operating NORM facility provides the diagnostic information necessary for maintaining protection and safety
Departures from normal operating conditions and the need for correction are quickly detected
The RPP should include provisions for:
  Monitoring the performance of control equipment such as ventilation
  Identifying deficiencies in design or operation
  Predicting and explaining trends as the operation proceeds
    Enables the planning of mitigatory measures in the longer term
    An essential part of the optimization process

## Slide 23
Overview of Monitoring
A comprehensive survey of gamma, dust and radon should be conducted during initial operation, in greater detail than during the pre-operational assessment
The frequency and scale of ongoing monitoring depends on the exposure levels and their variability, as determined in the initial and subsequent assessments
In facilities with a high potential for radon and/or dust, the RPO and ventilation officer should liaise closely in the execution of the monitoring programme
Undertaken by qualified person
The monitoring data should be used to predict individual exposures
The monitoring programme should be specified in the local operating instructions
Survey locations and monitoring results must be properly recorded

## Slide 24
Monitoring
Monitoring is required where NORM is:
  Produced Processed Handled
  Stored Transported Disposed
Three types of monitoring are generally recognized, requiring different levels of expertise:
  Task monitoring
  Routine monitoring
  Special monitoring

## Slide 25
Task Monitoring
Monitoring applies to a specific task.
It provides data to support the immediate decisions on the management of the task.
It may also support the optimization of protection.
Examples:
  Checking for contamination of clothing before leaving an area where NORM decontamination work is being carried out
  Monitoring the radon levels at the exit points of fluids and gases in an oil and gas production facility during maintenance
  Measuring gamma dose rates where high activity NORM may accumulate, including when equipment is opened for operational reasons
  Determining whether items meet clearance criteria prior to release

## Slide 26
Routine Monitoring
  Associated with continuing operations
  Intended to meet regulatory requirements
  Demonstrate that the working conditions, including the levels of individual dose, remain satisfactory.
Examples:
  Regular dust monitoring of production workers
  Monthly gamma survey of workplaces

## Slide 27
Special Monitoring
Investigative in nature
Where incomplete information is available
It is intended to provide detailed information
Examples
  During commissioning stage of new facilities,
  During decommissioning
  Following major modifications to facilities or procedures,
  When operations are being carried out under abnormal circumstances.

## Slide 28
Monitoring
Elements of the program will require monitoring of:
  Gamma
  Dust
    dust concentrations,
    particle size and
    potential for inhalation
  Radon and decay products
  Surface contamination
Monitoring depends on the work environment
(Refer to earlier lecture on monitoring for more detail)

## Slide 29
Monitoring of controls
Identify the key controls for radiation protection
Monitor that the controls are working
For example;
  Ventilation system performance
    Regular measurements should be made of the flow rates at the inlet and outlet of the auxiliary ventilation duct to demonstrate that leakages are under control
  Effectiveness of interlocks and access systems
    Checks if they are working
  Effectiveness of cleanup procedures
    Workplace inspections
  PPE is maintained and used correctly
    Correct use, wear and tear,
  Good housekeeping

## Slide 30
Monitoring of assessment of dose
Assessment of doses is required for :
  Optimization of protection
  Compliance with dose limits
  Individual dose records
Use individual or workplace monitoring, or a combination of both, as appropriate
Individual monitoring of a subset of workers may be appropriate for groups of workers with similar work patterns and moderate exposure levels

## Slide 31
Dose Assessment Monitoring
Monitor the exposure pathways;
  Gamma
  Dust
  Radon and decay products

## Slide 32
Education and training
The education and training programme should include topics specific to radiation protection in NORM industrial operations
Depending on the type of NORM facility, such topics might include:
  The properties and health effects associated with:
    Uranium, thorium, radium, etc.
    U, Th series radionuclides in dust
    Radon, thoron (where appropriate) and progeny
  Measurement of airborne activity (dust, radon)
  The functioning and purpose of the ventilation system, and its importance for radiation protection
  The purpose of and methods for controlling and suppressing airborne dust

## Slide 33
Worker’s health surveillance
Health surveillance programmes for workers in NORM industrial facilities need be no different in principle from those for general industrial activities involving exposure to radiation
Such programmes are:
  Based on the general principles of occupational health
  Designed to assess the initial and continuing fitness of workers for their intended tasks
The working and environmental conditions in many NORM facilities, especially mines, may be different from those in normal facilities involving radiation sources
In order to be familiar with such conditions, the occupational physician in charge of the health surveillance programme may need to periodically visit the workplaces concerned.
May not be required for all industries

## Slide 34
Audit and reviews
The RPP should be regularly audited and reviewed by persons who are technically competent to enhance the effectiveness and efficiency of the RPP
Audits and reviews should be performed using written procedures and check lists at appropriate intervals:
  When required by the regulatory body
  When considered necessary by management
  Following implementation of a new RPP or addition of significant new content
  Following significant reorganization/revision of the RPP
  To implement previously identified corrective actions

## Slide 35
Key Messages
The levels of detail should be commensurate with the risk (i.e.; a graded approach)
RPP should be established and maintained for NORM facilities
The content of an RPP is based on components outlined in GSR Part 3
Control measures should include; engineered, administrative controls and provide PPE necessary to ensure objective achieved

## Slide 36
Exercise
If you were thinking about a mine what might you think about for ventilation?
Ventilation systems are crucial in underground mines for the control of dust and/or radon
Design should be an integral part of mine planning/development
  Where possible, radon buildup should be minimized by:
    Not passing fresh air through mined-out areas
    Achieving a ‘one pass’ system
  Air velocities should not be so high as to resuspend dust
  Air intakes and exhausts should be well separated
  Primary ventilation should be operated continuously if possible
  Access of workers to any non-ventilated areas should be prevented unless specially authorized and adequately protected
  Fixed work stations in return airways should be avoided
    If this is not possible, provide operator booths with filtered air supply