## Slide 1: Radiation Measurements

## Slide 2
Content
Introduction
Why measure ?
Gamma radiation
Radionuclides in airborne dust
Radon (222Rn and 220Rn) and their progeny
Surface contamination
Quality control
Key messages

## Slide 3
Why monitor?
To identify existing levels
To confirm that the radiation controls are in place and effective
To identify elevated levels of radiation that require control
To confirm other measurements that may be occurring (eg; regulatory check)
For investigative purposes
For licence conditions
For dose assessment and epidemiology

## Slide 4
When to monitor?
As part of baseline characterisation
As part of routine or regular monitoring program
Randomly
When problems arise
As required by regulatory agency or when requested by workforce

## Slide 5
Occupational Monitoring
Monitor the exposure pathways
Workers
  Gamma radiation exposure
  Inhalation of radionuclides in dust
  Inhalation of decay products of radon and thoron
  Ingestion of radionuclides

## Slide 6
General types of monitoring
Personal
  Workers wear the monitor
  Portable and practicable
  May not be able to sample everyone
Workplace
  Surveys in area
  Where personal monitoring in not practical
  Fixed locations (identifying trends)
  May be used for sampling a workgroup or activity

## Slide 7
Gamma radiation
NORM material emit gamma radiation and require monitoring
Documented survey strategies are required
Portable instruments can be used for routine workplace monitoring for external gamma radiation exposure
Personal monitoring is carried out with active dosimeters (e.g. during maintenance activities) or passive dosimeters
Notes: Accumulations of materials containing radionuclides of the uranium and thorium decay chain can build up in underground and surface operations. The radionuclides of these decay chains include a wide variety of gamma emitters and emission energies. Strong gamma emitters include 226Ra and its short lived decay products (uranium decay chain) and 208Tl (thorium decay chain).
Gamma exposures are of particular importance where high grade uranium or thorium ores are mined or where there is a significant enhancement of radionuclide activity in the surface plants (e.g. scales, sediments and wastes).
Since beta doses are generally less significant than gamma doses, instruments that measure only the gamma dose rate will be adequate in most operations. Workplace gamma dose rates can be routinely measured with portable instruments and individual exposures can be assessed using a variety of active and passive dosimeters.
Significant beta exposures can occur in certain areas of rare earth extraction plants and uranium plants.
Fixed working stations should be located in areas of low gamma dose rate. In high grade uranium and thorium mines physical shielding may also be required.
A dose rate meter absorbs energy from penetrating radiation. A suitable and efficient instrument which is matched to the specific task should be capable of providing direct readings of the dose equivalent rate in microsieverts per hour (microSv/h or microSv·h–1). A smaller number of instruments indicate the absorbed dose rate in micrograys per hour (microGy·h–1). These usually respond only to X, gamma and/or beta radiations.
Instructions for the lecturer/trainer
Emphasize that the significance of the gamma exposures depends upon the mixture of gamma emitting radionuclides in the material, the activity concentration and the quantity of material present.
Gamma dose rates in the workplace can be measured with a variety of portable detectors e.g. ionization chambers, Geiger counters or scintillation detectors.
The frequency of measurements should be specified in the local operating instructions.
The frequency depends upon the historical results and the variability in dose rates;
Each working area should be surveyed, with particular attention paid to fixed working locations and to other areas where workers may remain for a large part of the day;
Details of the workplaces surveyed and the dose rates determined should be recorded.
Particular attention should be paid to areas containing materials (stockpiles of product and residues) with high activity concentrations.
Individual monitoring:
Individual dosimeters are required where the dose rates give rise to doses that represent a significant fraction of the dose limit. Dosimeter exchange periods of one to three months are typical.
In the mining environment, TLDs are preferable to photographic film dosimeters because they are more durable and less prone to damage.
Maintenance operations inside process equipment of certain operations can result in significant gamma exposures from radium scales. Small electronic dosimeters are used to assess full shift exposures in areas of high gamma dose rate. These devices provide an instantaneous readout of dose rates as well as the cumulative dose. They also incorporate dose alarms.
Instructions for the lecturer/trainer
Emphasize that the monitoring program should be related to the risk of exposure.

## Slide 8
Gamma radiation
Portable dose rate instruments:
  Used for workplace and environmental monitoring
  Dose rate can be displayed directly in μSv/h
  Instruments with sensitive probes are capable of measuring down to background levels (0.05–0.1 μSv/h)
Notes:     Ensure the calibration of the instrument and the units that it is reading
High sensitive meters are good for baseline surveys (ie; for measuring background levels)

## Slide 9
Gamma dose rate meters
The detector characteristics must be chosen such that the energy response matches the energy of the radionuclides to be measured
The detector must have a suitable response time to match the rate at which the dose rate varies
The detector must be calibrated for the gamma ray energies of interest
The detector must be sufficiently rugged for the environment in which it is to be used.
Some instruments can identify the radionuclides present

## Slide 10
Example of Instruments Energy Response
(From manufacturers documentation)

## Slide 11
Gamma dose rate meters
The instrument should be suitable for the application.
An incorrect choice can lead to inaccurate or even erroneous assessments of the external hazard.
Many different types
  Gas filled detectors
  Ionisation chambers
  Proportional counters
  Geiger-Müller counters
  Scintillation counters
  Solid state detectors
Notes: Before attempting to make a radiation measurement it is essential for the user to be completely familiar with the features and controls of the instrument.

## Slide 12
Gamma dose rate meters
Survey monitors may have different scales:
micro-Roentgens per hour (µR/hr)
  amount of ionisation in air
micro-Gray per hour (µGy/h)
  absorbed dose in air
micro-Sievert per hour (µSv/hr)
  equivalent dose
counts per second/minute
Notes: There are digital meters, they are also quite rugged and are preferable to analog ones due to the fact that the reading is typically an average over a certain period of time (usually 30 seconds) – instead of instantaneous reading from an analog monitor. Some of these types of monitors could also be coupled with a GPS receiver for the purposes of recording exact survey locations.
On the right – a portable gamma-spectrometer. This monitor is typically used in nuclear security applications, but can also detect natural radioisotopes in relatively significant concentrations

## Slide 13
Gamma dose rate meters –
Personal Monitoring
Used for direct measurement of a workers exposure
Integrates the dose rate over any period (for example, from 1 day up to 3 months)
Can be attached to the clothing of the exposed worker
Common types of dosimeter for exposure to NORM:
  Thermo-luminescent dosimeters (TLDs)
  Optically stimulated luminescent dosimeters (OSLDs)
Direct reading dosimeters for higher dose rates:
  Electronic dosimeters

## Slide 14
Gamma dose rate meters –
Personal Monitoring
14
14
14
Notes: Self-explanatory, with the note about the watch: whilst looking good may not be very accurate, particularly at low exposure levels.

## Slide 15
Radionuclides in airborne dust
Airborne contamination can occur wherever dry materials are handled or processed
Dust sampling involves taking a sample of air through a filter medium
The sample is then analyzed for radionuclides
Sampling needs to consider:
The occupancy time in the workplace
The mass concentration of dusts
The radionuclide activity concentration
The size distribution and inhalation potential (sampler characteristics)
Notes: Airborne contamination can occur wherever dry materials are handled. Dry process activities can result in the generation of radioactive aerosols. Ores and process materials can contain non-equilibrium mixtures of radionuclides of the uranium and thorium decay chains.
Radioactive aerosols are assessed using active sampling methods. Both workplace and personal monitoring may be required. The counting and analysis of the filter samples needs to be done with care, due to the variety of radionuclide mixtures that can be found in the ores, feed, waste and product materials.
Consideration of the need for monitoring of workers’ exposure to dust should take into account the working conditions, individual working patterns and tasks, the likely doses, and any action levels specified by the regulatory body. Airborne dust monitoring is the method generally used in mines and raw materials processing facilities, and should be performed regularly whenever there is a possibility of receiving significant doses from the inhalation of dust. In deciding on the frequency of this monitoring, the concentrations of radioactive dust, its size distribution and the potential for its inhalation should be taken into account. The monitoring programme for radioactive dust should be described in the local operating instructions. The exposure levels predicted from dust activity concentrations will be a key factor in deciding the nature and extent of any individual monitoring programme necessary. Intakes are calculated by integrating airborne dust concentrations over time and multiplying by the breathing rate (generally taken to be 1.2 m3/h) and occupancy time (in hours).
Airborne contamination meters are used to detect radioactive aerosols which may be present within the atmosphere. These may be dispersion aerosols (dusts), condensation aerosols (smoke) or liquid aerosols (mists). The instruments used normally draw potentially contaminated air at a constant rate through a filter. The instrument may then be capable of detecting the accumulated radioactive material on the filter or the filter may need to be assessed elsewhere.
Gas monitors contain a radiation detector and continuously sample the air directly to measure the presence of radioactive gases. The contaminant must be identified in order to determine the activity concentration in Becquerel's per cubic metre (Bq·m–3). Airborne contamination meters and gas monitors may be used to assess airborne contamination in the workplace. Personal air samplers (PAS) are used to monitor the often more significant hazard within the breathing zone of an individual worker. These instruments are often passive devices which do not provide immediate results. They only provide retrospective assessments of the working conditions but may also provide estimates of intakes. Instruments that are capable of detecting the radionuclide may be used as active devices to provide an alarm signal when the airborne radioactivity concentration reaches a pre-set value.
The aerodynamic diameter of an airborne particle is the diameter that a sphere of unit density would need to have in order to have the same terminal velocity when settling in air as the particle of interest.
Too much dust (high self absorption and loss of sample)
Unsure of composition of the dust (ore dust totally different from product dust – Tailings dust)
PAS not being worn or deliberately being placed in unrepresentative air
Area samplers not picking up the “real” dust
Time of use changed or incorrect
Loss or damage
Battery failure
 Note on the difference between personal monitoring data (work practices of a particular employee) and positional monitoring data (operational conditions in the working area)
Instructions for the lecturer/trainer
Emphasize that the extent of the dust monitoring program requires to be related to the dust potential, its variability and the projected exposure levels.

## Slide 16
Types of Dust Sampling
Workplace Sampling:
Locations where workers are working
The frequency of sampling will depend on the level of dust concentration and its variability
May have fixed location sampling (for identifying trends)
Personal sampling:
Allocation of sampler to a representative worker
Consider number of workers involved in a task
Consider tasks that contribute to exposure – dust generation during work, job rotation, work shifts, special exposures
Individual work practices
Location and time in the workplace.

## Slide 17
Sampling in practice –
Locational sampling
Good Location
Out of the way
Good height (breathing zone height)
Safe
Poor Location
In the way
Poor height
Unsafe – workplace hazard
Notes: Correct position is at breathing height, in work area
Incorrect is on floor

## Slide 18
Types of sampling equipment
Static air samplers:
Place at fixed locations
Can be high volume or low volumes sampler
Indicator of workplace conditions
Personal air sampling:
Provides measure of worker exposure
Should be small and practical
Notes: Average values of radionuclide concentrations in the workplace air can be measured using static air samplers, which collect radioactive materials from air flowing through the instrument at a prescribed flow rate for a known period of time. These flow rates should be carefully calibrated. A fixed position impactor should be positioned at around 1.5 m from the ground, at the site where occupational exposures may occur. The measured values of interest, however, apply only at the site of sampling, and may differ from that in the breathing zone of the worker by up to an order of magnitude. Moreover, static sampling data usually contain no information on chemical form or particle size, and may cover periods when the worker was not present. For these reasons, static air monitoring is commonly used only to provide information on workplace conditions or to assist in interpreting the results of individual monitoring, but, except for radon, is rarely used to estimate intakes. In setting up static sampling procedures, the sampling time should be determined in such a way as to avoid excessive saturation at any of the sampling stages.
Moreover, static sampling data usually contain no information on chemical form or particle size, and may cover periods when the worker was not present. For these reasons, static air monitoring is commonly used only to provide information on workplace conditions or to assist in interpreting the results of individual monitoring, but, except for radon, is rarely used to estimate intakes. In setting up static sampling procedures, the sampling time should be determined in such a way as to avoid excessive saturation at any of the sampling stages.
Area Monitoring
  Use medium volume air samplers (~30 L/min) to sample the air in a region representative of a work place
  Collect the dust on a filter paper (~50 mm)
  Measure the radionuclides by gross alpha (sometimes radiochemical analysis)
  Use a default ratio of radionuclides to determine the relative contributions of radionuclides
---------------------------------
Personal air sampling is a form of individual monitoring whereby samples of airborne activity in the breathing zone of the worker are collected using self‑powered equipment wom or carried by the worker. The sampler flow rates must be carefully calibrated particularly as intakes estimated by personal air sampling may result in assigned doses. Because activity concentrations can vary by an order of magnitude or more within short distances of the worker, particularly where the worker's own activities lead to resuspension of surface materials, personal air sampling can provide a much more reliable basis for estimating intake than static air monitoring. Moreover, personal air samplers (PASs) can be wom under some forms of protective equipment, and can thus be used to check on the adequacy of protective measures.
Some types of personal air samplers prevent particles of non‑respirable size from reaching the collection medium. In addition, personal cascade impactors provide information on determining particle size distributions. However, the determinations of chemical form and solubility characteristics require separate analyses. Personal air sampling data, together with reasonable assumptions on such factors as chemical form, particle size and breathing rates, are now commonly used to estimate intakes of radionuclides which are difficult to assess by other techniques. PASs are also useful for providing assurance at the end of a potential exposure period that unexpected intakes by inhalation are unlikely to have occurred. It should be noted, however, that this may not be reliable for high specific activity particles ('hot particles'), where the sample collected may not be representative of the activity inhaled.
Personal Air Sampling
  Small volume air samplers (2-5 L/min) worn on the person sampling air representative of the breathing air
  Small filter papers (15 – 37 mm)
  Measured by gross alpha
  Sometimes convert weight into activity but ONLY if a proven relationship Note on conversion: cannot be used for plants treating monazite in any form: monazite is softer than other heavy mineral sands and its concentration in the dust may be about 30 times higher than its content in the concentrate being treated

## Slide 19
Types of sampling equipment

## Slide 20
Equipment for analysis of dust samples
Notes: Self-explanatory:
Gross alpha counters (some can be used for beta counting as well)

## Slide 21
Sampling the right dust

## Slide 22
Filter holders (sampling cassettes)
Notes: Transparent cassettes: for 37 mm filters, appropriate calibration source should be available
Second right – cyclone for 25 mm filters (cuts off dust sizes >5 micron and is typically unsuitable in occupational environments where dust particle size is unknown)
Right top – SKC 7-hole cassette, OK for most situations
Bottom left – IOM open-face, OK – but filter is weighted together with the cassette (due to the dust adhering to the insides of the cassette more than in the case of the 7-hole one). Sometimes material from inside of the cassette will need to be washed out and combined with the material on the filter for subsequent analysis (too complex and expensive)
Bottom right – calibration sources. A standard 25mm diameter source is generally suitable for the active area of 21 mm in diameter (7-hole), may not be appropriate for the 18mm active area (IOM open face). “Point” calibration sources should be avoided.

## Slide 23
Radionuclides in airborne dust
DUST
Notes: A general summary of the process of the monitoring of airborne dusts: sampling  weighting  gross alpha counting  data processing

## Slide 24
Exercise: Where would you monitor dust?
Notes: If you see dust then it is too dusty already!!!
However, monitoring should be done on the truck driver – also any other workers

## Slide 25
Sampling equipment
Notes: On the left – high-volume (70 m3/hour) dust sampler, typically lugged in into a power point. Where the power not available a diesel generator is typically used.
Right: another form of dust measuring – dust deposition – dust falls into jar, which can be analysed at a later stage

## Slide 26
Radon and Thoron
Radon is a gas – and it is chemically inert
  If it is inhaled it does not accumulate in the lung
  Resulting dose is quite small
  Exposure occurs from the decay products present in the air
Radon and thoron and transport mechanisms for the decay products
Consider other factors such as;
  Equilibrium factor
  Unattached fraction
  Particle size
(Note that there is a more detailed lecture later)

## Slide 27
Workplace radon progeny concentrations are variable

## Slide 28
Concentrations by Time (uJ/m3)
Notes: Grab sampling might give these results

## Slide 29
Concentrations by Time (uJ/m3)
Notes: But, this is what is happening in real time

## Slide 30
Radon and Thoron Monitoring
Passive monitoring
  Track etch
  Inexpensive and easy to use
  Can be used for personal, locational or environmental
  Gives an average for the exposure period
Active monitoring
  Air sampling (“radon sniffers”)
  Sensitive equipment usually
  Needs to be calibrated (radon chamber)
  Can give either exposure averages or real time readings

## Slide 31
Decay Progeny Monitoring
Grab sampling
  Various techniques
    Take air sample and alpha count
    Rolle, Borak, Kusnetz, environmental Rolle
Active monitoring
  Monitors that measure in real time
  Can be expensive, require calibration
  Able to differentiate between decay products
  Advantage is that monitoring identifies concentration variations

## Slide 32
Equipment

## Slide 33
Measurement of radon
Radon monitoring in an underground mine using a portable continuous radon monitor with pulse-counting ionization chamber detector

## Slide 34
Surface contamination
Identify areas of removeable and non removeable contamination
Monitor the actual surface contamination or take a wipe test for later analysis
Wipe tests can be analysed for different radionuclides
Also used to ensure that plant and equipment is free from contamination

## Slide 35
Measurement of surface contamination
Alpha monitors may unsuitable for NORM contaminated items, especially when the surface is rough and/or non-flat:
  Limited penetrating ability of alpha particles
  Probe must be held within 5 mm of the contaminant layer
  Self-absorption within the contaminant layer
  The surface of the alpha probe is easily damaged
Beta monitors are generally more suitable for NORM, but self-absorption must still be taken into account
Most beta detectors are sensitive to gamma radiation — care is needed to ensure that ambient gamma is not misinterpreted as contamination
The radiological characteristics of the NORM contaminating layer may have to be established in advance

## Slide 36
Measurement of surface contamination
Two examples of a surface contamination monitor

## Slide 37
Measurement of surface contamination
Contamination monitor with beta probe and alpha–beta dual probe

## Slide 38
Instrument calibration and maintenance
For all measurement methods, instruments must be calibrated regularly and traceable to recognized national standards:
Equipment should be maintained in good working order
Not only radiation instruments – also applies to pumps, mass balances.

## Slide 39
Practical guide for radiation measurement
Identify what measurements are to be taken
Identify what instrument to use
Pre-use check of any instruments.
Ensure calibration
Are there any special considerations – such as access permits ?
Make sure you are aware of any hazards or risks
Check that personal protective equipment (PPE) is required
Stow instruments and equipment securely and safely.

## Slide 40
Practical guide for radiation measurement
Make sure you know how to use the instrument
Check that it is calibrated
Conduct regular instrument checks and minor maintenance (e.g. battery changes) as required.
Look and then take measurements at correct locations and times.
Have some idea of what you are measuring
Take a couple of measurements to ensure reliable data.
If the results don't seem right, stop and work out why.
Record data with the required precision, accuracy and units.
Make notes of site conditions that might affect the data

## Slide 41
Practical guide for radiation measurement
Record results in accordance with procedures
Check that recorded outcomes are consistent with expectations.
Compare results with relevant radiation limits and identify and record any significant differences.
Identify any issues as a result of the monitoring
Identify any improvements that could be made.
Maintain records that are complete, accurate, legible and secure.

## Slide 42
Key Messages
Many aspects to monitoring
Different consideration for workplace and personal monitoring
Different considerations for the different types of radiation
Need to understand what you want to measure
Need to understand what the instrument is measuring
Instruments must be fit for purpose
Many equipment options
Only use calibrated and maintained equipment