## Slide 1: Management of Bulk NORM Residues and Waste (Part 1)

## Slide 2
Content
NORM Residue/Waste - Definition
Types of NORM residue or waste
Management of NORM waste
Key messages

## Slide 3
Definitions
NORM residue
  Material that remains from a process and comprises or is contaminated by NORM
  NORM residue may or may not be a NORM waste
    It may be recycled back to the process or used as a by-product
NORM waste
  NORM for which no further use is foreseen

## Slide 4
Managing NORM residues and waste
IAEA Fundamental Safety Principle 7:
Protection of present & future generations
People and the environment, present and future, must be protected against radiation risks
Radioactive waste must be managed in such a way as to avoid imposing an undue burden on future generations; that is, the generations that produce the waste have to seek and apply safe, practicable and environmentally acceptable solutions for its long term management.

## Slide 5
Types of NORM residue
NORM residues take various forms:
  Solids (or solid–liquid mixtures)
    Bulk residues
    Scale
    Sediments and sludges
    Slag
    Furnace dust
  Liquid residues
  Gaseous residues

## Slide 6
Bulk NORM residues
Process / residue | Radionuclide | Activity concentration (Bq/g)
Uranium mining — tailings | 230Th, 226Ra | <10 to several 100
Uranium mining — waste rock | 238U | 0.1 – 20
Copper mining — waste rock | 238U | 0.1 – 2
Dry separation of mineral sand— tailings | 232Th | 1 – 20
Bauxite processing — red mud | 232Th | 0.1 – 3
Beneficiation of phosphate rock — tailings | 238U | 0.01 – 2
Phosphoric acid production — phosphogypsum | 226Ra | 0.01 – 3
Titanium dioxide production – filter cake | 232Th/238U | ~1
Notes: There are specific requirements for uranium mining.
Mainly presented here as expamles

## Slide 7
Bulk NORM residues
Uranium tailings:
  Concentrations of 230Th, 226Ra and their decay progeny remain high for about 105 years
    The only opportunity for recycling is the future extraction of residual uranium and other minerals
    Viability depends on extraction technology and market prices for uranium and other minerals
The very high volumes limit the options for storage/disposal:
  Above-ground engineered containments (tailings dams)
  Backfilling of mining voids
    Underground
    Open pits

## Slide 8
Bulk NORM residues
For tailings dams, comprehensive engineering control measures must be applied to ensure structural integrity
Prevention of migration of hazardous constituents (including radionuclides) into the surrounding environment needs to be considered

## Slide 9
Example: Tailings dam

## Slide 10
Disposal considerations
Control of hazards from tailings dams should rely as much as possible on passive control measures and the use of natural materials as barriers
Measures need to be taken for radiation protection of workers and radiological monitoring of the surrounding environment (groundwater, surface water, air, soil, biota etc.)
After closure of a tailings dam facility, ongoing institutional controls are likely to be required to restrict access and unauthorized use
  The need for and extent of institutional control should be minimized by good siting, design etc.

## Slide 11
Waste rock
Usually generated in very large quantities
May have a significant radionuclide content
Has to be stored/disposed of in surface or near-surface containments (waste rock piles, backfilling into open pits).
Not necessarily waste:
  The mineral content might be worth recovering in the future
  Can be used as a construction material
  Safety assessment is required

## Slide 12
Waste rock

## Slide 13
Waste/residues from mineral sands operations
May have a significant thorium content
Management options:
  Dispose of in earthen trenches with soil topping
  Backfill into the mining void and cover with non-radioactive sand or overburden
  In dredge mining operations, it may be returned to the dredge pond and recycled along with fresh feed to the plant
  If the monazite component of the tailings is not recovered, blend with residual (non-radioactive) sand and backfill into the mining pit

## Slide 14
Bauxite residue (red mud)
Red mud is the residue generated by the digestion of bauxite in sodium hydroxide, as the first step in the production of aluminium
It is disposed of as a slurry (10–30% solids) in engineered containments with adequate linings or dry disposal on land after dewatering
The radioactivity content is low, and only one of several constituents posing a potential risk to the environment
Notes:   It has many potential uses, not yet widely exploited: Recovery of metals such as iron and titanium Incorporation into construction materials, Catalysts, Ceramics
Red mud disposal as slurry or dry land fill.

## Slide 15
Phosphate rock tailings
Low levels of uranium
Pumped as a slurry back to the mining void
Environmental protection considerations
Radiological considerations are minor due to low activity concentration
Phosphate rock tailings returned to the mined-out area

## Slide 16
Phosphogypsum
Generated in large quantities (160 million t per year) during the production of phosphoric acid from phosphate rock
226Ra concentrations are moderately elevated
A variety of uses:
  Agricultural soil amendment
  Construction materials — buildings, roads
  Cover and liner material for conventional landfill disposal facilities
  No significant radiological implications except possibly in buildings
Stored in large engineered containments (‘stacks’)
  Wet deposition (slurry) or dry deposition
  Safety and environmental issues are similar to those for mine tailings
  Radiological issues are insignificant—structural integrity, heavy metals and acidity are the main concerns
Production far exceeds demand
  Many phosphogypsum stacks are likely to become final disposal sites

## Slide 17
Phosphogypsum stack

## Slide 18
Titanium Dioxide
Titanium dioxide pigment is made by reacting titanium ores with either chlorine gas or sulphuric acid
Pigment contains very little NORM with almost all activity in solid waste and liquid effluent
Activity concentrations in solid waste and effluent vary depending on ore used but typically are around 1 Bq/g and 1 Bq/l (both 232Th and 238U decay series)
Solid wastes used for construction materials or disposed to landfill
Notes: Titanium oxide pigment is produced from the ores rutile (TiO2) and ilmenite (TiO2·FeO). The traditional sulphate production process is being phased out in favour of the cleaner chloride process, but it is unlikely to be phased out completely as it is the only way to produce anastase. The average activity concentration in the rutile is set at 400 and 600 Bq kg-1 for the 238U chain and 232Th chain nuclides respectively. However, it is important to emphasis the potential variability of concentrations in such minerals.
The highly purified TiO2 pigment, virtually 100% of the rutile input, is practically completely free of the natural radionuclides contained in the ore. Emissions to the air, apart from the radon in the ore, are negligible. Consequently, all radioactivity from the ore appears in the liquid effluent and solid wastes.
Solid wastes arise as blowover of cokes and ore from the reactor and as precipitate from the treatment of acidic solutions of chlorides separated from TiCl4 in the condensation steps. This acidic solution of chlorides contains virtually the entire radioactivity contained in the ore. The partitioning of the radionuclides between solid waste and discharged wastewater depends on the treatment of the acidic liquid waste stream. This treatment involves the precipitation of the cations as hydroxides by increasing the pH. Radionuclides of the elements radium and lead tend to remain in solution if the pH endpoint is not high enough.

## Slide 19
Titanium Dioxide
Notes: 2 landfill sites accepting titanium dioxide waste

## Slide 20
Minimize NORM waste
Recycling of NORM residues, or their use in other applications (rather than disposing of them as waste) should be the first consideration: NORM residues should be regarded as a resource rather than as waste.
Examples may include:
  Recycling of contaminated waters in the process
  Salvage and recycling of reagents (e.g. resins, solvents)
  Agricultural use, e.g. phosphogypsum
  Building materials, e.g. fly ash, phosphogypsum, red mud
  Road construction, e.g. slag, phosphogypsum, fly ash
  Recycling of contaminated scrap

## Slide 21
Key messages
Very large quantities
Low activity concentrations
Can be regarded as a potential resource
Appropriate protection is achievable through different management options