## Slide 1: Exposure to Radon

## Slide 2
Content
Radon/thoron
Exposure of the lung
Application of the Standards to radon in workplaces
Special quantities for concentration and exposure
Measurements
Equipment and monitoring for radon
Radon concentrations
Calculation of dose
Thoron
Key messages

## Slide 3
Radon
Radon (222Rn)
  inert gas
  naturally radioactive
  Part of 238U decay series
  226Ra as its immediate parent
  Half-life 3.8 days
  Short-lived decay progeny: 218Po, 214Pb, 214Bi, 214Po
  Main exposure pathway — Escape of 222Rn to the air and subsequent inhalation
  Secondary exposure pathway — Dissolution of 222Rn in groundwater and subsequent ingestion (or inhalation on release from water into the air)
Notes: Radon is an inert gas that is naturally radioactive. Its most common isotope, 222Rn, is one of the decay progeny of 238U and is produced by the decay of 226Ra. The radioactive decay of 222Rn with a half-life of 3.8235 d generates decay progeny that also have short half-lives: 218Po, 214Pb, 214Bi and 214Po.
The natural presence of uranium in normal rocks and soil results in the production of 222Rn, some of which escapes to the air and some of which dissolves in groundwater. Exposure of individuals to 222Rn and its decay progeny occurs mainly by breathing air, resulting in a dose to the lung and an increased risk of lung cancer. Exposure from ingestion via the groundwater pathway is generally small in comparison.

## Slide 4
Decay chain of Rn-222
222Rn
Radon gas
3.8 d
Polonium
218Po
3 min
Lead
214Pb
27 min
Bismuth
214Bi
20 min
160 s
214Po
210Pb
22 y


Half-life

## Slide 5
Thoron
220Rn (thoron)
  Part of 232Th decay series
  224Ra as its immediate parent
  Gaseous form
  Short half-life ~56 seconds
  Rapidly decays into thoron progeny
  Progeny have a half-life of up to 10.66 hours
  Exposures from progenies 212Pb and 212Bi
  Inhalation exposure is the main concern particularly in thorium processing facilities
  Only transported over short distances
  In the absence of thoron gas the progeny concentrations decline slowly
Notes: 222Rn is not the only isotope of radon. The isotopes 220Rn (commonly referred to as thoron) and 219Rn are decay progeny of 232Th and 235U, respectively. Exposures to these isotopes and their progeny are generally small enough to be of no concern, although there are circumstances where exposure to 220Rn and its progeny may need to be considered in particular where monazite or thorium is processed.

## Slide 6
Exposure of the lung
Contribution of 222Rn itself to the lung dose is very small
  Most of the inhaled gas is breathed out again
Short-lived progeny are responsible for about 99% of the dose:
  Atoms attach to condensation nuclei and dust particles in the air that is inhaled
  Unattached progeny also inhaled
  Deposited along the various airways in the bronchial tree
  Most exposure comes from alpha particles
  Contributions from beta and gamma emissions are small in comparison
Notes: Only about 1% of the dose to the lung arises from 222Rn itself because most of the inhaled gas is breathed out again. The dose arises almost entirely from the short-lived decay progeny, atoms of which attach themselves to condensation nuclei and dust particles present in the air. These particles, as well as unattached particles, become deposited along the various airways of the bronchial tree. Exposure of the lung is caused mainly by the alpha particles emitted by the short-lived progeny radionuclides, even though there are also some emissions of beta particles and gamma radiation.

## Slide 7
Formation of radon progeny aerosol
Ventilation
Radon gas
Radon gas
Radon progeny
Aerosol particle
deposition
deposition

## Slide 8
Respiratory tract

## Slide 9
Application of the Standards to 222Rn in workplaces
Workplaces where exposure to other U, Th series radionuclides already needs to be controlled as a planned exposure situation:
  Exposure to 222Rn is subject to the requirements for planned exposure situations, regardless of the radon concentration
  Regulatory control must be considered
  Any necessary control measures for 222Rn must be included in the RPP

## Slide 10
Application of the Standards to 222Rn in workplaces
Workplaces where exposure to other U, Th series radionuclides does not need to be controlled:
  Above-ground workplaces:
    High 222Rn levels can usually be reduced to well below the reference level by remedial action:
    Regulatory control as a planned exposure situation is therefore unlikely to be needed
  Underground workplaces
    222Rn may be more difficult to control by remedial action:
      High 222Rn ingress via rock surfaces or water, limitations on ventilation
    Regulatory control as a planned exposure situation is necessary if the 222Rn concentration remains above the reference level
Notes:     High 222Rn levels can usually be reduced to well below the reference level by remedial action:
      Improved ventilation of the working area
  Remedial action on the building — sub-floor depressurization/ventilationUnderground workplaces
    e.g. mining of non-radioactive ore, tunnels, tourist caves, spas, water treatment facilities:
    222Rn may be more difficult to control by remedial action:
      High 222Rn ingress via rock surfaces or water
      Practical limitations on ventilation
    Regulatory control as a planned exposure situation is necessary if the 222Rn concentration remains above the reference level
    Control measures must be included in the RPP

## Slide 11
Special quantities for concentration and exposure
Short-lived 222Rn progeny are unlikely to be in equilibrium with the parent
Therefore, for radiation protection purposes, special quantities are needed for 222Rn progeny:
  Concentration in air
  The resulting exposure
These special quantities are derived from a quantity known as the ‘potential alpha energy’
Notes: The progeny of 222Rn are unlikely to be in equilibrium with the parent radionuclide. For purposes of radiation protection, special quantities are needed to characterize the concentration of 222Rn progeny in air and the resulting inhalation exposure. These special quantities are derived from the ‘potential alpha energy’, since most of the dose from 222Rn progeny comes from alpha particles in the lung

## Slide 12
Potential alpha energy
The potential alpha energy εp of a single atom of a short-lived 222Rn progeny radionuclide is the total alpha energy emitted by that atom during its progressive radioactive decay down to, but not including, the relatively long-lived radionuclide 210Pb
Notes: The key quantity is the ‘potential alpha energy’. The potential alpha energy, εp, of a single atom of a short-lived 222Rn progeny radionuclide is the total alpha energy emitted by that atom during its progressive radioactive decay down to, but not including, the relatively long-lived radionuclide 210Pb.

## Slide 13
Potential alpha energy concentration
Potential alpha energy concentration (PAEC) in air:
For any mixture of short-lived 222Rn progeny in air, the contribution of each radionuclide to the PAEC is its potential alpha energy per unit activity (εp/λ) given in the previous.
Table multiplied by its activity concentration, c. The total PAEC is then the sum of these individual contributions
Notes: When considering exposure situations involving 222Rn progeny, it is usual to express the total potential alpha energy as an energy concentration in air (in units of J/m3). This is referred to as the ‘potential alpha energy concentration’ (PAEC). For any mixture of short-lived 222Rn progeny in air, the contribution of each radionuclide to the PAEC is its potential alpha energy per unit activity (εp/λ) given in the previous Table multiplied by its activity concentration, c. The total PAEC is then the sum of these individual contributions

## Slide 14
Equilibrium factor
In practice, the progeny will rarely be in equilibrium
The PAEC will therefore be some fraction of 5.56 × 10–9 J/m3.
This fraction is called the equilibrium factor (F)
For a 222Rn concentration of 1 Bq/m3, the PAEC of any given non-equilibrium mixture will be:
Notes: In practice, the progeny will rarely, if ever, be in equilibrium, and the PAEC will therefore be some fraction of this value. This fraction is called the equilibrium factor, F. The equation shown here gives the PAEC for a 222Rn concentration of 1 Bq/m3

## Slide 15
Equilibrium factor
The equilibrium factor can vary from:
  Zero (radon gas diffusing out of the grain surface of the mineral)
to
  1 (radon gas after three hours in stagnant air)
An equilibrium factor of 0.4 is usually taken as a default value
The older the air the higher the progeny concentrations

## Slide 16
Equilibrium factor, F
F=1
Nuclide Bq m-3
222Rn gas 1.0
218Po 1.0
214Pb 1.0
214Bi 1.0
F=0.4
Nuclide Bq m-3
222Rn gas 1.0
218Po 0.7
214Pb 0.4
214Bi 0.3
The value of F depends on the ventilation rate :
Indoors : F  0.4 Natural ventilation
Mines : F  0.2 Forced ventilation
F is a measure of the degree of dis-equilibrium between radon gas and its progeny

## Slide 17
Potential alpha energy concentration Exposure
Multiply PAEC (J/m3) by occupancy (h) to give exposure in units of J·h·m–3
The PAEC will vary with time, so the exposure has to be calculated as an integral over time (which in practice is the average concentration):
Exposure usually determined over 1 year
A default annual occupancy time of 2000 h may be assumed for workplaces (often conservative)
Notes: The exposure of an individual to 222Rn progeny is determined by multiplying the PAEC (in J/m3) by the exposure period (in h). The exposure is therefore expressed in units of J·h·m–3. Since the PAEC will generally vary during the exposure period, the exposure has to be calculated as an integral over time, as shown by the equation here.
The exposure period is usually calculated over the course of one year. The individual will generally be exposed for only a percentage of the total time. If this percentage is unknown, it is common to adopt default values of 80% (7000 h/a) for homes and 23% (2000 h/a) for workplaces. It should be borne in mind that the adoption of these default values may lead to a conservative estimate of the annual exposure.

## Slide 18
Equilibrium equivalent concentration
Equilibrium equivalent concentration (EEC) is an alternative to using PAEC
EEC is the concentration of 222Rn in equilibrium with its progeny that would give the same PAEC as the actual non-equilibrium mixture
The EEC is related to the PAEC by a constant factor:
Notes: There is an alternative way of referring to the concentration of 222Rn progeny in air. If the 222Rn gas concentration (in Bq/m3) is multiplied by the equilibrium factor F, the resulting quantity is called the ‘equilibrium equivalent concentration’ (EEC) of the 222Rn parent (expressed also in units of Bq/m3). The EEC can be regarded as the concentration of 222Rn in equilibrium with its progeny that would give the same potential alpha energy concentration as the actual non-equilibrium mixture. The equation gives the numerical relationship between the PAEC and the EEC.

## Slide 19
Historical unit of exposure (for awareness)
Exposure is sometimes expressed in historical units of ‘working level month’ (WLM)
Commonly used in uranium mines
The use of this unit is discouraged
1 WLM = 0.00354 J·h·m–3
Notes: There is an alternative way of referring to the concentration of 222Rn progeny in air. If the 222Rn gas concentration (in Bq/m3) is multiplied by the equilibrium factor F, the resulting quantity is called the ‘equilibrium equivalent concentration’ (EEC) of the 222Rn parent (expressed also in units of Bq/m3). The EEC can be regarded as the concentration of 222Rn in equilibrium with its progeny that would give the same potential alpha energy concentration as the actual non-equilibrium mixture. The equation gives the numerical relationship between the PAEC and the EEC.

## Slide 20
222Rn gas concentration as a surrogate for 222Rn progeny concentration
Measurement of 222Rn gas concentration is simpler
  e.g. measurements in buildings over extended periods
Passive radon track-etch devices are small, simple, robust, inexpensive
An equilibrium factor has to be assumed
An assumed value of 0.4 is usually adequate for buildings, but can be significantly different in underground mines
Usual approach in buildings
It is also acceptable in many underground workplaces
Notes: In many situations involving exposure to 222Rn progeny, the measurement process can be simplified considerably by using the 222Rn gas concentration in air (in units of Bq/m3) as a surrogate for potential alpha energy. For instance, measurements in a large number of buildings over an extended time period are best made using passive track-etch devices that detect 222Rn. Such devices are small, simple, robust and inexpensive. When adopting this approach, an appropriate value for the equilibrium factor, F, has to be assumed. The use of a default value of 0.4 is usually adequate for this purpose. It has been found that most values of F in indoor air are within 30% of this value.

## Slide 21
Measurement
A wide variety of measurement methods are available
Either the gas or the progeny can be measured
Rapid temporal variations can occur
Integrated (long term measurements) are preferred due to the variability in the gas and progeny concentrations
Equipment calibration is important
Notes: Lecture notes
A wide variety of gas and progeny measurement methods is available. Since the gas and progeny concentrations can fluctuate significantly over time, integrated long term measurements are the preferred method of monitoring.
Radon measurements may be used to estimate progeny exposures if an equilibrium factor (F) is assumed. Alternatively, for control purposes, measurements of radon combined with measurements of radon progeny may be useful in determining equilibrium factors and deriving information on the age of the air at particular locations for control purposes e.g. to detect the leakage of radon from worked out areas.

## Slide 22
Notes: Y axis is log

## Slide 23
Variations

## Slide 24
Radon gas passive monitor
Some alpha particles emitted by radon and daughters strike detector
CR-39 detector
Radon gas diffuses in

## Slide 25
Workplace monitoring – radon gas
Grab sampling: Lucas cells
Grab sampling: pulse ionization chambers
Grab sampling: two filter method
Integrated measurements using nuclear track detectors (radon cup)
Continuous monitoring

## Slide 26
Types of radon detectors

## Slide 27
Workplace monitoring – radon progeny
Air is drawn through a filter
The particulate progeny are collected
The gross alpha (and/or beta) decay is measured
or
Alpha spectrometry can be used to measure each radon progeny
Notes: Lecture notes
Workplace monitoring of radon progeny concentrations generally involves active air sampling in which a known volume of air is drawn through a filter. Alpha and/or beta activity on the filter is counted during and/or after sampling. Some methods determine gross activities, while others determine the individual radon progeny concentrations. For gross alpha counting, the detection is often done simply with a scintillator disc mounted on a photomultiplier tube and placed a short distance from the filter at atmospheric pressure. Alpha spectroscopy can be used to determine the activity of individual radon progeny.
The sample durations can vary from 5 minutes (grab samples) up to several days depending on the method and type of instrument.
Instructions for the lecturer/trainer
Stress the importance of selecting the optimal method. Continuous measurements (i.e. full shift) are preferred.

## Slide 28
Sampling strategies
Sampling strategies require to be statistically based – random/ extensive screening
Usually assessed by grab sampling (10–30 minutes)
Requires a documented monitoring programme
The monitoring frequency depends upon:
  The level of concentration
  The variability of concentration
Notes: Lecture notes
Workplace monitoring is also used to verify the proper operation and efficiency of the ventilation control system.
Workplace monitoring for engineering control of concentrations of radon and radon progeny should be undertaken at the intervals stated in the local operating instructions. In setting the frequency of measurements, historical results, expected variations in measurements and the degree of hazard should be taken into account.

## Slide 29
Sampling strategies
The sampling frequency is increased when:
measured concentrations exceed the usual range
major changes are made to the ventilation system
reference levels are exceeded
the effectiveness of corrective actions is to be assessed
ingress of radon into the working area is suspected

## Slide 30
Individual passive radon monitoring
Radon gas
Personal radon monitors are usually passive devices
Passive monitors rely on radon diffusion into the detector
Track-etch detectors are solid state devices, i.e. plastic
Radon decays through alpha decay
The alpha particle marks the detector
Passive detectors are integrating devices
Their exposure periods can range up to three months
Notes: Lecture notes
Personal radon gas monitors (RGMs) are worn by the individual in the workplace for an extended period (e.g. one month). Personal RGMs are usually passive devices. Passive dosimeters rely on the natural diffusion of radon gas through a filter (to remove radon progeny) into the sensitive volume of the detector. Passive individual dosimeters usually use solid-state (a small piece of alpha-sensitive plastic) nuclear track detectors that are exposed for a specified period and then analysed by a chemical and/or electrochemical etching process. The number of tracks formed on the foil can be counted to assess the integrated exposure level. The integrated exposure to radon gas in Bq·m-3 h is proportional to the number of tracks.
Passive devices are simple to use and inexpensive and are suitable for the large scale (e.g. hundreds to thousands) monitoring of workers in underground workplaces.
Microprocessor-controlled passive radon monitors are now available. These devices can operate on batteries for up to 10 days or more.
Instructions for the lecturer/trainer
Emphasize that passive monitors are used over longer integrating periods (1–3 months). Active monitors are short term integrating devices (i.e. full shift up to 10 days). Information on electronic passive devices is given on the websites listed in the reference section.

## Slide 31
Individual active radon progeny monitoring
Radon progeny
Active monitors use pumps and filters
Known volumes of air are sampled
Short term integrating devices, e.g. full shift
Collects the particulate radon progeny
Types of detector:
Solid state silicon detectors
Track etch
Notes: Lecture notes
Active dosimeters collect airborne radioactive contaminants from a known volume of air drawn through a filter by a battery-powered pump.
The alpha particles emitted by the radon progeny deposited on the filter can be detected by a variety of detectors (e.g. thermoluminescent dosimeter, a silicon solid state surface barrier (SSSB) detector with its associated electronics, or a nuclear track foil.
Devices incorporating nuclear track films and SSSBs have the capability of measuring individual radon progeny rather than just the gross alpha activity produced by the progeny.
Active radon progeny personal dosimeters are used over short term periods.
Instructions for the lecturer/trainer
Emphasize that active radon progeny monitors are short term integrating devices (i.e. full shift up to 50 hours). Information on these devices is given in the web sites listed in the Reference section.

## Slide 32
Radon in buildings
Ingress mainly from underlying soil through cracks in floor:
  Indoor air pressure usually lower than outside
    Indoor air is warmer — convective flow
    Wind blowing over chimneys and other openings
  Other factors affecting ingress through floor:
    Relative humidity
    Soil moisture
    etc.
Notes: The accumulation of 222Rn in the air inside buildings occurs mainly as a result of the entry of 222Rn directly from the underlying soil through cracks in the floor. In temperate zones, the air inside buildings is normally at a slightly lower pressure than the air outdoors as a consequence of the air inside the building being warmer than the air outside. This causes a convective flow which, together with the effect of the wind blowing over chimneys and other openings, draws soil gas and hence 222Rn into the building. In addition to pressure differences, other factors, including relative humidity and soil moisture, can also influence 222Rn levels in buildings.

## Slide 33
Radon in buildings (2)
Other (usually less prominent) forms of ingress:
  Emission from building materials:
    Type of material
    Porosity
    226Ra concentrations
  Emission from water supply:
    222Rn concentration in water usually low
    May be higher if originating from groundwater
  Minerals and raw materials in workplaces, depending on:
    226Ra concentrations, surface area (particle size), porosity, radon emanation coefficient
Notes: The accumulation of 222Rn in buildings also occurs, usually to a lesser extent, through the escape of 222Rn from building materials into the air inside the building, particularly if such materials are porous and have elevated concentrations of 226Ra. The water supply can also provide a route for the entry of 222Rn into the air inside buildings, although 222Rn levels in domestic water are generally quite low, except possibly when the supply comes from groundwater. If the building is a workplace, the accumulation of 222Rn in the air may also be influenced by the presence of minerals and raw materials containing elevated concentrations of radionuclides in the 238U decay series.

## Slide 34
Radon in buildings (3)
Indoor concentrations:
  Variation between countries:
    Geology
    Climate
    Construction techniques
    Domestic habits
    National mean values: 7–200 Bq/m3
    Population weighted worldwide mean: 39 Bq/m3
  Variation within individual countries
    High background areas: 112 – 2745 Bq/m3
    Up to 84 000 Bq/m3 in some parts of northern Europe
Notes: Indoor 222Rn concentrations differ between countries because of differences in geology, climate, construction materials, construction techniques and domestic habits. Within individual countries, there may be marked regional variations. Data on indoor 222Rn concentrations around the world are given in Annex E of the 2006 UNSCEAR report. The arithmetic mean values for various countries vary from 7 to 200 Bq/m3. Arithmetic mean values in high background areas vary from 112 to 2745 Bq/m3. In some parts of northern Europe, maximum values of up to 84000 Bq/m3 have been reported. The population weighted worldwide arithmetic mean is 39 Bq/m3.

## Slide 35
Mitigation - buildings
Radon Sump
Underfloor Ventilation
Roof Fan

## Slide 36
Radon in underground workplaces
Examples:
  Tunnels
  Basement storage & parking facilities
  Underground water treatment plants
  Caves and former mines open to the public
  Spas
  Underground mines
Causes of high concentrations:
  Large areas of interface with the ground
  Practical limitations on ventilation
  Ingress of water laden with 222Rn
  High 226Ra concentrations in the ground (certain mines)
Notes: As one would expect, the highest concentrations of 222Rn tend to occur in underground workplaces. Such workplaces include tunnels, basement storage and parking facilities, underground facilities for water treatment and distribution, caves and former mines open to the public, spas and, of course, underground mines. In such workplaces, there are many surfaces via which there may be substantial entry of 222Rn into the air and there may be practical limitations on the amount of ventilation that can be provided. In some underground mines, including some in which the 226Ra concentrations in the host rock are not significantly elevated, high concentrations of 222Rn and its progeny arise from 222Rn that enters the workings via the groundwater and is subsequently released into the mine atmosphere. A similar situation may be encountered in underground facilities for water treatment and distribution.

## Slide 37
Radon in underground workplaces
Concentrations:
  Caves and mines open to the public: 20 to >20 000 Bq/m3
  Workplaces in tunnels: 200 to 7000 Bq/m3
  Even higher values possible in underground mines
    Particularly uranium mines
Notes: Concentrations of 222Rn are reported to vary from 20 to more than 20 000 Bq/m3 in workplaces in caves and underground mines open to the public and from about 200 to 7000 Bq/m3 in workplaces in tunnels (see IAEA Safety Reports Series No. 33). Much higher values have been found in some operating underground mines, particularly uranium mines.

## Slide 38
Calculation of dose
Reference levels are expressed in terms of 222Rn concentrations rather than dose
Conversion to dose is however necessary when exposure to 222Rn progeny is treated as a planned exposure situation
  UNSCEAR recommend a dose factor of 9 nSv per Bq·h·m–3
  1.6 Sv per J·h·m–3 potential alpha energy exposure
Dose due to 222Rn progeny has to be added to doses from external gamma and inhaled or ingested dust
Notes: The control of exposure to 222Rn progeny in existing exposure situations does not normally require the calculation of effective dose. Reference levels for 222Rn progeny exposure are expressed in terms of the time weighted average 222Rn gas concentration (in Bq/m3). However, a factor for calculating the effective dose arising from a given exposure to 222Rn progeny is needed in those special situations where occupational exposure to 222Rn progeny is subject to the requirements for planned exposure situations. This is necessary in order to ensure that dose limits are not exceeded. In addition, the conversion of 222Rn progeny exposure to effective dose enables it to be compared with occupational exposures to other sources such as external gamma radiation and inhalation of radionuclides in dust.
Discuss dose factords if necessary

## Slide 39
Thoron
Thoron (220Rn) is not normally of concern in NORM industries, except where material with a high thorium content is processed, e.g. monazite
Short lived progeny are likely to be severely out of equilibrium with the parent
In enclosed workplaces, the short half-life of thoron (55.6 s) means that the spatial distribution of thoron is much different from that of its progeny
  Assessment of equilibrium factor is difficult
  For dose assessment, an approach based on measurement of progeny concentration is easier and more appropriate than an approach based on measurement of thoron concentration

## Slide 40
Thoron
Dose factors:
  The UNSCEAR value for dose from inhalation of thoron is 40 nSv per Bq·h·m–3 equilibrium equivalent exposure
  Using this value:
    A thoron progeny potential alpha energy exposure of 1 mJ·h·m–3 gives a committed effective dose of about 0.5 mSv
      (Compared with 1.6 mSv for 222Rn progeny)

## Slide 41
Key messages
Radon is everywhere and concentrations can vary significantly
Exposure is subject to regulation
Dose comes from the radon progeny
Special quantities for concentrations and exposures
Many measurement methods exist and vary from simple to complex
Selection depends upon the situation and the possible concentration