## Slide 1: NORM Industries and Regulatory Considerations

## Slide 2
Content
What is NORM ?
Criteria for regulation
Graded approach to regulation
Understanding the project
Industrial sectors involving NORM
Key messages

## Slide 3
Background
NORM is present everywhere
Large throughput of raw materials and when concentrating occurs
Component of raw materials, products, residues
Radiation issues are usually not known or not expected or not wanted
Can have high public profile
Regulation (and thinking) required when above certain levels

## Slide 4
What is NORM?
Naturally Occurring Radioactive Material (NORM)
Radioactive material containing no significant amounts of radionuclides other than radionuclides of natural origin
    Definition of ‘significant amounts’ is a regulatory decision
    NORM also includes material in which the activity concentrations could have been changed by a process
    NORM refers only to material that is subject to regulatory control
  “If it is not regulated, then it is not NORM !”
Radioactive material
Material designated in regulation as being subject to regulatory control because of its radioactivity.
(Definitions derived from IAEA Glossary 2016, web only)

## Slide 5
Criteria for regulation
Excluded exposure situations
    Exposures that are unamenable to control are excluded from the requirements and therefore not subject to regulation
Non-excluded exposure situations
  The requirements for planned exposure situations apply if:
    The activity concentration of any radionuclide in the U or Th decay chains exceeds 1 Bq/g or 40K exceeds 10 Bq/g
  These criteria do not apply to radon, for which separate criteria have been established
  Regulation commensurate with the risk (the graded approach)
Notes: When determining which exposures should be subject to the requirements for existing exposure situations, only exposures that are amenable to control should be considered. Exposures that are unamenable to control are excluded from the IAEA safety standards and should thus be similarly excluded from the legal and regulatory framework for protection and safety.
Example of exclusion;
Cosmic radiation at surface of earth
K40 in the body

## Slide 6
Basis of exclusion criteria
Notes: This picture shows the basis for the value of 1 Bq/g for uranium and thorium series radionuclides. It represents the upper bound of activity concentrations in normal rocks and soil (green bands). Most industrial minerals have similar activity concentrations to normal rocks and soil, but a few have distinctly elevated concentrations (red bands). In many instances, the activity concentrations may still be below 1 Bq/g but in other instances the activity concentrations are well above 1 Bq/g. The value of 1 Bq/g serves as an entry level for regulation as a planned exposure situation. Below this entry level, it would be a waste of regulatory resources to regulate as a planned exposure situation.

## Slide 7
Regulating NORM in Practice
Generic clearance level <1 Bq/g (U and Th decay chain), 10 Bq/g for 40K
Specific clearance values derived to meet a dose criterion of the order of 1 mSv/a

## Slide 8
Graded approach to regulation
If criteria exceeded, regulatory control must be considered, based on “the graded approach to regulation”:
  Exemption
  Notification
  Notification + registration
  Notification + licensing
The graded approach is implementation of optimization of protection
Other forms of industrial regulation may contribute to the control of radiation:
  Occupational health and safety (OHS) regulation (dust control)
  Environmental protection regulation (licences)

## Slide 10
1. Exemption
Exemption is the lowest level of the graded approach
  Always the first consideration
Criteria for exemption:
  “Trivial dose” concept – The radiation risk is sufficiently low as to not warrant regulatory control
  or
  “No net benefit” concept – No reasonable control measures would achieve a worthwhile reduction in doses
    Could be important for NORM industries, where the dose may not necessarily be trivial
Notes: Criterion for automatic exemption without further consideration (for radionuclides of natural origin):
Annual effective dose is of the order of 1 mSv or less
In NORM industries, the 1 mSv criterion can usually be applied to worker doses, since public doses are likely to be at least an order of magnitude lower

## Slide 11
2. Notification only
The requirement for notification (without the need for an authorization) is appropriate when the annual effective dose is small compared to the relevant dose limit
The responsible person must formally submit a notification to the regulatory body of the intention to carry out the practice
Similar to exemption, but provides the reassurance that the regulatory body remains informed of all such practices.

## Slide 12
3. Notification + Registration
Registration is the lower of the two levels of authorization
Appropriate for situations where notification alone is not sufficient for providing an optimized regulatory approach
The regulatory body may decide that the responsible person has to meet additional (but limited) requirements to ensure adequate protection
Typical requirements :
  Measures to keep exposures under review
  Measures to ensure that the working conditions are such that exposures remain at moderate levels, with little likelihood of doses approaching or exceeding the dose limit

## Slide 13
4. Notification + Licensing
Licensing is the upper of the two levels of authorization
Appropriate for situations where:
  Notification alone is not sufficient for providing an optimized regulatory approach
  An acceptable level of protection can be ensured only through the enforcement of more stringent exposure control measures
Represents the highest level of the graded approach
For exposure to NORM, licensing is likely to be appropriate only in those situations involving substantial quantities of material with high activity concentrations (eg; uranium mining)

## Slide 14
Removal of regulatory control from material (clearance)
Criteria for clearance:
  ‘Trivial dose’ concept or‘ No net benefit’ concept
  Since the dose criterion for exemption is a dose of the order of 1 mSv per year, a similar dose criterion is appropriate for clearance
Automatic clearance without further consideration:
  Activity concentration does not exceed
    1 Bq/g (U, Th series)
    10 Bq/g (40K)
Notes:   Radiation risks from the cleared material are sufficiently low as not to warrant regulatory control
  Continued regulatory control of the material would yield no net benefit, in that no reasonable control measures would achieve a worthwhile return in terms of reduction of individual doses

## Slide 15
Pre-requisites for decision making
Successful implementation of a graded approach is possible only if you understand the operation;
  Processes,
  Materials involved
  Exposure pathways
  Potential exposures and doses
  The environmental factors
Requires discussion with industry sector or operator
(see IAEA Safety Guide GSG-7)

## Slide 16
Industrial sectors that may require regulatory considerations
Mining and processing of uranium ore HIGHER CONCERN
Extraction of rare earth elements
Production and use of thorium and its compounds
Production of niobium and ferroniobium
Mining of ores other than uranium ore
Production of oil and gas
The zircon and zirconia industries
Manufacture of titanium dioxide pigment
The phosphate industry
Production of tin, copper, aluminium, zinc, lead, iron & steel
Combustion of coal
Water treatment

## Slide 17
Other areas
Spas
Paper and pulp
Ceramics
Paints and pigments
Foundries
Optics
Refractory and abrasive sands
Electronics
Slag wool (insulation)

## Slide 18
IAEA Safety Report Series
Radiation protection and management of NORM residues in the Phosphate industry, Safety Report No. 78, 2013
Radiation Protection and NORM Residue Management in the Titanium Dioxide and Related Industries, Safety Report Series No. 76, 2012
Radiation Protection and NORM Residue Management in the Production of Rare Earths from Thorium containing Minerals, Safety Report Series No. 68, 2011
Radiation Protection and NORM Residue Management in the Zircon and Zirconia Industries, Safety Reports Series No. 51, 2007
Assessing the Need for Radiation Protection Measures in Work Involving Minerals and Raw Materials, Safety Reports Series No. 49, 2006
Radiation Protection and the Management of Radioactive Waste in the Oil and Gas Industry, Safety Reports Series No. 34 , 2003
Radiation Protection against Radon in Workplaces other than Mines, Safety Reports Series No. 33, 2003
Monitoring and Surveillance of Residues from the Mining and Milling of Uranium and Thorium, Safety Reports Series No. 27, 2002

## Slide 20
Occupational exposure
to potassium -40
Potassium-40 (K-40) is present naturally in human body
Amount in body in metabolic equilibrium so internal exposures not considered
IAEA Safety Report No 49 considers K-40 exposures
  Predicted annual dose per unit activity concentration of 40K is 0.02–0.03 mSv per Bq/g (External exposure pathway only; internal exposure excluded)
  K-40 activity concentration in pure potassium is 30.6 Bq/g
  For a material containing 100% potassium, the maximum annual dose is therefore
0.03 x 30.6 = 0.9 mSv/a
In practice, the potassium content, and hence the annual dose, will be much lower

## Slide 21
Examples of industries

## Slide 22
Oil and Natural Gas Production
Oil and gas exist in beds of permeable sandy sedimentary rocks
Rocks contain naturally occurring uranium (and thorium)
Radon can be released and caught in gas handling systems
Radon decays to decay products and Po210 and Pb210
Ra226 in water can precipitate as scale when pressures, temperatures or pH changes. Presence of H2S and CO2 can change water chemistry causing precipitation
Exposures can occur;
  From gamma radiation due to accumulation of scales or sludges
  During maintenance
Activity of material can vary widely
Waste disposal considerations

## Slide 23
Bauxite and Aluminium Industry
Bauxite ores sometimes contain elevated concentrations of natural U and Th
Two stage processing
  Bauxite to alumina (anhydrous aluminium oxide)
  Electrolysis to metal
Waste stream from first stage is ‘red mud’ carrying trace elements (and radionuclides)
Volume is reduce by half, but majority of radionuclides report to mud
Mud contains radionuclide concentrations above background levels
Very large volumes of residues

## Slide 24
Phosphate Industry
Natural phosphate usually contains wide range and elevated levels of U (and sometimes Th)
Ore is processed to produce;
  Fertiliser
  Phosphogypsum waste (calcium sulphate)
Uranium follows fertiliser
Radium follows waste stream
Final concentrations depend upon the original ore concentrations
  U up to 1.5 times in product
  Ra up to 5 to 15 times in waste

## Slide 25
Metal Mining and Processing
U and Th concentration varies with geologic formation and region.
Metals (Cu, Sn, Au, Ag)
Potential radioactive materials include;
  Ores
  Intermediate streams
  Metal concentrates
  Waste rock, Tailings, Smelter slags
Exposures pathways;
  Gamma
  Inhalation of radioactive dusts
  Radon and decay products
Exposures during; mining, processing, recycling and closure

## Slide 26
Metal Mining and Processing
Where concentrating of metals occurs
Extraction processes is an enriching process
Radionuclides are also found in some final products
Large bulk waste streams (e.g., copper, aluminum, iron, steel)
Usually in low concentration and high volume waste streams
Some processes concentrate specific radionuclides
  Actinium follows Lanthanum
  Radium follows Ba, Ca
  Polonium follows Te, Se
  Some radionuclides are acid soluble

## Slide 27
Coal Mining and Processing
Coal is mined, pulverised, mixed with hot air and burnt to produce steam.
Wastes are fly ash and bottom ash and slag
Radionuclides in coal remain in waste – enhanced by a factor or 3 to 20
Volatile radionuclides accumulate in the fly ash or stack emissions
Radon emitted as a gas
Potential issues with remediation

## Slide 28
Iron and Steel Production
Raw materials are; iron ore, coal and limestone
Waste is 2 to 4 t per tonne of steel
  Therefore, enhancing of radionuclides into waste (0.5Bqg -> 2Bq/g)
Waste contains radionuclides (and other heavy metals)
Volatile radionuclides (Po210 and Pb210) are in exhaust system and can accumulate in dust handling systems
Radionuclides can accumulate in other waste streams

## Slide 29
Rare Earths and Mineral Sands
Lanthanide rare earth metals – 16 elements
Mineral sands operations are well understood
Gravity processes concentrate the heavy minerals
Monazite in mineral sands contains about 6% thorium
Cracking uses concentrated H2SO4 – can mobilize radionuclides
Ilmenite, rutile, zirconia material
Rare earths used in electronics, super magnets and technology
Generally Th decay chain radionuclides
Selective concentrating of rare earth metals can also act to concentrate radionuclides

## Slide 30
Water Treatment
Some water supply systems treat water containing elevated levels of NORM
Radionuclides may be present in potable groundwater and surface water
Removing impurities tends to concentrate them in waste streams
Radium in groundwater (Ra226 and Ra228)
Wastes include sludges and solids
  Filter sludges
  Ion-exchange resins
  Activated charcoal
  Radium-selective resins - discrete wastes
Waste stream concentrates impurities

## Slide 31
Building Industry
Extensive use of recycled materials;
  Fly ash used as a concrete extender
  Bottom ash sometimes used in concrete
  Smelter slag used as filler for foundations (eg; roads)
  Steel recycling
Wastes and residues used as filler material
NORM in materials is source of gamma radiation (up to 0.4µSv/h per Bq/g)
Radon exhalation also potential source of exposure
Exposure scenarios (longer times)

## Slide 32
Underground Activities
Radiation impacts in enclosed spaces
Includes;
  Tunnelling
  Underground Mining
  Caving
Exposure pathways
  Gamma exposure
  Build up of radon with time
  Low ventilation rates leading to ingrowth
Radiation protection considerations for mines and excavations

## Slide 33
Wastes from Geothermal Energy Production
Using the natural heat, pressure and liquid from within the earth
Hot rock technology also a potential source of NORM
Minerals that precipitate out of solution forming scale or sludge on the inside surfaces of equipment
Contain barium, calcium, and strontium salts (carbonates, sulfates, silicates) as well as silica
Can contain significant concentrations of radium and radium decay products

## Slide 34
Practical Considerations
Identify sources;
  Understand radionuclide distributions
  Where are the radionuclides in the materials and processes ?
Identify exposure pathways to workers, the public and the environment
Understand natural background levels
Management measures; training, monitoring and safe work practices
Systems of Protection are generally standard for all industries
Excellent guidance exists (IAEA and from industry experts)
Radiation is only one of a number of hazards

## Slide 35
Key Messages
NORM present in many industries
Graded approach to NORM industries necessary
Application of graded approach requires understanding of industry dynamics
Each industry has unique characteristics and set of exposures
Important to have good understanding of industry

## Slide 36
Backup Slides

## Slide 37
1. Mining and processing of uranium ore
238U activity concentration | Ore: 4 – 1600 Bq/g Product: 10000 Bq/g
Exposure pathways | Gamma, dust, radon Potential for significant worker exposure Potential for significant public exposure Contamination of water bodies – discharges, mine residues
Occupational dose | 2 mSv average (12000 mine workers) 1 mSv (3000 ore processing workers)
Regulatory approach | Notification & Licensing

## Slide 38
2. Extraction of rare earth elements
(IAEA Safety Report Series No. 68)

## Slide 39
3. Production and use of thorium and its compounds
(IAEA Safety Report in publication)
232Th activity concentration | Th concentrate: 500–1000 Bq/g Th compounds: Up to 2000 Bq/g Industrial Products: Gas mantles: 500–1000 Bq/g Thoriated glass: 200–1000 Bq/g Th-containing optical polishing powders: 150 Bq/g Thoriated welding electrodes: 30–150 Bq/g Th alloys: 47–70 Bq/g
Exposure pathways | Gamma, dust, thoron Potential for significant worker exposure
Annual Effective dose (Occupational) | < 1 - 15 mSv
Regulatory approach | Notification & Licensing Solid wastes and effluents may need to be controlled.

## Slide 40
4. Production of niobium and ferroniobium
Activity concentrations | Extracted from pyrochlore, columbite, tantalite Pyrochlore concentrate 80 Bq/g 232Th Slag: 20–120 Bq/g 232Th Furnace dust: 100–500 Bq/g 210Pb, 210Po Residues from columbite and tantalite processing: 300 Bq/g 238U, 100 Bq/g 232Th, 500 Bq/g 226Ra Other residues: 200–500 Bq/g 228Ra
Exposure pathways | Gamma, dust, thoron Potential for significant worker exposure
Residues/wastes | May need to be monitored and controlled
Regulatory | Use of slag for construction may have to be restricted (potential for gamma, radon and thoron exposures in buildings).

## Slide 41
5. Mining of ores other than uranium ore
Activity concentrations | Activity in most ores are not elevated. In some cases 238U may range upto 10 Bq/g.
Exposure pathways | Radon main concern Potential for significant worker exposure. Worker doses could exceed dose limits if radon not properly controlled. (Radon influenced by properties of rock, e.g. porosity, inflow of Ra-rich water, ventilation)
Residues and wastes | Scales and sediments can have 226Ra, 228Ra concentrations up to 200 Bq/g Discharge of contaminated water can have significant environmental impact.

## Slide 42
6. Production of oil and gas
(IAEA Safety Report Series No. 34)
Source | Formation water contains 228Ra, 226Ra and 224Ra and decay progeny dissolved from the reservoir rock.
Changes in temperature and pressure at the well-head can cause | Scales rich in Ra & progeny inside pipes, valves, vessels Sludges rich in Ra & progeny in separators and skimmer tanks Deposits containing 210Pb & progeny in wet parts of gas production equipment
Exposures | Potential for significant exposure of maintenance workers to gamma and dust during maintenance and exposure to gamma of other workers spending time near pipes etc.
Residues and wastes | Activity concentrations are difficult to predict: Scales 0.1–15 000 Bq/g 226Ra Sludge 0.05–800 Bq/g 226Ra Disposal has to be controlled.

## Slide 43
7. The zircon and zirconia industries
(IAEA Safety Report Series No. 51)
Activity concentrations | Zircon: 2–4 Bq/g 238U Baddeleyite: 3–13 Bq/g 238U, 0.1–26 Bq/g 232Th Zirconia from fusion: 1.9–8 Bq/g 238U Zirconia from chemical processing: 0.001–1 Bq/g 226Ra SiO2 residue from zircon fusion: 1.5–6 Bq/g 226Ra, 0–10 Bq/g 210Pb, 210Po Furnace dust from baddeleyite fusion: 600 Bq/g 210Po Effluent treatment tank deposit: >5000 Bq/g 226Ra Chlorination residues: 0.3–48 Bq/g 226Ra
Annual effective doses received by workers: | Fusion or chemical processing of zircon or baddeleyite: 0.015–5.5 mSv All other processes: 0.0003–1 mSv
Exposures | Potential for significant exposure of workers if good OHS practices not adopted.
Notes: Zircon occurs naturally as a component of heavy-mineral sands.
Zirconia is manufactured from zircon or baddeleyite by fusion or chemical processing.

## Slide 44
8. Manufacture of titanium dioxide pigment
(IAEA Safety Report Series No.76)
Activity concentrations | Ores: 0.001–2 Bq/g 232Th TiO2 product, TiCl4 intermediate product: <0.1 Bq/g By-products: <0.01–1 Bq/g 232Th Scale: <1–1600 Bq/g 228Ra Filter cloths: 2–1000 Bq/g 228Ra Other residues: 0.02–24 Bq/g 232Th
Annual effective doses received by workers: | <0.01–1 mSv
Exposures | Potential for significant exposure of workers to gamma and dust.

## Slide 45
9. The phosphate industry
(IAEA Safety Report Series No.78)
Activity concentrations | Ore: 0.1–3 Bq/g 238U Process residues: Mine tailings: 0.01–2 Bq/g 238U Scale: 0.03–4000 Bq/g 226Ra Sediment, sludge: 1.3–4.3 Bq/g 226Ra Sludge from dicalcium phosphate production: 8–13 Bq/g 210Po Fertilizer and animal feed products: 0.04–3 Bq/g 238U Phosphogypsum by-product: 0.01–3 Bq/g 226Ra Slag from thermal phosphorus production: 1 Bq/g 238U Furnace dust from thermal phosphorus production: 1000 Bq/g 210Pb
Annual effective doses received by workers: | 0.1–0.7 mSv
Exposures | Potential for moderate exposure of workers to gamma and dust.
Environmental | Bulk storage of phosphogypsum in stacks has the potential for significant environmental impacts, mostly non-radiological. Decay storage of precipitator dust has to be controlled.

## Slide 46
10. Production of tin, copper, aluminium, zinc, lead, iron and steel
Activity concentrations | Feedstocks: Usually close to background levels Bauxite 0.035–1.4 Bq/g 232Th Furnace dust (smelting and refining): Up to 200 Bq/g 210Pb, 210Po Tin slag: 0.07–15 Bq/g 232Th Copper slag: 0.4–2 Bq/g 226Ra Sludge from iron smelting: 12–100 Bq/g 210Pb Red mud (from aluminium production): 0.1–3 Bq/g 238U, 232Th
Exposures | Potential for moderate exposure of workers to dust.
Environmental | Use of tin slag may need to be restricted.

## Slide 47
11. Combustion of coal
Activity concentrations | Coal: Typically at background levels, but sometimes higher Ash: Typically 0.2 Bq/g, but sometimes higher Fly ash contains the volatile radionuclides 210Pb, 210Po Flue gas desulphurization residues (sludges, gypsum): Lower than ash Scales inside burner kettles: Can exceed 100 Bq/g 210Pb
Exposures | Limited potential for worker exposure, doses < 1 mSv/a
Environmental | Bulk storage/disposal of residues have potential environmental impacts, mostly non-radiological — engineered containments required The use of fly ash and gypsum as by-products for construction materials does not usually need to be restricted

## Slide 48
12. Water treatment
Activity concentrations | Radionuclides can accumulate in water treatment residues, e.g. sludges, ion exchange resins 0.1–14 Bq/g 226Ra. Usually at the low end of this range, except when treating groundwater
Exposures | Limited potential for worker exposure
Environmental | Control of residue disposal needed for non-radiological reasons Measures may be needed to prevent the buildup of radon in underground facilities where groundwater is treated