## Slide 1: CHARACTERIZATION OF NORM

## Slide 2
Content
NORM analysis – purposes
Radionuclides of interest
Sampling
Analytical Techniques
Key messages

## Slide 3
NORM Characterization-Purposes
Understand preoperational baseline radiation levels
Understand characteristics of materials (ore, wastes, residues etc.)
For regulatory purposes (to determine of classification – exemption and clearance from regulation)
For additional information on dose assessments
Remediation goals for areas contaminated with NORM
Informed decision making on management of NORM residues and waste

## Slide 4
Baseline Background Radiation Surveys
To characterize the undisturbed natural levels of radionuclides in the environment prior to construction and operation of large scale industrial activities involving NORM
These levels can be used as reference levels during the remediation and closure of the industrial operation.
Samples of interest
  Surface soils (the top 40 cm)
  Surface and groundwater's (dissolved activity)
  Fallout dust
The environmental levels of natural radionuclides are generally very low and the analysis methods require high sensitivity with low levels of detection

## Slide 5
Understanding the NORM Material
Understand radiological properties
  A total of 36 radionuclides are found in the 238U (14), 235U (11) and 232Th (11) decay chains.
  In the analysis of a NORM material a decision is required on which radionuclides require to be analyzed and quantified.
  Mainly focus on long lived radionuclides.
Understand non radiological aspects (which may impact on the controls)
  Material may have acid forming minerals
  Solubility of host materials
  Does material easily form dust

## Slide 6
Focusing on Radiological Aspects Only
Consider the long lived alpha emitters
  Uranium series: 238U, 234U, 230Th, 226Ra, 210Pb and 210Po.
  Thorium series: 232Th, 228Ra and 228Th.
  These radionuclides can give rise to internal exposures
Consider significant gamma emitters (208Tl, 228Ac, 226Ra etc. )
Consider radon and thoron (and decay products)
Characterisation may vary depending on the material of interest
  For unprocessed material, U and Th decay chains can be assumed to be in secular equilibrium. In these cases only the parent radionuclides (ie; U and Th) require to be analyzed.
  For processed materials, need to understand what radionuclides are present and their concentrations
Notes: 210Pb and 228Ra are beta emitters. The radionuclides of the 235U decay chain are invariably found in very low concentrations and are rarely found in enhanced concentrations in NORM industries.

## Slide 7
Regulatory Purposes
Make a decision on the regulatory regime (i.e.; the graded approach to regulation)
Make a decision on the regulatory control to be implemented
Checking the measures that the operator provides for the protection of the workers, members of the public and the environment.

## Slide 8
Additional Information for Dose Assessment
Radiological characterization of workplaces
For contributing to the routine dose assessment of workers, for example; assessing the inhalation of long lived alpha emitting radionuclides and interpretation of dust sampling results.
For contribution to specific dose assessment of worker, for example; bioassays

## Slide 9
Bioassay Monitoring
The radioactive material in the body may need to be assessed in special circumstances:
  Specialized work situations (e.g. uranium product sections)
  Suspected over-exposure investigations
A variety of methods may be used:
  Urine analysis (e.g. uranium product sections)
  Faecal analysis (e.g. uranium and thorium facilities)
  Lung counting
  Radon or Thoron in breath
Notes: Many radionuclides of the uranium and thorium decay chains have extremely long lived half lives and are retained in the body for long periods. Bioassay is a specialized assessment technique used to quantify the total body burden. Assessment techniques include, urine and faecal analysis, breath measurements and in vivo monitoring (e.g. whole body or lung monitoring). Bioassay may be used to investigate suspected overexposures. In choosing the method or combination of methods, the purpose of the monitoring (i.e. routine or special), the working environment, the physical and chemical forms of the radioactive materials, and the practicability of measurement should be taken into account. For example:
Urine analysis is sufficiently sensitive for the monitoring of intakes of uranium, but not for thorium.
Faecal analysis is impracticable for routine monitoring but may be used for special monitoring to detect the passage of uranium through the gut or to determine intakes of thorium.
Lung counting may be used to detect the retention in the lung of uranium and thorium in chemical forms of low solubility. Lung counting needs to be performed at off-site locations equipped with specialized equipment and highly trained personnel.
The measurement of thoron in breath may be useful as an on-site screening technique, e.g. in the mining and processing of monazite, to identify individual workers with elevated thorium lung burdens that may need special monitoring by lung counting.
Instructions for the lecturer/trainer
Stress that bioassay is a specialized technique that is only used in certain situations where significant exposures are expected. Emphasize that, like any intake assessment technique, it is subject to uncertainties and errors, and must be interpreted with care.

## Slide 10
Fore Remediation Purposes
The large scale use of NORM in industrial activities can result in the contamination of the environment (e.g. surface soils) with radionuclides of the uranium and thorium decay chains
Characterizing any NORM contamination is a necessary step in deciding the optimum future management of that land e.g.
  predicting future impacts (doses to public and the environment)
  Selection of remediation measures that will work
  Worker protection during remediation
The remediated site may also need to be surveyed and sampled to confirm remediation has been successful

## Slide 11
Optimized Management of NORM residues and waste
The management of such materials should be optimized:
  ensuring workers and the public are protected
  minimizing disposals (e.g. recycling or use as construction or building materials)
  Cost effective
Good information obtained through appropriate characterization is an essential part of the optimization process

## Slide 12
Sampling
The materials requiring sampling and analysis include:
Large quantities with moderate or low activity concentrations (e.g. ore, tailings, slag, sludges, evaporates) ranging up to a few Bq/g per radionuclide
Small quantities with the possibility of high activity concentrations (e.g. mineral concentrates, scale, sludge, precipitator dust) ranging up to tens of thousands of Bq/g per radionuclide.
Therefore the sampling method and analysis sensitivity requirements will vary depending upon the nature of the material and the type of assessment.
Notes: An additional factor of importance is the radiological homogeneity of the material. Representative samples are more readily obtained from radiologically homogenous materials.

## Slide 13
Sampling
The sampling strategy selected will depend upon the type of material
The sampling techniques should be based upon a statistically rigorous criteria
It is important to obtain a representative sample of material for analysis
Many samples may require to be taken, mixed and homogenized to obtain a representative sample
Notes: For example the strategy for sampling large amounts of radiologically homogenous materials such as tailings may not be suitable for sampling non-homogenous areas such as sites contaminated with NORM.

## Slide 14
Elements to consider in Sampling Strategy
  The total number and location of sampling sites (site specific)
  The frequency of sampling
  The method of sampling (grab-continuous)
  Sample preservation techniques
  Identify representative person of
  the public and sensitive areas.
Notes: The sampling program should be designed to give a representative picture of the medium being sampled. A proper sampling methodology is critical to the success of a monitoring program.
Photo – taking tailings samples, Poland

## Slide 15
Introduction to Analytical Techniques
There are various analytical techniques available to quantify the radionuclide content of materials
      Radiometric techniques (e.g. alpha, beta or gamma spectrometry)
      Other analytical techniques (e.g. mass spectrometry)
  To be able to select the appropriate techniques, it is important to understand:
    the capabilities and limitations of the various techniques
        Selectivity (specific radionuclides, multiple radionuclides or type of radiation)
        Sensitivity (Limits of detection)
        Range of concentrations measurable (e.g. from 10 to >106 Bq.kg-1)
    technique complexity
    costs

## Slide 16
Analytical Techniques-
Gamma Spectrometry
Gamma spectrometry can detect and measure multiple radionuclides at the same time
Relatively simple sample preparation
Relatively short counting times (4-8 hours)
Different instrument required for low energy gamma emitters (mainly for 238U, 235U, 210Pb)
Relatively inexpensive
Notes: The technique is particularly suitable for 238U, 235U and 210Pb.
It is also possible for the technique to provide a determination of 226Ra, 227Ac, 231Pa and 230Th), but with a higher LLD.
Self absorption corrections will be required due to the low gamma energy.
A low background laboratory is required and the detector must be adequately shielded with old lead

## Slide 17
Analytical Techniques-
Alpha Spectrometry
Key method for identifying alpha emitters
Suitable for measuring very low concentrations
Complex sample preparation required - radiochemical extraction
Time consuming
Expensive
Notes: This technique requires considerable laboratory resources and validated methods and a high level of quality assurance. It is a key method for detecting and quantifying NORM alphas.
This technique is suitable for quantifying the very low concentrations of alpha emitters found in environmental samples and in the determination of 210Po concentration in industrial samples
This technique requires considerable laboratory resources and validated methods and a high level of quality assurance

## Slide 18
Analytical Techniques-
Proportional counting
Provides information on alpha and beta content
Cannot identity radionuclides
Relatively simple sample preparation (thin layer)
Relatively short count times
Relatively inexpensive

## Slide 19
Analytical Techniques-
Liquid Scintillation Counters
Provides information on alpha and beta content
Cannot identity radionuclides
Relatively simple sample preparation but needs to be put in solution
Relatively short count times
Relatively inexpensive

## Slide 20
Analytical Techniques- INAA
Instrumental neutron activation analysis (INAA):
A highly sensitive technique
The sample material is irradiated by neutrons in a nuclear reactor.
Activation products are formed and are then assessed using gamma spectroscopy.

## Slide 21
Other Analytical Techniques-XRF
The XRF (X ray fluorescence spectrometry) method is well suited to the rapid determination of elemental uranium and thorium concentrations in solid samples
Total U and Th can be detected to very low levels e.g. 1-2 ppm
The method is useful as a screening technique
The calibration of the XRF must be specific to the type of material being analyzed e.g. mineral ore, soils, scale, sludge etc.
Notes: There are two types of spectrometer:
(i) Wavelength dispersive spectrometers, in which photons are
separated by diffraction on an analysing crystal before being
detected.
(ii) Energy dispersive spectrometers, in which the detector allows the
determination of the energy of the photon when it is detected

## Slide 22
Other Analytical Techniques-ICP-AES
Inductively coupled plasma atomic emission spectroscopy (ICP-AES):
Used for the chemical analysis of aqueous solutions of rocks and other materials
Suitable for the determination of a wide range of major elements and a limited number of trace elements.
Notes: Sample preparation involves the digestion of the powdered material with 40 vol. % hydrofluoric acid mixed with either perchloric or nitric acid.
A number of minerals such as chromite, zircon, rutile and tourmaline will not completely dissolve using this digestion procedure. For these samples XRF analysis is probably more appropriate.

## Slide 23
Other Analytical Techniques-ICP-MS
Inductively coupled plasma mass spectroscopy (ICP-MS):
ICP-MS can be used to determine trace elements at environmental levels.
The technique is well suited to determination of total uranium and thorium.
Notes: The sample preparation procedure is the same as that for ICP-AES.

## Slide 24
PPM Conversions
The above analytical techniques provide the analysis results in ppm total uranium or thorium.
The following conversions from parts per million to Becquerel's per gram per radionuclide can be used
1 ppm uranium = 12.3 mBq 238U per gram of material;
1 ppm thorium = 4.1 mBq 232Th per gram of material.

## Slide 25
Analytical Technique Selection
Analytical technique selection will depend on your needs and should be fit for purpose
For NORM associated with most industrial processes, it is adequate to have a basic analytical infrastructure (eg; XRF, HPGe gamma spectrometry)
Techniques can be complimentary and used in combination if necessary e.g.
  Gross alpha-beta counting for routine measurements
  Radionuclide specific analysis when further detail is required
The more complex radiochemical techniques more likely to be required for:
  Background baseline surveys
  Liquid effluent discharges from NORM facilities
  Industrial processes where 210Pb and 210Po is of concern

## Slide 26
Quality Assurance
The analysis should be carried out by an ISO accredited laboratory and the methods will be documented.
The analytical standards and methods must be traceable to national and international standards. Such a laboratory would carry out regular intercomparison exercises.
If an accredited laboratory is not available the analytical technique must at least be validated against appropriate reference materials (e.g. NORM related materials provided by IAEA or other national/ international bodies)
Notes: Laboratories handling a wide range of sample activity concentrations would require to take particular care to avoid cross contamination of low activity NORM samples
The accuracy, precision and sensitivity of the analytical technique requires to be related to the radionuclide activity level in the sample media
Baseline radiation studies require the highest analytical sensitivity.
The analytical technique should be sensitive enough to measure down to the background activity concentration of radionuclides e.g.
Soils and fallout dust: <0.01 Bq.g-1 (per radionuclide)
Natural water samples: <0.01 Bq.l-1 (per radionuclide)
In the case of analysis of NORM for regulatory purposes an analysis sensitivity of 0.1 Bq.g-1 would be appropriate for comparison against the 1 Bq.g-1 criterion

## Slide 27
Key Messages
Characterisation of NORM is required for a number of important purposes
There are a number of standard techniques for sampling, measurement and analysis of NORM
Make sure your selection of techniques are appropriate
Use of an accredited laboratory for analyses
Seek competent assistance and advice if necessary