## Slide 1: Exposures from Legacy NORM Sites

## Slide 2
Content
Legacy sites contaminated by NORM
Environmental contamination by NORM
Potential exposure pathways
Mitigation and remediation options
Regulatory issues

## Slide 3
Legacy Sites
Areas affected by past activities involving NORM.
They are often abandoned or ownership is uncertain.
The areas may include facilities, residues, land and water bodies contaminated by NORM residues.
Legacy sites can be found in remote or urban areas.
The sites and contamination can be very old e.g. centuries

## Slide 4
Legacy Sites
Contaminated urban legacy sites may have been built over for residential purposes or used for other purposes.
A wide variety of NORM industries are involved.

## Slide 5
Legacy Sites
Some of these industries are no longer operated e.g. radium refineries, luminising operations, radium health cures.
There is a wide variation in the extent of contamination, the quantities of materials involved and the radionuclide characteristics and activity levels.
A wide variety of regulatory approaches are taken worldwide
Notes: These residues containing NORM as altered by human activities from outside the nuclear fuel cycle have developed over the past three decades from a little known issue to an issue that is receiving a considerable amount of global attention. Important reasons for the increasing levels of concern are the:
— Large amounts of such NORM containing wastes and other materials;
— Potential long term hazards resulting from the fact that NORM is
comprised of long lived radionuclides with relatively high radiotoxicities;
— Higher likelihood for members of the public to be exposed to NORM
contained in wastes and products than to most other sources of radiation.

## Slide 6
Regulatory Issues
Legacy sites contaminated with NORM arise from historical activities that were not regulated as “practices”.
In most cases the Regulatory approach should therefore be consideration as existing exposure situation and apply the use of Reference Level for optimisation of doses.
The clean up criteria require to be site specific and based on the principle of optimisation.
A national strategy may be required to be developed in those countries with significant legacy issues.
Notes: An important first step for industry and regulatory bodies in a
country is to understand when and where NORM can occur within a given
process and also to identify the locations where concentrations of NORM can
be greatest within a given process.
Determining at what concentration for a given exposure situation NORM
becomes a potential radiological concern is a high priority in many countries.A
number of countries have established concentration levels at which NORM is
considered ‘radioactive’ and must be controlled; however, there is no international
consensus on approaches to determine these concentration levels or on
the specific concentration levels. This has proved to be problematic firstly due
to the potential economic impacts associated with control of NORM containing
residues in a manner consistent with management of other radioactive wastes
and secondly due to the disagreement on appropriate exposure scenarios and
models [4].
The task is further complicated by the fact that the relevance of exposure
to NORM depends very much on local or regional circumstances andbehavioural patterns. For example, an oil well or mine located in an
unpopulated, remote area poses less of a risk for potential exposures to the
general public than similar facilities located near a populated area. Likewise,
rural populations in tropical developing countries will face a different potential
for exposure than a rural family in Europe (different types of homes, amount
of time spent at home, etc.). Thus, exposure scenarios to be considered when
determining the concentration levels at which NORM related doses are
considered significant will depend on living conditions and human behaviour in
that region.

## Slide 7
Factors Affecting the Strategy Selection
Availability of funding and experienced staff.
The level of radiological hazard.
Availability of waste management systems.
Social and economic impacts.

## Slide 8
Possible Exposure Scenarios
Building dwellings on contaminated land or residue dumps
Use of residues in building materials
Use of contaminated ground and surface waters
Contaminated foodstuffs
Soil ingestion (children)

## Slide 9
Mitigation Options
A wide variety of approaches are available to mitigate the radiation exposures of the public from historical NORM residues.
Removal of the contaminated material for re-use, recycling or disposal to a waste repository.
Removal of the population from a contaminated area.
Containment-stabilising, covering, shielding residue dumps.
Soil and water treatment.
Restrictions on access or land use.
Complete isolation of the area.

## Slide 10
Post Remediation Phase
Monitoring and surveillance may be required for some time after remediation to confirm that the site complies with the remediation criteria.

## Slide 11
Key Messages
Sites contaminated by historical NORM residues are a common phenomena worldwide.
A wide variety of industries and residues are involved.
Contaminated sites and materials may be used by the worker or public resulting in radiation exposures.
Remediation of sites and the mitigation of exposures may be treated as an existing exposure situation.
Radiation exposures can be reduced through a variety of mitigation options and technologies.
Monitoring and surveillance may be required for some time following rehabilitation.