## Slide 1: NORM –Environmental Monitoring

## Slide 2
Content
Objectives of monitoring
Steps in the development of the programme
Stages of monitoring
Key messages

## Slide 3
Objectives of the Monitoring Programme
Quantifies radionuclides and radiation levels in emissions and effluents.
Quantifies radionuclides and radiation levels in the environment.
Confirms the safety assessments.
Demonstrates compliance with regulatory requirements.
Demonstrates protection of the public and environment.
Notes: Provides evidence of the measurable presence or non-detectability of radionuclides and radiation in the facility emissions, effluents and the environment.
Confirms the conclusions of the safety assessments.
Demonstrates compliance with regulatory requirements.
Protects the workforce and the public.
Confirms the performance of the NORM waste disposal facility.
Identifies and assesses radioactive material migration from a disposal facility that was not built to the applicable standards.

## Slide 4
Stops in the development of the program
The identification of “radionuclides of interest”
Identification of releases
The identification of potential pathways of public exposure
Identify representative person and where applicable –reference plant/animal
Monitoring methods
Monitor and periodic review
Notes: There are several steps in the development of the program that will be addressed separately

## Slide 5
1. The identification of “radionuclides of interest”
Know your process
Know your materials
Refers to earlier lecture on characterisation
For NORM – natural radionuclides

## Slide 6
2. Identify releases

## Slide 7
3. Identification of exposure pathways

## Slide 8
3. The potential exposure pathways
Notes: In many cases it is relatively easy to determine possible pathways of exposure. It is, however, necessary to understand people’s life styles and habits – particularly in remote areas. The ‘default’ figures on water/milk/meat/fish/vegetables consumption will not apply in all situations and quite often country- and site-specific factors may need to be used.

## Slide 9
4. Identify representative person and where applicable – reference plant/animal
New definition (representative person – ICRP-103, 2007):
Representative Person is an individual receiving a dose that is representative of the more highly exposed individuals in the population. This term is the equivalent of, and replaces, ‘average member of the critical group’ described in previous ICRP Recommendations.
Doses are typically trivial, so you sometimes have to model a hypothetical person

## Slide 10
5. Monitoring Methods
Selection of equipment
Methods
Frequency
Proportionate with the risk
Carried out by suitably trained and experienced practitioners
Notes: The ‘period of time’ will significantly depend on the potential levels of exposure and the complexity of possible exposure pathways

## Slide 11
6. Monitoring and review
Monitoring is a dynamic process;
Monitoring programs should not be static;
Revision should be justified and documented;
The required outcome is an optimised, cost effective and focussed program;
The extent of the program must be commensurate with the risk.
Regulator and operator are involved in the review
Notes: These models can be derived from IAEA guides or purchased as proprietary software.
  These can include: Groundwater and surface water transport models, Air dispersion models for radon and particulate transport, Environmental transport models.
   Please note that country-and site-specific parameters may need to be developed.

## Slide 12
Stages of Monitoring
Monitoring is required throughout the lifetime of a facility:
Pre-operational (e.g. baseline)
Operational (effluents and environment)
After closure (environment, integrity of the engineered structure)
Notes: Photos:
Top – exploration, Australia
Middle – ore crushing in-pit, Australia
Bottom – tailing from the phosphate mine, South Africa

## Slide 13
Stage 1 – Pre-operational Monitoring
Defines the baseline radiological conditions around the facility prior to operations.
Provides data for background subtraction e.g. to separate impact of the operation from natural levels
Provides data useful in remediation activities.
Assists in the design of the operational monitoring program e.g. identification of sampling positions.
Notes: Defines the baseline radiological conditions around the facility for comparison with later operational monitoring results.
Collect samples of environmental media for archival purposes.
Provides input data for the safety assessments.
Provides input data needed for the safety assessment
Assist in characterization of pathways of radionuclides dispersion from the disposal facility
Define baseline radiological conditions for comparison with later monitoring results
Collect samples of environmental media for archival purposes
Assist in the design of the operational surveillance and monitoring programme.
Safety assessment plays a central role in the development of a disposal facility. It is used iteratively throughout the period of design and provides a basis for obtaining regulatory approval and public acceptance of the disposal facility as well as establishing the necessary controls and limitations on design, construction, operation and closure. Pre-operational monitoring in the area surrounding the planned disposal facility site should include collection of the site specific radiological, hydrological, geochemical, meteorological and biological data needed for the safety assessment.
Details of the parameters to be measured, the frequency of measurement and the required precision and accuracy of the measurements will be based on the aims of the safety assessment and will be specific to the particular site and facility. In this phase, the frequency of sampling and measurement has to be sufficient to allow for seasonal variations in site parameters to be adequately addressed and for spatial heterogeneities in hydrological and hydrogeological characteristics to be determined on a scale commensurate with the modelling requirements for the safety assessment
Define baseline radiological conditions for comparison with later monitoring results. Radionuclides that will be of concern for the disposal facility are monitored for in the general environment of the disposal facility during the pre-operational phase. For groundwater and surface waters, these locations should be sited both up-gradient and down-gradient of the disposal facility site. Ambient radiation dose rates, radon levels and dust emissions at and around the disposal facility site have to be measured. This baseline information is documented in such a manner that meaningful comparisons can be made with data that will be collected in the future.
Photo: Australia

## Slide 14
Stage 1 – Pre-operational Monitoring
Measure for 1-2 years across the whole site and surrounding environment
Gamma radiation across the proposed site and surrounding environment
Concentration of radionuclides in soil, groundwater, surface water and dust
Radon gas concentrations (and variability)
Dust mass concentrations and dust deposition
Notes: Photo: Australia

## Slide 15
Stage 1 – Pre-operational Monitoring
Assessment of gamma dose rate
Notes: Examples from a relatively cheap (~US$100) ‘3DField’ software.

## Slide 16
Stage 2 – Operational Monitoring
Need to be proportional to the exposure pathways and the material characteristics
Measure effluent discharges at the emission point e.g. dust, gas and water (to define the source term and for modelling)
Could include;
  Environmental gamma
  Activity concentrations in soil, water and biota
  Activity concentrations in airborne dust and deposited dust
  Radon and radon decay product concentrations
  Foodstuffs
Model the results to determine doses to the public
Notes: Photo: Turkey

## Slide 17
Stage 3 – Decommissioning and post closure
When decommissioning, review monitoring to verify the exposure pathways
At post closure reassurance monitoring may be required.
Final monitoring prior to relinquishment (compare to pre operational measurements)
(Note that later lecture on decommissioning and closure of facilities L12)
Notes: If any observation during development of disposal facility infrastructure indicates that the evolving disposal facility may be causing changes to the local hydrology, hydrogeology or geochemistry, then the appropriateness of the current radiological monitoring programme has to be re-evaluated. If the results of monitoring indicate that concentrations of radionuclides of interest are greater than the reference or predicted values, then an investigation has to be undertaken to determine the reason for the unanticipated values. This may involve repeated or more extensive sampling and possibly extension to include other potential contaminants. If results of monitoring indicate that the current or long term performance of the disposal facility may not be as anticipated and therefore not compliant with regulations, consideration may have to be given to taking remedial action.
The adequacy and appropriateness of the sampling and measurement protocols also need to be surveyed periodically (given potentially extensive duration of post-closure monitoring)
Photo – pit wall failure, Australia

## Slide 18
Non radiological aspects
Changes in the structural stability of a disposal site may occur and monitoring of the surrounding area is needed to assess its stability.
The state of the disposal facility cover and engineered barriers after closure is determined through the monitoring program.
Notes: The engineered barriers comprise all the materials placed around the waste to isolate it from the environment, including any low permeability or intrusion resistant covers placed over the disposal facility close to the ground surface. The state of the engineered barriers needs to be ascertained through the surveillance programme. Reference documents on the technique for surveillance are available. (e.g. IAEA 1999, ICRP 1984). Changes in the structural stability of a disposal site may occur as a result of natural processes or human activity. Processes that can affect barrier performance include erosion, landslides, flooding, degradation of covers due to shrinkage , intrusion by vegetation or animals. Continuing surveillance of the surrounding area is needed to assess its stability and to detect any movement of the disposal facility structure
It is necessary that the integrity of the disposal facility cover is ascertained in the surveillance programme, in particular verifying that erosion, cracking, subsidence, intrusion, … have not led to sufficient deterioration of the cover that the assumptions and predictions of the safety assessment are invalidated.
IAEA, 1999. Safety assessment for near surface disposal of radioactive waste WS-G-.1, 1999
ICRP, 1984. Principles of monitoring for the radiation protection of the population., Publication 43. Pergamon Press, Oxford and New York.
Photos: uranium tailings storage facility in Ukraine
>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>
The surveillance and monitoring programme designed in the pre-operational phase is to be implemented as soon as waste is delivered to the disposal facility.
The potential exists for changes to occur to the local environment as the result of construction and operation of the disposal facility, specifically from modifications to site features, which affect the assumptions made in the safety assessment. An example is increased water penetration due to disturbance of the ground surface, elimination of native vegetation over the disposal units, drilling of boreholes, or channelling of runoff water. The implications of such changes in site hydrogeological and geochemical parameters, detected by the surveillance and monitoring programme, need to be reviewed, the safety assessment revised and the programme adjusted accordingly.
Environmental contamination that may occur during the operational phase from waste handling during emplacement could affect the capability to detect the migration of any radionuclides from the engineered disposal facility. The operator has to be alert to this possibility and should adjust the surveillance and monitoring programme accordingly.
The programme to be followed when operation of the disposal facility ceases and the facility is closed is defined towards the end of the operational phase. This programme needs to be based on the safety assessment, data on the emplaced waste and information obtained in conducting the pathway characterization, and supplemented by the results of, and experience gained with, the surveillance and monitoring programme through the operating phase. All the features of the monitoring programme need to be included. The detection and monitoring methods need to be specified for all the radionuclides of concern.

## Slide 19
Summary
Identify source terms
Concentrate on the most critical pathways.
Data interpretation is as important as data collection.
Document and report the results.
Keep the monitoring relevant - review the program and amend it in the light of data collected.

## Slide 20
Key Messages
Monitoring is required throughout the life of the facility.
The monitoring of NORM facilities is complicated by the presence of natural background radiation.
Monitoring is essential to provide assurance that the NORM facility is operating in a safe manner in accordance with the regulatory requirements.
Obtaining the right compromise between monitoring and resource requirements is crucial.