## Slide 1
International Atomic Energy Agency
Example of Safety Technical Review

## Slide 2: Step by step review of the safety assessment
  Assessment context,
  Description of the system,
  Development and justification of scenarios,
  Formulation and implementation of models,
  Analysis of results.
<number>
Will be illustrated using some of the main components of the safety assessment:
Notes: <number>
The review process to some extent parallels the assessment process itself.
One model for the assessment process is given in this diagram:
establishment of the assessment context
review of the system description
development and justification of scenarios for analysis
formulation and implementation of computational models
performance of the calculations
interpretation of results
comparison against assessment criteria
If the results do not meet the criteria, either the assessment models or the input assumptions (including design parameters and operating limits) need to be adjusted and the process is repeated.
Regardless of whether the assessment process followed this model exactly, the outcomes of the steps listed here must be achieved at some point in the assessment, and one of the tasks of the regulatory review is to verify that this is the case.

## Slide 3: Safety Assessment Process
Assessment Context
Description of Facility or Activity
and Sources
Development and Justification of Scenarios
Identification of Hazards
Selection and Hazard Screening
Identification of Scenarios
Evaluation of results
Identification of Models and Data Needs
Performing Dose/Risk Calculations
Analysis of Safety Measures
Compare against Assessment Criteria
Analysis of Engineering
Adequate?
Adequate?
Review and Modify
Independent
verification
Accept
Purpose, Regulations, Standards
Engineering Design, Safety Measures,
Other relevant information: Normal operational procedures, Management systems operational experiences, site data
Events, Initiating events,
Expert judgments
Models and Computer codes
Generic, Facility/Activity specific data
Yes
Yes
No
No
Safety Assessment Process

## Slide 4: Review of the assessment context
The review should verify that:
  The scope and context of the assessment is clearly defined.
  The implementer understands the key components of the assessment context, particularly the existing regulatory requirements set by the regulatory body.
The components of the assessment context are:
  Purpose of performing the assessment;
  Regulatory framework;
  Assessment end-points;
  Assessment philosophy;
  Timeframes.
<number>
Notes: <number>
The safety assessment context is intended to clarify what is going to be assessed and why is it going to be assessed. In addressing the assessment context, information should be provided concerning the following key aspects that need to be considered at the start of the safety assessment: purpose; regulatory framework; assessment end-points; assessment philosophy; disposal system characteristics; and timeframes. It should be noted that many components of the assessment context are inter-related, and that decisions relating to one component can influence other components. For example, the end-points assessed should be appropriate for the timeframes considered in the assessment
principal purpose - demonstrate an acceptable level of protection of human health and the environment now and in the future. The purpose may vary from considering initial ideas for disposal concepts (Simple calculations), to support for a licence application for disposal or for upgrading.
The audience to will play a role in defining relevant assessment end-points, assumptions concerning the disposal system, justification of the assessment scenarios, as well as approach for presentation of the assessment results.
At one extreme these could be specified, prescriptive quantitative regulatory requirements, and at the other they could be non-prescriptive performance oriented requirements or may not have been fully developed. In all cases, it is important that consideration should be given to international guidance.
There is a trend in safety case development not to rely on assessment of just a single end-point, such as individual dose or risk. Multiple lines of reasoning, additional indicators (radionuclide fluxes and concentrations) are increasingly important.
The assessment philosophy is an expression of the extent to which the assessment is designed to provide a “realistic” estimate of potential impacts for comparison with the assessment end-points, or whether more cautious, or pessimistic assumptions should be adopted.
System characteristics - general description - near-field, geosphere, biosphere; brief overview of 1)present-day system, and 2)fundamental assumptions for system development.
Assessment timeframes - can be a function of the nature of the waste disposal system and the external influences on it, and the longevity of the radionuclides in the wastes. Timescales of an assessment should be justified on a case-by-case basis, although some may also be imposed by regulatory requirements (e.g. institutional control period). Balance greater certainty for shorter time periods with increasing uncertainty over longer time periods.

## Slide 5: Safety Assessment Process
Assessment Context
Description of Facility or Activity
and Sources
Development and Justification of Scenarios
Identification of Hazards
Selection and Hazard Screening
Identification of Scenarios
Evaluation of results
Identification of Models and Data Needs
Performing Dose/Risk Calculations
Analysis of Safety Measures
Compare against Assessment Criteria
Analysis of Engineering
Adequate?
Adequate?
Review and Modify
Independent
verification
Accept
Purpose, Regulations, Standards
Engineering Design, Safety Measures,
Other relevant information: Normal operational procedures, Management systems operational experiences, site data
Events, Initiating events,
Expert judgments
Models and Computer codes
Generic, Facility/Activity specific data
Yes
Yes
No
No
Safety Assessment Process

## Slide 6: Description of the System
The review should verify that the following elements are adequately described:
  Radiation sources including radioactive waste, volume, characteristics, inventory;
  Engineered systems,
  Installation design, and
  The environment.
  May include facility inspection
<number>
Personnel access door
Control panel
Source holder
Turntable
Notes: <number>
The purpose of the review of the system description is not to review the description itself, but rather to assure that all of the features of the system that have a material effect on the safety assessment have been taken into account, and that the assumptions in the safety assessment about these features are consistent with the actual system (“consistent with” includes the possibility that the assumptions in the analysis were chosen conservatively so as to bound the actual system behaviour).

## Slide 7: Examples of questions to be answered
Are the components of the systems significant for safety and their interfaces clearly defined?
  What are the safety functions of each system component?
    In case of normal operation of the system?
    In case of less likely events?
Can they be verified?
<number>
Notes: <number>
These are examples – depending on the nature of the facility and of the assessment, there may be other similar questions that should or could be asked.

## Slide 8: Examples of questions to be answered
  What support is there for the long-term effectiveness of the system components?
Is the level of available data adequate for the current stage of the facility development?
What are the uncertainties in the data and parameters used in the assessment?
<number>
Notes: <number>
These are examples – depending on the nature of the facility and of the assessment, there may be other similar questions that should or could be asked.

## Slide 9: Safety Assessment Process
Assessment Context
Description of Facility or Activity
and Sources
Development and Justification of Scenarios
Identification of Hazards
Selection and Hazard Screening
Identification of Scenarios
Evaluation of results
Identification of Models and Data Needs
Performing Dose/Risk Calculations
Analysis of Safety Measures
Compare against Assessment Criteria
Analysis of Engineering
Adequate?
Adequate?
Review and Modify
Independent
verification
Accept
Purpose, Regulations, Standards
Engineering Design, Safety Measures,
Other relevant information: Normal operational procedures, Management systems operational experiences, site data
Events, Initiating events,
Expert judgments
Models and Computer codes
Generic, Facility/Activity specific data
Yes
Yes
No
No
Safety Assessment Process

## Slide 10: Development and justification of scenarios
Review of scenarios should verify that:
  The selected scenarios adequately cover the assessment time frame;
  The set of scenarios developed is credible, comprehensive and has been developed in a systematic, transparent and traceable manner;
  The approach and screening criteria used to exclude or include scenarios are justified, well documented.
<number>
Notes: <number>
The choice of scenarios to be analyzed is a key component of the assessment process. It is important that the review identify whether the chosen set of scenarios is sufficiently complete, i.e. that the scenarios chosen adequately represent (or in some cases, bound) the conditions that might be encountered both under normal conditions and during credible accidents. Accident scenarios may include both failures internal to the system, including human errors where those may have an effect on safety, and external events (e.g. seismic events, severe weather, etc.). To this end, it is important that the process that the applicant used to select scenarios be systematic, transparent and traceable.
Some scenarios may have been excluded from analysis because they are considered to be improbable, because they do not result in significant challenges to safety, or because their outcomes can be seen to be covered by another included scenario. The approach used to screen and exclude scenarios should be reviewed to ensure that the scenario selection process was adequate.
The selected scenarios adequately cover both present and future, likely and less likely conditions.
The set of scenarios developed is credible, comprehensive and has been developed in a systematic, transparent and traceable manner
In general one would expect to see a “normal” (aka “design”) scenario, one or more human intrusion scenarios, scenarios that examine less likely natural disruptive events (earthquake, volcanicity), a reduced performance scenario showing the consequences of substandard implementation. For a near surface disposal intrusion by animals should also be considered and, in some circumstances, may form part of the normal scenario
Finally the reg rev needs to be confident that the approach and screening criteria used to exclude or include scenarios are justified and well documented

## Slide 11: Examples of questions to be answered
What type of intrusion scenarios have been used?
How have “what-if” scenarios been developed and analyzed?
What events have been considered and where did they come from?
Is there a clear distinction between the scenarios describing the “normal” (or “design”) evolution of the system and those describing low probability events?
<number>
Notes: <number>
These example questions relate specifically to a disposal example. If time permits, a class discussion on questions for a different type of facility may be conducted
. Examples of relevant questions to be asked with respect to the development and justification of scenarios are
What human intrusion scenarios have been used and how are they justified?
How have “what if?” scenarios been used and analysed?
What FEPs have been considered and where did they come from - were they from the IAEA FEPs list for instance? How confident can we be that the FEPs list was comprehensive?
Is there a clear distinction between scenarios describing the “normal” (aka “design”) evolution of the system and those describing low (annual) probability events? The word “annual” appears here because the probability of a natural disruptive event over ten million years may be close to unity but, because regulatory constraints are expressed in terms of annual doses, it is the annual probability of an event’s occurring that is important.

## Slide 12: Safety Assessment Process
Assessment Context
Description of Facility or Activity
and Sources
Development and Justification of Scenarios
Identification of Hazards
Selection and Hazard Screening
Identification of Scenarios
Evaluation of results
Identification of Models and Data Needs
Performing Dose/Risk Calculations
Analysis of Safety Measures
Compare against Assessment Criteria
Analysis of Engineering
Adequate?
Adequate?
Review and Modify
Independent
verification
Accept
Purpose, Regulations, Standards
Engineering Design, Safety Measures,
Other relevant information: Normal operational procedures, Management systems operational experiences, site data
Events, Initiating events,
Expert judgments
Models and Computer codes
Generic, Facility/Activity specific data
Yes
Yes
No
No
Safety Assessment Process

## Slide 13: Formulation and implementation of models
Verify that
conceptual models and data are consistent and appropriate;
conceptual models adequately represent the system and interactions between the components;
software tools adequately solve the problems under consideration;
alternative models, codes and data have been considered
models are adequately verified, validated and calibrated;
reviewer should develop a good understanding of the inputs that have the most influence on the results;
uncertainties and limitations of the models are clearly identified and their impact on the results assessed.
<number>
Notes: <number>
These points should be self-explanatory

## Slide 14: Safety Assessment Process
Assessment Context
Description of Facility or Activity
and Sources
Development and Justification of Scenarios
Identification of Hazards
Selection and Hazard Screening
Identification of Scenarios
Evaluation of results
Identification of Models and Data Needs
Performing Dose/Risk Calculations
Analysis of Safety Measures
Compare against Assessment Criteria
Analysis of Engineering
Adequate?
Adequate?
Review and Modify
Independent
verification
Accept
Purpose, Regulations, Standards
Engineering Design, Safety Measures,
Other relevant information: Normal operational procedures, Management systems operational experiences, site data
Events, Initiating events,
Expert judgments
Models and Computer codes
Generic, Facility/Activity specific data
Yes
Yes
No
No
Safety Assessment Process

## Slide 15: Analysis of results
The review should verify that a thorough understanding of the parameters and processes that govern safety assessment results has been developed;
The safety assessment is consistent with the approach described in the assessment context;
Associated uncertainties have been adequately considered
<number>
Notes: <number>
A key point here is that the safety assessor (i.e. the applicant) needs to develop a thorough understanding of the processes being analyzed. It is not enough simply to perform a set of prescribed calculations in order to demonstrate that the results are below regulatory criteria; the objective of the safety assessment is to reach an understanding of the system features, events and processes that have a significant impact on safety and ensure that remaining hazards and weak points have been adequately addressed and mitigated either in the design or by opeIn terms of top-level issues, the reg rev needs to verify that
The proponent has developed (and presented in his submission) a thorough understanding of the parameters and processes that govern post-closure safety
The SA is consistent with the approach described in the assessment context
Associated uncertainties have been adequately considered and shown to be unimportant - or possibly, the subject of future work
Any regulatory requirements have been complied with
The key areas for further work – additional information, modification of design, scenarios, etc. have been analyzed, identified and justified
rational controls.

## Slide 16: Analysis of results
Compliance with the regulatory requirements;
Assessment philosophy and approach mentioned in the “Assessment Context” have been applied;
The key areas for further work – additional information, modification of design, scenarios, etc. needs to be analyzed and justified.
<number>
Notes: <number>
A key point here is that the safety assessor (i.e. the applicant) needs to develop a thorough understanding of the processes being analyzed. It is not enough simply to perform a set of prescribed calculations in order to demonstrate that the results are below regulatory criteria; the objective of the safety assessment is to reach an understanding of the system features, events and processes that have a significant impact on safety and ensure that remaining hazards and weak points have been adequately addressed and mitigated either in the design or by opeIn terms of top-level issues, the reg rev needs to verify that
The proponent has developed (and presented in his submission) a thorough understanding of the parameters and processes that govern post-closure safety
The SA is consistent with the approach described in the assessment context
Associated uncertainties have been adequately considered and shown to be unimportant - or possibly, the subject of future work
Any regulatory requirements have been complied with
The key areas for further work – additional information, modification of design, scenarios, etc. have been analyzed, identified and justified
rational controls.

## Slide 17: Examples of common deficiencies
Lack of conservatism;
Lack of depth of scenario analysis;
Lack of data integration during the evolution of the facility development;
Conceptual model representation;
Lack of justification;
Lack of documentation.
<number>
Notes: <number>
This is a list of some issues which have been found by experience to be common deficiencies in safety assessments.

## Slide 18
<number>