## Slide 1
Presentation
INDUSTRIAL RADIOGRAPHY
METHODOLOGY FOR DOSE ESTIMATES IN ACCIDENT CONDITIONS.
International Atomic Energy Agency.

## Slide 2: OBJECTIVE
<number>
Example of dose estimates in industrial practice installations during accident conditions.

## Slide 3
The estimations of doses in conditions of accident start from identifying the main scenarios, that because of their probability and the consequences, could happen in extreme conditions. It is recommended to analyze accident scenarios previously occurred.
Dose estimates are required for people who may be affected:
  Occupationally Exposed Personnel.
  Members of the Public.
INTRODUCTION

## Slide 4
Most important scenarios in the practice of Gammagraphy
Blockage of the source of the gammagraphy equipment when the source is exposed.
Loss of a source of Gammagraphy during storage or transportation.
Inadvertent entry of a worker or a member of the public to the controlled area while the source is exposed.
Inadverted permanence of an operator or a member of the public within the controlled area, while the source is exposed.
SCENARIOS

## Slide 5
Generally, there are two different conditions of exposure of the person in this scenario:
The source is in contact with the body (in the hand or in a pocket) during a certain time.
The source is at a distance "d" of the person for a certain time.
Loss of a source of Gammagraphy during storage or transportation.
SCENARIOS

## Slide 6
Fc, Is the conversion factor of the absorbed dose rate, applied to the soft tissue absorbed dose. ( Table 14 y 15 EPR-D-VALUES 2006) (For I-192 Fc = 8.5 10-15 Gy/Bq*s), (For Cs-137 Fc = 5.9 10-15 Gy/Bq*s), (For Am-Be (ᵧ+n) sources ,Fc = 8.9 10-17 Gy/Bq*s)
Tc, Is the period of time the person keeps the source in contact.
A, Is the initial Activity of the source (assuming conservative considerations)
Dose received by the person due to the possession of the source, in contact with the body, during a certain time.
Dc = Fc * Tc * A
DOSE ESTIMATION

## Slide 7
The dose rate by Irradiation can be determined by equation:
  Γ, is the gamma constant for the radioisotope used (Γ for I-192 is 0.135 mSv m2/ GBq h).
  A, is the activity of the source.
  d, is the distance between the source and the person irradiated.
Dose received by people due to placement of the source at a distance "d" from these people, for a certain time.
ir
D = H * T
T, it is the time of permanence of the person under conditions of irradiation.
DOSE ESTIMATION FOR GAMMA SOURCES
The dose received by the person by irradiation “D” is calculated by the equation:

## Slide 8
The total dose received by a person exposed to a source of neutrons includes two fundamental components:
  The dose received by the GAMMA radiation, associated with the ALPHA and GAMMA emitting isotopes, containing the neutron sources.
  The dose due to neutron radiation emitted by these sources.
Dose received by people due to placement of the neutron source at a distance "d", for a certain period of time.
The dose due to GAMMA radiation is estimated in a manner similar to that described above.
DOSE ESTIMATION FOR NEUTRON SOURCES

## Slide 9
The dose rate per neutron can be determined by the following equations:
Øn=A*Ef
H = (Cdn* Øn)/4π(dh)2
Ef, is the efficiency of the ALFA-NEUTRON reaction
Cdn, is the neutron dose coefficient, for neutrons of 5.45 MeV
H, is the dose rate per neutron
dh, is the distance between the neutron source and the exposed person.
Dose received by people due to placement of the neutron source at a distance "d“, for a certain period of time.
D = H * T
DOSE ESTIMATION FOR NEUTRON SOURCES
T, is the time used in the manipulation of the source

## Slide 10
<number>