## Slide 1
Presentation
RADIOTHERAPY
METHODOLOGY FOR DOSE ESTIMATES IN ACCIDENT CONDITIONS.
International Atomic Energy Agency.

## Slide 2: OBJECTIVE.
<number>
Example of dose estimation for a potential accident in Teletherapy practice.
Example of dose estimation for a potential accident in Brachytherapy practice.

## Slide 3
The estimations of doses in conditions of accident start from identifying the main scenarios, that because of their probability and the consequences, could happen in extreme conditions. It is recommended to analyze accident scenarios previously occurred.
Dose estimates are required for people who may be affected:
  Exposed Workers.
  Members of the Public.
INTRODUCTION

## Slide 4
Most relevant scenarios in the teletherapy practice
SCENARIOS. TELETHERAPY PRACTICE
Unnoticed blockage of the source while a patient is treated: Consequences for patients and workers.
Loss of a source during storage or transportation: Consequences for the public.
Wrong calibration of the teletherapy unit: Consequences for patients.
Wrong elaboration of a patient’s treatment plan: Consequences for patients.
Inadvertent entry of a worker or a member of the public into the treatment room: Consequences for the public and workers.
Inadvertent permanence of a worker or a member of the public inside de Bunker while a patient is treated: Consequences for public and workers.

## Slide 5
There are 3 different ways of exposure of a person once an event happens:
1. The person is exposed to the primary radiation beam.
2. The person only receives secondary radiation (leakage radiation from the head of the unit that is scatter to the patient).
3. The person holds the teletherapy source in his hands (Just in cases where the teletherapy source remains in public premises).
EXPOSURE SCENARIOS
Primary barrier
Secondary barrier

## Slide 6
Example 1: Unnoticed blockage of the source while a patient is treated: Consequences for patients and workers.
1. The person is exposed to the primary radiation beam.
The person only receives secondary radiation (leakage radiation from the head of the unit that is scatter to the patient).
EXAMPLE OF DOSE ESTIMATIONS Co-60 UNIT. EXPOSED WORKERS
Primary barrier
Secondary barrier

## Slide 7
The dose rate that a person located at a «d» distance from the equipment source primary beam, can be estimated by the equation:
DHp: dose rate received from the primary beam.
DTTo: dose rate at the isocentre of the unit.
do: distance from the source to the isocentre of the unit .
d: distance from the source to the exposed person.
.
EXAMPLE OF DOSE ESTIMATIONS Co-60 UNIT. EXPOSED WORKERS
1. The person is exposed to the primary radiation beam.
DHp = DTTo (do2/ d2)

## Slide 8
EXAMPLE OF DOSE ESTIMATIONS Co-60 UNIT. EXPOSED WORKERS
The dose received by a person located at a certain distance from the isocenter of the unit, out of the primary beam, is the sum of the received dose due to the scatter radiation in the patient and the radiation leakage from the head of the unit.
The person is exposed to secondary radiation.
DT Total dose.
Df Dose due to the leakage radiation.
Dp Dose due to the scatter radiation.

## Slide 9
EXAMPLE OF DOSE ESTIMATIONS Co-60 UNIT. EXPOSED WORKERS
Both dose contributions can be estimated by the following equations:
Dp – Dose due to the scatter radiation.
Df – Dose due to the leakage radiation.
D – Patient absorbed dose,
dsca – Distance from the radiation source to the patient, in meters,
dsec – Distance from the point of interest to the patient, in meters,
df – Distance from the head of the unit to the interest point, in meters,
α – Scatter fraction defined at the distance dsca. (α(30°)= 3,18E-03 (15MV)= 6,00E-03 (Co-60 1.25 MeV)).
F - Radiation field area affecting the patient, in cm2. It is assumed a typical treatment radiation field size of 15x15 cm
The person is exposed to secondary radiation.

## Slide 10
EXAMPLE OF DOSE ESTIMATIONS Co-60 UNIT. MEMBERS OF THE PUBLIC
Potential accidental doses might vary significantly depending on the particularly initiating event .Three mayor accidental groups can be identified:
Potential doses to patients.
Accidents that cause major dose deviations with respect the prescribed doses (more than 25%) and many patients are affected. This group of accidents can be classified as systematic accidents.
Accidents that cause major dose deviations with respect the prescribed doses (more than 25%) but only one patient is affected. It might cause death and incapacity damage just to the affected patient .This group of accidents can be classified as programmatic accidents.
Accidents that cause moderate dose deviations with respect the prescribed doses (up to 25%). Patient`s life is not at risk. Usually, patient is affected during the treatment session. This group of accidents can be classified as episodic accidents.

## Slide 11
SCENARIOS. BRACHYTHERAPY PRACTICE
Unnoticed blockage of the source while a patient is treated: Consequences for patients and workers.
Unplugging the brachytherapy HDR push cable during patient treatment: Consequences for patients and workers.
Loss of a source during storage or transportation: Consequences for the public.
Wrong calibration of the brachytherapy unit: Consequences for patients.
Wrong elaboration of a patient’s treatment plan: Consequences for patients.
Inadvertent entry of a worker or a member of the public into the treatment room: Consequences for the public and workers.
Inadvertent permanence of a worker or a member of the public inside de Bunker while a patient is treated: Consequences for public and workers.
Most relevant scenarios in the brachytherapy practice

## Slide 12
There are 2 different ways of exposure of a person once an event happens:
The person is exposed to the primary radiation beam from the brachytherapy source. (In brachytherapy, sources emit radiation in all directions, “4¶”)
The person holds the brachytherapy source in his hands.
EXAMPLE OF DOSE ESTIMATIONS BRACHYTHERAPY. EXPOSED WORKERS

## Slide 13
The radiation dose rate that a person receives, located at a «d» distance from the source, can be estimated by the equation:
EXAMPLE OF DOSE ESTIMATIONS BRACHYTHERAPY. EXPOSED WORKERS
1. A person is exposed to primary radiation.
ir
Where:
    Γ is the gamma constant for the radioisotope used (Γ for I-192 is 0.135 mSv m2/ GBq h).
    A is the source activity.
    d is the distance from the irradiation point to the irrradiated person.
D = H * to
where to is the time of exposure.

## Slide 14
EXAMPLE OF DOSE ESTIMATIONS BRACHYTHERAPY. EXPOSED WORKERS
The person holds the brachytherapy source in his hands.
Where:
    Fc is the conversion factor of the absorbed dose rate applied to the soft tissue, in Gy/Bq*s. ( Table #15 EPR-D-VALUES 2006) ( for I-192 Fc= 8.5 e-15 Gy/Bq*s)
    Tc is the time that a person holds the source in his hands.
    A Initial source activity (assuming conservative considerations)
The received dose for holding the source during a determinate period of time can be estimated by the following equation:
Dc = Fc * Tc * A

## Slide 15
<number>