## Slide 1: Standards and Guidance
L 6

## Slide 2: Answer True or False
ICRP recommends a second, speciﬁc level of training in radiation protection for interventional fluoroscopy practices, additional to that undertaken for diagnostic radiology.
ICRP recommends that interventional radiology departments develop a policy that staff should wear two personal dosimeters, one under the apron and the second over the apron.

## Slide 3: Educational Objectives
International Standards & guidance
Who is responsible for what?
What actions are needed by cardiologists?

## Slide 4: Why do we need Standards and Guidance ?
There are radiation effects.
There are principles and methods to avoid radiation injuries and minimize the occurrence of cancer effects.
It is necessary to ensure that these methods are applied.
To make basic requirements mandatory.
To provide advice on how to meet the requirements.

## Slide 5
Basis for
Standards

## Slide 6: The Basis for the International Safety Standards
(*) United Nations Scientific Committee on the Effects of Atomic Radiation
(**) International Commission on Radiological Protection

## Slide 7: Summary of the Presentation
Studying radiation effects: UNSCEAR
Providing basic principles of protection and recommendations: ICRP
Making basic requirements mandatory: The International Basic Safety Standards (BSS)
BSS requirements relevant to interventional Cardiology
Industry standards for equipment (International Electrotechnical Commission)
National and regional approaches (such as USA and EU)

## Slide 8: Radiation effects: UNSCEAR
United Nations Scientific Committee on the Effects of Atomic Radiation

## Slide 9: Radiation Effects: UNSCEAR
UNSCEAR was established by the General Assembly of the United Nations in 1955. Its mandate in the United Nations system is to assess and report levels and effects of exposure to ionizing radiation. Governments and organizations throughout the world rely on the Committee's estimates as the scientific basis for evaluating radiation risk, establishing radiation protection and safety standards, and regulating radiation practices and interventions.

## Slide 11: Principles of Radiation Protection and Recommendations: ICRP
International Commission on Radiological Protection

## Slide 12: Principles and Recommendations on Radiation Protection
The International Commission on Radiological Protection, ICRP, is an independent Registered Charity, established to advance for the public benefit the science of radiological protection, in particular by providing guidance on the fundamental principles on which radiological protection can be based and recommendations on all aspects of protection against ionising radiation.

## Slide 13: ICRP Publications relevant to Interventional Cardiology
ICRP 73 Radiological Protection and Safety in Medicine During 2009 an updated version of this document is expected

## Slide 14: Contents of ICRP 73
Principles of Protection applied to Medicine
  Justification
  Optimization
  Dose Limitation (only for occupational and public, not for patients)

## Slide 15: Radiation and Your Patients: A Guide for Medical Practitioners
Supporting guidance 2

## Slide 16: Contents of Supporting Guidance 2
Is the use of radiation in medicine beneficial?
Are there risks?
What are the radiation-induced effects?
What are the typical doses?
Are there special procedures requiring special justification?
Do children and pregnant women require special consideration?
What can be done to reduce radiation risks?

## Slide 17
ICRP 85 Avoidance of Radiation Injuries from Medical Interventional Procedures
A new document addresed to interventional cardiology is expected to be published during 2008-09

## Slide 18: Contents of ICRP 85
Case reports (radiation injuries)
Radiopathology of skin and eye and radiation risk
Controlling dose
Patient’s needs
Interventionist’s needs
Recommendations
Annexes, including Procurement Checklist

## Slide 19
ICRP 84 Pregnancy and Medical Radiation

## Slide 20: Contents of ICRP 84
Effects of “in-utero” irradiation
Informed consent and understanding
Diagnostic radiology
Nuclear medicine
Radiotherapy
Pregnant physicians and other staff
Consideration of termination of pregnancy after radiation exposure

## Slide 21: ICRP 93
Managing Patient Dose in Digital Radiology

## Slide 22: Contents ICRP 93
Introduction to the technique
Patient dose and image quality
Regulatory aspects
ICRP recommendations for digital radiology
Appendices
  Advantages of digital systems
  Patient dosimetry

## Slide 23: Standards of Safety: IAEA

## Slide 24: IAEA statutory functions related to Radiation Safety
Functions related to radiation safety:
To establish standards of safety for the
protection of health … and to provide
for the application of these standards …
IAEA is an Organization of United Nations
144 Member States
Objectives: promote the contribution of atomic energy to ... health:

## Slide 25: The basis for safety standards

## Slide 26: International
International Basic Safety Standard (BSS)
“…marks the culmination of efforts that have continued over the past several decades towards the harmonization of radiation protection and safety standards internationally”
A new updated version of the BSS is in preparation from 2007

## Slide 27: Medical Exposure
Radiation doses incurred—
By patients as part of their own medical or dental diagnosis or treatment
By individuals (other than those occupationally exposed) knowingly exposed while voluntarily helping patients
By volunteers exposed for biomedical research purposes (must be under approved protocol; usually children may not participate, only exceptionally and for their own diagnosis or treatment)

## Slide 28: Responsibilities
Supervisor
Medical Practitioner
Worker
Principal responsibility for radiation protection
  Legal person subject of authorization (licensee) and employer
Subsidiary responsibilities
Cardiologists

## Slide 29
Cardiologist
Patient Protection
Responsibilities
Advice of qualified expert
Training criteria
Optimization
Equipment design and suppliers
Quality assurance
BSS
Justification

## Slide 30: Responsibilities for Medical Exposure
Medical exposure has to be prescribed by a medical practitioner (e.g., like yourselves)
medical practitioners (yourselves) be assigned the primary task and obligation of ensuring overall patient protection and safety in the prescription of, and during the delivery of, medical exposure

## Slide 31: Responsibility for Medical Exposure
… training criteria be specified or be subject to approval, as appropriate, by the Regulatory Authority in consultation with relevant professional bodies (i.e., cardiology, radiology, interventional cardiology)

## Slide 32: Responsibility for Medical Exposure
… the imaging and quality assurance requirements of the Standards be fulfilled with the advice of a qualified expert in … radiodiagnostic physics
Optimization requirement on equipment design: ensure that whether imported into or manufactured in the country where it is used, the equipment conforms to applicable standards of the International Electrotechnical Commission (IEC) and the ISO or to equivalent national standards;

## Slide 33: Regulations
Promulgated by “national or local authorities”
Should be based on International BSS (standards) and ICRP
Compliance is mandatory
They are usually performance oriented, not too much detail in the regulations
As part of optimization– do the best you can under the prevailing circumstances by maintaining radiation doses from imaging use of radiation as low as reasonably achievable compatible with achieving the expected medical outcome
Notes: Most regulations, guidance, etc. set a minimum, level and should not be considered the goal of good radiation practices. For example, guidance levels and provided in the BSS and in many regulations throughout the world. However, the guidance levels usually represent about the 80th percentile of a dose distribution for that country. Consequently, the guidance levels do not indicate where state-of-the-art facilities are functioning but merely point out those facilities that are using doses which are higher than 80% of the other facilities in that country. State-of-the-art doses are significantly lower than the guidance levels, e.g., half or less of the guidance level.

## Slide 34: Optimization
ensure that the appropriate equipment be used
the medical practitioner, the technologist or other imaging staff select the following parameters, as relevant, such that their combination produces the minimum patient exposure consistent with acceptable image quality and the clinical purpose of the examination, paying particular attention to this selection for paediatric radiology and interventional radiology

## Slide 35: Quality assurance
… shall establish a comprehensive quality assurance programme for medical exposures,
with the participation of appropriate qualified experts in the relevant fields, such as radiophysics
include measurements of the physical parameters of the radiation generators, imaging devices … at the time of commissioning and periodically thereafter

## Slide 36: Limits on Patient Doses?
There are no regulatory limits on the radiation dose a patient may receive
  Question: do you think that the benefit outweighs the risk?
Notes: There are no limits on patient doses. However, one must keep the optimization of protection principle in mind, and the exposure of the patient the minimum necessary to achieve the required objective of the procedure.

## Slide 37: Accidental Medical Exposures
… any diagnostic exposure substantially greater than intended …
Investigation required
  Calculate or estimate doses received
  Indicate corrective measures
  Submit a report
  Inform the patient and his/her doctor about the incident

## Slide 38
Occupational Protection
Responsibilities
Personal protective devices
Individual exposure monitoring
BSS
Pregnant workers
Workplace monitoring
Health surveillance

## Slide 39
Responsibilities of licensees and employers (BSS I.10)
Protection of workers (dose limitation and optimization)
Facilities, protective devices and exposure monitoring
Training of the workers and updating
Rules and supervision of compliance (Possible functions of cardiologists as heads of department ?)
Records

## Slide 40
DOSE LIMIT (1)
Occupational
APPLICATION
Effective dose
Effective dose to the embryo or foetus
Annual equivalent dose in: the lens of the eye
the skin (4)
the hands and feet
The limits apply to the sum of the relevant doses from external exposure in the specified period and the 50-year committed dose (to age 70 years for children) from intakes of radioactive nuclides in the same period.
With the further provision that the effective dose should not exceed 50 mSv in any single year.
In special circumstances, a higher value dose could be allowed in a single year, provided that the average over 5 years does not exceed 1 mSv in any single year.
The limitation on the effective dose provides sufficient protection for the skin against stochastic effects. An additional limit is needed for localised exposures to prevent deterministic effects.
20 mSv per year averaged over defined periods of 5 years (2)
1 mSv
150 mSv 500 mSv 500 mSv

## Slide 41: Pregnant workers
A female worker should, on becoming aware that
she is pregnant, notify the employer in order that
her working conditions may be modified if necessary.
The notification of pregnancy shall not be considered a reason to exclude a female worker from work; however, the employer of a female worker who has notified pregnancy shall adapt the working conditions in respect of occupational exposure so as to ensure that the embryo or fetus is afforded the same broad level of protection as required for members of the public.

## Slide 42
Workers shall:
follow any applicable rules for protection
use properly the monitoring devices and the protective equipment and clothing provided
co-operate with the licensee with respect to protection
...
Responsibilities (BSS I.10)

## Slide 43: Standards for Medical Equipment
International Electrotechnical Commission (IEC)

## Slide 44: IEC
International standards for all electrical, electronic and related technologies. This includes medical equipment
The standards provide performance requirements, specifications, acceptance testing and periodic testing
They are important to you for purchasing and testing

## Slide 45
IEC Standard for interventional equipment (2000)

## Slide 46: WHO publication on Efficacy and Radiation Safety in Interventional Radiology (2000)
World Health Organization
  Clinical aspects
  Radiation safety
  Training
  Equipment

## Slide 47: In summary… what actions are needed from you, as cardiologists?
You have responsibilities for
  the overall protection of patients
  your own protection and that of the staff working under your supervision
  Obtaining the advice of a qualified expert in imaging physics and radiation protection
  Using appropriate equipment
  Quality assurance programme

## Slide 48: In summary… what actions are needed from you, as cardiologists?
You have responsibilities for
  Estimating the radiation doses in your procedures (with advice of qualified expert)
  Arranging patient follow-up if skin doses could be higher than 3 Gy.
Possibly collaborate in writing training criteria, as member of professional bodies, in cooperation with authorities

## Slide 49: Answer True or False
Occupational dose limits also apply when an interventional cardiologist is being examined as a patient.
ICRP states that patients whose estimated skin dose is 3 mGy or greater should be reviewed.
ICRP recommends that patients submitted to complex procedures should be informed about the risk of skin injuries and a clinical follow-up should be foreseen.

## Slide 50: Answer True or False
There are no regulatory limits on the radiation dose a patient may receive.
If an accidental or unintended medical exposures occurs, a report should be prepared but information to the patient and his/her doctor about the incident should be avoided.
The notification of pregnancy shall be considered a reason to exclude a female worker from work in an interventional cardiology laboratory.

## Slide 51: Additional Information

## Slide 52: National and Regional Initiatives

## Slide 53: USA

## Slide 54: FDA Advice (1994)

## Slide 55: RECOMMENDATIONS FOR IR (1994) (1)
Establish standard operating procedures and clinical protocols for each specific type of procedure performed (including consideration of limits on fluoroscopic exposure time).
Knowing the radiation dose rates for the specific fluoroscopic system and for each mode of operation used during the clinical protocol (measurements)
Assess the impact of each procedure's protocol on the potential for radiation injury to the patient.

## Slide 56: FDA RECOMMENDATIONS FOR IR (1994) (2)
Modify the protocol, as appropriate, to limit the cumulative absorbed dose to any irradiated area of the skin to the minimum necessary for the clinical tasks, and particularly to avoid approaching cumulative doses that would induce unacceptable adverse effects.
Use equipment that aids in minimizing absorbed dose.
Enlist a qualified medical physicist to assist in implementing these principles in such a manner so as not to adversely affect the clinical objectives of the procedure.

## Slide 57: FDA RECOMMENDATIONS FOR IR (1994) (2)
Be aware that radiation injuries are not immediately apparent (may appear weeks following the exposure)
Information that permits estimation of skin dose in the patient’s records
Advise patients to report symptoms of radiation injury to their physicians

## Slide 58
Which patients should have such information recorded?.
  When absorbed dose in skin approaches or exceeds a threshold for radiation injury. This assessment should also include consideration of whether the procedure is likely to be repeated.
  Radiation injury to the skin (transient erythema) has been observed at absorbed doses in the skin of about 2 Gy (200 rad).

## Slide 59
What information should be recorded?.
  An unambiguous identification of those areas of the patient's skin that received an absorbed dose that may approach or exceed the selected threshold.
  An estimate of the cumulative absorbed dose to each irradiated area of the skin noted in the patient record or sufficient data to permit estimating the absorbed dose to those areas of skin.

## Slide 61
J Am Coll Radiol 2007;4:272-284.
Copyright © 2007 American College of Radiology

## Slide 62: European Standards

## Slide 63
Article 31 (EURATOM treaty, Chapter 3: Health and safety ):
The basic standards shall be worked out by the Commission after it has obtained the opinion of a group of persons appointed by the Scientific and Technical Committee from among scientific experts, and in particular public health experts, in the Member States. The Commission shall obtain the opinion of the Economic and Social Committee on these basic standards.

## Slide 64
Two relevant Directives have been enacted:
  Council Directive 96/29/Euratom of 13 May 1996 laying down basic safety standards for the protection of the health of workers and the general public against the dangers arising from ionizing radiation.
  Council Directive 97/43/Euratom of 30 June 1997 on health protection of individuals against the dangers of ionizing radiation in relation to medical exposure.

## Slide 65
INTERVENTIONAL RADIOLOGY INCLUDED AS SPECIAL PRACTICE
MED Directive 1997

## Slide 66: Medical Exposures Directive (97/43/Euratom)
Article 9. Special Practices
  Member States shall ensure that appropriate radiological equipment, practical techniques and ancillary equipment are used for the medical exposure involving high doses to the patient, such as interventional radiology.
  Special attention shall be given to the quality assurance programmes, including quality control measures and patient dose.
  Member States shall ensure that practitioners and those individuals entitled to perform the exposure obtain appropriate training on these radiological practices.

## Slide 67: Importance of training
European Guidelines published in 2000.
    Radiologists 30-50 hours
    Cardiologists 20-30 hours
    Other doctors using fluoroscopy X rays systems 15-20 hours
Available at: http://europa.eu.int/comm/environment/radprot