## Slide 1
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
Overview of radiation protection L01

## Slide 2: Summary
We live in the presence of radiation each day
Radiation that can be lethal
Radiation effects
Dose limits
Principles of protection
Application of protection principles in diagnostic radiology
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 3
Is there RADIATION in this room?
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 4
Yes, but not all forms of radiation are harmful!
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 5
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Radiation Spectrum
Notes: <number>

## Slide 6
Only Ionizing radiation is harmful.
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 7: Radiation in Our Environment
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
Natural Radiation: Cosmic rays, radiation within our body, in food we eat, water we drink, house we live in, lawn, building material etc.
Human Body: K-40, Ra-226, Ra-228
e.g. a man with 70 kg wt. 140 gm of K 140 x 0.012%= 0.0168 gm of K-40 0.1 Ci of K-40
24,000 photons emitted/min
(T1/2 of K-40 = 1.3 billion yrs)
<number>

## Slide 8
Forms of Radiation Used in Medicine
Machine produced radiation from X ray tubes used in medical imaging
Linear accelerators used in cancer therapy
Radioactive materials used in nuclear medicine imaging and in some cancer therapy applications.
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 9
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Cosmic Radiation Penetrating the Atmosphere

## Slide 10: Radiation – From Food Sources
Food | Radioactive levels (Bq/kg) |  |  |  | 
 | Daily intake (g/d) | Ra-226 | Th-228 | Pb-210 | K-40
Rice | 150 | 0.126 | 0.267 | 0.133 | 62.4
Wheat | 270 | 0.296 | 0.270 | 0.133 | 142.2
Pulses (legumes) | 60 | 0.233 | 0.093 | 0.115 | 397.0
Other Vegetables | 70 | 0.126 | 0.167 | -- | 135.2
Leafy Vegetables | 15 | 0.267 | 0.326 | -- | 89.1
Milk | 90 | -- | -- | -- | 38.1
Composite Diet | 1370 | 0.067 | 0.089 | 0.063 | 65.0
Normally 1-3 mSv/year
In areas of high background, 3-13 mSv/year
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 11
CAN X RAYS
CAUSE
DEATH?
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 12: The Energy in Drinking Hot Coffee
Excess Temperature = 60º - 37º = 23º
1 sip= 3ml = 3 grams
specific heat of water= 4.18 J per gram per degree
4.18 x 3 x 23 = 288.4 J
4.18 Cal/J
288.4 J/4.18 = 69 calories of energy
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 13: Lethal Dose= 4Sv or 4000 mSV
LD 50/60 = 4 Sv
(For man of 70 kg)
Energy absorbed = 4 x 70 = 280 Joules
= 280/4.18= 67 calories
= 1 sip
X rays
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
https://rpop.iaea.org/RPOP/RPoP/Content/InformationFor/HealthProfessionals/1_Radiology/QuantitiesUnits.htm
Notes: <number>

## Slide 14
DO WE NEED
RADIATION
PROTECTION ?
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 15: What can radiation do?
Death
Cancer
Skin Burns
Cataract
Infertility
Genetic effects
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 16
Dose
Deterministic effects
Cataract
infertility
erythema
epilation
Cancer
Genetic
Prob  dose
500 mSv cataract
150 mSv for sterility (temporary-males)
2500 mSv for ovarian
Effect
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 17
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 18
We live with
1-3 mSv
Can kill
4000 mSv
Radiation
Where to stop, where is the safe point?
What are the effects of radiation?
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 19
We need
protection
from
Radiation Risks
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 20: Two Types of Radiation
Tissue reactions (Deterministic injuries)
Stochastic effects (cancer & genetic effects)
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 21: Tissue reactions (Deterministic)
A deterministic effect of radiation is one that can be predicted and whose severity is proportional to the amount of exposure. An example of this is a radiation skin burn.
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 22: Stochastic Effects of Radiation
A stochastic effect of radiation is one that is random and whose probability of occurrence is known. The degree of the radiation induced effect is not linked to the amount of radiation exposure. An example of this is a radiation induced cancer.
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 23: OBJECTIVES OF RADIATION PROTECTION
PREVENTION of deterministic effect
LIMITING the probability of stochastic effect
HOW? Up to what point?
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 24
OPTIMIZATION
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Deliver only the dose needed to make the diagnosis and no more.
Set X ray control techniques that are unique to each patient based on size.
Only image the body part needed to make the diagnosis by using collimation
An image that needs to be re-taken due to poor quality is a 100% wasted radiation dose.
An image taken with too low X ray exposure risks a false-negative diagnosis thereby put the patient at risk.

## Slide 25
Study of atomic bomb survivors
Low exposures (30 mSv)
Increased risk of malignancy
Shimizu, et al
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 26: Dose Limits (ICRP 60)
Occupational Public
Effective dose 20 mSv/yr averaged* 1 mSv in a yr
over 5 yrs.
Annual equivalent
dose to
Lens of eye 20 mSv*,**
Skin 500 mSv 50 mSv
Hands & Feet 500 mSv
* with further provision that dose in any single year should not exceed 50 mSv
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
**In a recent statement ICRP (Statement on Tissue Reactions Approved by the Commission on April 21, 2011) the ICRP proposed a limit of 20 mSv/yr, averaged over 5 years, not exceeding 50 mSv at any single year.

## Slide 27: Changes in Dose Limit (ICRP) (Safe levels)
mSv
Year
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 28
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
WHAT IS
BASIS FOR
DOSE LIMITS?
<number>

## Slide 29: The Basis for Radiation Protection
PREVENTION of deterministic effect
LIMITING the probability of stochastic effect
Atomic Bomb data show a correlation between radiation exposure and increased cancer risk
Until proven false the linear-no-threshold model of radiation exposure versus risk is a conservative approach for public policy
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 30: The Basis for Radiation Protection
Reductions in radiation exposure are now possible due to advances in new imaging techniques, more advanced radiation delivery devices and a keener sense of public safety
Until proven false the linear-no-threshold model of radiation exposure versus risk is a conservative approach for public policy
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 31: Biological Effects of Ionizing Radiation VII
“At doses below 40 times the average yearly background exposure of 100 mSv, statistical limitations make it difficult to evaluate cancer risk in humans. A comprehensive review of the biology data led the committee to conclude that the risk would continue in a linear fashion at lower doses without a threshold and that the smallest dose has the potential to cause a small increase in risk to humans. This assumption is termed the “linear-no-threshold” (LNT” model.”
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 32
PRINCIPLES
OF
RADIATION
PROTECTION
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 33
Justification of practices
Optimization of protection by keeping exposure As Low As Reasonably Achievable (ALARA)
Dose limits (for occupational, no limit for patient, but reference levels)
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 34
How much time one works with radiation?
RADIOGRAPHY
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 35
Radiation ON Time
Workload=100 exposures/day
Chest X ray = 50x50 m sec = 2500 = 2.5s
Lumbar Spine = 50x800 m sec = 40000=40s
Total time = 45 sec/day
Not greater than 1 min/day
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 36
Staff dose
Dose limit ICRP = 20 mSv/yr
In Radiography  0.1 mS/yr.
i.e. 1/200th of dose limit
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 37
IS IT POSSIBLE TO GET
DETERMINISTIC EFFECTS IN
RADIOGRAPHIC WORK ?
For staff, for patient..??
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 38
Radiography
Risk of
Staff
Patient
Public
Death
Skin burn
Infertility
Cataract
Cancer
Genetic effect
No
No
No
No
U
U
No
No
No
No
U
U
No
No
No
No
U
U
U: unlikely as long as proper procedures are followed
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>
Notes: <number>

## Slide 39
FLUOROSCOPY
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 40: Fluoroscopy
Barium study: 3-6 min/pt x 8 patients/d
=40 min/d
ANGIOGRAPHY
Diagnostic = 50 min/d
Therapeutic = 2-5 hr/d
CT = 10-45 min/d
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 41
Fluoroscopy (excl. ther. angio)
Risk of
Staff
Patient
Public
Death
Skin burn
Infertility
Cataract
Cancer
Genetic effect
No
No
No
No
U
U
No
No
No
No
U
U
No
No
No
No
U
U
U: unlikely as long as proper safety procedures are followed
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>

## Slide 42: Thank you
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L01. Overview of Radiation Protection
<number>