## Slide 1: Radiation Exposure in Gastroenterology L06B
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy

## Slide 2: Objectives
Discuss radiation exposure in gastroenterology
  Doses to patients and staff
  Determinants of that dose
  Methods to reduce exposure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 3
Will not discuss
  Radiology procedures for GI conditions
    Barium enemas, CT, TIPS, nuclear tagged RBC scans
  Radiation therapies
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 4: Fluoroscopy
Uses of fluoroscopy in GI
  Endoscopic retrograde cholangiopancreatography (ERCP)
  Enteroscopy
    Double/single balloon
  Luminal stenting
    Esophagus
    Small intestine
    Colon/rectum
  Luminal stricture dilation
  Colonoscopy
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 5: Most Frequent Use of Fluoroscopy: ERCP
During ERCP, fluoroscopy is primarily used to obtain cholangiograms and/or pancreatograms via the injection of radiopaque contrast into the desired duct.
It may also be employed to aid in cannulation of the duct and during interventions to confirm the position of the diagnostic and therapeutic endoscopic devices.
Trends indicate declining utilization and the move from diagnostic to therapeutic procedures.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 6: Cholangiogram
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 7: Pancreatogram
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 8
In diagnostic cases an average of 74% (4.5 minutes) of the total fluoroscopy time (6.1 minutes) was used to achieve cannulation.
In therapeutic cases 40% of fluoroscopy time was used for cannulation (6.4 of 16.2 minutes).
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Obideen K, Hoteit M, Affronti J, Cai Q. Fluoroscopy Time During Endoscopic Retrograde Cholangiopancreatography. 2005; 61: AB200

## Slide 9: Modern Image Intensifier based fluoroscopy system
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 10: What is dose?
Notes: <number>

## Slide 11: Dose Definitions
In GI, dose can be expressed in several ways:
  Entrance Surface Dose (ESD) - mGy
  Absorbed dose is the energy absorbed per unit mass at a given point. – Gy
  Dose-area Product (DAP) – Gy· cm2 Is the dose emitted by the fluoroscopic equipment
  Equivalent dose to an organ or tissue – Sv
  Effective dose is a quantity defined in ICRP Publication 60 as a weighted sum of equivalent doses to all relevant tissues and organ (“Whole body dose” )
  Fluoroscopy time (FT) – minutes or seconds. Strong correlation with dose and the only endpoint in some studies
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 12: Radiation Effects
X rays cause ionization in the medium through which they pass which can further lead to DNA damage or cell death.
Radiation effects are broadly divided into two categories :
  1) Deterministic effects or tissue reactions such as cataract formation, infertility, skin injury, and hair loss and
  2) Stochastic effects (cancer and genetic effects).
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 13: Radiation Effects
Deterministic effects (primarily cataracts and hair loss) have been documented among interventional radiologists and interventional cardiologists.
There are no reports of such effects in gastroenterologists.
The amount of radiation currently being employed by gastroenterologists is relatively small compared to interventional radiologists or interventional cardiologists
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology

## Slide 14: Dose
What determines dose?
Notes: <number>

## Slide 15: Room setup factors
Type of fluoroscopy unit – Digital vs. conventional
Position of X ray tube “overcouch” vs. “Undercouch”
Height - Distance between the patient and the X ray tube
Distance between the X ray tube and staff
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 16: X ray tube position
Notes: <number>

## Slide 17
All other conditions unchanged, moving patient toward or away from the X ray tube can significantly affect dose rate to the skin
Lesson: Keep the X ray tube at the practicable maximum distance from the patient.
  Inverse Square Law
2 units of intensity
4 units of intensity
16 units of intensity
64 units of intensity
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 18
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Distance between patient and X ray source
<number>
Notes: <number>

## Slide 19: Dose rate dependence field-of-view or magnification mode
INTENSIFIER
Field-of-view (FOV)
RELATIVE PATIENT ENTRANCE DOSE RATE
FOR SOME UNITS
12" (32 cm) 100
9" (22 cm) 177
6" (16 cm) 400
4.5" (11 cm) 700
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06A. Anatomy of Fluoroscopy & CT Fluoroscopy Equipment

## Slide 20: Beam angulation
  Be aware of tube angulations. More oblique beams give higher dose rates.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
D1
D3
D2
D1<D2<D3
Notes: <number>

## Slide 21: Fluoroscopy Beam Settings
X ray beam voltage (kV)
  Higher kV correlates with lower doses
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 22: Fluoroscopy Beam Settings
Pulse vs. continuous
  Reduce output from a continuous beam to 30, 15, or 7.5 images per second with likely reduction in dose-rate.
  Keeping the same pulse intensity, reducing fluoroscopy pulse rate from 30 to 15 pulses/sec will reduce radiation dose to patient by 50%.
Continuous ______________________________________
Pulse fast ||||||||||||||||||||||||||||||||||||||
Pulse slow | | | | | | | | | |
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Singhal A, et al. Gastrointest Endosc. 2006; 63: AB300

## Slide 23: kV setting & Patient Dose Rate
Factors that affect patient dose rate
  kVp: Use the lowest manufacturer’s setting of fluoroscopic dose rates and the highest kVp consistent with maintenance of image quality
  mA
  last image hold
  Be aware of alarm levels for time and higher dose rates in fluoroscopy
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06A. Anatomy of Fluoroscopy & CT Fluoroscopy Equipment

## Slide 24: Fluoroscopy Beam Settings
Tube Current (mA)
  Often not directly manipulated.
  Automatically adjusted in real time with Automatic Brightness Control (ABC)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 25: A word about collimation
What does collimation do?
Collimation confines the X ray beam to an area of the user’s choice.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 26: Collimation
Why is narrowing the field-of-view beneficial?
Reduces stochastic risk to patient by reducing volume of tissue at risk
Reduces scatter radiation at image receptor to improve image contrast
Reduces scatter radiation to in-room personnel
Reduces potential overlap of fields when beam is reoriented
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 27
Collimation to reduce exposure
FOV 15 cm
dose reduction 25% compared to 13 cm FOV
[still]
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Insert GI picture

## Slide 28: Procedure factors
Notes: <number>

## Slide 29: Fluoroscopy Time
Larkin C, et al. Gastrointest Endosc 2001;53:161-164
Screening time (min)
DAP (Gy cm2)
There is a strong positive correlation between fluoroscopy time and radiation exposure and dose
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 30: Procedure Factors
Therapeutic procedures have much higher average fluoroscopy times (FT) and doses than diagnostic cases.
In a study of 28 Patients (21 Therapeutic, 7 diagnostic)
 | Diagnostic | Therapeutic
Mean DAP (Gy cm2) | 13.7 | 41.8
FT (minutes) | 3.1 | 6
Tsalafoutas A, et al. Radiat Prot Dosimetry 2003;106:241-246
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 31: Diagnostic vs. Therapeutic
Uradomo LT, Lustberg ME, Darwin PE. Dig Dis Sci 2006;51:909-914.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 32: Procedure Interventions
Specific interventions are known to increase fluoroscopy time and dose
  Stent insertion
  Stricture Dilation
  Stone extraction
  Lithotripsy
  Needle Knife Sphincterotomy
  Multiple wire use
  Trainee involvement / Lack of experience
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Uradomo LT, Lustberg ME, Darwin PE. Dig Dis Sci 2006;51:909-914.

## Slide 33: Procedure Complexity
Uradomo LT, Lustberg ME, Darwin PE. Dig Dis Sci 2006;51:909-914.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 34: Patient factors
Thickness
Body mass
Medical conditions
Indications
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 35: Typical patient doses
Procedure | Mean dose area product (Gy.cm2) | Mean effective dose (mSv) | Equivalent number of PA chest radiographs (each 0.02 mSv)
ERCP (diagnostic) [HA] | 15 | 3.9 | 195
Percutaneous transhepatic cholangiography (PTC) [HA] | 31 | 8.1 | 405
Bile duct drainage [HA] | 38 | 9.9 | 495
Bile duct stenting [HA] | 54 | 14 | 700
ERCP (therapeutic) [OL] | 90 | 20 | 1000
<number>
[HA] HART, A., WALL, B.F., Radiation exposure of the UK population from medical and dental X-ray examinations. NRPB-W4 (2002)
[OL] OLGAR, T., BOR, D., BERKMEN, G., et. al. Patient and staff doses for some compelx X-ray examinations, J. Radiol. Prot. 29 (2009) 393-407.

## Slide 36: Factors affecting staff doses (I)
The main source of radiation for the staff in a fluoroscopy room is the patient (scattered radiation).
The scattered radiation is not uniform around the patient.
The level of dose rate around the patient is a complex function of a great number of factors.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 37: Factors affecting staff doses (II)
X RAY TUBE POSITION
FACTORS
AFFECTING
STAFF DOSE
HEIGHT OF STAFF
RELATIVE POSITION WITH
RESPECT TO THE PATIENT
IRRADIATED PATIENT VOLUME
kV, mA and time (NUMBER AND
CHARACTERISTICS OF PULSES)
EFFECTIVE USE OF ARTICULATED
SHIELDING AND/OR PROTECTION
GOGGLES
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 38
Scattered dose rate is lower when distance from patient increases
100 kV
11x11 cm
1 mA
mGy/h at 1m
mGy/h at 0.5m
DISTANCE VARIATION
Staff Distance
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 39: Staff exposure
Measurement of radiation at 1 meter from c-arm.
  Unshielded: 2.5-8.3mR per procedure
  Shielding and lead aprons decreased that to 0.04-0.28 mR per procedure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Heyd R, et al. Gastrointest Endosc 1996;44:287-292. Chen M, et al. Gastrointest Endosc 1996;43:1-5

## Slide 40: Staff dose limit recommendations
International Commission on Radiological Protection (ICRP)
20 mSv/year
The dose in any particular year should not exceed 50 mSv and 100 mSv in 5 years.
Based on the calculation of radiation risk over a full working life from the age of 18 years to 65 years (47 years) at the rate of 20 mSv per year
  20x47= 940 mSv (approximately 1 Sv) and resulting in excess cancer risk of 1 in 1000.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology

## Slide 41: Methods to Reduce Exposure
Notes: <number>

## Slide 42: Interventions to Reduce Dose
What can the endoscopist do?
Decrease Fluoroscopy Time
  Limit the “beam-on” time to the shortest necessary to effectively complete the procedure.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 43: Interventions to Reduce Dose
  A Radiation Protection Monitoring Program
    Simply starting a program which makes users aware of doses and tracks data decreased mean fluoroscopy time by 31%
    Record and track time +/- DAP
  Time Alarm/Reminder
    Alarm rings after a predetermined duration of fluoroscopy (5 minutes)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Vehmas T. Hawthorne Effect: shortening of fluoroscopy times during radiation measurement studies. Br J Radiol 1997;70:1053
Uradomo L, et al. Time-limited fluoroscopy to reduce radiation exposure during ERCP: a prospective randomized trial. Gastrointest Endosc 2007;66:84-9.

## Slide 44: Interventions to Reduce Dose
Personal Protection
  Lead Apron with lead equivalence of 0.25-0.5 mm (>90% protection from scattered radiation)
  Leaded upper body shields (>90% protection from scattered radiation)
  Eyewear
  Thyroid
  Effective but not universally utilized
    Thyroid shield 42% “never”
    Eyewear 95% “never”
    Monitor badge 32% “never”
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
  Rajoriya N, Mee A. A UK National Survey into Safety Awareness and Practice in Diagnostic and Therapeutic ERCP. 2008. Gastrointest Endosc; 67: AB231

## Slide 45: Protection tools
CURTAIN
THYROID
SCREEN AND GOGGLES
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
LEAD APRON
Notes: <number>

## Slide 46: Personal dosimetry
Several personal dosemeters are recommended
From: Avoidance of radiation injuries from interventional procedures. ICRP draft 2000
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
20 mSv*
*ICRP Statement on Tissue Reactions. Approved by the Commission on April 21, 2011
Notes: <number>

## Slide 47: Staff protection
Question: Can I work my full professional life with radiation in operating rooms and have no radiation effects?
Yes, with use of good practice and adequate protection from available aprons, shields, eyewear and use of proper technique.
Question: Is the exposure to a gastroenterologist higher or lower than to an interventional cardiologist?
It is lower based on typical workload. Current published data indicate that radiation dose to a gastroenterologist can be substantially lower than that to an interventional cardiologist. Typically the fluoroscopy times in gastroenterological procedures are much lower than in cardiac interventional procedures.
<number>

## Slide 48: Interventions to Reduce Dose
Pulse fluoro mode
Last image hold
Distance
  Inverse Square Law
  Separator Cone
Avoid magnification modes
Use Collimation
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 49: Special Circumstance Pregnancy
Supine position
Uterus Shield
  One study using dosimeters in 15 patients estimated fetal exposure 0.4 mGy1
  More recent study: Monte Carlo normalized conceptus dose data estimated that fetal dose may exceed 10mGy when total DAP surpasses 130 mGy cm2 (range in the study was 62 to 491 mGy cm2) 2
  1. Kahaleh et al. Gastrointest Endosc 2004; 60: 287
  2. Samara E. Therapeutic ERCP and Pregnancy: is the radiation risk for the conceptus trivial? Gastrointest Endosc 2009; 69: 824
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 50: Special Circumstance Pregnancy
The patient's position (supine, prone, or lateral) should be adjusted to minimize fetal exposure.
A posteroanterior projection of the X ray beam results in a fetal dose that is 20% to 30% lower than an anteroposterior projection because of the increased shielding from the mother's tissues.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
https://rpop.iaea.org/RPOP/RPoP/Content/SpecialGroups/1_PregnantWomen/PregnancyAndRadiology.htm
Notes: <number>

## Slide 51: Special Circumstance Children
All recommendations and good practices apply
In children, there is special emphasis to protection of thyroid and the breast in younger females by shielding or beam adjustment wherever feasible.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
https://rpop.iaea.org/RPOP/RPoP/Content/SpecialGroups/2_Children/index.htm

## Slide 52
ERCP PROCEDURES
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology

## Slide 53: Gastroenterology - ERCP Dose & Variability
Endoscopic Retrograde Cholangiopancreatography (ERCP)
NRPB Survey (UK) Published 2000
  28 Hospitals 55 Rooms, 4873 Patients
    Mean fluoroscopy time = 271 sec (4 min 31 sec)
    Mean number films = 4
  Variations in Mean Dose-Area Product (Gy-cm2)
    Mean of all rooms = 15.5 Gy-cm2
    Min = 2 Gy-cm2
    Max = 37 Gy-cm2
  Factor of 18 between min and max
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology

## Slide 54: Typical Variations in Mean Dose -ERCP
NRPB-W14 Doses to Patient from Medical X ray Examinations in the UK – 2000 Review
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology

## Slide 55
Typical dose to ERCP staff
Endoscopist
    In the range of 0,07 mSv per procedure when wearing lead apron
    Dose to eyes around ~ 0,1 to 1,7 mGy per procedure
    Dose to hands around ~ 0,5 mGy per procedure
Assisting personnel
    Few factors lower due more distant position
Mobile lead shield to reduce scatter radiation towards operators
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>
Technical advances in instrumentation last decades added a therapeutic dimension
Estimate doses to both patients and staff and compare to doses from other more common IR procedures.
Remote control fluoroscopy system with the tube above the patient

## Slide 56: Non-ERCP Procedures
Notes: <number>

## Slide 57: Balloon Enteroscopy
Newer endoscopic modality using an overtube with a balloon on the distal end to achieve passage of an enteroscope deep into the small bowel.
Technique initially described using fluoroscopy.
  Fluoroscopy times of 2-3.5 minutes with doses of 155 to 236 dGy cm2
Also used for ERCP in surgically altered anatomy (as in case on left)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 58: Other fluoroscopy-assisted endoscopic techniques
Luminal stents and dilation
  No data on radiation exposure
  Often performed for palliation of unresectable malignancy (stents)
  Growth of indications to benign disease
  Short fluoroscopy times
Fluoroscopic assisted colonoscopy
  Practiced by many endoscopists. Primarily used to assist in completion of a difficult procedure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 59: Other fluoroscopy-assisted endoscopic techniques
The principle of good practice may also be emphasized in these procedures.
  Especially limiting fluoroscopy times
One should make sure that the use of fluoroscopy is necessary to achieve the desired clinical outcome.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 60: Summary
Fluoroscopy is widely used in Gastroenterology
ERCP is the most common and well studied use
Radiation exposure is determined by patient, procedure, equipment, behavioral factors.
Multiple modalities are available to reduce radiation exposure during ERCP.
The principle of ALARA
Exposure in other GI procedures has not been investigated as extensively but good practice is still essential
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology
Notes: <number>

## Slide 61: More information
https://rpop.iaea.org/RPOP/RPoP/Content/InformationFor/HealthProfessionals/6_OtherClinicalSpecialities/gastroenterology/gastroenterology-patient-protection.htm
https://rpop.iaea.org/RPOP/RPoP/Content/InformationFor/HealthProfessionals/6_OtherClinicalSpecialities/gastroenterology/gastroenterology-staff-protection.htm
<number>

## Slide 62: Thank you
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L06B. Radiation Exposure in Gastroenterology