## Slide 1
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
International standards and recommendations L07
Notes: <number>
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Answer True or False
ICRP recommends a second, speciﬁc level of training in radiation protection for interventional fluoroscopy practices, additional to that undertaken for diagnostic radiology.
As a doctor performing fluoroscopic procedures, you rather than the radiation safety officer have the responsibility for radiation safety of the patient.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 3: Educational Objectives
International Standards & guidance
Who is responsible for what?
What actions are needed by doctors who use fluoroscopy?
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 4: Why do we need Standards and Guidance ?
There are radiation effects.
There are principles and methods to avoid radiation injuries and minimize the occurrence of cancer effects.
It is necessary to ensure that these methods are applied.
To make basic requirements mandatory.
To provide advice on how to meet the requirements.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 5
Basis for
Standards
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 6: The Basis for the International Safety Standards
(*) United Nations Scientific Committee on the Effects of Atomic Radiation
(**) International Commission on Radiological Protection
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 7: Summary of the Presentation
Studying radiation effects: UNSCEAR
Providing basic principles of protection and recommendations: ICRP
Making basic requirements mandatory: The International Basic Safety Standards (BSS)
BSS requirements relevant to doctors using fluoroscopy
Industry standards for equipment (International Electrotechnical Commission)
National and regional approaches (such as USA and EU)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 8: Radiation effects: UNSCEAR
United Nations Scientific Committee on the Effects of Atomic Radiation

## Slide 9: Radiation Effects: UNSCEAR
UNSCEAR was established by the General Assembly of the United Nations in 1955. Its mandate in the United Nations system is to assess and report levels and effects of exposure to ionizing radiation. Governments and organizations throughout the world rely on the Committee's estimates as the scientific basis for evaluating radiation risk, establishing radiation protection and safety standards, and regulating radiation practices and interventions.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 10
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 11: Principles of Radiation Protection and Recommendations: ICRP
International Commission on Radiological Protection

## Slide 12: Principles and Recommendations on Radiation Protection
The International Commission on Radiological Protection, ICRP, is an independent Registered Charity, established to advance for the public benefit the science of radiological protection, in particular by providing guidance on the fundamental principles on which radiological protection can be based and recommendations on all aspects of protection against ionising radiation.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 13: ICRP Publications relevant to doctors using fluoroscopy
ICRP 105: RADIOLOGICAL PROTECTION IN MEDICINE
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 14: Contents of ICRP 105
Principles of Protection applied to Medicine
  Justification
  Optimization
  Dose Limitation (only for occupational and public, not for patients)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 15: Radiation and Your Patients: A Guide for Medical Practitioners
Supporting guidance 2
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 16: Contents of Supporting Guidance 2
Is the use of radiation in medicine beneficial?
Are there risks?
What are the radiation-induced effects?
What are the typical doses?
Are there special procedures requiring special justification?
Do children and pregnant women require special consideration?
What can be done to reduce radiation risks?
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 17
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
ICRP 85 Avoidance of Radiation Injuries from Medical Interventional Procedures
<number>

## Slide 18: Contents of ICRP 85
Case reports (radiation injuries)
Radiopathology of skin and eye and radiation risk
Controlling dose
Patient’s needs
Interventionist’s needs
Recommendations
Annexes, including Procurement Checklist
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 19
ICRP 84 Pregnancy and Medical Radiation
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 20: Contents of ICRP 84
Effects of “in-utero” irradiation
Informed consent and understanding
Diagnostic radiology
Nuclear medicine
Radiotherapy
Pregnant physicians and other staff
Consideration of termination of pregnancy after radiation exposure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 21: ICRP 93
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Managing Patient Dose in Digital Radiology
<number>

## Slide 22: Contents ICRP 93
Introduction to the technique
Patient dose and image quality
Regulatory aspects
ICRP recommendations for digital radiology
Appendices
  Advantages of digital systems
  Patient dosimetry
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 23: Standards of Safety: IAEA

## Slide 24: IAEA statutory functions related to Radiation Safety
Functions related to radiation safety:
To establish standards of safety for the
protection of health … and to provide
for the application of these standards …
IAEA is an Organization of United Nations
144 Member States
Objectives: promote the contribution of atomic energy to ... health:
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 25: The basis for safety standards
Consensus of IAEA Member States ...
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 26: International
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
International Basic Safety Standards (BSS)
“The IAEA safety standards reflect an international consensus on what constitutes a high level of safety for protecting people and the environment from harmful effects of ionizing radiation”
The Interim Edition of the new IAEA BSS (2011)
The final edition is expected to be ready in 2012
<number>
Notes: <number>

## Slide 27: Medical Exposure
Exposure incurred
By patients for the purposes of medical or dental diagnosis or treatment
By carers and comforters
By volunteers subject to exposure as part of a programme of biomedical research
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 28: Responsibilities for protection and safety
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
The person or organization responsible for facilities and activities that give rise to radiation risks shall have the prime responsibility for protection and safety. Other parties shall have specified responsibilities for protection and safety
The principal parties responsible for protection and safety are:
(a) Registrants or licensees, or the person or organization responsible for facilities and activities for which notification only is required;
(b) Employers, in relation to occupational exposure;
(c) Radiological medical practitioners, in relation to medical exposure;
(d) Those persons or organizations designated to deal with emergency exposure situations or existing exposure situations..
Supervisor
Medical Practitioner
Worker
Doctor using fluoroscopy
<number>

## Slide 29
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Physician
Patient Protection
Responsibilities
Advice of qualified expert
Training criteria
Optimization
Equipment design and suppliers
Quality assurance
BSS
Justification
<number>

## Slide 30: Responsibilities for Medical Exposure
3.150. Registrants and licensees shall ensure that no patient, whether symptomatic or asymptomatic, undergoes a medical exposure unless:
(a) The radiological procedure has been requested by a referring medical practitioner and information on the clinical context has been provided, or it is part of an approved health screening programme;
(b) The medical exposure has been justified through consultation between the radiological medical practitioner and the referring medical practitioner, as appropriate, or it is part of an approved health screening programme;
(c) A radiological medical practitioner has assumed responsibility for protection and safety in the planning and delivery of the medical exposure as specified in para. 3.153(a);
(d) The patient or the patient’s legal authorized representative has been informed, as appropriate, of the expected diagnostic or therapeutic benefits of the radiological procedure as well as the radiation risks.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 31: Responsibility for Medical Exposure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
2.44. The relevant principal parties and other parties having specified responsibilities in relation to protection and safety shall ensure that all personnel engaged in activities relevant to protection and safety have appropriate education, training and qualification so that they understand their
responsibilities and can perform their duties competently, with appropriate judgement and in accordance with procedures.

## Slide 32: Responsibility for Medical Exposure
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
3.153 Registrants and licensees shall ensure that:
(e) For diagnostic radiological procedures and image guided interventional procedures, the requirements of these Standards for medical imaging, calibration, dosimetry and quality assurance, including the acceptance and commissioning of medical radiological equipment, as
specified in paras 3.166, 3.167(a), 3.167(b), 3.168, 3.169 and 3.170, are fulfilled by or under the oversight of or with the documented advice of a medical physicist, whose degree of involvement is determined by the complexity of the radiological procedures and the associated radiation risks;

## Slide 33: Responsibility for Medical Exposure
3.161. In addition to ensuring that the responsibilities stated in para. 3.49 are discharged, as applicable, registrants and licensees, in cooperation with suppliers, shall ensure that medical radiological equipment, and software that could influence the delivery of medical exposure is used only if it conforms to the applicable standards of the International Electrotechnical Commission and the International Organization for Standardization or to national standards adopted by the regulatory body.
<number>

## Slide 34: Regulations
Promulgated by “national or local authorities”
Based on International BSS (standards)
Compliance with national regulations is mandatory
They are usually performance oriented, not too much detail in the regulations
As part of optimization– do the best you can under the prevailing circumstances by maintaining radiation doses from imaging use of radiation as low as reasonably achievable compatible with achieving the expected medical outcome
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Notes: <number>
Most regulations, guidance, etc. set a minimum, level and should not be considered the goal of good radiation practices. For example, guidance levels and provided in the BSS and in many regulations throughout the world. However, the guidance levels usually represent about the 80th percentile of a dose distribution for that country. Consequently, the guidance levels do not indicate where state-of-the-art facilities are functioning but merely point out those facilities that are using doses which are higher than 80% of the other facilities in that country. State-of-the-art doses are significantly lower than the guidance levels, e.g., half or less of the guidance level.

## Slide 35: Optimization
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Operational considerations
3.162. For diagnostic radiological procedures and image guided interventional procedures, the radiological medical practitioner, in cooperation with the medical radiation technologist and the medical physicist, and if appropriate with the radiopharmacist or radiochemist, shall ensure that the following are used:
  Appropriate medical radiological equipment and software and also, for nuclear medicine, appropriate radiopharmaceuticals;
  (b) Appropriate techniques and parameters to deliver a medical exposure of the patient that is the minimum necessary to fulfil the clinical purpose of the procedure, with account taken of relevant norms of acceptable image quality established by relevant professional bodies and relevant diagnostic reference levels established in accordance with paras 3.147 and 3.168.

## Slide 36: Quality assurance
… shall establish a comprehensive quality assurance programme for medical exposures,
with the participation of medical physicists, radiological medical practitioners, medical radiation technologists and, for complex nuclear medicine facilities, radiopharmacists and radiochemists, and in conjunction with other health professionals as appropriate
include measurements of the physical parameters of medical radiological equipment made by, or under the supervision of, a medical physicist
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 37: Limits on Patient Doses?
There are no regulatory limits on the radiation dose a patient may receive
  Question: do you think that the benefit outweighs the risk?
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Notes: <number>
There are no limits on patient doses. However, one must keep the optimization of protection principle in mind, and the exposure of the patient the minimum necessary to achieve the required objective of the procedure.

## Slide 38: Accidental Medical Exposures
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Accident
Any unintended event, including operating errors, equipment failures and other mishaps, the consequences or potential consequences of which are not negligible from the point of view of protection and safety.
3.179. Registrants and licensees shall promptly investigate any of the following unintended or accidental medical exposures: exposures investigated as required in para. 3.179:
(a) Calculate or estimate the doses received and the dose distribution within the patient;
(b) Indicate the corrective actions required to prevent the recurrence of such an unintended or accidental medical exposure;
(c) Implement all the corrective actions that are under their own responsibility;
<number>

## Slide 39: Accidental Medical Exposures
(d) Produce and keep, as soon as possible after the investigation or as otherwise required by the regulatory body, a written record that states the cause of the unintended or accidental medical exposure and includes the information specified in (a) to (c) above, as relevant, and any other information as required by the regulatory body; and for significant unintended or accidental medical exposures or as otherwise required by the regulatory body, submit this written record, as soon as possible, to the regulatory body, and to the relevant health authority if appropriate;
(e) Ensure that the appropriate radiological medical practitioner informs the referring medical practitioner and the patient or the patient’s legal authorized representative of the unintended or accidental medical exposure.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 40
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
Occupational Protection
Responsibilities
Personal protective devices
Individual exposure monitoring
BSS
Pregnant workers
Workplace monitoring
Health surveillance
<number>

## Slide 41
Responsibilities of licensees and employers (BSS I.10)
Requirement 21: Responsibilities of employers, registrants and licensees for the protection of
Workers Employers, registrants and licensees shall be responsible for the protection of workers against occupational exposure. Employers, registrants and licensees shall ensure that protection and safety is optimized and that the dose limits for occupational exposure are not exceeded.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 42
DOSE LIMIT (1)
Occupational
APPLICATION
Effective dose
Effective dose to the embryo or foetus
Annual equivalent dose in: the lens of the eye
the skin (4)
the hands and feet
The limits apply to the sum of the relevant doses from external exposure in the specified period and the 50-year committed dose (to age 70 years for children) from intakes of radioactive nuclides in the same period.
With the further provision that the effective dose should not exceed 50 mSv in any single year.
In special circumstances, a higher value dose could be allowed in a single year, provided that the average over 5 years does not exceed 1 mSv in any single year.
The limitation on the effective dose provides sufficient protection for the skin against stochastic effects. An additional limit is needed for localised exposures to prevent deterministic effects.
20 mSv per year averaged over defined periods of 5 years (2)
1 mSv
20 mSv 500 mSv 500 mSv
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 43: Pregnant workers
3.114. Notification of the employer by a female worker if she suspects that she is pregnant or if she is breast-feeding shall not be considered a reason to exclude a female worker from work.
The employer of a female worker, who has been notified of her suspected pregnancy or that she is breastfeeding, shall adapt the working conditions in respect of occupational exposure so as to ensure that the embryo or fetus or the infant is afforded the same broad level of protection as is required for members of the public.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 44
3.83. Workers:
(a) Shall follow any applicable rules and procedures for protection and safety as specified by the employer, registrant or licensee;
(b) Shall use properly the monitoring equipment and personal protective equipment provided;
(c) Shall cooperate with the employer, registrant or licensee with regard to protection and safety, and programmes for workers’ health surveillance and programmes for dose assessment;
Requirement 22: Compliance by workers
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 45: Standards for Medical Equipment
International Electrotechnical Commission (IEC)

## Slide 46: IEC
International standards for all electrical, electronic and related technologies. This includes medical equipment
The standards provide performance requirements, specifications, acceptance testing and periodic testing
They are important to you for purchasing and testing equipment
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 47
IEC Standard for interventional equipment (2000)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 48: WHO publication on Efficacy and Radiation Safety in Interventional Radiology (2000)
World Health Organization
  Clinical aspects
  Radiation safety
  Training
  Equipment
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 49: In summary… what actions are needed from you, as a doctor using fluoroscopy?
You have responsibilities for
  the overall protection of patients
  your own protection and that of the staff working under your supervision
  Obtaining the advice of a qualified expert in imaging physics and radiation protection
  Using appropriate equipment
  Quality assurance programme
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 50: In summary… what actions are needed from you, as a doctor using fluoroscopy?
You have responsibilities for
  Estimating the radiation doses in your procedures (with advice of qualified expert)
  Arranging patient follow-up if skin doses could be higher than 3 Gy.
Possibly collaborate in writing training criteria, as member of professional bodies, in cooperation with authorities
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 51: Answer True or False
Occupational dose limits also apply when a spine surgeon is being examined as a patient.
ICRP states that patients whose estimated skin dose is 3 mGy or greater should be reviewed.
ICRP recommends that patients submitted to complex procedures should be informed about the risk of skin injuries and a clinical follow-up should be foreseen.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 52: Answer True or False
There are no regulatory limits on the radiation dose a patient may receive.
If an accidental or unintended medical exposures occurs, a report should be prepared but information to the patient and his/her doctor about the incident should be avoided.
The notification of pregnancy shall be considered a reason to exclude a female worker from work in an interventional cardiology laboratory.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 53: Additional Information

## Slide 54: National and Regional Initiatives

## Slide 55: USA
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 56: FDA Advice (1994)
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 57: FDA RECOMMENDATIONS FOR IR (1994) (1)
Establish standard operating procedures and clinical protocols for each specific type of procedure performed (including consideration of limits on fluoroscopic exposure time).
Knowing the radiation dose rates for the specific fluoroscopic system and for each mode of operation used during the clinical protocol (measurements)
Assess the impact of each procedure's protocol on the potential for radiation injury to the patient.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 58: FDA RECOMMENDATIONS FOR IR (1994) (2)
Modify the protocol, as appropriate, to limit the cumulative absorbed dose to any irradiated area of the skin to the minimum necessary for the clinical tasks, and particularly to avoid approaching cumulative doses that would induce unacceptable adverse effects.
Use equipment that aids in minimizing absorbed dose.
Enlist a qualified medical physicist to assist in implementing these principles in such a manner so as not to adversely affect the clinical objectives of the procedure.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 59: FDA RECOMMENDATIONS FOR IR (1994) (2)
Be aware that radiation injuries are not immediately apparent (may appear weeks following the exposure)
Information that permits estimation of skin dose in the patient’s records
Advise patients to report symptoms of radiation injury to their physicians
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 60
Which patients should have such information recorded?.
  When absorbed dose in skin approaches or exceeds a threshold for radiation injury. This assessment should also include consideration of whether the procedure is likely to be repeated.
  Radiation injury to the skin (transient erythema) has been observed at absorbed doses in the skin of about 2 Gy (200 rad).
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 61
What information should be recorded?.
  An unambiguous identification of those areas of the patient's skin that received an absorbed dose that may approach or exceed the selected threshold.
  An estimate of the cumulative absorbed dose to each irradiated area of the skin noted in the patient record or sufficient data to permit estimating the absorbed dose to those areas of skin.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 62: European Standards

## Slide 63
Article 31 (EURATOM treaty, Chapter 3:Health and safety ):
The basic standards shall be worked out by the Commission after it has obtained the opinion of a group of persons appointed by the Scientific and Technical Committee from among scientific experts, and in particular public health experts, in the Member States. The Commission shall obtain the opinion of the Economic and Social Committee on these basic standards.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 64
Two relevant Directives have been enacted:
  Council Directive 96/29/Euratom of 13 May 1996 laying down basic safety standards for the protection of the health of workers and the general public against the dangers arising from ionizing radiation.
  Council Directive 97/43/Euratom of 30 June 1997 on health protection of individuals against the dangers of ionizing radiation in relation to medical exposure.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 65
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations
HIGH DOSE X RAY PROCEDURES INCLUDED AS SPECIAL PRACTICE
MED Directive 1997
<number>

## Slide 66: Medical Exposures Directive (97/43/Euratom)
Article 9. Special Practices
  Member States shall ensure that appropriate radiological equipment, practical techniques and ancillary equipment are used for the medical exposure involving high doses to the patient, such as interventional radiology.
  Special attention shall be given to the quality assurance programmes, including quality control measures and patient dose.
  Member States shall ensure that practitioners and those individuals entitled to perform the exposure obtain appropriate training on these radiological practices.
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 67: Importance of training
European Guidelines published in 2000.
    Radiologists 30-50 hours
    Cardiologists 20-30 hours
    Other doctors using fluoroscopy X rays systems 15-20 hours
Available at: http://europa.eu.int/comm/environment/radprot
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations

## Slide 68: Thank you
<number>
IAEA Training Course on Radiation Protection for Doctors (non-radiologists, non-cardiologists) using Fluoroscopy
L07. International standards and recommendations