## Slide 1: Radiation Protection in Paediatric Radiology
Quality Assurance
in Paediatric Radiological Procedures
L09
Notes: <number>

## Slide 2: Educational objectives
<number>
At the end of the programme, the participants should appreciate:
  Importance and basic principles of Quality Assurance (QA) and Quality Control (QC)
  Importance of implementation QA in paediatric radiology
  Specific requirements related to QA concepts and radiation protection in paediatric radiology

## Slide 3: Answer True or False
<number>
Quality assurance is important only in large hospitals.
Quality control tests are to be performed every 5 years.
Quality control is related to X-ray generator only.
Diagnostic reference levels are used as dose limits in paediatric radiology.

## Slide 4: Contents
<number>
Quality Assurance Programme: definition, and basic elements
QA management and responsibilities
Quality Control
Outline of a Quality Assurance for paediatric radiology:
  Standards of acceptable image quality
  Retake analysis
  Image quality and patient dose
  Effect of poor-quality images

## Slide 5: Introduction
Equipment used for paediatric radiology:
  well designed
  suited for the purpose for which it is applied
This is best ensured by:
  having a good procurement policy
  good Quality Assurance programme to ensure the equipment continues to be both functional and safe throughout its life

## Slide 6: Introduction
A Quality Assurance (QA) programme in diagnostic imaging aims to ensure quality during all phases of the operation the service
One aspect of such programmes focuses on the operation of equipment, and is required by the BSS, many governments, the EU and recommended by numerous professional bodies
A quality assurance programme may be seen as part of clinical audit and part of the optimization process;
  it is important to ensure that equipment is working properly
  delivering the exposures expected
  compliant with good standards of installation and design

## Slide 7: Introduction
The QA in paediatric radiology does not differ from general radiology besides that children are more sensitive to ionizing radiation and QA is therefore even more important
Yes, we are

## Slide 8: Quality Assurance
<number>
The World Health Organisation defines QA as:
  “An organised effort by the staff operating a facility to ensure that the diagnostic images produced by the facility are of sufficient high quality so that they constantly provide adequate diagnostic information at the lowest possible cost and with the lowest possible exposure of the patient to radiation”
Emphasis is on diagnostic quality not the best quality or pretty images
    Rational use of diagnostic imaging in paediatrics, WHO, Tech report Series 757, 1987
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in Pediatric Radiology

## Slide 9: Quality assurance
QA programs for medical exposures includes:
  Measurements of the physical parameters of the radiation generators and imaging devices at the time of commissioning and periodically thereafter
  Verification of the appropriate physical and clinical factors used in patient diagnosis (or treatment)

## Slide 10: Quality assurance and quality control
QA program ensures that the radiology equipment can yield the desired information. They include:
  Quality control (QC) techniques
  Administrative procedures or management actions to verify that:
    the QC techniques are performed properly and according to a planned timetable,
    the results of these techniques are evaluated promptly and accurately
    the necessary corrective measures are taken in response to these results.

## Slide 11: Administration procedures
Administrative procedures also include:
  the assignment of responsibility for quality assurance actions
  the establishment of standards of quality for equipment in the facility
  the provision of adequate training
  the selection of the appropriate equipment for each examination.

## Slide 12: Quality assurance
General term
Planned and systematic actions to ensure adequate performance of the system
Practical term
Measurements to test the components of the radiological system and to verify that the equipment is operating satisfactorily
Quality control

## Slide 13
<number>
The following parties have roles and responsibilities in QA:
    The Regulatory Authority
    The legal person (Licensee/Hospital)
    Employers
    Medical practitioners
    Qualified experts (e.g. medical physicists, radiation protection officers)
    Manufacturers or suppliers, and other parties with specific responsibilities
Responsibilities

## Slide 14: Talking about quality…
Of a product?
What is a product in diagnostic radiology?
  Image?
  Diagnosis?

## Slide 15: Step by step…
Quality of the final product depends of the quality of each step
Quality control:
  Each step
  Final product

## Slide 16: In diagnostic radiology…
QA and QC provides timely detection of any quality degradation of the final product
In diagnostic radiology:
  Final product is an IMAGE
  Dose to patient is a necessary but minimizable side effect
Quality
=
image of sufficient quality
+
reasonable low dose

## Slide 17: Outline of a QA
System performance
  Patient dosimetry
  Image quality evaluation
  Repeat/Retake analysis
Quality control procedures
  Acceptance test and commissioning
  Constancy tests
  Status tests
  Verification of radiation protection (RP) and QC equipment and material
  Follow up of the corrective actions proposed
Staffing levels and responsibilities

## Slide 18: Outline of QA
Quality audits
Arrangements for individual monitoring and health surveillance
Patient dosimetry and image quality evaluation
Education and training
Safety rules and procedures
Records (authorization certificate)
  Individual staff doses, results of workplace monitoring, quality control test, calibration records, incidents/accidents, training, maintenance.…

## Slide 19: Acceptance test
The acceptance testing of the equipment after installation should be performed by the supplier in presence of the local medical physicist to confirm that the equipment actually performs at the level described in the technical specifications agreed upon by the manufacturer and the purchaser.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in Pediatric Radiology
<number>

## Slide 20: Commissioning
Commissioning is the process of acquiring all the data from equipment that is required to make it clinically usable in a specific department
This commissioning test will give the baseline values for the QC procedures

## Slide 21: How to start ? (I)
Look for past experience in the existing literature
Taking into account the personnel and material available
Define priorities if it is not possible to develop the full program
Look for the usefulness of the actions to be done

## Slide 22: How to start ? (II)
Start with the “basic” quality controls (image quality and patient dose).
Criteria to decide if the results of the controls are good enough (comparison with guidance levels) or if it is necessary to propose corrective actions.
Leave the more difficult controls for a second step!

## Slide 23: Basic advice !
Any action (quality control, corrective action, etc) should be reported and documented, and:
  Should be performed within a reasonable time.
  The reports should be understood and known by radiologists and radiographers.
  The cost of the proposed corrective actions should be taken into account (useless actions should be avoided).

## Slide 24: Organisation of QC
Which tests?
  Does the parameter have an influence on image quality?
  Is it measurable?
  Has it changed over time?
Reference values ?
  Standards, regulations, guidelines, protocols
Frequency of tests?

## Slide 25
Standards and guidelines

## Slide 26: Quality control is…
Repetition of tests
Comparison with reference values

## Slide 27: It is successful, if…
Tests are simple
Easy to perform
Quick
Not expensive…
Given information on diagnostic system used and corrective actions to be set

## Slide 28: Quality control tests
<number>
Regular Quality Control test should
be performed at least annually
or after any major repair that
effect the radiation output of the
device, tube replacement
Annual QC tests should be carried out by a Medical Physicist (or under his/her supervision as appropriate)
More frequent (e.g., weekly, monthly) checks should be carried out by staff in radiology department

## Slide 29: Quality assurance program
QC aspects of a quality assurance program are, not necessarily related to the quality (information content) of the image
There are evidences of production of poor quality images and give unnecessary radiation exposure in radiological departments

## Slide 30: Standards of acceptable image quality
Prior to the initiation of a QC program, standards of acceptable image quality should be established.
Ideally these standards should be:
  Objective, for example “acceptability limits for parameters that characterize image quality”, but they may be
  Subjective for example “the opinions of professional personnel” in cases where adequate objective standards cannot be defined

## Slide 31: Effect of poor quality images
A poor quality image has negative effects:
Practitioners may not have all the possible diagnostic information and this may lead to an incorrect diagnosis
If the quality of the radiograph is so poor that it cannot be used, then the patient shall be exposed again, causing:
  Unnecessary radiation exposure
  An increase in the cost of diagnosis

## Slide 32: Retake analysis
The analysis of retaken images is a basic component of the quality assurance program
Those images judged to be of inadequate quality are categorized according to cause of retake, related to:
  Competence of the technical personnel
  Equipment problems or specific difficulties associated with the examination
  Or combination of these elements
Examples of the main causes of retake:
  Exposure faults
  Bad positioning
  Equipment malfunction…

## Slide 33: Test objects for objective image quality evaluation
Test for QC of monitors and laser printers
Test for QC of geometry in
fluoroscopy
Test for QC of
fluoroscopy system

## Slide 34: Clinical images and quality criteria for image quality evaluation
European Guidelines on Quality Criteria for Diagnostic Radiographic Images in Paediatrics, July 1996.
EUR 16261 EN
Free PDF version available at:
http://www.cordis.lu/fp5-euratom/src/lib_docs.htm

## Slide 35: Quality Criteria List

## Slide 36
Chest

## Slide 37: Dose management
<number>
The purpose of a good radiation protection and dose management programme is to ensure that acceptable diagnostic image quality is achieved on a consistent basis and at the lowest possible dose

## Slide 38: Dose to patient
Dose indicators (see L02 for more information):
  Entrance surface air kerma for simple examinations
  Kerma area product and total number of images and fluoroscopy time for complex procedures
  For some complex interventional procedures, maximum skin dose
  For CT scanner, CTDIvol and the number of slices (also Dose Length Product)
Diagnostic reference levels (DRLs)

## Slide 39: General recommendations for QA in paediatric radiology
<number>
Retake analysis
  The causes of repeating films in paediatrics radiology should be analyzed periodically (retake analysis) as part of the audit program. Also for digital systems. Feedback should be foreseen…
Diagnostic Reference Levels (DRLs)
  Must be established and audits conducted at least annually
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in Pediatric Radiology

## Slide 40: Summary
QA programs thus contribute to the provision of high quality health care
An ongoing QA programme, using the team approach, should be employed
It is essential that the results from QC assessments be integrated into the work of the management of the department, so that the findings are noted and acted on
QA program directed at equipment and operator performance can be of great value in:
  improving the diagnostic information content
  reducing radiation exposure
  reducing medical costs

## Slide 41: Answer True or False
<number>
Quality assurance is important only in large hospitals.
Quality control tests are to be performed every 5 years.
Quality control is related to X-ray generator only.
Diagnostic reference levels are used as dose limits in paediatric radiology.

## Slide 42: Answer True or False
<number>
False - Quality assurance is important in all practices including radiology.
False - Quality control tests must be performed as per frequency determined by professional bodies which may be daily, weekly, quarterly or annually by the medical physicist and wherever applicable by the radiographer.
False - Quality control applies to the entire imaging chain and process.
False – The concept of Diagnostic reference levels is not same as limits. They should be used with flexibility whether in adult or children.

## Slide 43: References
<number>
THE INSTITUTE OF PHYSICS AND ENGINEERING IN MEDICINE, Recommended Standards for the Routine Performance Testing of Diagnostic X-ray Imaging Systems, IPEM Report 91, York, UK, (2005)
AMERICAN ASSOCIATION OF PHYSICISTS IN MEDICINE, Acceptance Testing and Quality Control of Photostimulable Storage Phosphor Imaging Systems, Report of AAPM Task Group 10, AAPM Report No. 93, College Park, MD, USA, (2006)
NATIONAL COUNCIL ON RADIATION PROTECTION AND MEASUREMENTS, Quality Assurance for Diagnostic Imaging, NCRP Report No. 99, NCRP, Bethesda, MD, (1988)
EUROPEAN COMMISSION, European Guidelines on Quality Criteria for Diagnostic Radiographic Images in Paediatrics, Rep. EUR 16261, Office for Official Publications of the European Communities, Luxembourg Communities, Luxembourg, (1996)
COOK, V., Radiation protection and quality assurance in paediatric radiology, Imaging, 13 (2001) 229–238
EUROPEAN COMMISSION, Guidelines on Education and Training in Radiation Protection for Medical Exposures. Radiation Protection 116, Office for Official Publications of the European Communities, Luxembourg, (2000).

## Slide 44: References
<number>
EUROPEAN COMMISSION. Criteria for Acceptability of Radiological (including radiotherapy) and Nuclear Medicine Installations, Radiation protection 91, Office for Official Publications of the European Communities, Luxembourg, (1997).
INTERNATIONAL ELECTROTECHNICAL COMMISSION, Medical Electrical Equipment — Part 2–43: Particular Requirements for the Safety of X-ray Equipment for Interventional Procedures, Rep. IEC-60601-2-43, IEC, Geneva, (2000).
INTERNATIONAL ELECTROTECHNICAL COMMISSION, X-ray Tube Assemblies for Medical diagnosis: Characteristics of Focal Spots, Rep. IEC-60336, IEC, Geneva (1993).
INTERNATIONAL ELECTROTECHNICAL COMMISSION, Determination of the Permanent Filtration of X-ray Tube Assemblies, Rep. IEC-60522, IEC, Geneva (2003).
INTERNATIONAL ELECTROTECHNICAL COMMISSION, Medical Electrical Equipment — Part 1: General Requirements for Safety — 3. Collateral Standard: General Requirements for Radiation Protection in Diagnostic X-ray Equipment, Rep. IEC-60601-1-3, IEC, Geneva (1994).
INTERNATIONAL ELECTROTECHNICAL COMMISSION, Medical Electrical Equipment — Part 2–7: Part 2: Particular Requirements for the Safety of High-Voltage Generators of Diagnostic X-ray Generators, Rep. IEC-60601-2-7, IEC, Geneva (1998).