## Slide 1: Radiation Protection in Paediatric Radiology
Why Talk About Radiation Protection during Radiological Procedures in Children
L01
Notes: <number>

## Slide 2: Educational Objectives
<number>
At the end of the programme, the participants will:
Understand radiation effects in paediatric radiology
Learn potential risk from the use of ionising radiation in paediatric radiology
Be familiar with measures to control the risk
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 3: Answer True or False
<number>
There is a precise threshold for stochastic effects.
For deterministic effects of radiation, the severity of the effect increases with dose.
Radiation risk in children is 2-3 times lower than in people above 45 years.
Skin injuries and lens opacities are deterministic effects of radiation.
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 4: Contents
<number>
Medical imaging benefits for pediatric patients
Benefit risk ratio
Biological effects of ionizing radiation
  Stochastic ( eg carcinogenesis)
  Deterministic
Magnitude of radiation exposure in paediatric radiology
Potential consequences of radiation exposure in paediatric radiology
Models used to discuss effects of radiation
  LNT model
Epidemiological evidence for biological effects
Application of radiation protection principles
  Justification
  Optimisation
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 5: Introduction
Paediatric radiology involves imaging those with the diseases of childhood and adolescence
Children undergoing these examinations require special attention:
  There are specific diseases unique to childhood
  Children need age-appropriate care when performing the exam
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 6: How does medical imaging help children ?
<number>
Medical imaging can help doctors and other medical professionals
save children’s lives by diagnosing disease and injury.
These imaging tests can reduce the need surgical intervention
and shorten hospital stays.
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 7
COST
BENEFIT
It is important to weigh the benefit of the exam against the potential risk
of performing the test for the child.
This presentation discusses
potential risks when performing medical imaging that uses ionizing radiation in children.
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 8: Introduction
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Children are of special concern in radiation protection:
  Higher radiation sensitivity
  Longer life expectancy
  Identical settings provide higher organ doses than in adults
More susceptible to radiation damage
The number of imaging tests using ionizing radiation
are increasing around the world !!! And….

## Slide 9
<number>
Radiation exposure of different organs and tissues in the body results in different probabilities of harm and different severity of radiation effect
The combination of probability and severity of harm is called “detriment”
In young patients, high organ doses may increase the risk of radiation-induced cancer in later life
What can ionizing radiation do?
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Notes: <number>

## Slide 10: Radiation risk is a complex topic
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
One cannot see radiation
Some effects may take decades to appear
Risk to a group of patients can be estimated and numbers like 1:1000 apply to a group rather than to an individual
Radiation risk is a small further addition to the natural incidence of about 20%

## Slide 11: Two types of radiation effects
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Stochastic effects
  Where the severity of the result is the same but the probability of occurrence increases with radiation dose, e.g., development of cancer
  There is no threshold for stochastic effects
  Examples: cancer, hereditary effects
Deterministic effects
  Where the severity depends upon the radiation dose, e.g., skin burns
  The higher the dose, the greater the effect
  There is a threshold for deterministic effects
  Examples: skin burns, cataract
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 12: What can ionizing radiation do? General Effects
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Cancer
Genetic effects
Skin injuries
Cataracts
Infertility
Death
Other: such as cardiovascular effects
NB. In this lecture, we shall predominantly deal with cancer

## Slide 13: Radiation effects
<number>
Epidemiology
Stochastic
Tissue reactions
Biology
Probability
Certainty
(100%)
Dose (mSv)

## Slide 14: Thresholds for tissue effects in the adults (ICRP 103)
Tissue and effect | Threshold | 
 | Total dose in a single exposure (Gy) | Annual dose if the case of fractionated exposure (Gy/y)
Testes Temporal sterility Permanent sterility | 0.15 3.5-6.0 | 0.4 2.0
Ovaries Sterility | 2.5-6.0 | >0.2
Lens Detectable opacity Cataract | 0.5-2.0 5.0 | >0.1 >0.15
Bone marrow Depression of hematopoesis | 0.5 | >0.4
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 15
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
IS IT POSSIBLE TO GET
DETERMINISTIC EFFECTS IN
DIAGNOSTIC RADIOLOGY?
For staff, for patients..??

## Slide 16
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Paediatric radiology
Risk of
Staff
Patient
Death
Skin burn
Infertility
Cataract
Cancer
Genetic effect
×
×
×
×
S
S
×
×
×
×
S
S
S: small
x: not possible
UNSCEAR 2000:
Average worldwide patient dose: 0.4 mSv/procedure
Annual number of procedures: 330/1000 population
Average occupational dose in radiology: 0.5 mSv/y

## Slide 17: How does one determine probability of cancer?
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>

## Slide 18: Radio-sensitivity
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Probability of a cell, tissue, or organ suffering an effect per unit dose
Will be greater if the cell:
  Is highly mitotic
  Is undifferentiated*
Children’s cells divide rapidly and organs
may be less differentiated than an adult, so
they are more radiosensitive.
*there are exceptions, as stem cells
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 19: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Linear no threshold (LNT) model is internationally agreed upon as the most appropriate dose-response relationship for radiation protection purposes
There are sound biophysical arguments supporting the LNT model
But, one should be aware that true low dose experiments at cellular level are very difficult and are a work in progress
In other words, we do not know if low level (eg range of CT) medical radiation increases cancer risk. But we should act conservatively to lower dose to be safe.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 20: LIFE SPAN STUDY Atomic Bomb Survivors
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Detriment adjusted nominal risk coefficient:
5.5% per Sievert (1000 mSv)*
for the whole population
! Note: The probability applies to a group of people and is not suitable for an individual case
*ICRP 103

## Slide 21
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Children are more sensitive to radiation compared to adults

## Slide 22: Hereditary effects
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Effects observed in offspring born after one or both parents had been irradiated prior to conception
Study on descendants of Hiroshima and Nagasaki survivors:
  no statistically significant increase in abnormalities were detected

## Slide 23
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
A cohort of 31,150 children born to parents who were within 2 km of the hypocenter at the time of the bombing was compared with a control cohort of 41,066 children:
No indicator was significantly modified by parental radiation exposure.
Why so much fuss
about genetic effects?
Hereditary effects

## Slide 24
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
In the absence of human data the estimation of hereditary effects is based on animal studies.
Hereditary effects

## Slide 25: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
What is the magnitude of
radiation used in paediatric
radiology?
  Magnitude of the radiation used in paediatric imaging should be less than in an adults
  The associated risk for equal exposures is greater due to the size, age and radio-sensitivity of paediatric organs/tissue
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 26: Effective dose and potential lifetime risk of cancer for a 5 year old child from common procedures
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
5 year old child |  | 
Natural incidence | 1 in 5 | 
Radiography | Effective dose (mSv) | Risk
Chest (PA) | 0.01 | 1 in 1 million
Abdomen (AP) | 0.12 | 1 in 80 000
Pelvis (AP) | 0.08 | 1 in 120 000
Martin CJ and Sutton DG (2002), Practical Radiation Protection In Health Care, Oxford Press
This does not mean that any one child will get cancer from a single X-ray. It applies to populations of patients.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 27: Radiation risk in paediatric radiology - CT dose for various ages
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
  UNSCEAR, 2008
Parameter | CT examination | <1 year | 5 years | 10 years
Dose-length product (mGy cm) | Head Chest Abdomen | 300 200 330 | 600 400 360 | 750 600 800
Effective dose (mSv) | Head Chest Abdomen | 1.3-2.3 1.9-5.1 4.4-9.3 | 1.5-2.0 3.1-7.9 9.2-14 | 2.8 3.0 3.7
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 28
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Is there RADIATION RISK from being a health care worker using radiation?

## Slide 29: Radiation risk in perspective
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
We are all exposed to radiation from the sun, rocks and food and other natural resources.
Average background
3 mSv/year
http://www.hpa.org.uk/web/HPAwebFile/HPAweb_C/1194947388410
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 30: How much radiation is used in paediatric radiology examinations compared to other exposures?
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
 | Estimated dose | Days of background radiation
Natural background | 3 mSv/year | 1 day
Airline passenger | 0.04 mSv | 4 days
Chest X-ray | 0.01 mSv | 1 day
Head CT | 2 mSv | 8 months
Chest CT | 3 mSv | 12 months
Abdominal CT | 5 mSv | 20 months
Angiography or venography | 11-33 mSv | 4-11 years
CT guided intervention | 11-17 mSv | 4-6 years
www.imagegently.org

## Slide 31: We all exposed to risks on a daily basis even when riding in a car or plane
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
What are the risks from
medical radiation?
Risk from abdominal CT scan
is equivalent to:
Risk of accident when driving 12 000 km

## Slide 32
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>

## Slide 33: Radiation ON Time
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Workload=100 exposures/day
Chest X-Ray = 50x50 ms = 2500 ms = 2.5 s
Lumbar Spine = 50x800 ms = 40000 ms =40 s
Total time = 45 s/day
Not greater than 1 min/day

## Slide 34
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Staff Doses
Dose limit (ICRP) = 20 mSv/year
Radiography < 0.1 mSv/year
i.e. 1/200th of dose limit

## Slide 35: What are the risks from medical radiation?
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
The risk of developing cancer should be evaluated against the statistical risk for developing cancer in the entire population
The overall risk of a cancer death over a person’s lifetime is estimated to be 20%
  For every 1,000 children, 200 will eventually die of cancer even if never exposed to medical radiation
The additional risk from a single CT scan is controversial, but estimated to be a fraction of this risk (0.03-0.05%)
Problem: cumulative effect of repeated examinations
Frush D, et al, CT and Radiation Safety: Content for Community Radiologists
www.imagegently.org

## Slide 36: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Public Health Risk
  The main issue from a
  public health perspective
  is the “potential problem
  that accumulates when
  a risk that is acceptable
  to the individual is multiplied
  by the 2.7 million procedures
  performed each year in children”
  Hall EJ, Lessons we have learned from our children: cancer risks from diagnostic radiology, Pediatr radiol (2002) 32: 700-706
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 37: Benefit versus Risk
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Ionising radiation dose carry with it an increased risk of malignant disease
However, the overall benefit to the person should be much greater than the risk from the ionising radiation
The general health, quality and longevity of life of the population would decrease without the diagnostic capabilities of ionising radiation imaging systems !

## Slide 38: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Epidemiological studies provide the best evidence to date regarding the risks of radiation inducing cancer in an exposed population
Problem is that these studies do not have sufficient statistical power especially at low radiation doses
Therefore it is unclear what are the effects at doses of less than 50-100mSv
Cellular and biological studies provide some insight but have limitations and are not always reproducible
Also one cannot directly infer radiation-induced carcinogenesis in these experiment to humans
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 39: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Multiple X-ray examinations can occur on the same patients (dose comparable with the dose to atomic bomb survivors)
And, we are not certain yet about the effect of low doses
  Cohen BL, Review, Cancer Risk from Low-Level Radiation AJR 179 (5): 1137. (2002)
  Upton AC, The state of the art in the 1990’s: NCRP Report No 136 on the scientific bases for linearity in the dose-response relationship for ionizing radiation, Health Physics. 85(1):15-22, July 2003.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 40: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
The risk associated with the chance of developing a fatal cancer from radiation exposure in children is higher then in adults
Special needs for children can often be addressed at dedicated paediatric care centers or other centers with pediatric imaging expertise
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 41: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Examination | Effective dose (mSv) | Lifetime risk of fatal cancer
Limbs | <0.005 | 1/a few million
Chest (PA) | 0.01 | 1/million
Spine (AP, PA, Lat) | 0.07 | 1/150000
Pelvis | 0.08 | 1/120000
AXR | 0.10 | 1/100000
MCU | 1.0 | 1/10000
CT Head | 2 | 1/5000
CT Body | 10 | 1/1000
Cook JV, Imaging, 13 (2001), Number 4
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 42: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
But because of their smaller size radiation dose should be lower since the risk is higher!
In certain case such as CT and some of the newer digital radiographic systems doses can exceed adult doses if techniques are not optimized to children.
As a simplification, consider the risk-numbers for paediatric radiology to be 2-5 times higher than for adults !
So, how we control the risk?

## Slide 43
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Justification of practices
Optimization of protection by keeping exposure as low as reasonably achievable
Dose limits for occupational exposure
Principles of radiation protection

## Slide 44: Objectives of radiation protection
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Prevention of tissue reactions (deterministic effect)
Limiting the probability of stochastic effect

## Slide 45
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
HOW DO WE APPLY
THESE PRINCIPLES IN
PAEDIATRIC RADIOLOGY?

## Slide 46: Radiation risk in paediatric radiology
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Health benefits:
  Let us not forget that radiological imaging provides significant benefits to the health care of the population
  Therefore we have to reduce the risk to a minimum by strict adherence to justification, optimisation, essentially the ALARA principle in both adult and paediatric imaging
  As the dose and risk increases
  benefits should be greater
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 47: Justification
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Process in which the referring health care provider and radiologist make a decision as to whether the examination is clinically indicated and whether the benefits outweigh the likely radiation risks
There are estimates that a significant fraction of paediatric examinations are unjustified
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 48: Justification
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Tools to help improve justification:
  Use of evidence based referral guidelines and local protocols
  Use of clinical audit of justification (including appropriateness of examinations)
Examinations will only be conducted when appropriate and necessary
When available, alternative techniques such as ultrasound and MRI will be used
Pay attention to previous procedures and the information available from the referring practitioner, the patient and their family

## Slide 49: Optimisation
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
ALARA principle states that dose should be kept As Low As Reasonable Achievable
But not to the extent that compromises diagnostic image quality
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 50: Optimisation
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
All persons directing and conducting medical radiation exposure of children, including radiologists and technologists, should have received recognised education and training in their discipline, including radiation protection, and specialist training in its paediatric aspects
Radiological equipment shall be in accordance with international standards
A team approach to each stage should be taken
All examinations should be conducted using “child sized” protocols/exposures

## Slide 51: How to control the risk in paediatric radiology?
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Practical advice:
Perform examination only when medical benefit is appropriately high
Tailor examination parameters to size of the child – to use minimal possible amount of radiation
Image only indicated area
Avoid repeated examinations and multiple phase scans
Consider use of alternative modalities (US, MRI)
Personnel, radiologists and technicians must be specially trained in paediatric diagnostic imaging

## Slide 52: Radiation risk in paediatric radiology
<number>
Every Radiology Department should have information for parents
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 53: Summary
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Increasing numbers of radiological examinations are being performed in infants and children
Children are more radiosensitive than adults
They have longer life expectancy
  higher probability of developing cancer
Radiation protection principles are applied to minimise probability for stochastic effects and prevent occurrence of tissue reactions
All paediatric examination most be justified and optimised
They should be planned taking into account the size and age of the patient
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection in paediatric Radiology

## Slide 54: Answer True or False
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
There is precise threshold for stochastic effects.
For deterministic effects of radiation, the severity of effect increases with dose.
Radiation risk in children is 2-3 times lower than in people above 45 years.
Skin injuries and lens opacities are deterministic effects of radiation.

## Slide 55: Answer True or False
False- International organizations agree that with current state of knowledge the linear non-threshold theory is valid.
True- Higher dose, more cell are killed and more is severity.
False - It is opposite, children have longer life expectancy and more developing tissues that have higher radio- sensitivity.
True–They require significant number of killed/malfunctioning cell.
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology

## Slide 56: References
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Cook JV, Radiation protection and quality assurance in paediatric radiology, Imaging, 13 (2001),229-238
Cohen BL, Review, Cancer Risk from Low-Level Radiation AJR 179 (5): 1137. (2002)
Don S, Radiosensitivity of children: potential for overexposure in CR and DR and magnitude of doses in ordinary radiographic examinations, Pediatr radiol (2004) 34(Suppl 3): S167-S172
European Guidelines on Quality Criteria for Diagnostic Radiographic Images in Paediatrics, July 1996. EUR 16261. Available at: http://www.cordis.lu/fp5-euratom/src/lib_docs.htm
Hall EJ, Lessons we have learned from our children: cancer risks from diagnostic radiology, Pediatr radiol (2002) 32: 700-706
Martin CJ and Sutton DG (2002), Practical Radiation Protection In Health Care, Oxford Press

## Slide 57: References
Radiation Protection in Paediatric Radiology L01. Why talk about radiation protection in paediatric radiology
<number>
Mettler FA, Wiest PW, Locken JA, Kelsey CA (2000) CT scanning patterns of use and dose. J Radiol Pro 20:353-359
Persliden J, Helmrot E, Hjort p and Resjö M, Dose and image quality in the comparison of analogue and digitasl techniques in paediatric urology examinations. Eur Radiol, (2004) 14:638-644
Shrimpton PC, Edyvean S (1998) CT scanner dosimetry. BJR 71:1-3
Suleimam OH, Radiation doses in paediatric radiology: influence of regulations and standards, Pediatr Radiol (2004) 34(Suppl 3): S242–S246
Wall BF, Kendall GM, Edwards AA, Bouffker S Muirhead CR and Meara JR, What are the risks from medical X-rays and other low dose radiation?, BJR, 79 (2006), 285-294
Vock P, CT dose reduction in children, Eur Radiol (2005) 15: 2330-2340