## Slide 1: L 8
STAFF AND PUBLIC DOSES

## Slide 2: Answer True or False
Typical annual whole body staff doses are about the same for occupationally exposed workers at conventional Nuclear Medicine facilities as at PET/CT facilities
PET/CT staff members can minimize their dose by minimizing time, maximizing distance and maximizing shielding in all instances involving radioactive sources
Following a patient undergoing a PET/CT examination, it is important that children, relatives and friends have no contact with the patient for at least 24 hours following the scan

## Slide 3: Objective
Consideration of staff doses received from PET/CT and how the basic principles of radiation protection can be used to minimize them: pregnant staff, visitors to the unit and friends and relatives of the patient

## Slide 4: Content
Staff doses
Reduction of staff doses
Visitors
Relatives and friends

## Slide 5
8.1 Typical Staff Doses

## Slide 6: Staff Doses – Cyclotron Unit
Fully automated production system
  No whole body doses
Dose received from
  Maintenance of cyclotron
  QC of FDG
  Typically 0.1 mSv/month

## Slide 7: Dose Limits set by ICRP (International Commission on Radiation Protection)
* Averaged over 5 years and not more than 50 mSv in any 1 year
 | Occupational | Public
Effective Dose (mSv/y) | 20* | 1
Equivalent Dose (mSv/y) to: |  | 
Lens of eye | 150 | 15
Skin | 500 | 50
Hands and Feet | 500 | -

## Slide 8: Dose to Worker per Typical 18F-FDG Scan
0
0,5
1
1,5
2
2,5
Dispensing
Injection
Examination
Dose (uSv)
Whole body scan
370 MBq FDG
Measured in a well-designed unit
Notes: Measurements of this kind can show different results in different hospitals

## Slide 9: PET/CT Staff Whole Body Doses
Average PET/CT whole body doses (in a well designed facility):
  Initial measuring of vial 2 µSv
  Dispensing and injection 2-4 µSv/patient
  Positioning patient/scan 1-2 µSv/patient
For mobile/non dedicated PET unit the whole body dose increase due to dispensing/injecting is at least 3-6 µSv/patient
Escorting patient to toilet and scanner room
  5-10 µSv/patient

## Slide 10: Typical Annual Whole Body Staff Doses
PET/CT | <6 mSv
Nuclear medicine | 0.1 mSv
Radiochemist | 1 mSv

## Slide 11: Technologist Dose per Procedure (µSv)
Chiesa et al, Eur J Nucl Med 1997: 24: 1380 - 1389
WB Tc-99m bone scan | 0.3 ± 0.2
Tc-99m MIBI SPECT | 1.7 ± 0.2
I-131 at 4 d post Rx | 0.2 ± 0.2
WB FDG | 5.9 ± 1.2

## Slide 12: Important Note:
Escorting patient to toilet and scanner room
  5-10 µSv/patient
Essential that facility design is such that staff DO NOT accompany ambulatory patients to either the toilet or the scanning room

## Slide 13: PET/CT Staff Finger Doses
Dose varies considerably depending on where the finger monitor is worn
Dose measured using finger stall on index finger (tip of finger) is 2-5 times great than reading using finger ring on index finger

## Slide 14: Finger Doses Measured Depends on with Position Worn (FDG)
Monthly dose
2.1 mGy
8.0 mGy
0.39 mGy

## Slide 15: Monthly Finger Doses (mSv/GBq handled)
PET/CT (finger stall, TLD at tip of index finger) | 1.4
Nuclear medicine (finger stall, TLP at tip of index finger) | 0.04
Radiopharmacy (finger stall, TLD at tip of index finger) | 0.006
Radiochemist | 0.3

## Slide 16
8.2 Reduction of Staff Doses

## Slide 17: Reduction of Staff (and Public) Doses
Good facility design
Good practice
Basic radiation protection principles (distance, shielding and time)
Use of protective equipment

## Slide 18: Distance
distance
dose-rate
Dose-rate  1/(distance)2
Inverse square law (ISL):

## Slide 19: Practical Measures to Reduce Staff Doses
Use long-handle forceps or tongs
Don’t walk next to ambulatory patient unless they need support
Use intercom to communicate with the patient if possible
Use CCTV to observe patient in waiting area and camera room
Use separate rest areas
Do not operate the camera from gantry controls while standing next to patient

## Slide 20: Shielding
incident
radiation
transmitted
radiation
Barrier thickness

## Slide 21: Practical Issues
Syringe shields
Carry (shielded) syringe to patient in additional shielding
Shielded dispensing unit
Additional lead L block

## Slide 22: Time
Dose is proportional to the time exposed
Dose = Dose-rate x Time

## Slide 23: Practical Issues
Reduce time in contact with radiation sources as much as possible compatible with the task
Practice rapid dose-dispensing
Calculate volume required before drawing up
Confirm ID of patient (name, date of birth and address) before administration
Explain to patient what is happening before giving the FDG
Cannula or butterfly for venous access
Optimize injection procedure

## Slide 24: Accompanying Nursing Staff
Nurse providing high dependency care may receive 0.1 mSv from a single patient
May need to monitor staff if large throughput from single high dependency unit

## Slide 25: Pregnant Staff
Should notify the employer that she is pregnant
Risk assessment
1 mSv during remainder of pregnancy
ALARP (As Low as Reasonable Practicable)
  may need to re-assign duties

## Slide 26
8.3 Visitors

## Slide 27: Control of Visitors
BSS III.5. Registrants and licensees, in co-operation with employers when appropriate, shall:
(a) ensure that visitors be accompanied in any controlled area by a person knowledgeable about the protection and safety measures for that area;
(b) provide adequate information and instruction to visitors before they enter a controlled area so as to ensure appropriate protection of the visitors and of other individuals who could be affected by their actions; and
(c) ensure that adequate control over entry of visitors to a supervised area be maintained and that appropriate signs be posted in such areas.

## Slide 28: Visitors to Controlled Area
Avoid if possible
Otherwise:
Permission of Radiographer/Technologist
No children
No pregnant women
No eating and drinking in controlled area

## Slide 29: Cleaners, Maintenance and Outside Contractors
Only enter controlled area when it is safe to do so
Monitor controlled area before they enter
Supervise if necessary

## Slide 30
8.4 Relatives and Friends

## Slide 31: Contact with Patients after Scan
Dose rates measured at various distances as patients leave the department
Integrated doses calculated from various contact times at different distances
Social situations modelled
Total doses received have been estimated for various situations

## Slide 32: Recommendations
No restrictions on contact with partner following FDG scan
Restrictions on travel by public transport may vary in different countries. It can take 15-26 hrs before 400 MBq of 18F-FDG decays below 37 kBq. Some radiation monitors used for public transport protection are activated at 37 kBq*
Children should not accompany patient to PET/CT unit but no restrictions on contact once patient leaves the unit
Reduce close contact time with infants during first 12 hours post injection
*MacDonald J, J Radiol Prot 2005;25:219-20.

## Slide 33: SUMMARY OF STAFF AND PUBLIC DOSES
Typical annual whole body staff doses at conventional Nuclear Medicine facilities are 0.1 mSv, but are closer to 6 mSv at PET/CT facilities. While a substantially higher dose, this is still below the ICRP limit of 20 mSv per year
PET/CT staff members must use their personal monitors diligently, and should do so in a consistent manner so that comparisons of their doses are meaningful from one month to the next
PET/CT staff members can minimize their dose by minimizing time, maximizing distance and maximizing shielding in all instances involving radioactive sources
While children should not accompany the patient to the PET/CT facility, otherwise there are no restrictions for children, relatives or friends once the patient leaves the facility