## Slide 1: L 4
PROTECTION ISSUES IN CLINICAL METHODOLOGY

## Slide 2: Answer True or False
PET scans should be performed immediately following the 18F-FDG injection
There are means of optimizing PET dose, such as by scaling activity by weight for paediatric patients
It is important to assess the pregnancy status of all female subjects of child-bearing age before beginning any part of a PET/CT exam

## Slide 3: Objective
To become familiar with the basic PET/CT procedure from the patient perspective, including patient preparation, administration of the radiopharmaceutical, imaging and discharge of the patient. Factors that influence patient dose will also be considered especially for paediatric and female patients
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4
Patient preparation
Imaging
Patient dose
Paediatric considerations
Female patients
Content
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
4.1 Patient Preparation

## Slide 6: Patient Preparation
Fast (water only) for 6 hours before appointment
IDD (Insulin dependent diabetics) normal diet, normal morning insulin
Patient should be relaxed before procedure starts
Bowel preparation can be given

## Slide 7: Pre-Administration of Radiopharmaceuticals
Patient in gown (CT scan – no metal on patient)
Lie patient in rest area to relax
Perform glucose test
Butterfly or cannula for venous access (contra-lateral side to site of concern)
Explain the procedure to the patient before administering the dose
Confirm ID of patient (name, date of birth and address) before administration
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Post-Administration of Radiopharmaceutical
Allow patient to relax for 45-60 minutes post injection
Talking can increase uptake in jaw/throat area
Movement will increase the FDG to those muscles involved
Soothing music and dim lights
Use CCTV to monitor patient
Empty bladder before scan

## Slide 9: FDG Scanning Protocol
inject
scan
rest

## Slide 10
4.2 Imaging

## Slide 11: The PET/CT Scan
CT
PET
Survey
scan
CT
Reconstruction algorithm
Attenuation correction
PET
Fused Image

## Slide 12: Scan Process
CT scout view performed
Full CT performed
Patient moved further into scanner and PET scan acquired

## Slide 13: Contrast CT
Perform contrast CT immediately following PET/CT only if necessary

## Slide 14
4.3 Patient Dose

## Slide 15: Typical Activity Administered (UK)

## Slide 16: Typical CT Scan Factors
80-140 kVp
10 to 300 mAs
0.3 to 1 sec
Pitch 0.2 to 1.5
Notes: CTDI - CT Diagnostic Index

## Slide 17: Optimization of CT Dose
Select appropriate kVp, mAs and pitch
Scan minimum length needed to address diagnostic question
For Attenuation Correction alone mAs can be reduced to 10. However, with reduced mA there is a potential for artefacts

## Slide 18: Other Considerations
Has request also been made for CT ?
Will PET/CT answer the diagnostic question?
Is stand-alone CT really needed?

## Slide 19: To Reduce Effective Dose (PET)
Administer correct activity
Hydrated patient
Frequent voiding of the bladder especially when the scan is completed
For paediatric patients, scale activity by weight
For paediatric patients, use 3D PET if possible to enable lower injected activity

## Slide 20: Repeat Scans
Consider accumulative dose if patient is having repeat scans (monitoring treatment, disease progression)

## Slide 21
3.4 Paediatric Considerations

## Slide 22: Activity to Children
The amount of activity to be administered to a child can be calculated by one of the following formulae (based on values for adults):
body weight/70 kg
body surface area/1.73 m2
height/174 cm
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Fraction of the Adult Activity
Notes: <number>
<footer>
<header>
<date/time>
This image shows that the activity to a child will depend on the method used for calculation. Using body height will generally result in higher values than using body weight
BW - body weight
H - height
BSA - body surface area

## Slide 24: European Association of Nuclear Medicine (EANM)
Paediatric Task Group European Association Nuclear Medicine members. A radiopharmaceutical schedule for imaging paediatrics. Eur J Med 127-9, 1990

## Slide 25: CT Dose Reduction for Paediatric Patients
Reduce mAs or/and kVp
Use dose reduction features – mAs modulation, etc.
Increase pitch
Reduce number of bed positions

## Slide 26
4.5 Female patients

## Slide 27: Female Patients
Check clinical history
Pregnancy status of all females 12-55 years should be known before administering the radiopharmaceutical

## Slide 28: Dose to Uterus

## Slide 29: Pregnancy
If patient unsure of pregnancy status, verify status
If pregnant, contact Referrer and PET/CT consultant
If subsequently found to be pregnant, refer to local Radiation Protection Advisor

## Slide 30: Breast Feeding
  Baby should be fed by mother just prior to mother’s FDG injection
  While FDG concentration in breast milk is low,
  NONETHELESS
    Advise that baby is fed by a third party up to 4hours after the injection to avoid dose to the baby due to close contact with mother
  J Nucl Med 2001;42:1238-1242

## Slide 31: SUMMARY OF PROTECTION ISSUES IN CLINICAL METHODOLOGY
PET scans require the patient to fast for 6 hours prior to 18F-FDG injection, and remain quiet for 1 hour afterward prior to the acquisition of the PET scan
PET dose can be optimized by hydrating patient, requesting frequent voiding of the bladder after the scan, and for paediatric patients scaling activity by weight and using 3D PET if possible to enable lower injected activity
CT dose can be optimized by selecting appropriate kVp and mAs depending on the diagnostic question which the CT is intended to answer
As radiation risk is strongly age-dependent, it is especially important to assess the pregnancy status of all female subjects of child-bearing age before beginning any part of a PET/CT exam