## Slide 1: INTRODUCTION TO RADIATION PROTECTION IN PET/CT
L 1
Notes: Part 1: Introduction to Radiation Protection in PET/CT
Learning objectives: To get a general overview of PET/CT cyclotrons and the protection issues
Activity: Lecture
Duration: 1 h
Materials and equipment needed: Computer and computer projector

## Slide 2: Answer True or False
The most common use of PET/CT scans currently is to diagnose potential oncology conditions
The reason that both PET and CT scans are performed is because the PET scan is needed to perform attenuation corrections of the CT scan
The radiation protection measures needed for a PET facility are no different from those needed for a conventional Nuclear Medicine facility

## Slide 3: Course Objective
To be aware of PET/CT technology, operational principles, safe design of facilities, dosimetry relating to staff and patients and the radiation protection considerations relating to the use of this emerging technique

## Slide 4: Course Content - Modules
Introduction
PET/CT Technology
Medical Exposure- BSS requirements
Protection Issues in Clinical Methodology
Facility Design
Protective Equipment
Personal & Workplace Monitoring
Staff & Public Doses
Transport Safety, Source Security & Dealing with Waste
Written Procedures and Organization
Quality Control
SPECT/CT Technology and Facility Design

## Slide 5: Objective
Introduction to PET/CT includes a brief history, some applications and staff and patient dose considerations

## Slide 6: Content
PET, CT, PET/CT
History
Cyclotrons
Imaging equipment
Dose considerations

## Slide 7: PET
Positron Emission Tomography
Functional information
Tracers produced in cyclotron
Biological tracers
‘Hot spot’ on image
Few anatomical landmarks

## Slide 8: PET Radiopharmaceuticals
Nuclide | Half-life | Tracer | Application
O-15 | 2 mins | Water | Cerebral blood flow
C-11 | 20 mins | Methionine | Tumour protein synthesis
N-13 | 10 mins | Ammonia | Myocardial blood flow
F-18 | 110 mins | FDG | Glucose metabolism
Ga-68 | 68 min | DOTANOC | Neuroendocrine imaging
Rb-82 | 72 secs | Rb-82 | Myocardial perfusion

## Slide 9: FDG
CH2HO
HO
HO
O
OH
18F
CH2HO
HO
HO
O
OH
OH
glucose
2-deoxy-2-(F-18) fluro-D-glucose
Most widely used PET tracer
Glucose utilization
Taken up avidly by most tumours

## Slide 10: FDG Metabolism
FDG
FDG -6-P
Radio-
active Glucose
18F-FDG
Radioactive Glucose 18F-FDG
X
Glucose
Glucose
Glucose
Glucose-6-Phosphate
Unlike glucose, FDG is trapped

## Slide 11: CT
Anatomical detail
Cannot differentiate between active and benign disease
Better resolution than PET
Good dynamic range bone to lung

## Slide 12: PET/CT
Combines the functional information with the anatomical detail
Accurate anatomical registration
Higher diagnostic accuracy than PET or CT alone

## Slide 13: History Cyclotron & PET
1930 Cyclotron, Lawrence et al.
1953 Annihilation coincidence detection Brownell & Sweet
1975 Transaxial tomography
Ter-Pogossian, Phelps & Hoffman
1977 14C deoxyglucose, Sokoloff et al.
1979 18FDG PET, Relvich et al.
1980s Multislice tomographs & PET cyclotrons
1990s Clinical PET applications
2000s PET/CT

## Slide 14: History of CT
CT was invented in 1972 by Godfrey Hounsfield of EMI Laboratories
South Africa-born physicist Allan Cormack of Tufts University, Massachusetts was simultaneously working on reconstruction theory that was used
Both shared the Nobel prize
First clinical CT scanners installed 1974- 1976. Original systems dedicated to head imaging, "whole body" systems with larger patient openings became available in 1976

## Slide 15: History of CT (Contd.)
Initial CT scanner took several hours to acquire the raw data for a single scan or "slice" and took days to reconstruct a single image
Current multi-slice CT systems collect 64 slices of data in about 350 ms and reconstruct a 512 x 512-matrix image from millions of data points in less than a second. An entire chest can be scanned in five to ten seconds

## Slide 16: Pioneers
Michel Ter-Pogossian prepares a radiopharmaceutical for an
examination of Henry Wagner Jr with one of the first PET-
scanners (1975)

## Slide 17: Example of Cyclotrons

## Slide 18: Cyclotrons in a vault or self-shielded
Currently most cyclotrons are in a vault; they are the safest solution, can have higher energies with higher production capabilities
Some cyclotrons are self-shielded; they can have fixed energy, are compact for hospital's nuclear medical department, have simple control and operation with easy maintenance without skilled personnel

## Slide 19: Cyclotrons in Hospitals

## Slide 20: PET/CT-Scanner

## Slide 21: Mobile PET

## Slide 22: Mobile PET

## Slide 23: PET with Gamma Camera

## Slide 24: Clinical Applications
Oncology
Cardiology
Neurology
Oncology
85%
Cardiology
5%
Neurology
10%
Typical clinical applications in UK

## Slide 25: Role in Oncology
Differentiate benign from malignant disease
Staging of disease
Treatment response
Recurrence
Radiotherapy treatment planning
Ca Lung

## Slide 26: Oncology
Ca Breast

## Slide 27: Disease Progression
2005
2004

## Slide 28: Response to Treatment
Pre chemotherapy
Post chemotherapy

## Slide 29: Role in Cardiology

## Slide 30: Cardiology

## Slide 31: Role in Neurology
Alzheimers Disease
Normal

## Slide 33: Radiation Protection Issues
Difference from standard Nuclear Medicine
99mTc 140 keV photons
HVL (lead) around 0.3mm
TVL (lead) around 0.99mm
PET radionuclides 511 keV photons
  HVL (lead) 4mm (narrow beam) & 5mm (broad beam)
  TVL (lead) 13.2mm (narrow beam) & 16.5mm (broad beam)

## Slide 34: Instantaneous Dose Rate from Patient
Dose rate measured immediately after injection. Note considerably higher dose rate for 18F versus 99mTc.
Radiopharma-ceutical | Dose rate at 0.1 m, µSv/hr | Dose rate at 1m, µSv/hr
Tc-99m MDP (600 MBq) | 114 | 5
F-18 FDG (350 MBq) | 550 | 70
Notes: Large variation in quoted dose rate depending on distribution of source and position of measuring devise. However dose rate from FDG is considerably (in order of 12 times) greater than that from Tc bone scan.

## Slide 35: CT Radiation Protection Issues
Multislice – greater scanned volume
80-140 kVp, 100-380 mA, sub-second rotation time
Patient dose can be significant
Scattered radiation in and out of the room a potential problem

## Slide 36: Protection Considerations
PET - Penetrating photons
  Staff doses
  Doses in adjacent areas
  Facility design
  Protection equipment
  Heavier shielding needed at hot lab
CT
  Patient doses
  Scattered radiation for persons in CT room

## Slide 37: SUMMARY OF INTRODUCTION TO PET/CT
While there are many clinical situations diagnosed by PET/CT scans, currently oncology procedures far outnumber all other clinical indications
PET is performed to reveal sites of unusually high metabolic activity, and CT is performed both for attenuation correction of PET images and for anatomical localization of areas of unusually high metabolic activity
Because 511 keV photons are more penetrating than the 140 keV photons of 99mTc, more stringent protective measures are required for a PET facility compared to a conventional nuclear medicine facility