## Slide 1: L 6
PROTECTIVE EQUIPMENT

## Slide 2: Answer True or False
Technologists need not bother with gloves or lab coats when injecting a patient with 18F-FDG, as it is not absorbed by the skin and washes off quite easily
The positrons emitted by 18F travel only a few mm in water, so no special radiation protection precautions are needed, and syringes containing 18F-FDG can be handled just like any other syringe filled with saline

## Slide 3: Objective
To consider protective equipment for reduction of staff doses in cyclotron and PET/CT facilities, including shielding, handling devices and personal protective equipment (PPE)

## Slide 4: Content
Shielding
Handling radionuclides
PPE

## Slide 5
6.1 Shielding

## Slide 6: Shielding
For 511 keV typically 30-50 mm lead
For 99mTc (140 keV) usually 3 or 6 mm
Biggest problem with 511 keV shielding is the weight (density of lead 11 kg/litre)

## Slide 8: Transport Case
Source
Liner
Lead container
(47-57 mm )
Weight 15-25 kg
Container

## Slide 9: Syringe Shields
18F-FDG
(8 mm tungsten)
99mTc-
(2 mm tungsten)

## Slide 10: Dose rate from FDG using Various Syringe Shields
Notes: Perspex sometimes used for positrons. Syringe shields clearly required. Depleted uranium suggested to reduce size of shields.

## Slide 11: Storage of Radionuclides
Storage safe (sources and waste)
  50 mm lead
  Various sizes
  Weight 500-1500 kg
  Reduces dose rate by 10-3
  Security for removal
Notes: These images are examples of bad storage. The image to the left shows an equipment for ventilation studies that is stored in an office

## Slide 12: Storage of Solid Waste
Shielded bins for papers, gloves, empty vials and syringes.
Separate bins for active and non-active waste
Contaminated linen must be stored for 24 hours in protected cupboard before removal to laundry

## Slide 13: Dispensing
Dispensing unit
  50 mm lead thickness
  Weight 25 kg
  Reduces dose rate by 10-3
Additional lead L block
  30 mm lead thickness
  Weight 250 - 500 kg
Need to consider loading on work surface due to weight of lead

## Slide 14: Calibrators
Calibrators may need extra shielding
Work surfaces may need strengthening to take the weight of extra lead

## Slide 15
6.2 Handling

## Slide 16: PET Radiopharmacy Lab

## Slide 17: Drawing Up
Calculate volume required
Gloves
Long handle forceps or tongs
Only fill syringe to 50% capacity

## Slide 18: Long Forceps - 30 cm
Reduce dose by 60% compared with 18 cm tools

## Slide 19: Calibrator
Calibrator ‘sunk’ into worktop helps to reduce exposure time of operator

## Slide 20: Worktop Surfaces
Cover the surface with absorbing paper or disposable tray
Change daily or when spill is suspected

## Slide 21: Administration of Radiopharmaceuticals
Butterfly or cannula for venous access
Syringe shield
Carry shielded syringe to patient in additional shielding
Gloves

## Slide 22: Remote Injection System (Lemer Pax)
Connect to patient by catheter
Manually activated remote system
Operator behind protective screen
30 mm lead shielding

## Slide 23
6.3 Personal Protective Equipment

## Slide 24: Personal Protective Equipment (BSS)
“I.28. Employers, registrants and licensees shall ensure that:
(a) workers be provided with suitable and adequate personal protective equipment which meets any relevant standards or specifications, including as appropriate:
(i) protective clothing;
………..
(iii) protective aprons and gloves and organ shields;
………..
(b) all personal protective equipment be maintained in proper condition and if appropriate be tested at regular intervals;

## Slide 25: Personal Protective Equipment (BSS) cont.
(c) appropriate personal protective equipment be maintained for use in the event of intervention; and
(d) the use of personal protective equipment is considered for any given task, account be taken of any additional exposure that could result owing to the additional time or inconvenience, and of any additional non-radiological risks that might be associated with performing the task while using protective equipment. ”

## Slide 26: Personal Protective Equipment Unsealed Radioactive Material
Gloves
White coat
Aprons, etc.

## Slide 27: Personal Protective Equipment CT
Lead apron 0.35 mm
Thyroid shield
Only required for those who must remain in room during scanning, e.g. contrast injection
Notes: Slightly more modern than this from 1916! Most centres do not allow staff in room during CT therefore lead protection not required.

## Slide 28: SUMMARY OF PROTECTIVE EQUIPMENT
The 511 keV gamma rays emitted by 18F are more penetrating than the 140 keV gamma rays emitted by 99mTc, so special precautions are needed when handling syringes containing 18F-FDG, including the use of long forceps in handling vials and syringe shields and L blocks specifically intended to shield positron emitters
It is important for technologists to use gloves and lab coats whenever handling positron emitters, so as to be able to easily decontaminate themselves
It is important for personnel involved in PET/CT scanning to protect themselves from the CT exposure, especially if their presence is ever required in the room while the CT scan is in progress