## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L13.1: Occupational exposure -Regulatory aspects
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
13.1: Occupational exposure - Regulatory aspects
<number>
Subject matter: occupational exposure and regulatory aspects
The main component of the organizational procedures for applying the radiation protection principles to staff in a radiology department
Investigation and follow up protocols
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
13.1: Occupational exposure - Regulatory aspects
<number>
Organization, responsibilities and training
Conditions of service
Classification of areas
Local rules and supervision
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
13.1: Occupational exposure - Regulatory aspects
<number>
To become familiar with the BSS detailed requirement for radiation protection of workers in diagnostic radiology.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 13.1: Occupational exposure
Topic 1: Responsibilities and training
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Occupational exposure definition
13.1: Occupational exposure - Regulatory aspects
<number>
All exposures of workers incurred in the course of their work, with the exception of exposures excluded from the Standards (BSS) and exposures from practices or sources exempted by the Standards

## Slide 7: The Basic Safety Standards
13.1: Occupational exposure - Regulatory aspects
<number>
Responsibilities
Conditions of service
Classification of areas
Local rules and supervision
Personal protective equipment
Co-operation between employers registrants and licensees
Individual monitoring and exposure assessment
Monitoring of the workplace
Health surveillance
Records
Special circumstances

## Slide 8: Responsibilities (BSS 3.73)
13.1: Occupational exposure - Regulatory aspects
<number>
Licensee shall ensure for all workers that:
  Occupational exposure be limited and optimized
  Suitable and adequate facilities, equipment and services for protection be provided
  Appropriate protective devices and monitoring equipment be provided and properly used
  Appropriate training be provided as well as periodic retraining and updating
  Adequate records be maintained
  A safety culture be provided

## Slide 9
13.1: Occupational exposure - Regulatory aspects
<number>
DOSE LIMIT (1)
Occupational
APPLICATION
Effective dose
Effective dose to the embryo or foetus
Annual equivalent dose in: the lens of the eye
the skin (4)
the hands and feet
The limits apply to the sum of the relevant doses from external exposure in the specified period and the 50-year committed dose (to age 70 years for children) from intakes of radioactive nuclides in the same period. 2. With the further provision that the effective dose should not exceed 50 mSv in any single year. 3. In special circumstances, a higher value dose could be allowed in a single year, provided that the average over 5 years does not exceed 1 mSv in any single year. 4. The limitation on the effective dose provides sufficient protection for the skin against stochastic effects. An additional limit is needed for localised exposures to prevent deterministic effects.
20 mSv per year averaged over 5 years (2)
1 mSv
20 mSv averaged over 5 years (2) 500 mSv 500 mSv

## Slide 10: Optimization of protection
13.1: Occupational exposure - Regulatory aspects
<number>
Risk/dose
Unacceptable Dose limit
Source related
constraints
Optimized working procedures
Tolerable
Acceptable Occupational
exposure

## Slide 11
13.1: Occupational exposure - Regulatory aspects
<number>
Workers shall:
follow any applicable rules for protection
use properly the monitoring devices and the protective equipment and clothing provided
co-operate with the licensee with respect to protection
etc...
Responsibilities (BSS 3.83)

## Slide 12: Conditions of service
13.1: Occupational exposure - Regulatory aspects
<number>
Special compensatory arrangements
The conditions of service of workers shall be independent of the existence or the possibility of occupational exposure
Special compensatory arrangements or preferential treatment with respect to salary or special insurance coverage, working hours, length of vacation, additional holidays or retirement benefits shall neither be granted nor be used as substitutes for the provision of proper protection and safety measures to ensure compliance with the requirements of the Standards

## Slide 13: Conditions of service
13.1: Occupational exposure - Regulatory aspects
<number>
Pregnant workers
A female worker should, on becoming aware that
she is pregnant, notify the employer in order that
her working conditions may be modified if necessary.
The notification of pregnancy shall not be considered a reason to exclude a female worker from work; however, the employer who has been notified shall adapt the working conditions to assure that the embryo or fetus is afforded the same level of protection as for members of the public.

## Slide 14
13.1: Occupational exposure - Regulatory aspects
<number>
Alternative employment
3.112 Employers shall make every reasonable effort to provide workers with suitable alternative employment in circumstances where it has been determined, either by the Regulatory Authority or in the framework of the health surveillance program required by the Standards, that the worker, for health reasons, may no longer continue in employment involving occupational exposure.
Conditions of service

## Slide 15
13.1: Occupational exposure - Regulatory aspects
<number>
Conditions for young persons
3.115 No person under the age of 16 years shall be subjected to occupational exposure.
3.116 No person under the age of 18 years shall be allowed to work in a controlled area unless supervised and then only for the purpose of training.
Conditions of service

## Slide 16: Part 13.1: Occupational Exposure
Topic 2: Classification of Areas
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 17
13.1: Occupational exposure - Regulatory aspects
<number>
3.88 Registrants and licensees shall designate as a controlled area any area in which specific protective measures or safety provisions are or could be required for:
(a) controlling normal exposures during normal working conditions; and
(b) preventing or limiting the extent of potential exposures
Controlled areas (BSS)

## Slide 18
13.1: Occupational exposure - Regulatory aspects
<number>
3.89 In determining the boundaries of any controlled area, registrants and licensees shall take account of the magnitudes of the expected normal exposures, the likelihood and magnitude of potential exposures, and the nature and extent of the required protection and safety procedures
Controlled areas (BSS)

## Slide 19
13.1: Occupational exposure - Regulatory aspects
<number>
In a radiology facility, all X Ray rooms shall be controlled areas
Supervised areas should include parts of the facility where mobile X Ray units are used, and all other parts other than public areas.
Each room of the facility should only be used for its specified work
Controlled and supervised area (BSS)

## Slide 20
13.1: Occupational exposure - Regulatory aspects
<number>
On the basis of a safety assessment including the planned use of each area and an evaluation of shielding, the registrant or licensee should determine whether an area will be maintained as a controlled or public area
The registrant or licensee should also assess which other areas (e.g. other patient rooms, stairwells, nursing stations, waiting areas, toilets) should be controlled, or public areas
Controlled area

## Slide 21
13.1: Occupational exposure - Regulatory aspects
<number>
I.23. Registrants and licensees shall:
(a) delineate controlled areas by physical means or, where this is not reasonably practicable, by some other suitable means
(b) display a warning symbol, such as that recommended by the International Organization for Standardization (ISO), and appropriate instructions at access points and other appropriate locations within controlled areas
Controlled area

## Slide 22
13.1: Occupational exposure - Regulatory aspects
<number>
(c) establish occupational protection and safety measures, including local rules and procedures that are appropriate for controlled areas
(d) restrict access to controlled areas by means of administrative procedures, such as the use of work permits, and by physical barriers, which could include locks or interlocks; the degree of restriction being commensurate with the magnitude and likelihood of the expected exposures
Controlled area

## Slide 23: Part 13.1: Occupational exposure
Topic 3: Local rules and supervision
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 24: Local rules and supervision (BSS)
13.1: Occupational exposure - Regulatory aspects
<number>
Employers, registrants and licensees shall, in consultation with workers, through their representatives, if appropriate (BSS 3.94):
Ensure protection and safety for workers and other persons
Include investigation level or authorized level and procedure in the event that any such value is exceeded
Make the local rules known to workers and to other persons
Ensure any work be adequately supervised

## Slide 25: Local rules and supervision
13.1: Occupational exposure - Regulatory aspects
<number>
These local rules should include
procedures for wearing, handling, and storing personal dosimeters
actions to minimize radiation exposure during unusual events

## Slide 26: Summary
13.1: Occupational exposure - Regulatory aspects
<number>
The classification system in which working areas are classified by the BSS
Operating rules which cover working area where radiation is used
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 27: Where to Get More Information
13.1: Occupational exposure - Regulatory aspects
<number>
Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards, Revision of IAEA Safety Series No. 115, IAEA, Vienna Austria, 2011
The 2007 Recommendations of the International Commission on Radiological Protection, ICRP 103, Annals of the ICRP 37(2-4):1-332 (2007)
Safety Report on Methodology for Investigation of Accidents involving Sources of Ionizing Radiation, IAEA, Vienna (in press).
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources