## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L17.1: Optimization of Protection in Interventional Radiology
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
17.1: Optimization of Protection in Interventional Radiology
<number>
Interventional radiology comprises fluoroscopically guided therapeutic and diagnostic techniques.
These are complex procedures require specially designed equipment, and result in high exposures to both personnel and patients.
A good knowledge of equipment specification and characteristics is essential for an effective optimization of radiation protection
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Content
17.1: Optimization of Protection in Interventional Radiology
<number>
  Principles of Interventional radiology
  Design requirement and international recommendations: WHO, FDA, and ACR
  Purchase specifications
  Operational modalities
  Risk level (staff and patients)
  Factors affecting staff and patient doses
  Examples of radiation doses
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
17.1: Optimization of Protection in Interventional Radiology
<number>
To be able to apply the principle of radiation protection to interventional radiology system including equipment design, operational considerations, and Quality Control.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 17.1: Optimization of protection in Interventional Radiology
Topic 1: Principles of Interventional radiology
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Principle of Interventional Radiology
17.1: Optimization of Protection in Interventional Radiology
<number>
Interventional radiology (fluoroscopically-guided) techniques are being used by an increasing number of clinicians not adequately trained in radiation safety or radiobiology
Patients are suffering radiation-induced skin injuries due to unnecessarily high radiation doses.
Patients, especially younger ones, may face an increased risk of future cancer
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 7: Principle of Interventional Radiology
17.1: Optimization of Protection in Interventional Radiology
<number>
Many interventionists are not aware of the potential for injury from procedures, their occurrence or the simple methods for decreasing their incidence utilising dose control strategies.
Many patients are not being counselled on the radiation risks, nor followed up for the onset of injury, when radiation doses from difficult procedures may lead to injury.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 8: Principle of Interventional Radiology
17.1: Optimization of Protection in Interventional Radiology
<number>
Interventionists are having their practice limited or suffering injury, and are exposing their staff to high doses.
Occupational doses can be reduced by reducing patient dose. The correct use of equipment (including shielding devices) is essential.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 9
17.1: Optimization of Protection in Interventional Radiology
<number>
IR procedures may be classified into:
  cardiac (cardiologists), noncardiac (radiologists)
  vascular, nonvascular
DRAINAGE and PUNCTURE
PERCUTANEOUS NEEDLE BIOPSY
STENT PLACEMENT
COAGULATION THERAPY
EMBOLIZATION
DRUG INFUSION (Tumor catheter placement), ANGIOPLASTY (PTA, Atherectomy, stent graft placement),
CARDIAC INTERVENTION (PTCA, radiofrequency ablation)
TRANSJUGULAR INTRAHEPATIC PORTOSYSTEMIC SHUNT
VASCULAR PROCEDURES:
NON-VASCULAR PROCEDURES:

## Slide 10: The IR environment
17.1: Optimization of Protection in Interventional Radiology
<number>
Lengthy and complex procedures
Operating staff very close to the patient
Prolonged exposure time
Limited shielding
One must look for
Modern sophisticated X Ray systems
Use of protection tools, goggles, specific
shielding, etc
Suitable knowledge of the system
Skill, rational (shared) workload

## Slide 11: Part 17.1: Optimization of Protection in Interventional Radiology
Topic 2: Design requirement and international recommendations: WHO, FDA, and ACR
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 12
17.1: Optimization of Protection in Interventional Radiology
<number>
Constant potential generator
C-arm system (Under table x-ray tube)
High efficiency intensifier or flat panel imaging system
Digital image storage and retrieval
Interventional X-Ray System Requirements

## Slide 13: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (1))
17.1: Optimization of Protection in Interventional Radiology
<number>
RECOMMENDED TECHNICAL SPECIFICATION (1):
Use of audible dose or dose rate alarms is not considered appropriate (cause of confusion)
Dose and image quality: user selectable variables
Additional filtration
Removable Grid
Pulsed fluoroscopy modes
Image hold system
Flexibility for AEC (IMAGE or DOSE weighted)
Recursive or temporal filtering: temporal averaging in fluoroscopy (dose reduction, improvement of SNR)

## Slide 14: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (2))
17.1: Optimization of Protection in Interventional Radiology
<number>
* Roadmapping (use of a reference image on which the current image is overlayed)
* Image simulation (impact of changes in technique factors displayed prospectively, effect of semitransparent filters simulated)
* Region of Interest (ROI) fluoroscopy: a low noise image in the centre is presented surrounded by a low dose (noisy) region.
* provision of additional shielding to optimize occupational protection

## Slide 15: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (3))
17.1: Optimization of Protection in Interventional Radiology
<number>
RECOMMENDED TECHNICAL SPECIFICATION (2):
Overcouch image intensifier
Source-intensifier distance tracking
Concave couch top for patient comfort
Dose-area product meter
Provision of Staff protective shielding
Display of fluoroscopy time, total dose-area product (fluoroscopy and radiographic) and estimated skin entrance dose.

## Slide 16: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (4))
17.1: Optimization of Protection in Interventional Radiology
<number>
RECOMMENDED TECHNICAL SPECIFICATION (3):
Computer interface for dosimetric information
Provision of iso-scatter distribution diagrams for normal and boost modes
All instrumentation and switches clearly labeled
Minimum size of image store
Roadmapping facility
Availability of an automatic injector
Means of patient immobilization

## Slide 17: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (5))
17.1: Optimization of Protection in Interventional Radiology
<number>
X RAY TUBE AND GENERATOR:
Focal spot:
cardiology 1.2/0.5 mm
neuroradiology 1.2/0.4 mm
peripheral vascular 1.2/0.5 mm
Minimum focus-to-skin distance 30 cm
Heat capacity of X Ray tube should be adequate to perform all anticipated procedures without time delay
80 kW generator
Constant potential generator
Pulsed fluoroscopy available
Automatic collimator to the size of the intensifier input area.

## Slide 18: Requirements for Image Intensifier (Joint WHO-IRH-CE workshop 1995 (6))
17.1: Optimization of Protection in Interventional Radiology
<number>
Cardiology: 25 cm; max. dose rate: 0.6 µGy/s
Neuroradiology: 30 cm; max. dose rate: 0.6 µGy/s
Peripheral vascular: 35-40 cm; max. dose rate: 0.2 µGy/s Note: dose rate in normal mode, should be measured at the entrance surface of Image Intensifier
2 x magnification available
low dose rate and boost modes available
Manual selection of the AEC
Operational design of the AEC must be specified

## Slide 19: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (7)
17.1: Optimization of Protection in Interventional Radiology
<number>
Image Intensifier
Tube potential - tube current characteristic of the AEC (or automatic dose-rate control) should be a user selectable feature
The delay between depressing the footswitch and seeing the displayed image should be less than 1 s
Last image hold
Diaphragm position indicator on the last image hold is desirable.

## Slide 20: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (8))
17.1: Optimization of Protection in Interventional Radiology
<number>
CONSTANCY TESTS (monthly):
Reference dose, dose rates
Resolution
Field diameter
Collimation
Contrast resolution
Tube and generator parameters
Hard copy devices

## Slide 21: Requirements for equipment (Joint WHO-IRH-CE workshop 1995 (9))
17.1: Optimization of Protection in Interventional Radiology
<number>
SUGGESTED ACTION LEVELS FOR STAFF DOSE
Body 0.5 mSv/month
Eyes 5 mSv/month
Hands and Extremities 15 mSv/month

## Slide 22: FDA Recommendations for IR (1994) (I)
17.1: Optimization of Protection in Interventional Radiology
<number>
To establish standard operating procedures and clinical protocols for each specific type of procedure performed (including consideration of limits on fluoroscopically exposure time)
To know the radiation doses rates for the specific fluoroscopic system and for each mode of operation used during the clinical protocol
To assess the impact of each procedure's protocol on the potential for radiation injury to the patient

## Slide 23: FDA Recommendations for IR (1994) (II)
17.1: Optimization of Protection in Interventional Radiology
<number>
To modify the protocol, as appropriate, to limit the cumulative absorbed dose to any irradiated area of the skin to the minimum necessary for the clinical tasks, and particularly to avoid approaching cumulative doses that would induce unacceptable adverse effects
To use equipment that aids in minimizing absorbed dose
To enlist a qualified medical physicist to assist in implementing these principles in such a manner so as not to adversely affect the clinical objectives of the procedure.

## Slide 24: Part 17.1: Optimization of protection in Interventional Radiology
Topic 3: Purchase specifications
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 25: Purchase specifications (an example for a C-arm system) (1)
17.1: Optimization of Protection in Interventional Radiology
<number>
Dimensions, weight, and C-arm movements
Steering (control for movement)
Generator and X Ray tube
Collimator
Grid and Semi-transparent shutters
Image intensifier
Video camera, Monitors
Digital processor
Print and recording options

## Slide 26: Purchase specifications (an example for a C-arm system) (2)
17.1: Optimization of Protection in Interventional Radiology
<number>
Generator
Constant potential
Voltage: Adjustable in steps of 1 kV from 40 -105 kV
mAs values: Adjustable in steps of about 25% from 0,20 to 80 mAs
Max. fluoro current: 3 mA
Max. HDF (high dose fluoroscopy) current: 7 mA
Max. HDF time: 20 s
Fixed radiography current: 20 mA
Nominal power: 3 - 15 kw

## Slide 27: Purchase specifications (an example for a C-arm system) (3)
17.1: Optimization of Protection in Interventional Radiology
<number>
Image intensifier:
Input field sizes:
  23 - 17 - 14 cm (9 - 7 - 5 inch)
  31 - 23 - 17 cm (12 - 9 -7 inch)
Input screen: ICs
Video camera Type: High resolution CCD sensor with image brightness regulation
Lines (interlaced): minimum of 625 at 50 Hz power supply (525 at 60 Hz).

## Slide 28: Purchase specifications (an example for a C-arm system) (4)
17.1: Optimization of Protection in Interventional Radiology
<number>
Monitors:
Type: high resolution, anti-reflection screen.
Size: 43 cm / 17 inch
Brightness control: automatic.
Digital processor:
Display matrix: 1008 x 576 x 8 at 50 Hz
Disk storage capacity: 50-200-1000 images
Processing options:
Image display: 100 Hz / 625 lines PAL

## Slide 29: Part 17.1: Optimization of protection in Interventional Radiology
Topic 4: Operational modalities
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 30
17.1: Optimization of Protection in Interventional Radiology
<number>
TV CAMERA TYPES
PLUMBICON TV cameras:
have much less Image Lag than VIDICON cameras
Lower Image Lag permits motion to be followed with minimal Blurring
but QUANTUM NOISE is increased (cameras for cardiology)
DIGITAL FLUOROSCOPY
Digital fluoroscopy SPOT films are usually limited by their poor resolution, which is determined by the TV camera and is no better than about 2 c/mm for a 1000 line TV system
If the TV system is a nominal 525 line, one frame generally consists of 525² = 250000 pixels. Each pixel needs 1 byte (8 bits) or 2 bytes (16 bits) of space to record the signal level
VIDICON
PLUMBICON (cardiology systems)
CCD

## Slide 31
17.1: Optimization of Protection in Interventional Radiology
<number>
THE KNOWLEDGE OF DOSE RATES FOR
DIFFERENT OPERATIONAL MODES AND
FOR DIFFERENT INTENSIFIER INPUT SIZE
IS IMPORTANT
THEN, IT IS POSSIBLE TO HAVE
CRITERIA FOR THE CORRECT
USE OF DIFFERENT OPERATION
MODES

## Slide 32
17.1: Optimization of Protection in Interventional Radiology
<number>
EQUIPMENT
RELATED
SETTING MADE BY
THE TECHNICAL
SERVICE
IMAGE and DOSE
AT THE ENTRANCE
OF THE IMAGE
INTENSIFIER
SPECIALIST
RELATED
NUMBER OF IMAGES
RECORDED IN EACH
PROCEDURE

## Slide 33: Part 17.1: Optimization of protection in Interventional Radiology
Topic 5: Risk level (staff and patients)
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 34
17.1: Optimization of Protection in Interventional Radiology
<number>
AWARENESS OF INTERNATIONAL
BODIES ON INCREASED NUMBER OF INJURIES
FOR INTERVENTIONAL RADIOLOGISTS
SEARCH FOR
POSSIBLE
REASONS
INCREASE IN
WORKLOAD
INADEQUATE RP
CONDITIONS
OLD X Ray
SYSTEMS

## Slide 35: Radiation effects on humans
17.1: Optimization of Protection in Interventional Radiology
<number>
CANCER
STOCHASTIC
EFFECTS
DETERMINISTIC
EFFECTS
LENS INJURIES
SKIN INJURIES
HEREDITARY
DISORDERS IN THE
DESCENDANTS

## Slide 36
17.1: Optimization of Protection in Interventional Radiology
<number>
CATARACT
0.5 - 2.0 Sv in a
SINGLE EXPOSURE
5 Sv in FRAC. EXPOS.
>0.1 Sv/year CONTIN.
ANNUAL RATE
5 Sv SINGLE EXPOS.
> 8 Sv FRAC. EXPOS.
>0.15 Sv/year CONTIN.
ANNUAL RATE
DETERMINISTIC LENS
THRESHOLD AS QUOTED
BY THE ICRP
OPACITIES
THRESHOLD
New epidemiological data suggest that the threshold for opacities is at 0.5 mSv*
*According to the statement on tissue reactions issued by the ICRP on April 21, 2011

## Slide 37: Dosimetric parameters
17.1: Optimization of Protection in Interventional Radiology
<number>
Useful quantities for patient and staff risk
evaluation:
Dose area product (for stochastic effect)
Entrance surface dose (for deterministic effect)
Staff dose per procedure (in more than one location)

## Slide 38: Part 17.1: Optimization of protection for Interventional Radiology
Topic 5: Factors affecting staff doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 39: Factors affecting staff doses (I)
17.1: Optimization of Protection in Interventional Radiology
<number>
The main source of radiation for the staff in a fluoroscopy room is the patient (scattered radiation).
The scattered radiation is not uniform around the patient.
The dose rate around the patient is a complex function of a number of factors.

## Slide 40
17.1: Optimization of Protection in Interventional Radiology
<number>
THE SCATTERED DOSE RATE AT 1 METER FROM THE PATIENT CAN BE HIGHER THAN 1 mGy/min FOR SOME C-ARM POSITIONS
WITH DIGITAL FLUOROSCOPY MODE, DOSE RATE COULD BE REDUCED (25%) WITH RESPECT TO CONVENTIONAL MODE

## Slide 41: Part 17.1: Optimization of protection in Interventional Radiology
Topic 6: Factors affecting staff and patient doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 42: Radiation level in IR procedures Important factors
17.1: Optimization of Protection in Interventional Radiology
<number>
Fluoroscopy time
Number of series (Images)
Patient size
Performance of the X Ray system used
Available protection tools

## Slide 43
17.1: Optimization of Protection in Interventional Radiology
<number>
INTENSIFIER
DIMENSION
RELATIVE PATIENT
ENTRANCE DOSE
12" (32 cm) dose 100
9" (22 cm) dose 150
6" (16 cm) dose 200
4,5" (11 cm) dose 300

## Slide 44: Part 17.1: Optimization of protection in Interventional Radiology
Topic 7: Examples of radiation doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 45
17.1: Optimization of Protection in Interventional Radiology
<number>
More information at: https://rpop.iaea.org/RPOP/RPoP/Content/InformationFor/HealthProfessionals/5_InterventionalCardiology/index.htm
Examples of dose values

## Slide 46: Examples of dose values
17.1: Optimization of Protection in Interventional Radiology
<number>
More information at: https://rpop.iaea.org/RPOP/RPoP/Content/InformationFor/HealthProfessionals/5_InterventionalCardiology/index.htm

## Slide 47: INDICATIVE VALUES
17.1: Optimization of Protection in Interventional Radiology
<number>
75
25
24
17
15
12
10
9
6,3
5
3,3
1
TIPS
HEPATIC EMBOLIZ.
BILIAR DRAINAGE
ABDOM. ANGIOPLAST.
HEPATIC MANOM.
CEREBRAL ARTER.
ABDOM. ARTERIOGR.
BRONQUIAL ARTERIOGR.
RENAL ARTERIOGR.
LOWER LIMB ARTER.
UPPER LIMB FISTUL.
LOWER LIMB PHLEBOGR.
0
20
40
60
80
100
FLUOROSCOPY TIME (min.)

## Slide 48: DOSE AREA PRODUCT INDICATIVE MEAN VALUES
17.1: Optimization of Protection in Interventional Radiology
<number>
353,7
96,42
92,92
87,5
81,68
68,87
68,16
66,63
66,51
25,3
24,7
8,71
2,94
TIPS
VALVULOPLASTY
RENAL ARTERIOGR.
PTCA
HEPATIC EMBOLIZ.
BILIAR DRAINAGE
CEREBRAL ARTERIOG.
LOW EXTREM. ART.
CORONARIOGRAPHY
HEPATIC MANOMETRY
AORTIC ARTERIOGR.
UPPER EXTREM. FISTUL.
LOW EXTREM. PHLEBOG.
0
100
200
300
400
Gy.cm
2

## Slide 49: INDICATIVE VALUES
17.1: Optimization of Protection in Interventional Radiology
<number>
10
6
4
4
3
3
160
120
64
60
60
60
CEREBRAL ARTERIO.
LOWER LIMB ARTERIO.
UPPER LIMB FISTUL.
BRONCHIAL ARTERIO.
RENAL ARTERIO.
ABDOMINAL ARTERIO.
0
50
100
150
SERIES OF IMAGES
NUMBER OF IMAGES

## Slide 50: CINE AND DSA DOSES
17.1: Optimization of Protection in Interventional Radiology
<number>
Patient entrance doses for Cine can require between 70 and 130 µGy/fr:
1 minute of Cine at 25 fr/s would lead to 150 mGy, almost equivalent to:
  15 abdomen X Rays or 400 chest X Rays
A digital image can require 4 mGy

## Slide 51: Summary
17.1: Optimization of Protection in Interventional Radiology
<number>
Many physical and technical factors may significantly affect patient and staff dose in interventional radiology.
The equipment used in this field should comply with international requirement and purchase specifications.
Practitioners should be aware of such recommendations
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 52: Where to Get More Information
17.1: Optimization of Protection in Interventional Radiology
<number>
Wagner LK and Archer BR. Minimising risks from fluoroscopic x rays. Third Edition. Partners in Radiation Management (R.M. Partnership). The Woodlands, TX 77381. USA 2000.
Avoidance of radiation injuries from medical interventional procedures. ICRP Publication 85.Ann ICRP 2000;30 (2). Pergamon.
Radiation Dose Management for Fluoroscopically-Guided Interventional Medical Procedures, NCRP Report No. 168, National Council on Radiation Protection and Measurement. Bethesda, MD. 2010
Interventional Fluoroscopy: Physics, Technology, Safety, S. Balter, Wiley-Liss, 2001
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources