## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L16.2: Optimization of Protection in Fluoroscopy
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
16.2: Optimization of protection in fluoroscopy
<number>
Subject matter : radiation protection in fluoroscopy equipment
Both physical and technical parameters may have an influence on patient and staff dose.
Good radiation protection policy and personnel skill are essential for reducing both staff and patient exposures.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Content
16.2: Optimization of protection in fluoroscopy
<number>
  Factors affecting staff doses
  Factors affecting patient doses
  Examples of doses
  Protection tools
  Radiation protection rules
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
16.2: Optimization of protection in fluoroscopy
<number>
To become familiar with the application of practical radiation protection principles to fluoroscopy system.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 16.2: Optimization of Protection in Fluoroscopy
Topic 1: Factors affecting staff doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Refresher slide: absorption and scatter
16.2: Optimization of protection in fluoroscopy
<number>
For every 1000 photons reaching the patient, about 100-200 are scattered, about 20 reach the image detector, and the rest are absorbed (= radiation dose)
Scatter x rays also obeys the Inverse Square Law, so distance from the patient improves safety
In radiology, scatter mainly directed towards the source
X-Ray tube

## Slide 7: Factors affecting staff doses (I)
16.2: Optimization of protection in fluoroscopy
<number>
The main source of radiation for the staff in a fluoroscopy room is the patient (scattered radiation).
The scattered radiation is not uniform around the patient.
The dose rate around the patient is a complex function of a great number of factors.

## Slide 8: Factor affecting staff doses (II)
16.2: Optimization of protection in fluoroscopy
<number>
X RAY TUBE POSITION
FACTORS
AFFECTING
STAFF DOSE
HEIGHT OF STAFF
RELATIVE POSITION WITH
RESPECT TO THE PATIENT
IRRADIATED PATIENT VOLUME
kV, mA and time (NUMBER AND
CHARACTERISTICS OF PULSES)
EFFECTIVE USE OF ARTICULATED
SHIELDING AND/OR PROTECTION
GOGGLES

## Slide 9: Factor affecting staff doses (III)
16.2: Optimization of protection in fluoroscopy
<number>
Scattered dose rate is higher near the area where the X-ray beam enters the patient
0.3 mGy/h
0.6 mGy/h
0.9 mGy/h
100 kV
11x11 cm
1m patient distance
patient thickness 18 cm
1 mA
ANGLE DEPENDENCE

## Slide 10: Factor affecting staff doses (IV)
16.2: Optimization of protection in fluoroscopy
<number>
Scattered dose rate is higher when field size increases
0.3 mGy/h
0.6 mGy/h
0.8 mGy/h
100 kV
1m patient distance
Patient
thickness 18 cm
0.7 mGy/h
1.1 mGy/h
1.3 mGy/h
17x17 cm
11x11 cm
17x17 cm
1 mA
FIELD SIZE DEPENDENCE

## Slide 11: Factor affecting staff doses (V)
16.2: Optimization of protection in fluoroscopy
<number>
Scattered dose rate is lower when distance to the patient increases
100 kV
11x11 cm
1 mA
mGy/h at 1m
mGy/h at 0.5m
DISTANCE VARIATION

## Slide 12: Factor affecting staff doses (VI)
16.2: Optimization of protection in fluoroscopy
<number>
Tube undercouch position reduces, in general, high dose rates to the specialist’s eye lens
THE BEST
CONFIGURATION
INTENSIFIER UP
X-RAY TUBE DOWN
SAVES A FACTOR OF
3 OR MORE IN DOSE
IN COMPARISON
TO:
X-RAY TUBE UP
INTENSIFIER DOWN

## Slide 13: Factor affecting staff doses (VII)
16.2: Optimization of protection in fluoroscopy
<number>
Tube undercouch position reduces, in general, high dose rates to the specialist’s eye lens
1.3 (59%)
2.0 (91%)
2.2 (100%)
100 kV
20x20 cm
1m patient distance
1 m
1 Gy/h
(17mGy/min)
mGy/h
1.2 (55%)
X-Ray tube
1.3 (59%)
1.2 (55%)
1.2 (55%)
100 kV
20x20 cm
1m patient distance
1 m
1 Gy/h
(17 mGy/min)
mGy/h
2.2 (100%)
X-Ray tube

## Slide 14: Staff and patient dose are partially linked
16.2: Optimization of protection in fluoroscopy
<number>

## Slide 15: Staff and patient dose are partially linked
16.2: Optimization of protection in fluoroscopy
<number>

## Slide 16: Factors affecting staff and patient doses (I)
16.2: Optimization of protection in fluoroscopy
<number>
IF PATIENT SIZE INCREASES
PATIENT SKIN DOSE AND THE LEVEL OF SCATTERED RADIATION INCREASE SUBSTANTIALLY

## Slide 17: Factors affecting staff and patient doses (II)
16.2: Optimization of protection in fluoroscopy
<number>
CHANGING FROM NORMAL FLUOROSCOPY MODE TO THE HIGH DOSE RATE MODE
INCREASES DOSE RATE BY A FACTOR OF 2 OR MORE

## Slide 18: Factors affecting staff and patient doses (III)
16.2: Optimization of protection in fluoroscopy
<number>
THE USE OF THE ANTISCATTER GRID
INCREASES PATIENT ENTRANCE DOSE BY A FACTOR OF 2 TO 6

## Slide 19: Part 16.2: Optimization of Protection in Fluoroscopy
Topic 2: Factors affecting patient doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 20: Factors affecting patient doses (I)
16.2: Optimization of protection in fluoroscopy
<number>
CHANGING FROM HIGH TO LOW NOISE MODE (FOR CINE AND DSA - Digital Subtraction Angiography)
INCREASES DOSE PER IMAGE BY A FACTOR OF 2 TO 10

## Slide 21: Factors affecting patient doses (II)
16.2: Optimization of protection in fluoroscopy
<number>
CHANGING FROM CONVENTIONAL FLUOROSCOPY TO DIGITAL MODE
CAN DECREASE DOSE RATE DOWN TO 25%

## Slide 22: Factors affecting patient doses (III)
16.2: Optimization of protection in fluoroscopy
<number>
INTENSIFIER
DIAMETER
RELATIVE PATIENT
ENTRANCE DOSE
12" (32 cm) dose 100
9" (22 cm) dose 150
6" (16 cm) dose 200
4.5" (11 cm) dose 300

## Slide 23: Factors affecting patient doses (IV)
16.2: Optimization of protection in fluoroscopy
<number>
CHANGING TO A SMALLER IMAGE INTENSIFIER FIELD
CAN INCREASE PATIENT ENTRANCE DOSE OF A FACTOR UP TO 3

## Slide 24: Part 16.2: Optimization of Protection in Fluoroscopy
Topic 3: Examples of doses
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 25: Example of dose per frame GE-CGR Advantix LCV
16.2: Optimization of protection in fluoroscopy
<number>
TYPICAL
DOSE
4 mGy/im. or
0.1 mGy/fr
A mode:
DOSE 1
high noise
B mode:
DOSE
FACTOR 2.5
C mode:
DOSE
FACTOR 5
D mode:
DOSE
FACTOR 10
low noise

## Slide 26: Example of entrance dose rate in fluoroscopy
16.2: Optimization of protection in fluoroscopy
<number>
GE-CGR Advantix LCV (Fluoroscopy)
LOW DOSE 10 mGy/min
MEDIUM DOSE 20 mGy/min
HIGH DOSE 40 mGy/min

## Slide 27: Example of scattered dose rate
16.2: Optimization of protection in fluoroscopy
<number>
Scattered dose is higher at the X-ray tube side

## Slide 28: Example of dose rate around mobile C-arm
16.2: Optimization of protection in fluoroscopy
<number>
Patient
Image Intensifier
100 cm 50 cm 0
Scale
1.2
3
6
12
X-ray tube
All Contour values in µGy/min

## Slide 29: Part 16.2: Optimization of Protection in Fluoroscopy
Topic 4: Protection tools
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 30: Protection tools (I)
16.2: Optimization of protection in fluoroscopy
<number>
CURTAIN
THYROID SHIELD
SCREEN AND GOGGLES

## Slide 31: Protection tools (II)
16.2: Optimization of protection in fluoroscopy
<number>
DIRECT BEAM
SCATTERED
RADIATION
LEADED
GLOVE
90 %
60 %
70 %
80 %
WITH W THE
ATENUATION IS  3 TIMES
BETTER THAN WITH Pb!!
100 kV
TRANSMITTED INTENSITY
100 kV
DIRECT BEAM
SCATTERED
RADIATION
GLOVE
WITH W
FOR THE SAME
TACTILE PERCEPTION

## Slide 32: Personal dosimetry
16.2: Optimization of protection in fluoroscopy
<number>
Several personal dosemeters are recommended
From: Avoidance of radiation injuries from interventional procedures. ICRP draft 2000

## Slide 33: Part 16.2: Optimization of Protection in Fluoroscopy
Topic 5: Radiation protection rules
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 34: Practical radiation protection rules (I)
16.2: Optimization of protection in fluoroscopy
<number>
ARTICULATED SHIELDING, LEADED APRONS, GLOVES, THYROID PROTECTORS, ETC, MUST BE READILY AVAILABLE IN THE X-RAY ROOMS
THEY MUST BE USED PROPERLY
POSSIBLE
PROBLEM:

## Slide 35: Practical radiation protection rules (II)
16.2: Optimization of protection in fluoroscopy
<number>
REGULAR QUALITY CONTROL
CHECKS MUST BE
ESTABLISHED
STAFF MUST SCHEDULE THESE
CHECKS AND PROVIDE
SUFFICIENT ROOM AVAILABILITY
POSSIBLE
PROBLEM:

## Slide 36: Practical radiation protection rules (III)
16.2: Optimization of protection in fluoroscopy
<number>
DOSE RATES MUST BE KNOWN IN EACH OPERATIONAL MODE AND FOR EACH INTENSIFIER INPUT SCREEN SIZE
CRITERIA FOR THE CORRECT USE OF ANY GIVEN OPERATION MODE MUST BE ESTABLISHED

## Slide 37: Practical radiation protection rules (IV)
16.2: Optimization of protection in fluoroscopy
<number>
IMPORTANT PARAMETERS:
SOURCE-TO- SKIN DISTANCE
PATIENT-IMAGE INTENSIFIER DISTANCE
PATIENT DOSE WILL INCREASE IF :
THE SOURCE-TO-SKIN DISTANCE IS SHORT
THE PATIENT-IMAGE INTENSIFIER DISTANCE IS LARGE

## Slide 38: Equipment and specialist (I)
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT
DEPENDENT
SETTINGS MADE BY
THE TECHNICAL
SERVICE
DOSE AND IMAGE AT
THE INTENSIFIER
INPUT
SPECIALIST
DEPENDENT
NUMBER OF IMAGES
RECORDED FOR EACH
PROCEDURE

## Slide 39: Equipment and specialist (II)
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT CHARACTERISTICS
THE ROLE OF THE SPECIALIST
ACTUAL INTENSIFIER PERFORMANCE CAN REQUIRE INCREASE IN DOSE RATE
TO KNOW THE ACTUAL INTENSIFIER PERFORMANCE AND THE REQUIRED DOSE RATE

## Slide 40: Equipment and specialist (III)
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT CHARACTERISTICS
THE ROLE OF THE SPECIALIST
GOOD WORKING CONDITIONS OF THE AUTOMATIC BRIGHTNES CONTROL AND THE POSSIBILITY TO DISABLE IT
USE IT PROPERLY IN ORDER TO AVOID HIGH DOSE RATE WHEN LEADED GLOVES ARE IN THE BEAM

## Slide 41: Equipment and specialist (IV)
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT CHARACTERISTICS
THE ROLE OF THE SPECIALIST
EASY SELECTION OF FIELD COLLIMATION
EFFECTIVE USE OF THE COLLIMATION

## Slide 42: Equipment and specialist (V)
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT CHARACTERISTICS
THE ROLE OF THE SPECIALIST
GRID FACTOR
INTENSIFIER PERFORMANCE
LEVEL OF NOISE, PULSE RATE, PULSE LENGTH, ETC.
PROTOCOL 
TOTAL PATIENT DOSE PER PROCEDURE

## Slide 43: Radiation risk for staff
16.2: Optimization of protection in fluoroscopy
<number>
EQUIPMENT CHARACTERISTICS
THE ROLE OF THE SPECIALIST
ROOM DIMENSIONS
SHIELDING THICKNESS
X-RAY SYSTEM POSITION
DISTANCE AND RELATIVE POSITION OF THE STAFF WITH RESPECT TO THE PATIENT

## Slide 44: Summary (I)
16.2: Optimization of protection in fluoroscopy
<number>
Many physical factors may significantly affect patient and staff dose while working with a fluoroscopy equipment: beam geometry, distance from the source, Image Intensifier diameter, and type of fluoroscopy system.
There exist practical RP rules which allow to reduce such exposures
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 45: Summary (II): ”Golden rules”
16.2: Optimization of protection in fluoroscopy
<number>
Keep the II close to the patient
Do not overuse magnification modes
Keep the x-ray tube at maximal distance from patient
Use higher kVp where possible
Wear protective aprons and radiation monitors, and know where scatter is highest
Keep your distance, as far as is practicable
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 46: Where to Get More Information
16.2: Optimization of protection in fluoroscopy
<number>
Wagner LK and Archer BR. Minimising risks from fluoroscopic x rays. Third Edition. Partners in Radiation Management (R.M. Partnership). The Woodlands, TX 77381. USA 2000.
Avoidance of radiation injuries from medical interventional procedures. ICRP Publication 85.Ann ICRP 2000;30 (2). Pergamon
Radiation Dose Management for Fluoroscopically-Guided Interventional Medical Procedures, NCRP Report No. 168, National Council on Radiation Protection and Measurement. Bethesda, MD. 2010
Interventional Fluoroscopy: Physics, Technology, Safety, S. Balter, Wiley-Liss, 2001
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources