## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L19: Optimization of Protection in Mammography
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
19: Optimization of Protection in Mammography
<number>
Subject matter: mammography (scope is breast cancer screening)
The physics of the imaging system
How to maintain the image quality while complying with dose requirements
Main features of quality control
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
19: Optimization of Protection in Mammography
<number>
Introduction to the physics of mammography
Important physical parameters
The mammographic X-ray tube
The focal spot size
The high voltage generator
The anti-scatter grid
The Automatic Exposure Control
The dosimetry
Quality control

## Slide 4: Overview / objective
19: Optimization of Protection in Mammography
<number>
To be able to apply the principle of radiation protection to mammography including design, quality control and dosimetry.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 19: Optimization of Protection in Mammography
Topic 1: Introduction to the physics of mammography
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Introduction to the physics of mammography
19: Optimization of Protection in Mammography
<number>
X-ray mammography is the most reliable method of detecting breast cancer
It is the method of choice for breast screening programs in many developed countries
In order to obtain high quality mammograms at an acceptable breast dose, it is essential to use the correct equipment

## Slide 7: Main components of the mammography imaging system
19: Optimization of Protection in Mammography
<number>
Mammographic X-ray tube
Device for compressing the breast
Anti-scatter grid
Mammographic image receptor
Automatic Exposure Control System

## Slide 8: Mammography geometry
19: Optimization of Protection in Mammography
<number>

## Slide 9: Main variables of the mammographic imaging system
19: Optimization of Protection in Mammography
<number>
Contrast: capability of the system to exhibit small differences in soft tissue density
Sharpness: capability of the system to make visible small details (calcifications down to 0.1 mm)
Dose: the female breast is a radiosensitive organ and associated carcinogenic risk
Noise: determines how of a dose can be used given the task of identifying a particular object against the background

## Slide 10: Part 19: Optimization of Protection in Mammography
Topic 2: Important physical parameters
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 11: The contrast
19: Optimization of Protection in Mammography
<number>
Linear attenuation coefficients for different types of breast tissue are similar in magnitude and the soft tissue contrast can be quite low
The contrast must be made as high as possible by imaging with a low photon energy (hence increasing breast dose)
In practice, to avoid a high breast dose, a compromise must be made between the requirements of low dose and high contrast

## Slide 12: Variation of contrast with photon energy
19: Optimization of Protection in Mammography
<number>
10 20 30 40 50 Energy (keV)
1.0
0.1
0.01
0.001
Ca5 (PO4)3 OH
Calcification
of 0.1mm
Glandular tissue
of 1mm
Contrast
The contrast decreases
by a factor of 6 between
15 and 30 keV
The glandular tissue
contrast falls below 0.1
for energies above 27 keV

## Slide 13: Contributors to the total unsharpness in the image
19: Optimization of Protection in Mammography
<number>
Receptor blur: (screen-film combination) can be as small as 0.1 - 0.15 mm (full width at half maximum of the point response function) with a limiting value as high as 20 cycles per mm
Geometric unsharpness: focal spot size and imaging geometry must be chosen so that the overall unsharpness reflects the performance capability of the screen
Patient movement: compression is essential

## Slide 14: Radiation dose to the breast
19: Optimization of Protection in Mammography
<number>
Dose decreases rapidly with depth in tissue due to the low energy X-ray spectrum used
Relevant quantity: The average glandular dose (AGD) related to the tissues which are believed to be the most sensitive to radiation-induced carcinogenesis

## Slide 15: Radiation dose to the breast
19: Optimization of Protection in Mammography
<number>
The breast dose is affected by:
  the breast composition and thickness (use compression)
  the photon energy
  the sensitivity of the image receptor
The breast composition has a significant influence on the dose
The area of the compressed breast has a small influence on the dose
  the mean path of the photons < breast dimensions
  majority of the interactions are photoelectric

## Slide 16: Variation of mean glandular dose with photon energy
19: Optimization of Protection in Mammography
<number>
10 20 30 40 (keV)
20
10
2
1
0.2
8 cm
Mean Glandular Dose (arb. Units)
The figure demonstrates
the rapid increase in dose
with decreasing photon energy
and increasing breast thickness
For the 8 cm thick breast there
is a dose increase of a factor of 30
between photon energies of 17.5
and 30 keV
At 20 keV there is a dose increase
of a factor of 17 between
thicknesses of 2 an 8 cm
2 cm

## Slide 17: Contributors to the image noise
19: Optimization of Protection in Mammography
<number>
1) Quantum mottle
2) Screen mottle
3) Film Grain
4) Electronic noise

## Slide 18: Part 19: Optimization of Protection in Mammography
Topic 3: The mammographic X-ray tube
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 19: Contradictory objectives for the spectrum of a mammographic X-ray tube
19: Optimization of Protection in Mammography
<number>
The ideal X-ray spectrum for mammography is a compromise between
  High contrast and high signal-to-noise ratio (low photon energy)
  Low breast dose (high photon energy)

## Slide 20: The X-ray spectrum in mammography
19: Optimization of Protection in Mammography
<number>
It is not be possible to vary the SNR because the film may become over- or under-exposed
The figure gives the conventional mammographic spectrum produced by a Mo target and a Mo filter
10 15 20 25 30
15
10
5
Energy (keV)
Number of photons (arbitrary normalisation)
X-ray spectrum at 30 kV for an X-ray tube
with a Mo target and a 0.03 mm Mo filter

## Slide 21: Main features of the X-ray spectrum in mammography
19: Optimization of Protection in Mammography
<number>
Characteristic X-ray lines at 17.4 and 19.6 keV and the heavy attenuation above 20 keV (position of the Mo K-edge)
Reasonably close to the energies optimal for imaging breast of small to medium thickness
A higher energy spectrum is obtained by replacing the Mo filter with a material of higher atomic number with its K-edge at a higher energy (Rh, Pd)
W can also be used as target material

## Slide 22: Options for an optimum X-ray spectrum in mammography
19: Optimization of Protection in Mammography
<number>
Contrast is higher for the Mo-Mo target-filter combinations
This advantage decreases with increasing breast thickness
Using W-Pd for target-filter combination brings a substantial dose reduction but only recommended for thicker breasts

## Slide 23: Options for an optimum X-ray spectrum in mammography
19: Optimization of Protection in Mammography
<number>
Focal spot size and imaging geometry:
  The overall unsharpness U in the mammographic image can be estimated by combining the receptor and geometric unsharpness
  U = ([ f2(m-1)2 + F2 ]1/2) / m (equation 1)
  where:
  f: effective focal spot size
  m: magnification
  F: receptor unsharpness

## Slide 24: Variation of the overall unsharpness with the image magnification and focal spot
19: Optimization of Protection in Mammography
<number>
1.0 1.5 2.0
magnification
0.15
0.10
0.05
0.8
Overall unsharpness (mm)
For a receptor
unsharpness of 0.1 mm
Magnification can only
improve unsharpness
significantly if the focal
spot is small enough
If the focal spot is too
large, magnification
will increase
the unsharpness
0.4
0.2
0.1
0.01

## Slide 25: Part 19: Optimization of Protection in Mammography
Topic 4: The focal spot size
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 26: The focal spot size
19: Optimization of Protection in Mammography
<number>
For a screening unit, a single-focus X-ray tube with a 0.3 mm focal spot is recommended
For general mammography purposes, a dual focus X-ray tube with an additional fine focus (0.1 mm), to be used for magnification techniques exclusively, is required
The size of the focal spot should be verified (star pattern, slit camera or pinhole method) at acceptance testing, annually, or when resolution appears to have decreased

## Slide 27: Target/filter combination
19: Optimization of Protection in Mammography
<number>
The window of the X-ray tube should be beryllium (not glass) with a maximum thickness of 1 mm
The typical target-filter combinations are:
  Mo + 30 m Mo Mo + 25 m Mo
  W + 60 m Mo W + 50 m Rh
  W + 40 m Pd Rh + 25 m Rh
  W + 75 m Ag

## Slide 28: X-ray tube filtration
19: Optimization of Protection in Mammography
<number>
The beam quality is defined by the HVL
The European Protocol specifies that the HVL be between 0.3 and 0.4 mm Al at 28 kVp for a Mo-Mo combination

## Slide 29: Part 19: Optimization of Protection in Mammography
Topic 5: The high voltage generator
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 30: State-of-the-art specifications for screen-film mammography
19: Optimization of Protection in Mammography
<number>
Waveform with ripple not greater than that produced by a 6-pulse rectification system
The tube voltage range should be 25 - 35 kV
The tube current should be at least 100 mA on broad focus and 50 mA on fine focus.
The range of tube current exposure time product (mAs) should be at least 5 - 800 mAs
It should be possible to repeat exposures at the highest loadings at intervals < 30 seconds

## Slide 31: Part 19: Optimization of Protection in Mammography
Topic 6: The anti-scatter grid
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 32: Why an anti-scatter grid ?
19: Optimization of Protection in Mammography
<number>
Scatter significantly degrades the contrast of the image requiring an efficient anti-scatter
The effect is quantified by the:
Contrast Degradation Factor (CDF): CDF=1/(1+S/P)
where: S/P: ratio of the scattered to primary radiation amounts
Calculated values of CDF: 0.76 and 0.48 for breast thickness of 2 and 8 cm respectively

## Slide 33: The anti-scatter grid
19: Optimization of Protection in Mammography
<number>
Two types of anti-scatter grids available:
  stationary grid*: with high line density (e.g. 80 lines/cm) and an aluminum interspace material
  moving grid: with about 30 lines/cm with paper or cotton fiber interspace
The performance of the anti-scatter grid can be expressed in terms of the contrast improvement (CIF) and Bucky factors (BF)
*Should not be used as it introduces grid artifacts.

## Slide 34: The anti-scatter grid: performance indexes
19: Optimization of Protection in Mammography
<number>
The CIF relates the contrast with the grid to that without the grid while
The BF gives the increase in dose associated with the use of grid
CIF and BF values for the Philips moving grid
Breast thickness (cm) | CIF | BF
2 4 6 8 | 1.25 1.38 1.54 1.68 | 1.68 1.85 2.06 2.24

## Slide 35: Part 19: Optimization of protection in Mammography
Topic 7: The Automatic Exposure Control
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 36: Automatic exposure control device (AEC)
19: Optimization of Protection in Mammography
<number>
The system should produce consistent optical densities (optical density variation of less than  0.20 ) over a wide range of mAs
The system should use an AEC chamber located after the screen-film cassette to compensate for different breast characteristics
The detector should be movable to cover different anatomical sites on the breast
The system should be adaptable to at least three screen-film combinations

## Slide 37: Part 19: Optimization of Protection in Mammography
Topic 8: Dosimetry
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 38: Dosimetry in screen-film mammography
19: Optimization of Protection in Mammography
<number>
There is a low risk of radiation induced cancer associated with mammography
Essential to obtain high image quality images at the lowest possible dose
The Average Glandular Dose (AGD) is the dosimetry quantity recommended for risk assessment

## Slide 39: Dosimetry quantities
19: Optimization of Protection in Mammography
<number>
The AGD cannot be measured directly but it is derived from measurements with a standard phantom for the actual technique set-up of the mammographic equipment
The Entrance Surface Air Kerma (ESAK) free-in-air, i.e., without backscatter is the most frequently used quantity for mammography dosimetry
For other purposes (compliance with reference dose level) one may refer to ESD which includes backscatter

## Slide 40: Dosimetry quantities
19: Optimization of Protection in Mammography
<number>
ESAK can be determined by:
  a TLD or OSL dosimeter calibrated in terms of air kerma free-in-air at an HVL as close as possible to 0.4 mm Al with a standard phantom
  a TLD or OSL dosimeter calibrated in terms of air kerma free-in-air at a HVL as close as possible to 0.4 mm Al on the patient skin (appropriate backscatter factor should be applied to Entrance Surface Dose to obtain the ESAK)
  Note: due to low kV used the TLD and OSL are seen on the image
  a radiation dosimeter with a dynamic range covering at least 0.5 to 100 mGy (better than  10% accuracy)

## Slide 41: Part 19: Optimization of Protection in Mammography
Topic 9: Quality Control
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 42: Why Quality Control ?
19: Optimization of Protection in Mammography
<number>
BSS requires Quality Assurance for medical exposures
Principles established by WHO, (ICRP for dose), guidelines prepared by EC, PAHO,…
A Quality Control program should assure:
  The best image quality
  With the least dose to the breast
  Optimization

## Slide 43: QC Program Requirements (1)
19: Optimization of Protection in Mammography
<number>
X-Ray generation and control
  Focal Spot size (star pattern, slit camera, pinhole)
  OR System resolution
  Tube voltage (reproducibility, accuracy, HVL)
  AEC system (kV and object thickness compensation, optical density control, short term reproducibility...)
  Compression (compression force, compression plate alignment)
Bucky and image receptor
  Anti Scatter grid (grid system factor)
  Screen-Film (inter-cassette sensitivity, screen-film contact)

## Slide 44: QC Program Requirements (2)
19: Optimization of Protection in Mammography
<number>
Film Processing
  Base line (temperature, processing time, film optical density)
  Film and processor (daily quality control)
  Darkroom (safelights, light leakage, film hopper, cleanliness.….)
Viewing Conditions
  Viewing Box (brightness, homogeneity)
  Environment (room illumination)

## Slide 45: QC Program Requirements (3)
19: Optimization of Protection in Mammography
<number>
System Properties
  Reference Dose (entrance surface dose or mean glandular dose)
  Image Quality (spatial resolution, image contrast, threshold contrast visibility, exposure time)

## Slide 46: Introduction to measurements
19: Optimization of Protection in Mammography
<number>
This protocol is intended to provide the basic techniques for the quality control (QC) of the physical and technical aspects of mammography.
Many measurements are performed using an exposure of a test object or phantom.
All measurements are performed under normal working conditions: no special adjustments of the equipment are necessary.

## Slide 47: Introduction to measurements
19: Optimization of Protection in Mammography
<number>
Two types of exposures:
The reference exposure is intended to provide the information of the system under defined conditions, independent of the clinical settings.
The routine exposure is intended to provide the information of the system under clinical conditions, dependent on the settings that are clinically used.

## Slide 48: Introduction to measurements
19: Optimization of Protection in Mammography
<number>
The optical density of the processed image is measured at the reference point, which lies 60 mm from the chest wall side and laterally centred.
The measured optical density at the reference point is: 1.60 ± 0.15.

## Slide 49: Introduction to measurements
19: Optimization of Protection in Mammography
<number>
All measurements should be performed with the same cassette to rule out AEC variations and differences between screens and cassettes
Limits of acceptable performance are given, but often a better result would be desirable.

## Slide 50: Production of reference or routine exposure
19: Optimization of Protection in Mammography
<number>
- tube voltage
- compression device
- plexiglass phantom
- anti scatter grid
- SID
- phototimer detector
- AEC
- optical density control
Reference
exposure
28 kV
in contact with phantom
45 mm
present
matching with focused grid
in position closest to chest wall
on, central density step
central position
Routine
exposure
clinical setting
in contact with phantom
45 mm
present
matching with focused grid
clinical setting
on
clinical setting
For the production of the reference or routine exposure, a plexiglass phantom is exposed and the machine settings are as follows:

## Slide 51: Summary
19: Optimization of Protection in Mammography
<number>
To achieve the best image quality while keeping the breast dose as low as reasonably achievable is the goal for consistent screen-film mammography.
A well defined QC program can contribute significantly to the achievement of such a goal.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 52: References (1)
19: Optimization of Protection in Mammography
<number>
European Protocol for the Quality Control of the Physical and Technical Aspects of Mammography Screening. 2005. http://euref.org/index.php?option=com_phocadownload&view=category&id=1&Itemid=8
Birch R, Marshall M and Ardran G M 1979. Catalogue of spectral data for diagnostic X-Rays SRS30.
European Guidelines for quality assurance in mammography screening, 3rd Edition (2001) ISBN 92-894-1145-7.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources

## Slide 53: References (2)
Mammography quality control: Radiologic technologists manual. American College of Radiology, Reston, VA. 1999
Quality Control in Diagnostic Radiology, Gray JE. et al. http://diquad.com/QC%20Book.html
19: Optimization of Protection in Mammography
<number>