## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L11: Quality Assurance
General lecture
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Topics
11: Quality Assurance
<number>
  Quality Assurance definition.
  QA Management and responsibilities
  Outline of a Quality Assurance and Radiation Protection program for diagnostic radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Overview
11: Quality Assurance
<number>
To become familiar with the specific requirements related to QA concepts, radiation protection in diagnostic radiology and procedures for reviewing and assessing the overall effectiveness of radiation protection.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 4: Part 11: Quality Assurance General lecture
Topic 1: Quality Assurance Definition
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 5: Quality assurance programs (I)
11: Quality Assurance
<number>
A quality assurance program in diagnostic radiology, as defined by the WHO, is an organized effort by the staff to assure that the diagnostic images produced are of sufficiently high quality to provide adequate diagnostic information at the lowest possible cost and with the least possible exposure of the patient to radiation

## Slide 6: Quality assurance programs (II)
11: Quality Assurance
<number>
Registrants and licensees shall establish a comprehensive Quality Assurance program for medical exposures with the participation of appropriate qualified experts in radiation physics, taking into account the principles established by the WHO and the PAHO

## Slide 7: Quality assurance programs (III)
11: Quality Assurance
<number>
QA programs for medical exposures shall include:
Measurements of the output (e.g., dose, image quality, etc.) of the radiation generators and imaging devices at the time of commissioning and periodically thereafter
Verification of the appropriate physical and clinical factors used in patient diagnosis (or treatment)

## Slide 8: Quality assurance programs (IV)
11: Quality Assurance
<number>
QA programs for medical exposures shall include:
Written records of relevant procedures and results
Verification of the appropriate calibration and conditions of operation of dosimetry and monitoring equipment
Regular and independent quality audit of the QA program

## Slide 9: Quality assurance and quality control
11: Quality Assurance
<number>
QA programs are designed to ensure that the radiology equipment can yield the desired information. They include:
  Quality control techniques used to test the components of the radiological system and verify that the equipment is operating satisfactorily
  Administrative procedures or management actions designed to verify that:
    the quality control techniques are performed properly and according to a planned timetable,
    the results of these techniques are evaluated promptly and accurately,
    the necessary corrective measures are taken in response to these results.

## Slide 10: Quality administration procedures
11: Quality Assurance
<number>
Quality administrative procedures also include:
the assignment of responsibility for quality assurance actions
the establishment of standards of quality for equipment in the facility
the provision of adequate training
the selection of the appropriate equipment for each examination.

## Slide 11: QA Programs (VIII)
11: Quality Assurance
<number>
Responsibilities for certain quality control techniques and corrective action may be assigned to personnel qualified through training and experience, such as consultants, qualified medical physicists
Authorities at the state, federal, and international level can also play a key role in encouraging the implementation of effective quality control and assurance programs

## Slide 12: Part 11: Quality Assurance General lecture
Topic 2: Outline of a QA and RP program
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 13: Outline of a quality assurance and radiation protection program for diagnostic radiology (I)
11: Quality Assurance
<number>
Policy statement
Organization and responsibilities
Quality Assurance (and Radiation Protection) Committee
Radiation Protection Officer (these duties could be assumed by the medical physics expert, the radiologist or the radiographer)

## Slide 14: Outline of a quality assurance and radiation protection program for diagnostic radiology (II)
11: Quality Assurance
<number>
Medical Practitioner (Radiologist, other Physicians)
Qualified Expert in Diagnostic radiology Physics (Medical Physicist)
Justification and optimization of radiological procedures

## Slide 15: Outline of a quality assurance and radiation protection program for diagnostic radiology (III)
11: Quality Assurance
<number>
Patient dosimetry and image quality evaluation
Reject analysis
Quality control procedures
  Acceptance test and commissioning
  Constancy tests
  Status tests
  Verification of RP and QC equipment and material
  Follow up of the corrective actions proposed
Staffing levels and responsibilities

## Slide 16: Acceptance test
11: Quality Assurance
<number>
The acceptance test of the equipment after installation should be performed by the local medical physicist in the presence of the supplier to confirm that the equipment actually conforms to the technical specifications

## Slide 17: Commissioning
11: Quality Assurance
<number>
Commissioning is the process of acquiring all the data from equipment that is required to make it clinically useable in a specific department. This commissioning test provides the baseline values for the QC procedures

## Slide 18: End of Warranty (Acceptance) Test
A second test, similar to the acceptance test, should be performed about 30 days prior to the end of the warranty period
This assures that the equipment is still performing according to specification
This also provides the manufacturer time to correct items which do not meet specifications at no cost to the purchaser
11: Quality Assurance
<number>

## Slide 19: Outline of a quality assurance and radiation protection program for diagnostic radiology (IV)
11: Quality Assurance
<number>
Patient dosimetry and image quality evaluation
Education and training
Safety rules and procedures
    Purchasing procedure for diagnostic radiology equipment
    Use of Diagnostic radiology equipment and safety devices
    Individual exposure monitoring
    Calibration of measurement instruments
    Inspection and maintenance of diagnostic radiology equipment
    Workplace Monitoring

## Slide 20: Outline of a quality assurance and radiation protection program for diagnostic radiology (V)
11: Quality Assurance
<number>
Quality audits
Arrangements for individual monitoring and health surveillance
Records
  The authorization certificate
  Name of the person responsible for the QA program.
  Individual staff doses
  Results of area surveys

## Slide 21: Outline of a quality assurance and radiation protection program for diagnostic radiology (VI)
11: Quality Assurance
<number>
Records (cont.)
  Results of the calibration and verification of the measurement instruments.
  Results of acceptance and quality control tests.
  Patient dosimetry results and comparison with diagnostic reference levels (DRL’s).
  Inventory of X ray systems.

## Slide 22: Outline of a quality assurance and radiation protection program for diagnostic radiology (VII)
11: Quality Assurance
<number>
Records (cont.)
  Incident and accident investigation reports.
  Audits and reviews of the QA and radiation safety program.
  Installation, maintenance and repair work.
  Follow-up testing after maintennce and repair work
  Facility modification.
  Training provided (initial and continuous)

## Slide 23: Where to Get More Information (I)
11: Quality Assurance
<number>
Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards, Revision of IAEA Safety Series No. 115, IAEA, Vienna Austria, 2011
ICRP 73. Radiological Protection and Safety in Medicine. Annals of the ICRP, 26(2), 1996.
Quality Control in Diagnostic Radiology, Gray JE. et al. http://diquad.com/QC%20Book.html
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources

## Slide 24: Where to Get More Information (II)
11: Quality Assurance
<number>
European guidelines on quality criteria for diagnostic radiographic images, EUR 16260 report, (Luxembourg, EC), 1996. http://www.sprmn.pt/legislacao/ficheiros/EuropeanGuidelineseur16260.pdf
European guidelines on quality criteria for diagnostic radiographic images in pediatrics, EUR 16261 report, (Luxembourg, EC), 1996. http://www.e-radiography.net/regsetc/European_guide_children_extract.pdf
Quality criteria for computed tomography, EUR 16262 report, (Luxembourg, EC), 1997. http://w3.tue.nl/fileadmin/sbd/Documenten/Leergang/BSM/European_Guidelines_Quality_Criteria_Computed_Tomography_Eur_16252.pdf
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources