## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L 4: International system of radiation protection
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
4: International system of radiation protection
<number>
Subject matter: the international framework of radiation protection (RP) in medical field
The role of the international organizations in RP
The dose limitation system
Audience: radiographers, radiologists, medical physicists
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
4: International system of radiation protection
<number>
Concept and aims of Radiation Protection (RP)
The framework of RP
Relevant organizations in RP (ICRP, IAEA and UNSCEAR)
System of RP
  Justification of practices
  Limitation of doses
  Optimization of protection
Occupational, medical and public exposures
Dose limits
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
4: International system of radiation protection
<number>
To become aware of the ICRP’s conceptual framework and the international Basic Safety Standards requirement (BSS) for radiation protection in the medical field.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 4: International system of radiation protection
Topic 1: Concept and aims of Radiation Protection (RP)
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Concepts and aims of radiation protection
4: International system of radiation protection
<number>
Radiation Protection (RP) is a tool for the management of measures to protect health against the risks (for people and environment) generated by the use of ionizing radiation
Detriment: The total harm that would eventually be experienced by an exposed group and its descendents as a result of the group's exposure to radiation from a source
Always consider BENEFITS Vs RISKS

## Slide 7: Biological effects of ionizing radiation: aims of radiation protection
4: International system of radiation protection
<number>
Deterministic effects
  RP aims at PREVENTING them.
Stochastic effects
  RP aims at REDUCING them.

## Slide 8: Part 4: International system of radiation protection
Topic 2: The framework of RP
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 9: The framework of radiation protection (I)
4: International system of radiation protection
<number>
According to the BSS, any human activity that introduces additional sources of exposure so as to increase the exposure or the likelihood of exposure of people or the number of people exposed is called practice.
No practice should be authorized unless it produces sufficient benefit to the exposed individuals or to society to offset the radiation harm that it might cause; that is: unless the practice must be justified

## Slide 10: The framework of radiation protection (II)
4: International system of radiation protection
<number>
A limit should be applied to the dose (other than from medical exposures) received by any individual as the result of all practices to which he/she is exposed
This is called “application of individual dose limits”

## Slide 11: The framework of radiation protection (III)
4: International system of radiation protection
<number>
In relation to exposures from any particular source within a practice, except for therapeutic medical exposures, protection and safety shall be optimized in order that the magnitude of individual doses, the number of people exposed and the likelihood of incurring exposures all be kept as low as reasonably achievable, economic and social factors being taken into account, within the restriction that the doses to individuals delivered by the source be subject to dose constraints
This is called “optimization of protection”.

## Slide 12: Part 4: International system of radiation protection
Topic 3: Relevant organizations in RP (ICRP, IAEA and UNSCEAR)
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 13: How the system works
4: International system of radiation protection
<number>
ICRP
IAEA
UNSCEAR
INTERNATIONAL STANDARDS

## Slide 14: Relevant organizations in radiation protection: ICRP, IAEA, UNSCEAR
4: International system of radiation protection
<number>
ICRP provides recommendations
IAEA establishes standards of safety and provides for the application of the standards
UNSCEAR studies the effects of atomic radiation

## Slide 15: Relevant organizations in radiation protection: ICRP (I)
4: International system of radiation protection
<number>
ICRP (http://www.icrp.org)
  In preparing its recommendations, ICRP considers the fundamental principles and quantitative bases upon which appropriate radiation protection measures can be established, while leaving to the various national protection bodies the responsibility of formulating the specific advice, codes of practice, or regulations that are best suited to the needs of their individual countries.

## Slide 16: Relevant organizations in radiation protection: ICRP (II)
4: International system of radiation protection
<number>
ICRP (http://www.icrp.org)
  ICRP offers its recommendations to regulatory and advisory agencies and provides advice intended to be of help to management and professional staff with responsibilities for radiation protection. While ICRP has no formal power to impose its proposals on anyone, in fact legislation in most countries adheres closely to ICRP recommendations.

## Slide 17: Relevant organizations in radiation protection: UNSCEAR
4: International system of radiation protection
<number>
United Nations Scientific Committee for the Effects of the Atomic Radiation
UNSCEAR provides reports to United Nations General Assembly about use and effects of atomic radiation.

## Slide 18: Relevant organizations in radiation protection: IAEA (I)
4: International system of radiation protection
<number>
An independent intergovernmental, science and technology-based organization, in the United Nations family, that serves as the global focal point for nuclear cooperation
Statutory Objectives: to seek, to accelerate and enlarge the contribution of atomic energy to …. health …. throughout the word
IAEA (http://www.iaea.org)

## Slide 19: Relevant organizations in radiation protection: IAEA (II)
4: International system of radiation protection
<number>
Statutory functions with regard to safety:
  to establish standards of safety for the protection of health
  to provide for the application of these standards …. at the request of a state

## Slide 20: Part 4: International system of radiation protection
Topic 4: System of Radiation Protection
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 21: System of radiation protection
4: International system of radiation protection
<number>
Justification of practices
Limitation of doses
Optimization of protection

## Slide 22: Justification of a practice
4: International system of radiation protection
<number>
Justification means that any exposure produces sufficient benefit to offset the radiation harm that it might cause.
Thus, if the exposure has benefit it is not justified.

## Slide 23: Optimization of protection
4: International system of radiation protection
<number>
Optimization includes the criterion: doses should be “as low as reasonably achievable” assuming image quality is adequate for diagnostic purposes
Optimization means that minimum risk and maximum benefits should be achieved,
BENEFIT
RISK

## Slide 24: As Low As Reasonably Achievable
4: International system of radiation protection
<number>
refers to the continual application of the optimization principle in the day-to-day practice, i.e., while assuring adequate diagnostic image quality.
DOSE

## Slide 25: Limitation of doses
4: International system of radiation protection
<number>
The normal exposure of individuals shall be restricted so that neither the total effective dose nor the total equivalent dose to relevant organs or tissues, caused by the possible combination of exposures from non-medical authorized practices, exceeds any relevant dose limit, except in special circumstances
Dose limits shall not apply to medical exposures from authorized practices.

## Slide 26: Part 4: International system of radiation protection
Topic 5: Type of exposure
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 27: Occupational, medical and public exposures
4: International system of radiation protection
<number>
Occupational exposure
All exposures of workers incurred:
  in the course of their work, with the exception of exposures excluded from the Standards
  exposures from practices or sources exempted by the Standards

## Slide 28: Occupational, medical and public exposures
4: International system of radiation protection
<number>
Medical exposure:
Exposure incurred by patients
  as part of their own medical or dental diagnosis or treatment;
  by persons, other than those occupationally exposed, knowingly while voluntarily helping in the support and comfort of patients;
  by volunteers in a programme of biomedical research involving their exposure

## Slide 29: Occupational, medical and public exposures
4: International system of radiation protection
<number>
Public exposure:
Exposure incurred by:
  members of the public from radiation sources,
  excluding any occupational or medical exposure and the normal local natural background radiation
  but including exposure from authorized sources and practices and from intervention situations.

## Slide 30: Dose constraints (I)
4: International system of radiation protection
<number>
A prospective and source related restriction on the individual dose delivered by the source, which serves as a bound in the optimization of protection and safety of the source.
For occupational exposures, dose constraint is a source related value of individual dose used to limit the range of options considered in the process of optimization.

## Slide 31: Dose constraints (II)
4: International system of radiation protection
<number>
For medical exposure the dose constraint levels should be interpreted as diagnostic reference levels, except when used in optimizing the protection of persons exposed for medical research purposes or of persons, other than workers, who assist in the care, support or comfort of exposed patients.
Except…

## Slide 32: Dose constraints (III)
4: International system of radiation protection
<number>
Dose constraints are not dose limits.
Dose constraints do not apply to patients
In general, dose constraints should be established on the basis of the results of optimization
Except…

## Slide 33: Part 4: International system of radiation protection
Topic 6: Dose limits
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 34: Dose limits (occupational exposure)
4: International system of radiation protection
<number>
The occupational exposure of any worker should be controlled so that the following limits be not exceeded:
500 mSv
The hands and feet
500 mSv
The skin
20 mSv
The lens of the eye
Annual equivalent dose in:
20 mSv per year, averaged over defined periods of 5 years
50 mSv in any single year
Effective dose
Occupational dose limit
Application

## Slide 35: Dose limits (apprentices and students)
4: International system of radiation protection
<number>
For apprentices of 16 to 18 years of age who are being trained for employment involving exposure to radiation and for students of age 16 to 18 who are required to use sources in the course of their studies, the occupational exposure should be so controlled that the following limits be not exceeded:
  an effective dose of 6 mSv in a year;
  an equivalent dose to the lens of the eye of 20 mSv in a year; and
  an equivalent dose to the extremities or the skin of 150 mSv in a year.

## Slide 36: Pregnant workers
4: International system of radiation protection
<number>
A female worker should, in becoming aware that she is pregnant, notify the employer in order that her working conditions may be modified if necessary.

## Slide 37: The occupational exposure of women
4: International system of radiation protection
<number>
The notification of pregnancy shall not be considered a reason to exclude a female worker from work
The employer of a female worker who has indicated that she is pregnant shall adapt the working conditions in respect of occupational exposure so as to ensure that the embryo or foetus is afforded the same broad level of protection as required for members of the public

## Slide 38: Dose limits (public)
4: International system of radiation protection
<number>
50 mSv
The skin
15 mSv
The lens of the eye
Annual equivalent dose in:
1 mSv in a year (*)
Effective dose
Public dose limit
Application
(*) In special circumstances, an effective dose of up to 5 mSv in a single year provided that the average dose over five consecutive years does not exceed 1 mSv per year.

## Slide 39: Dose limitation for comforters and visitors of patients (I)
4: International system of radiation protection
<number>
The dose limits should not apply to comforters of patients, i.e., to individuals exposed while voluntarily helping (other than in their employment or occupation) in the care, support and comfort of patients undergoing medical diagnosis or treatment, or to visitors of such patients.

## Slide 40: Dose limitation for comforters and visitors of patients (II)
4: International system of radiation protection
<number>
However, the dose of any such comforter or visitor of patients should be constrained so that it is unlikely that his or her dose will exceed 5 mSv during the period of a patient's diagnostic examination or treatment. The dose to children visiting patients who have ingested radioactive materials should be similarly constrained to less than 1 mSv.

## Slide 41: Not considered for dose limits
4: International system of radiation protection
<number>
Some cases are not considered for dose limits, although they may increase the effective dose:
  Natural background radiation
    Origin: cosmic radiation and natural radioactive elements in the environment (2-3 mSv/year)
  Radiation received as consequence of medical exposure
    It may represent an increment of dose > than natural radiation, but it is not taken into consideration for dose limits.

## Slide 42: Summary
4: International system of radiation protection
<number>
The international RP system applies to different categories of personnel and to general public
Medical exposure is concerned only by two RP principles: justification and optimization
Dose constraints should be interpreted as diagnostic reference levels for medical exposure
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 43: Where to Get More Information
4: International system of radiation protection
<number>
Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards. Revision of IAEA Safety Series No. 115, IAEA, Vienna Austria, 2011
ICRP 73, Radiological Protection and Safety in Medicine. Annals of the ICRP, Vol. 26, Num. 2, 1996. Pergamon. UK.
The 2007 Recommendations of the International Commission on Radiological Protection, ICRP 103, Annals of the ICRP 37(2-4):1-332 (2007)
UNSCEAR 2008 Report to the General Assembly, with scientific annexes, United Nations Scientific Committee on the Effects of Atomic Radiation, United Nations, Vienna, Austria, 2008
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources