## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L 7: X Ray beam
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources

## Slide 2: Introduction
7: X Ray beam
<number>
A review is made of:
The production of X Rays for diagnostic radiology : Bremsstrahlung and characteristic X Rays
Beam filtration,scattering of X Rays, Quality and quantity of X Rays, X Ray spectrum and factors affecting X Ray spectrum
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
7: X Ray beam
<number>
  Bremsstrahlung production
  Characteristic X Rays
  Beam filtration
  Scattered radiation
  Factors affecting X Ray spectrum, Quantity and Quality
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
7: X Ray beam
<number>
To become familiar with the technological principles of the X Ray production.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 7: X Ray beam
Topic 1: Bremsstrahlung production
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6
7: X Ray beam
<number>
Electron-nucleus interaction (I)
Bremsstrahlung:
  radiative energy loss (E) by electrons slowing down on passage through a material
   is the deceleration of the incident electron by the nuclear Coulomb field
   radiation energy (E) (photon) is emitted.

## Slide 7
7: X Ray beam
<number>
With materials of high atomic number
  the energy loss is higher
The energy loss by Bremsstrahlung
  > 99% of kinetic E loss as heat production
  it increases with increasing electron energy
X Rays are dominantly produced by Bremsstrahlung
Electron-nucleus interaction (II)

## Slide 8
7: X Ray beam
<number>
Electrons strike the nucleus
N
N
n(E)
E
E1
E2
E3
n1
n3
n2
E1
E2
E3
n1E1
n2E2
n3E3
E
Emax
Bremsstrahlung
spectrum

## Slide 9
7: X Ray beam
<number>
Bremsstrahlung continuous spectrum
Energy (E) of Bremsstrahlung photons may take any value between “zero” and the maximum kinetic energy of incident electrons
Number of photons as a function of E is proportional to 1/E
Thick target  continuous linear spectrum

## Slide 10
7: X Ray beam
<number>
Bremsstrahlung spectra
dN/dE
dN/dE (spectral density)
E
From a “thin” target
E
E0
E0
E0= energy of electrons
From a “thick” target
E = energy of emitted
photons

## Slide 11
7: X Ray beam
<number>
X Ray spectrum energy (continuous part)
Maximum energy of Bremsstrahlung photons
  kinetic energy of incident electrons
In X Ray spectrum of radiology installations:
  Max (energy) = X Ray tube peak voltage
Bremsstrahlung
E
keV
50 100 150 200
Bremsstrahlung
after filtration
keV

## Slide 12: Part 7: X Ray beam
Topic 2: Characteristic X Rays
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology

## Slide 13
7: X Ray beam
<number>
Characteristic X Rays: Electron-Electron interaction (I)
Starts with ejection of e- mainly from k shell (also possible for L, M,…) by ionization
e- from L or M shell fall into the vacancy created in the k shell
Energy difference is emitted as photons
A sequence of successive electron transitions between energy levels
Energy of emitted photons is characteristic of the atom

## Slide 14
7: X Ray beam
<number>
L
K
M
N
O
P
Energy
(eV)
6
5
4
3
2
0
- 20
- 70
- 590
- 2800
- 11000
- 69510
0 10 20 30 40 50 60 70 80
100
80
60
40
20
L
L
L
K1
K2
K2
K1
(keV)
Characteristic X Rays (II)

## Slide 15
7: X Ray beam
<number>
Atom characteristics
A, Z and associated quantities
Hydrogen A = 1 Z = 1 EK= 13.6 eV
Carbon A = 12 Z = 6 EK= 283 eV
Molybdenum A = 96 Z = 42 EK= 19.0 keV
Tungsten A = 183 Z = 74 EK= 69.5 keV
Uranium A = 238 Z = 92 EK= 115.6 keV

## Slide 16: Radiation emitted by the X Ray tube
7: X Ray beam
<number>
Primary radiation: before interacting photons
Scattered radiation: after at least one interaction; need for Antiscatter grid
Leakage radiation: not absorbed by the X Ray tube housing shielding
Transmitted radiation: emerging after passage through matter

## Slide 17: Part 7: X Ray beam
Topic 3: X Ray Beam filtration
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology

## Slide 18
7: X Ray beam
<number>
What is beam filtration?
10 15 20 25 30
15
10
5
Energy (keV)
Number of photons (arbitrary normalisation)
X Ray spectrum at 30 kV for an X Ray tube
with a Mo target and a 0.03 mm Mo filter
Absorber placed between
Source and object
Will preferably absorb
the lower energy photons
Or absorb parts of spectrum
(K-edge filters)

## Slide 19
7: X Ray beam
<number>
Tube filtration
Inherent filtration (always present)
   reduced entrance (skin) dose to the patient (cut off the low energy X Rays which do not contribute to the image)
Additional filtration (removable filter)
  further reduction of patient skin and superficial tissue dose without loss of image quality
Total filtration (inherent + added)
Total filtration must be > 2.5 mm Al for a > 110 kV generator
Measurement of filtration  Half-Value Layer

## Slide 20
7: X Ray beam
<number>
Tube filtration
Filter
Exit window

## Slide 21
7: X Ray beam
<number>
Filtration
Change in QUANTITY
&
Change in QUALITY
spectrum shifts to higher energy
1- Spectrum out of anode
2- After window tube housing
(INHERENT filtration)
3- After ADDITIONAL filtration

## Slide 22: Part 7: X Ray beam
Topic 4: Scattered radiation
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology

## Slide 23
7: X Ray beam
<number>
Radiation emitted by the X Ray tube
Primary radiation : before interacting photons
Scattered radiation : after at least one interaction
Leakage radiation : not absorbed by the X Ray tube housing shielding
Transmitted radiation : emerging after passage through matter  Antiscatter grid

## Slide 24
7: X Ray beam
<number>
Scattered radiation
Effect on image quality
  loss of contrast
Effect on patient dose
  increasing of superficial and depth dose
Possible reduction through :
 use of grid
 limitation of the field to the useful portion
 limitation of the irradiated volume (e.g.:breast compression in mammography)

## Slide 25
7: X Ray beam
<number>
Anti scatter grid (I)
Radiation emerging from the patient
  primary beam: contributes to the image
  scattered radiation: reduces image contrast and contributes to the major part of the patient dose
the grid (between patient and film) eliminates most of scattered radiation
stationary grid
moving grid (better performance)
focused grid
Potter-Bucky system

## Slide 26
7: X Ray beam
<number>
Source of -rays
Lead
Scattered X Rays
Useful X Rays
Film and cassette
Patient
Anti scatter grid (II)

## Slide 27: Part 7: X Ray beam
Topic 5: Factors affecting X Ray spectrum
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology

## Slide 28
7: X Ray beam
<number>
FACTORS AFFECTING X Ray BEAM
TUBE CURRENT
TUBE POTENTIAL
FILTRATION
HIGH OR LOW Z TARGET MATERIAL
TYPE OF WAVEFORM

## Slide 29
7: X Ray beam
<number>
X Ray spectrum: tube current
400 mA
200 mA
X Ray Energy (keV)
Number of X Rays per unit Energy

## Slide 30
7: X Ray beam
<number>
X Ray spectrum: tube current
Change of QUANTITY
NO change of quality
Effective kV not changed

## Slide 31
7: X Ray beam
<number>
X Ray spectrum: tube potential
Change in QUANTITY
&
Change in QUALITY
- spectrum shifts to higher Energy
- characteristic lines appear

## Slide 32
7: X Ray beam
<number>
X Ray spectrum: filtration
Change in QUANTITY
&
Change in QUALITY
spectrum shifts to higher energy
1- Spectrum out of anode
2- After window tube housing
(INHERENT filtration)
3- After ADDITIONAL filtration

## Slide 33
7: X Ray beam
<number>
X Ray spectrum: Target Z
Higher Z
Lower Z
X Ray Energy (keV)
Number of X Rays per unit Energy

## Slide 34
7: X Ray beam
<number>
X Ray spectrum: Target Z
Three Phase
Single Phase
X Ray Energy (keV)
Number of X Rays per unit Energy

## Slide 35: Factors affecting
7: X Ray beam
<number>
X Ray Quantity
  TUBE CURRENT (mA)
  EXPOSURE TIME (s)
  TUBE POTENTIAL (kVp)
  WAVEFORM
  DISTANCE (FSD)
  FILTRATION
X Ray Quality
  TUBE POTENTIAL (kVp)
  FILTRATION
  WAVE FORM

## Slide 36: Summary
7: X Ray beam
<number>
We learned about the continuous Bremsstrahlung spectrum and the characteristic lines
Several factors (kV,filtration,current, waveform,target material) influence quality and/or quantity of the X Ray beam
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 37: Where to Get More Information
7: X Ray beam
<number>
The Essential Physics of Medical Imaging. JT Bushberg, JA Seibert, EM Leidholdt, JM Boone. Lippincott Williams & Wilkins, Philadelphia, 2011
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources