## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L 23: Organizing a QC in Diagnostic Radiology
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
23: Organizing a QA in Diagnostic Radiology
<number>
Subject matter: Quality control planning and organization
Description of the main step to follow to be able to put in place an effective QC program
The radiation protection related rules to QC in diagnostic radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
23: Organizing a QA in Diagnostic Radiology
<number>
  Standards of acceptable image quality
  Retake analysis
  Image quality and patient dose
  Effect of poor-quality images
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 4: Overview
23: Organizing a QA in Diagnostic Radiology
<number>
To become familiar with the specific requirements related to QC concepts, radiation protection in diagnostic radiology, and procedures for reviewing and assessing the overall effectiveness of radiation protection.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 23: Organizing a QC in diagnostic radiology
Topic 1: Standards of acceptable image quality
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Quality control programs (I)
23: Organizing a QA in Diagnostic Radiology
<number>
Radiology imaging equipment should produce images that meet the needs of the radiologist or other interpreters without involving unnecessary radiation dose to the patient.
Quality control contributes to the production of diagnostic images of a consistent quality by reducing the variations in performance of the imaging equipment.
The quality control aspects of a quality assurance program are not necessarily related to the quality (information content) of the image.

## Slide 7: Quality control programs (II)
23: Organizing a QA in Diagnostic Radiology
<number>
Quality control programs directed at equipment and operator performance can be of great value in improving the diagnostic information content, reducing radiation dose, reducing medical costs, and improving departmental management.
Quality control programs contribute to the provision of high quality health care.

## Slide 8: Quality control programs (III)
23: Organizing a QA in Diagnostic Radiology
<number>
Several studies have indicated that many diagnostic radiological facilities produce poor quality images and give unnecessary radiation exposure.
Poor equipment performance makes a significant contribution to the high prevalence of poor image quality.

## Slide 9: Effect of poor quality images
23: Organizing a QA in Diagnostic Radiology
<number>
A poor quality image has three negative effects:
  If the image is not of adequate quality, practitioners may not have all the possible diagnostic information and this may lead to an incorrect diagnosis.
  If the quality of the radiograph is so poor that it cannot be used, then the patient shall be exposed again, causing an increase in the cost of diagnosis.
  Unnecessary radiation dose also occurs in the production of inadequate quality radiographs.

## Slide 10: Standards of acceptable image quality
23: Organizing a QA in Diagnostic Radiology
<number>
Prior to the initiation of a quality control program, standards of acceptable image quality should be established.
Yhese standards should be objective, for example “acceptability limits values that characterize image quality”, but they may be subjective for example “the opinions of professional personnel” in cases where adequate objective standards cannot be defined.

## Slide 11: Retake analysis
23: Organizing a QA in Diagnostic Radiology
<number>
The analysis of rejected images is a basic component of the quality control program
Those images judged to be of inadequate quality are categorized according to cause, which may be related to the competence of the technical personnel, to equipment problems, or specific difficulties associated with the examination.
Maib causes of retakes:
  Exposure faults (particularly important in mobile radiographic equipment)
  Poor positioning
  Equipment function degradation or malfunction

## Slide 12: How to start ? (I)
23: Organizing a QA in Diagnostic Radiology
<number>
Look for past experience in the existing literature.
Take into account the personnel and resources available.
Assess the impact of the program

## Slide 13: How to start ? (II)
23: Organizing a QA in Diagnostic Radiology
<number>
“Basic” quality control focuses on image quality and patient dose
Establish criteria for each measurement, i.e., operating levels and control limits

## Slide 14: Basic advice !
23: Organizing a QA in Diagnostic Radiology
<number>
Corrective action should be documented, and:
  Should be performed within a reasonable time.
  The reports should be understood and known by radiologists and radiographers.

## Slide 15: Test objects for objective image quality evaluation
23: Organizing a QA in Diagnostic Radiology
<number>
Test for QC of monitors and laser printers
Test for QC of geometry in
fluoroscopy
Test for QC of radiography
Test for QC in mammography

## Slide 16: Clinical images and quality criteria for image quality evaluation (I)
23: Organizing a QA in Diagnostic Radiology
<number>
For a chest examination (P/A) projection:
Performed at full inspiration (as assessed by the position of the ribs above the diaphragm - either 6 anteriorly or 10 posteriorly) and with suspended respiration.
Symmetrical reproduction of the thorax as shown by central position of the spinous process between the medial ends of the clavicles.
Medial border of the scapulae outside the lung fields.
Reproduction of the whole rib cage above the diaphragm.

## Slide 17: Clinical images and quality criteria for image quality evaluation (II)
23: Organizing a QA in Diagnostic Radiology
<number>
For a chest examination (cont’d):
Visually sharp reproduction of the vascular pattern in the whole lung, particularly the peripheral vessels
Visually sharp reproduction of :
  a) the trachea and proximal bronchi,
  b) the borders of the heart and aorta,
  c) the diaphragm and lateral costo-phrenic angles
Visualization of the retrocardiac lung and the mediastinum
Visualization of the spine through the heart shadow
EUR 16260. CEC 1996.

## Slide 18: Patient dosimetry
23: Organizing a QA in Diagnostic Radiology
<number>
Dose indicators:
Entrance dose for simple examinations.
Dose area product, total number of images, and fluoroscopy time for complex procedures.
For some complex interventional procedures, maximum skin dose.
For CT scanner, CTDI, DLP, and the number of slices

## Slide 19: References (1)
23: Organizing a QA in Diagnostic Radiology
<number>
Quality Assurance in Diagnostic Radiology. World Health Organization. Geneva, 1982.
International Basic Safety Standards for Protection Against Ionizing Radiation and for the Safety of Radiation Sources. Safety Series115, IAEA, 1996.
ICRP 73. Radiological Protection and Safety in Medicine. Annals of the ICRP, 26(2), 1996.
NCRP 99, Quality Assurance for Diagnostic Imaging, 1988.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources

## Slide 20: References (2)
23: Organizing a QA in Diagnostic Radiology
<number>
European guidelines on quality criteria for diagnostic radiographic images. Report EUR 16260, 1996.
Quality Criteria for Diagnostic Radiographic Images in Pediatrics, (Office for Official Publications of the European Communities, Luxembourg), Report EUR 16261, 1996.
Quality Criteria for Computed Tomography. Report EUR 16262, 1999.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources