## Slide 1: RADIATION PROTECTION IN DIAGNOSTIC AND INTERVENTIONAL RADIOLOGY
L14: Radiation exposure in pregnancy
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 2: Introduction
14: Radiation exposure in pregnancy
<number>
Thousands of pregnant women are exposed to ionizing radiation each year
Lack of knowledge is responsible for great anxiety and probably unnecessary termination of pregnancies
For most patients, radiation exposure is medically appropriate and the radiation risk is minimal
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Explanation or/and additional information
Instructions for the lecturer/trainer

## Slide 3: Topics
14: Radiation exposure in pregnancy
<number>
Introduction to the problem
Example of dose per examination
Fetal radiation risk

## Slide 4: Overview / objective
14: Radiation exposure in pregnancy
<number>
To become familiar with the radiation exposure in pregnancy and associated dosimetry considerations.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Lecture notes: ( about 100 words)
Instructions for the lecturer/trainer

## Slide 5: Part 14: Radiation exposure in pregnancy
Topic 1: Introduction to the problem
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 6: Introduction
14: Radiation exposure in pregnancy
<number>
In some circumstances, the exposure is inappropriate and the unborn child may be at increased risk
Prenatal doses from most properly done diagnostic procedures present no measurably increased risk of prenatal death, malformation, mental impairment
Higher doses such as those from therapeutic procedures can result in significant fetal effects.

## Slide 7
14: Radiation exposure in pregnancy
<number>
Fetal skull
ribs
Blood outside uterus
Fetal dose 20 mGy
Example of justified use of CT in a pregnant female who was in a motor vehicle accident

## Slide 8
14: Radiation exposure in pregnancy
<number>
Free blood
Kidney ripped
off aorta (no contrast in it)
Splenic laceration
3-minute CT exam and taken to the operating room. She and the child survived.

## Slide 9: Situation analysis
14: Radiation exposure in pregnancy
<number>
Number of females getting exposed every week without knowing that they are pregnant: Inadvertent radiation exposure of early conceptus
Planned Exposures:
  patients needing radiological/nuclear medicine examinations or even therapy while pregnant
  Assessment of valve functions or implants screening or situations requiring cardiac catheterization
Accidental exposure in pregnancy
Occupational exposures in pregnancy
Exposure of female of reproductive capacity

## Slide 10: Inadvertent exposure
14: Radiation exposure in pregnancy
<number>
LMP
Periods due
Psychological
issue or uncertainty
14
28
Exposure
period
Qn. How sensitive is early conceptus

## Slide 11: Prevention of inadvertent exposure in pregnancy
14: Radiation exposure in pregnancy
<number>
When a female of reproductive age presents for an examination involving exposure of pelvic area. Ask:
  Is she likely to be pregnant? Is period overdue?
  This should be recorded at appropriate place in the form
  ? Females under 16, LMP
Depending upon answer:
  No possibility of pregnancy
  Proceed with the examination

## Slide 12: Sensitivity of the early conceptus
14: Radiation exposure in pregnancy
<number>
Till early 1980’s, early conceptus was considered to be very sensitive to radiation - although no one knew how sensitive?
Realization that
  organogenesis starts 3-5 weeks after conception
  in the period before organogenesis high radiation exposure may lead to failure to implant. Low dose may not have any observable effect.

## Slide 13: Patient definitely or probably pregnant
14: Radiation exposure in pregnancy
<number>
If pregnancy is established or likely: Review justification
  Can examination be deferred until after delivery
  Does delaying examination involve greater risk
  If procedure is to undertaken, the fetal dose should be kept to the minimum consistent with the diagnostic purpose(s)

## Slide 14: Part 14: Radiation exposure in pregnancy
Topic 2: Example of dose
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 15: High dose procedures
14: Radiation exposure in pregnancy
<number>
Defined as procedures resulting in fetal doses of tens of mGy
  Abdominal and pelvic CT, Ba studies
Dose estimations, typical doses in each department
If inadvertent exposure - the risk from radiation may be smaller than risks with invasive fetal diagnostic procedures. Further, termination may not be justified.

## Slide 16: Exposure of females of reproductive capacity
14: Radiation exposure in pregnancy
<number>
That is, non-pregnant females
Alternative investigations not involving radiation, whenever possible
At diagnostic level - death, malformation, growth retardation, severe mental retardation, heritable effects - not a significant issue. Only cancer induction needs considerations

## Slide 17: Pre-implant stage (up to 10 days)
14: Radiation exposure in pregnancy
<number>
Only lethal effect, all or none
Embryo contains only few cells which are not specialized
If too many cells are damaged - embryo is resorbed
If only few killed - remaining pluripotent cells replace the cells loss within few cell divisions
Atomic Bomb survivors - high incidence of both - normal birth and spontaneous abortion

## Slide 18: Approximate fetal doses from conventional X Ray examinations (data from the UK 1998)
14: Radiation exposure in pregnancy
<number>
M
e
an
(
mGy
)
M
a
x
i
mum
(
mGy
)
A
b
d
o
men
1
.
4
4
.
2
C
h
es
t
<
0
.
0
1
<
0
.
0
1
I
n
t
r
a
v
e
no
u
s
u
r
o
g
r
a
m o
r
l
um
b
a
r
s
p
i
n
e
1
.
7
1
0
P
e
l
vi
s
1
.
1
4
S
k
u
ll
o
r
t
h
o
ra
ci
c s
p
i
n
e
<
0
.
0
1
<
0
.
0
1

## Slide 19: Approximate fetal doses from fluoroscopic and computed tomography procedures (data from the U.K. 1998)
14: Radiation exposure in pregnancy
<number>

## Slide 20: Cardiac catheterization in pregnancy
14: Radiation exposure in pregnancy
<number>
Lead apron wrapped around mother’s abdomen from diaphragm to symphysis pubis
If possible, procedure should be performed after the period of major organogenesis (>12 weeks). At 4th month, volume of fetus is small so that there is great distance between fetus and chest
Dose in the range of 2 mSv

## Slide 21: Part 14: Radiation exposure in pregnancy
Topic 3: Fetal radiation risk
IAEA Training Material on Radiation Protection in Diagnostic and Interventional Radiology
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Part …: (Add part number and title)
Module…: (Add module number and title)
Lesson …: (Add session number and title)
Learning objectives: Upon completion of this lesson, the students will be able to:
…
. (Add a list of what the students are expected to learn or be able to do upon completion of the session)
Activity: (Add the method used for presenting or conducting the lesson – lecture, demonstration, exercise, laboratory exercise, case study, simulation, etc.)
Duration: (Add presentation time or duration of the session – hrs)
Materials and equipment needed: (List materials and equipment needed to conduct the session, if appropriate)
References: (List the references for the session)

## Slide 22: Fetal Radiation Risk
14: Radiation exposure in pregnancy
<number>
There are radiation-related risks throughout pregnancy which are related to the stage of pregnancy and absorbed dose
Radiation risks are most significant during organogenesis and in the early fetal period somewhat less in the 2nd trimester and least in the third trimester
Less
Least
Most risk

## Slide 23: Radiation-Induced Malformations
14: Radiation exposure in pregnancy
<number>
Malformations have a threshold of 100-200 mGy or higher and are typically associated with central nervous system problems
Fetal doses of 100 mGy are not reached even with 3 pelvic CT scans or 20 conventional diagnostic X Ray examinations
These levels can be reached with fluoroscopically guided interventional procedures of the pelvis and with radiotherapy

## Slide 24: Central Nervous System Effects
14: Radiation exposure in pregnancy
<number>
During 8-25 weeks post-conception the CNS is particularly sensitive to radiation
Fetal doses in excess of 100 mGy can result in some reduction of IQ (intelligence quotient)
Fetal doses in the range of 1000 mGy (1 Gy) can result in severe mental retardation particularly during 8-15 weeks and to a lesser extent at 16-25 weeks

## Slide 25
14: Radiation exposure in pregnancy
<number>
Heterotopic gray matter (arrows) near the ventricles in a mentally retarded individual occurring as a result of high dose in-utero radiation exposure

## Slide 26
14: Radiation exposure in pregnancy
<number>
Frequency of microcephaly as a function of dose and gestational age occurring as a result of in-utero exposure in atomic bomb survivors (Miller 1976)

## Slide 27: Leukemia and Cancer
14: Radiation exposure in pregnancy
<number>
Radiation has been shown to increase the risk for leukemia and many types of cancer in adults and children
Throughout most of pregnancy, the embryo or fetus is assumed to be at about the same risk for carcinogenic effects as children

## Slide 28: Leukemia and Cancer
14: Radiation exposure in pregnancy
<number>
The relative risk may be as high as 1.4 (40% increase over normal incidence) due to a fetal dose of 10 mGy
Individual risk, however, is small with the risk of cancer at ages 0-15 being about 1 excess cancer death per 1,700 children exposed “in utero” to 10 mGy

## Slide 29: Probability of bearing healthy children as a function of radiation dose
14: Radiation exposure in pregnancy
<number>

## Slide 30: Pre-conception irradiation
14: Radiation exposure in pregnancy
<number>
Pre-conception irradiation of either parent’s gonads has NOT been shown to result in increased risk of cancer or malformations in children
This statement is from comprehensive studies of atomic bomb survivors as well as studies of patients who had been treated with radiotherapy when they were children

## Slide 31: Radiation Exposure of Pregnant Workers
14: Radiation exposure in pregnancy
<number>
Pregnant medical radiation workers may work in a radiation environment as long as there is reasonable assurance that the fetal dose can be kept below 1 mGy during the pregnancy.
1 mGy is approximately the dose that all persons receive annually from natural background radiation.

## Slide 32: Research on Pregnant Patients
14: Radiation exposure in pregnancy
<number>
Radiation research involving pregnant patients should be discouraged

## Slide 33: Termination of pregnancy
14: Radiation exposure in pregnancy
<number>
Termination of pregnancy at fetal doses of less than 100 mGy is NOT justified based upon radiation risk
At fetal doses in excess of 100 mGy, there can be fetal damage, the magnitude and type of which is a function of dose and stage of pregnancy
In these cases decisions should be based upon individual circumstances

## Slide 34: Termination of pregnancy
14: Radiation exposure in pregnancy
<number>
High fetal doses (100-1000 mGy) during late pregnancy are not likely to result in malformations or birth defects since all the organs have been formed

## Slide 35: Risks in a pregnant population not exposed to medical radiation
14: Radiation exposure in pregnancy
<number>
Risks:
  Spontaneous abortion > 15%
  incidence of genetic abnormalities 4-10%
  intrauterine growth retardation 4%
  incidence of major malformation 2-4%

## Slide 36: Summary
14: Radiation exposure in pregnancy
<number>
Thousands of pregnant women are exposed to ionizing radiation each year
An appropriate risk evaluation should be made in order to avoid probably unnecessary termination of pregnancies
The justification principle of radiation protection should always be based upon individual circumstances.
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources
Let’s summarize the main subjects we did cover in this session. (List the main subjects covered and stress again the important features of the session)

## Slide 37: Where to Get More Information
14: Radiation exposure in pregnancy
<number>
ICRP Publication 84. Pregnancy and Medical Radiation (1999).
ICRP, 1986. Developmental effects of irradiation on the brain of the embryo and fetus. Annals of the ICRP 16 (4), Pergamon Press, Oxford
ICRP Publication 90, 2003. Biological Effects after Prenatal Irradiation (Embryo and Fetus). Annals of the ICRP 33 (1-2), Pergamon Press, Oxford
Notes: Part No...., Module No....Lesson No
Module title
IAEA Post Graduate Educational Course in Radiation Protection and Safe Use of Radiation Sources