## Slide 1: PREVENTION OF ACCIDENTAL EXPOSURE IN RADIOTHERAPY
Part 4: Clinical consequences of accidental exposures in radiotherapy
IAEA Training Course

## Slide 2: Overview / Objectives
Module 4.1: Clinical consequences of accidental exposures in radiotherapy
Objectives:
To provide basic knowledge of clinical consequences from the major case histories and to outline the clinical detection of radiotherapy accidents
Notes: <number>
<footer>
<header>
<date/time>
The single module in this part of the workshop has the objective to give some basic knowledge on the subject at hand.

## Slide 3: Module 4.1: Clinical consequences of accidental exposures in radiotherapy
IAEA Training Course

## Slide 4: Outline
Therapeutic ratio
Acute and late reactions
Normal tissue tolerance and reaction scoring
Accidental under- and over-exposure
Clinical consequences
  Organ specific
Clinical detection of accidental exposure
Lessons & recommendations

## Slide 5: Therapeutic ratio in radical radiotherapy
Radiation doses given for curative treatment of cancers are at the limit of normal tissue tolerance.
Late complications can be expected for a certain proportion of cure rate.
Notes: Slides 5 – 7:
Tumour control and normal tissue complications are non-stochastic or deterministic effects. Tumour control begins at a certain dose level (depending on the tumour types) and control rates increases rapidly with dose (Graph on Slide 6). Tissue complication rate starts at a certain dose depending on organ and increases rapidly with dose similar to tumour control rate. Tissue complications may reach 100% while tumour control may not reach 100%.

## Slide 6: Tissue response vs. absorbed dose
D1 = Low cures, no complications
D3 = High cures high complications
D2 = Moderate cures, minimal complications
Tumour control
Normal tissue damage
Notes: Acceptable” risk of complications depends on risk level, organ involved and severity on complications. The level of risk may differ between physician and patients.
At Dose Level 1 (D1), few patients are cured but no complications are seen. At D3, many patients are cured but with high rate of complications. At D2, there is moderate rate of cures with few complications. The dose level chosen for curative therapy may differ between physicians and centre but generally, a 5-10% rate of long term complication is expected.

## Slide 7: Therapeutic ratio in radical radiotherapy
“Acceptable” complications depend on
  Rate of complications
  Organ concerned
  Severity of effect
The risk level may differ between clinicians and patients
  Usual acceptable level is 5%
    Lower levels are accepted for serious complications e.g. spinal myelitis
Notes: Acceptable complications depends strongly on the severity and consequence to the patient. “Inconsequential” complications such as 100% risk of skin telengiectasia may be acceptable for curative therapy but 5% risk of myelitis is usually unacceptable

## Slide 8: Side-effects & complications of radiotherapy
Radiation reactions are divided according to time scale
  Acute - < 6 months from exposure
  Sub-acute - 6 - 12 months post-exposure
  Late - > 12 months post-exposure
Notes: Note : these time scales are taken from IAEA reference text and may differ from textbooks.

## Slide 9: Acute reactions
Acute reactions are a part of normal radiotherapy.
  Less important as they are usually minor and transient
Usually observed in tissues with rapid cell turnover (skin, mucosa, bone marrow …)
  Due to decreased cell replacement
  Manifested according to normal tissue turn-over time
Overexposure may increase the frequency and severity (up to necrosis)
Notes: Acute reaction occurs due to depletion of stem cell and consequently, senescence cell are not replaced. Cellular/tissue turn-over time differs between organs. Oral mucosa turns over in about 7-10 days and will manifest acute reactions earlier than skin which turns over in about 2 weeks.

## Slide 10: Acute reactions
Determinant factors for acute reactions are:
  1) total delivered dose
  2) total time of exposure
  3) organ concerned
  4) size of irradiated volume
  5) concomitant drugs (chemotherapy) or disease, e.g. diabetes, previous surgery
For a given dose, little correlation of early reactions with fraction size unless fraction size is high
For specified doses that are protracted, damage is reduced
Notes: 2. Prolonged overall treatment time allows cellular repopulation and therefore decreases acute reactions.
3. Organs have varying radiosensitivity
4. Larger area /proportion of organ irradiated will result in increased reaction.
5. Certain chemotherapeutic drugs may act as radiosensitisers. Diabetes may compromise vasculature and surgery especially to the abdomen and pelvis may cause bowel adhesions and may result in the same portion of bowel to be irradiated daily in pelvic radiotherapy.

## Slide 11: Acute reactions
Usually do not correlate with late effects therefore relatively high frequency acceptable
Except when reactions are severe leading to consequential late reactions
Examples:
  mucositis
  skin changes
Notes: Pictures show confluent (Grade 3) mucositis which do not necessarily translate to late complications.

## Slide 12: Acute reactions - reporting
Evaluation of radiation reactions are mostly subjective
To enhance uniformity, reactions are graded
  e.g. skin grade 2, mucosa grade 1
Commonly used scales include:
  NCIC
  RTOG
  EORTC
  LENT-SOMA

## Slide 13: Acute Morbidity Scoring System
Grade | [ 0 ] | [ 1 ] | [ 2 ] | [ 3 ] | [ 4 ]
UPPER G.I. | No change | Anorexia with <=5% weight loss from pretreatment baseline/ nausea not requiring antiemetics/ abdominal discomfort not requiring parasympatholytic drugs or analgesics | Anorexia with <=15% weight loss from pretreatment baseline/nausea &/ or vomiting requiring antiemetics/ abdominal pain requiring analgesics | Anorexia with >15% weight loss from pretreatment baseline or requiring N-G tube or parenteral support. Nausea &/or vomiting requiring tube or parenteral support/abdominal pain, severe despite medication/hematemesis or melena/ abdominal distention (flat plate radiograph demonstrates distended bowel loops | Ileus, subacute or acute obstruction, performation, GI bleeding requiring transfusion/abdominal pain requiring tube decompression or bowel diversion
LOWER G.I. INCL. PELVIS | No change | Increased frequency or change in quality of bowel habits not requiring medication/ rectal discomfort not requiring analgesics | Diarrhea requiring parasympatholytic drugs (e.g., Lomotil)/ mucous discharge not necessitating sanitary pads/ rectal or abdominal pain requiring analgesics | Diarrhea requiring parenteral support/ severe mucous or blood discharge necessitating sanitary pags/abdominal distention (flat plate radiograph demonstrates distended bowel loops) | Acute or subacute obstruction, fistula or perforation; GI bleeding requiring transfusion; abdominal pain or tenesmus requiring tube decompression or bowel diversion
Example for some tissues from the RTOG Acute Morbidity Scoring System
Notes: Slides 13 and 14:
Scoring systems have detailed description of symptoms which can be graded accordingly. However these descriptions are lengthy and are difficult to remember except for common ones such as skin toxicity which are seen daily. Table in S14 is a practical simplified form which roughly correlates with the established scales and can be used in a busy clinic. Grade 1 is when there are mild symptoms which does not require intervention. Grade 2 reactions require medication. Grade 4 reactions usually requires radiation to be stopped and extensive supportive care given to patients. Grade 3 reactions are more difficult where clinical judgement is required on whether radiation should be continued, delayed or stopped bearing in mind, delays in radiation therapy may reduce cure rates.

## Slide 14: Reaction grading summary
Grade | Symptoms | Intervention | Radiation
0 | Nil | Nil | Cont.
1 | Mild | Nil | Cont.
2 | Moderate | Medication | Cont.
3 | Severe | Supportive | ?Delay / Stop
4 | Life threatening | Supportive ++ | Stop

## Slide 15: Acute side effects - grades
Grade 1
Erythema
Grade 2
Dry desquamation
Grade 3
Moist desquamation
Grade 4
Necrosis
Notes: Pictures are examples of various grades of skin reactions from Grade 1-4.

## Slide 16: Late reactions
Manifest >12 months from exposure
  but may occur earlier if severe overdose
Incidence increases over time
Bladder and rectal complications following radiotherapy for cervical cancer
Notes: Graph shows rate of urinary tract and rectal complication following radiotherapy for cervical cancer. The rate of rectal complications stabilises after 5 years but bladder complications continue to rise up to 25 years on follow-up.

## Slide 17: Late reactions
Mainly observed in tissues with slowly proliferating cells
  complications are due to arteriolar / capillary narrowing which occur over time
    causes hypoxic damage
Late complications can also manifest on rapidly proliferating cells
  in addition to and after acute effects
They are irreversible and often slowly progressive
  late reacting tissue are considered as dose-limiting for conventional radiotherapy
Late complications can also be consequential to severe acute reactions
  they are slowly progressive, and potentially possible to delay using vascular modifiers
Notes: Late complication of radiotherapy is due mainly to vascular damage and hypoxia. These complications are considered dose-limiting as they are usually progressive and irreversible. Organs such as nervous system, bladder etc are known as late-reacting tissues.

## Slide 18: Late reactions
Determinant factors:
  total delivered dose
  fraction size and dose rate
    In the case of accidental exposure, the increased fraction size may amplify the effects (this was the case in some accidents)
    Late responding tissue are more sensitive to increases in fraction size than are early reacting tissues (low α/β ratio)
  organ concerned
    e.g. nervous system, lung, rectum, bladder

## Slide 19: Late reactions
In serial organs (spinal cord, intestine, large arteries), a lesion of a small volume irradiated above threshold may cause major incapacity, for example paralysis
In organs arranged in parallel, such as lung and liver, severity is related to the irradiated tissue volume above threshold
Notes: Human organs may be divided into serial and parallel arrangement. In serially arranged organs such as spinal cord or intestine, disruption of function in one segment will affect the function of the organ distal to the affected segment. Therefore injury to a small segment proximally will cause major incapacity.
In organ arranged in parallel, the functional capacity is more dependent on the amount of normal tissue available. Therefore severity is related to the volume of tissue irradiated –higher volume irradiated results in increased severity.

## Slide 20: Late reactions
Complications are more severe and are irreversible
  Example: radiation myelitis
  Measured as risk, therefore not inevitable
    Expected only in very low frequency
    Given as % per 5 years
Necrosis
Ulcer
Notes: Picture 1 (above) is an MRI of a patient who received radiotherapy for thyroid cancer and develop spinal myelitis (hyperintense lesion on MRI)
Picture 2 (below) shows telengiectasia and ulceration of the chest wall following radiotherapy for recurrent breast cancer.

## Slide 21: Radiation tolerance doses (cGy)
Notes: Every organ in the body has a tolerance level to radiation. The risk of late reactions in these organs depends on the dose and is given as percentage risk of complication in 5 years. TD 5/5 means 5% risk of complication in 5 years and TD 50/5 is 50% risk in 5 years.
For example there is a 5% risk of developing ulceration of fibrosis from irradiation of 100cm2 of skin to 5500 cGy. This risk increases to 50% at 7000cGy.The brain is more sensitive and whole brain irradiation to 5000 cGy carries a 5% risk of cerebral necrosis with a 50% risk at 6000cGy. Visceral organs are generally sensitive to radiation. Whole lung irradiation has a 5% risk of pneumonitis/ fibrosis at 1500 cGy and 50% risk at 2500cGy. Note that with partial lung irradiation, the tolerance is much higher (4000Cgy and 6000cGy respectively).

## Slide 22: Late Radiation Morbidity Scoring
Example for some tissues from the RTOG Late Morbidity Scoring System
Notes: As with acute reactions, late reactions can be graded using a scoring system. The table shows an example from the RTOG scoring system.

## Slide 23: Accidental medical exposure
Under-exposure
Over-exposure
  Total dose
  Dose per fraction
  Site / area of exposure
    Normal tissue tolerance
    Normal tissue irradiation
Notes: Accidental exposure could mean either under or over-exposure.
Under-exposure means the tumour has received less dose than intended.
Over-exposure could be an increase in total dose, increased dose per fraction for a given total dose, wrong dose by mistake given relative to normal tissue tolerance or wrong site irradiated (e.g. left instead of right) resulting in irradiation of normal tissues.

## Slide 24: Consequences of accidental exposure
Reduced tumour control rate
Acute complications
Late complications
Notes: Accidental exposure (AE) could result in reduced tumour control both from under-exposure due to reduced tumour dose and also from over-exposure as if discovered, treatment parameters may have to be modified possibly compromising cures.

## Slide 25: Accidental medical exposure
Accidental exposure may be
  Random (one-off)
    Minimize by double-checking and independent calculations
    Under-exposure can be compensated by, e.g. accelerated treatment
    Over-exposure may cause increased reaction and also compromised tumour control
  Systematic
    Due to failure of system, e.g. calibration, calculation, TPS, etc.

## Slide 26: Random accidental exposure
Involves one or a few patients only
Examples
  Wrong calculation
  Wedge not inserted
    Wedge factor calculation
  Source displacement
    Movement after insertion
  Wrong source strength
    Higher activity than ordered
Notes: Random AE is usually due to human error and can be minimised or detected by independent checks and fail-safe systems.
Human error could easily lead to wrong calculation even by experienced staff
Example include wedges (manual) not inserted after calculation of wedge factors which is typically 2 – 6; brachytherapy source displacement due to movement especially with LDR systems or machine malfunction. (e.g. HDR machine USA 1992)

## Slide 27
Systematic accidental exposure
This is due to failing in the system of planning and delivery of radiation therapy
Includes
  Calibration of machine or source
  TPS related
  Systematic manual miscalculation
More serious than random event as it potentially affects all patients in a time period

## Slide 28: Systematic under-exposure
Accidental under dosage effects are difficult to detect clinically through reduced side effects and may only manifest as poor tumour control.
  May only be apparent years later after audit or not detected due to change in treatment patterns
  This may involve large number of patients
Notes: Slides 28 - 30
Due to variation in sensitivity of patients to irradiation, under-exposure is difficult to detect. Clinicians may congratulate themselves on ”good planning” when patients have less side-effects. Detection may only occur after audit or noticeably poor treatment results years later
Example is the TPS problem in UK with systematic under-dosing of patients by 30%. If we consider an 85% control probability for prostate cancer at a dose of about 78Gy, a 10% underdose (72Gy) results in a control rate of only 30%.

## Slide 29: Case 1: Incomplete understanding and testing of a TPS (UK 1982 – 90)
SSD correction for distance were usually done by the technologist
When a new TPS was acquired, same correction continued
  however the TPS already corrected for distance
Therefore double distance correction was done causing under dosage of up to 30%
The problem not discovered for 8 years,1045 patients affected
492 patients developed local recurrence

## Slide 30: TCP vs. absorbed dose
Data from Hanks et al 2002
Notes: This slide is based on the clinical data from the original Fox Chase radiation dose escalation study for prostate with >9 years follow-up. It is used here to illustrate the clinical consequence when treating patients with too low dose as in this TPS under dosage accident.

## Slide 31: Accidental medical over-exposure
Over-exposure may be
  Localized
    Related to treatment by EBRT or brachytherapy
  Whole body
    Accidental non-medical exposure, e.g. industrial exposure or public exposure

## Slide 32: Localized over-exposure
Depends on treatment area
  Organ specific but skin usually involved
Radiation modality
  Photon
    Deeper tissues involved
  Electrons
    Superficial tissues
  Brachytherapy
    Local tissues
Notes: Skin may not be involved in brachytherapy incidents.

## Slide 33: Accidental systematic over-exposure
Wrong calibration of source
  Use of incorrect decay curve for 60Co, USA 1974 –1976
    22 months of no beam measurement
  Reuse of outdated computer file for 60Co treatment, USA, 1987–1989
  Beam miscalculation of 60Co, Costa Rica,1996
    During beam calibration reading of the timer was confused, leading to underestimation of the dose rate

## Slide 34: Accidental systematic over-exposure
TPS related
  Untested change of procedure for data entry into TPS, Panama, 2000
    Calculated treatment time double the normal value leading to 100% overdose
  Change in practice - use of trimmer bars (computer file not updated, USA, 1987-1988
    Patients received 75% higher dose
  Accelerator software problem, USA and Canada,1985-1987

## Slide 35: Accidental systematic over-exposure
Machine related
  Incorrect accelerator repair and communication problems, Spain, 1990
    Electron energy was misadjusted
  Dose monitoring system
    Białystok incident Poland

## Slide 36: Types of overdose
According to AAPM-Tg35
Type A > 25% overdose
  Dose range may put patient in LD 50 / 5 range, i.e. 50% risk of death in 5 years
Type B 5-25% overdose and most underdosage
  Not life threatening
  Increased risk of complications or reduced tumour control
Notes: The AAPM report 56 divides overexposure into types A & B according to relative degree of overexposure.

## Slide 37: Clinical consequences of over-exposure
Severe over-exposure (off the chart)
  Early manifestation of symptoms
    Skin erythema, nausea & vomiting, diarrhea
  Often leads to death
    USA 1974–1976 300 of 450 died within 1 year
    Panama 2000 8* of 28 died
    USA / Canada 1985–1987 3 of 6 died
    USA source left in patient 1 of 1 died
  Survivors usually have chronic organ related symptoms e.g. diarrhea, bleeding, etc.
    88% of survivors in USA had severe complications
*5 patients - radiation related
Notes: With severe over-exposure, there are early symptoms chiefly in skin and gastro-intestinal tract. There is high risk of death and survivors have severe complications.

## Slide 38: Radiation tolerance doses (cGy)
Notes: The repeated table is a reminder of organ tolerance doses before the subsequent clinical scenarios. Note tolerance dose of GI tract.

## Slide 39: Clinical consequences of over-exposure
Skin (Białystok)
  Erythema usually develops after 1 week
    Erythema after few hours
  Moist desquamation (usually does not occur)
    Moist desquamation after few weeks
  Ulceration
    5 of 5 patients
  Late effects include fibrosis
Notes: As radiation needs to penetrate skin, there is almost always a skin reaction to over-exposure (example of Bialystok). With normal radiotherapy, the skin reaction develops after 1 week (or more) of treatment but with severe overdose, erythema occurred a few hours after treatment. Moist desquamation developed after a few weeks and ulceration, which is usually not seen, developed in all 5 patients (NB: following slides from the accident in Poland).

## Slide 40: Moist desquamation

## Slide 41: Ulceration

## Slide 42: Necrosis

## Slide 43: Clinical consequences of over-exposure
Gastro-intestinal (Panama)
  Mild diarrhea (grade 1 – 2) usual
    Severe diarrhea (G3) or necrosis (G4) in at least 20 of 28 patients
    8* patients died
  Symptoms usually resolve by 1 month post radiation
    Chronic symptoms about 100 – 230 days
  Long term
    Bowel stenosis, malabsorbtion, chronic diarrhea & dysentry
* 5 patients - radiation related
Notes: The gastro-intestinal tract namely small bowel is moderately sensitive to radiation and reactions manifests early following severe over-exposure (e.g. Panama). With conventional radiotherapy, grade 1 -2 diarrhoea is usual, but with severe over-exposure 20 patients(70%) developed grades 3 & 4 reaction. Acute reactions normally resolves a month post-radiation but lasted about 3 – 8 months for the Panama patients, many of whom (9 of 20) had long term severe complications such as stenosis and chronic diarrhoea (NB: following slides from the accident in Panama).

## Slide 44: Bowel ulceration
Notes: Slides 44 - 48 are pictures of bowel mucosa from over-exposure.

## Slide 45: Bowel necrosis
Necrosis

## Slide 46: Hemorrhagic rectal mucosa: two days before death

## Slide 47: Stenosis & obstruction
Notes: CT pelvis showing rectal stenosis
Radiograph of small bowel obstruction showing dilated loops of bowel.

## Slide 48: Rectal over-dosage
Notes: The rectal lumen is markedly narrower indicating stricture. There is also ulceration of the mucosa.

## Slide 49: Clinical consequences of over-exposure
Nervous system (brain)
  Tolerance dose is 50 Gy
    Younger patients with developing brain are at higher risk
  Cerebral atrophy, leucoencephalopathy, calcification
  Reduced IQ & dementia
  Spasticity
  Necrosis
Notes: Although the whole brain tolerance is 50 Gy, young children with developing brain are more sensitive to radiation and are at higher risk.

## Slide 50: Leucoencephalopathy
Notes: Picture of leucoencephalopathy.

## Slide 51: Beam miscalibration of 60Co
Whole brain radiation
  8 Gy in 4 fractions
  50 Gy in 16 fractions
Dose equivalent
  69.25 Gy (72 Gy)
Child affected by overdoses to brain and spinal cord, and the child lost his ability to speak and walk
Notes: <number>
<footer>
<header>
<date/time>
Example of over-exposure. The larger fraction size results in dose equivalent of about 70 Gy. The adult TD 50/5 is about 60 Gy hence the severe clinical consequence of retardation.

## Slide 52: Clinical consequences of over-exposure
Nervous system (spinal cord)
  Tolerance dose is 45 Gy (1-5% risk)
    Serially arranged therefore damage will manifest at all lower levels
  Acute myelitis occurs 2-4 months post-radiation
  Delayed myelopathy occurs at mean of 20 months
Notes: The spinal cord is a serially arranged organ and therefore radiation injury is potentially devastating. Acute myelitis usually recovers but delayed myelopathy is often permanent.

## Slide 53: Patient 80 – Undifferentiated Ca Pharynx
Notes: Slide 53 shows the treatment plan for a patient with hypopharyngeal cancer where the opposing fields included the spinal cord. The increased fraction size resulted in dose equivalent of about 65 Gy with clinical consequence of cord transection (necrosis) at cervical spine level and quadriplegia.

## Slide 54: Spinal cord myelopathy
Young woman who became quadriplegic as a result of accidental overexposure to the spinal cord
Dose
  51.7 Gy in 16 #
  = 64.4 Gy (67.6 Gy)

## Slide 55: Clinical consequences of over-exposure
Lung
  Pneumonitis
    Sub-acute reaction
    Dry cough, dyspnea, fever
    Prolonged course of high dose steroids required
    5% risk at 20 Gy
    50% risk at 30 Gy
  Fibrosis as late complication
Notes: The lungs are sensitive to radiation. Pneumonitis is a sub-acute reaction occurring a few months post-radiation with symptoms of dry cough, dyspnea and fever. Lung fibrosis is a late complication. Pictures show radiation pneumonitis and lung fibrosis.

## Slide 56: Other organs
Pleural Effusion
Pericardial Effusion
Notes: Other consequences include pericardial and pleural effusion following over-exposure.

## Slide 57: Other risks
Heart
  Ischaemic heart disease
Bladder
  Bleeding, frequency
Bone
  Fractures, necrosis
Alopecia
Non-specific life shortening & pain
Osteo-radio necrosis
Subcutaneous fibrosis
Notes: Other risk include Ischemic heart disease, alopecia and non-specific life-shortening and pain e.g. due for skin fibrosis. Picture show mandibular osteoradionecrosis following repeat irradiation for recurrent parotid carcinoma.

## Slide 58: Clinical detection of over-exposure
Careful clinical follow up may detect accidental overdose through early enhanced reactions
  This may be easier in uniform patient population
Experienced radiation oncologists may be able to detect clinically, during regular weekly consultation, dose variations of 10%
  In practice this is difficult due to varying radio-sensitivity between patients
Some overdoses may cause late severe effects without abnormal early effects
Notes: Detection of over-exposure requires knowledge, alertness and careful clinical follow-up during treatment to detect enhanced reaction. This may be easier in a uniform population e.g. all Caucasians with fair skin. Where there is a mix of patients treated on the same machine e.g. Caucasians, Oriental & African, it may be more difficult to appreciate subtle changes. It is reported that experienced oncologists can detect clinically a dose variation of 10% but in practice this is difficult e.g. USA where 450 patients were treated and overdosed undetected.

## Slide 59: Clinical detection of over-exposure
In case of unusual reactions of a single patient, other patients treated in the same period may need to be recalled
  Re-check all treatment parameters
  Check concomitant medications
  Check concomitant therapies
Notes: In practice, where unusual reaction is seen, a careful review of the patient’s treatment parameters, medication and concomitant therapies (e.g. traditional medication) is required. Other patients treated at the same period should be recalled and reviewed as well.

## Slide 60: Evaluation of accidental exposure
Determine if emergency or non-emergency
  Look for early prodromal symptoms
Skin may be a clue to radiation injury
  Appear similar to thermal injury but patient has no recollection of injury
  Associated with intractable pain
Notes: If there is evidence of over-exposure, determine if it is an emergency by looking for early prodromal symptoms. Skin reaction is a clue especially with severe overdose (e.g. Samut Prakarn) where the appearance is similar to thermal burn but the patient would not recall holding a hot object.
With lesser exposure, skin erythema and vomiting are early clinical symptoms. The severity and onset following exposure may give a guide to the dose received by the patient either by Whole Body Exposure (WBE) or (Localised Exposure).

## Slide 61: Guide for the management of radiation injuries based on early symptoms
Clinical signs |  | Corresponding dose (Gy) |  | Decisions
WBE | LE | WBE | LE | 
No vomiting | No early erythema | <1 | <10 | Outpatient with five week surveillance period (blood, skin)
Vomiting 2-3 h after exposure | Early erythema or abnormal sensation 12-24 h after exposure | 1-2 | 8-15 | Surveillance in a general hospital (or outpatient for 3 weeks followed by hospitalization if necessary)
Vomiting 1-2 h after exposure | Early erythema or abnormal sensation 8-15 h after exposure | 2-4 | 15-30 | Hospitalization in an haematological or surgical (burns) department
Vomiting earlier than 1 h after exposure and/or other severe symptoms e.g. hypotension | Early erythema within the first 3-6 h (or less) after exposure of skin and/or mucosa with oedema | >4 | >30 | Hospitalization in a well equipped haematological or surgical department with transfer to a specialized centre for radiopathology
Notes: The table gives a guide to the symptoms, estimated dose and suggest clinical action.

## Slide 62: Skin injury
Notes: Picture of bullae following direct handling of radioisotopes. Appearance is similar to thermal burn.

## Slide 63: Evaluation of radiation exposure
Determine type of exposure
  Whole body
  Local
  Inhaled / ingested
Determine site, exposure dose and number of fractions
  Calculate dose equivalent for organ in terms of Biological Equivalent Dose (BED) and 2 Gy equivalent
  Estimate risk of complications according to organ(s) concerned
Notes: Once over-exposure is suspected, try to determine the type of exposure. By knowing the site (s) and organs involved, the equivalent dose can be calculated and risk of complication estimated according to the specific organ.

## Slide 64: Treatment of injuries
Acute phase
  Symptomatic
    Pain relief, antibiotics
    Vasodilators, anti-platelets
Chronic phase
  Symptomatic
    Pain relief,
    Rehabilitation
  Surgical
    Debridement
    Grafts
Notes: Treatment in the acute phase is symptomatic with emphasis on pain relief as radiation injury often cause intractable pain. Antibiotics may be required and adjuncts such as vasodilator and anti-platelet agents may be used.
In the chronic phase, pain relief continues to be important. Rehabilitation especially of injured limbs may be necessary. Skin /tissue necrosis may require debridement and grafts.

## Slide 65: Healing of radiation injuries
Depends on extent of damage
  Healing by secondary intention
Slow process
  Takes months
  Results in scarring
Results in functional loss
  Skin, small bowel, etc.
June 2001
Dec 2001
Notes: Healing from radiation injury depends on extent of damage. This is a slow process which usually takes months and with functional loss. In the skin, with extensive moist dequamation or ulceration, due to depletion of the basal layer, healing is by secondary intention with skin closure occurring from the sides to centre.
Note the time-line of 6 months before partial closure of the ulcer.

## Slide 66: Progression of late injury
Injuries may worsen due to
  Increasing vascular compromise
  Infection
  Concomitant disease, e.g. diabetes
Early surgical intervention indicated if tumour controlled
June 2001
May 2002
Notes: However some lesion may worsen due to further complication such as infections. Pictures show progression of skin ulceration.

## Slide 67: Surgery for radiation necrosis
Omentum flap
Skin graft
Notes: Where there is good local tumour control, surgery may be consider in order to excise the dead tissues and obtaining skin cover. A vascularised flap is required due to vascular compromise in the area. However surgery often requires extensive procedures and should be done at specialised centres.

## Slide 68: Lessons learned
Working with Awareness and Alertness
  Maintain awareness for unusual and complex treatments
Procedures
  Use comprehensive acceptance, commissioning, quality control and documentation
Training and Understanding
Responsibilities
  Functions and responsibilities should be allocated
Notes: When a treatment plan is not routine and complex, staff must have increased awareness for potential complications.
The responsibility for the patient lies with all staff. Although the physician may be overall responsible, all categories of staff e.g. radiation technologist, nurses must alert the medical staff if they detect unusual reactions.

## Slide 69: Recommendations for prevention
A quality assurance program, involving:
  Organization
  Education and training
  Acceptance testing and commissioning
  Follow up of equipment faults
  COMMUNICATION
  Patients’ identification and charts

## Slide 70: Summary
Accidental exposure can be catastrophic and affect many patients
  Effects are often irreversible, progressive and increasing in frequency
  Careful clinical follow-up may detect overdoses of 10% or more
Underdosage is more difficult to detect clinically and may affect long term cures
A Quality Assurance program is a key element in prevention of accidental exposures.
  Good communication and lines of responsibility are essential

## Slide 71: References
IAEA publications
  Accidental Overexposure of Radiotherapy Patients in Bialystok (2004)
  Investigation of An Accidental Radiation Exposure of Radiotherapy Patients in Panama (2001)
  Accidental Overexposure of Radiotherapy Patients in San José (1998)
  Safety Report Series No.2
Nuclear Radiation Commission USA reports
Principles and practice of radiation oncology, Brady & Perez, 4th edition, Lippincott Williams
Radiobiology for radiologists, E.J. Hall, 5th Edition, Lippincott (2003)
Hanks G E et al. Dose response in prostate cancer with 8-12 years follow-up, IJROBP 54: 427-435 (2002)
AAPM report 56. Medical accelerator safety considerations. Report of AAPM Task Group 35
TecDoc no 88.